## Slide 1: Beam Test Facility Performance Update
Presented at the
SNS Accelerator & Target
Advisory Committee Meeting
Alexander Aleksandrov
SNS BTF Manager
May 16, 2018

## Slide 2: SNS Beam Test Facility (BTF) is close replica of SNS Front End
Particles | H-
Energy | 2.5 MeV
Current | < 50 mA
Pulse width | < 1 ms
Rep rate | < 60 Hz
Beam Power | < 7.5 kW
Ion Source and LEBT
RFQ
MEBT

## Slide 3: BTF construction and operation timeline
J
F
M
A
M
J
J
A
S
O
N
D
2014
J
F
M
A
M
J
J
A
S
O
N
D
2015
J
F
M
A
M
J
J
A
S
O
N
D
2016
J
F
M
A
M
J
J
A
S
O
N
D
2017
New RFQ arrives
Space allocated
End of BTF operation
New RFQ moved to SNS Front End
Ready for beam
Readiness Review
First beam
First 6-D scan complete
new RFQ characterization complete
1 year of operation
~50% beam availability

## Slide 4: BTF recovery and future operation timeline
J
F
M
A
M
J
J
A
S
O
N
D
2018
J
F
M
A
M
J
J
A
S
O
N
D
2019
Install Berkeley RFQ at BTF
Restore BTF operation with original MEBT configuration
installation of BTF beam line extension
Begin installation
Ready for beam
Plan is to operate:
for ~1 year
with ~50% beam availability
for high intensity beam dynamics experiment

## Slide 5: BTF diagnostics for measuring RFQ output beam
Movable phase detector (BPM)
y [mm]
y’ [radian]
Energy spectrum
Longitudinal emittance
[⁰]
Beam current
Beam energy
Transverse emittance
High power beam dump

## Slide 6: BTF can be used for
Ion Source testing in real environment
  External antenna source
Beam diagnostics development
  High dynamic range measurements
New SNS accelerator subsystems testing
  Controls, Power Supplies, etc.
High Intensity Beam Dynamics Study
  Beam Halo Experiment
Computer simulations tools benchmarking
  PyORBIT linac simulation code
Source of secondary particles
  Moderator Demonstration Facility
Training ground for young physicists and engineers

## Slide 7: High Intensity Beam Dynamics Experiment
Funded by National Science Foundation (NSF) grant through the University of Tennessee (S. Cousineau is the Principal Investigator)
  Support for postdoc, students and some hardware
Experimental investigation of halo formation in high intensity beam and computer simulation benchmarking
  Develop Six-dimensional (6D) particles distribution measurement system
  Build a test FODO line
  Develop reliable halo measurement system
Phase space density plot

## Slide 8: 6D Phase space measurement principle
SLIT_X_1
SLIT_Y_1
SLIT_X_2
SLIT_Y_2
dxdy
BEAMLET
dxdydx´dy´
BEAMLET
SLIT_X_4
SLIT_X_3
RF deflector
BENDING MAGNET
FARADAY CUP or other detector
MCP
Phosphor screen
Video Camera

## Slide 9: List of successful D>4 dimensionality scans*
Date |  | D | Scan time | Rep. rate | # points | Average # steps / dim
28 Nov 2016 | 40 mA | 5 | 0h 45min | 5 Hz | 270,000 | ~12
28 Nov 2016 | 40 mA | 5 | 0h 40min | 5 Hz | 240,000 | ~12
29 Nov 2016 | 43 mA | 5 | 3h 55min | 5 Hz | 1,530,000 | ~17
30 Nov 2016 | 41 mA | 5 | 3h 00min | 5 Hz | 1,080,000 | ~16
21 Dec 2016 | 38 mA | 5 | 5h 00min | 5 Hz | 1,800,000 | ~18
3 Mar 2017 | 32 mA | 5 | 2h 50min | 5 Hz | 1,020,000 | ~16
5 Mar 2017 | 30 mA | 5 | 5h 10min | 5 Hz | 1,860,000 | ~18
8 May 2017 | 41 mA | 5 | 20h 05min | 5 Hz | 7,300,000 | ~24
10 May 2017 | 19 mA | 5 | 4h 50min | 5 Hz | 1,740,000 | ~18
12 May 2017 | 30 mA | 5 | 4h 30min | 5 Hz | 1,620,000 | ~17
10 Jul 2017 | 25 mA | 5 | 13h 8min | 5 Hz | 4,730,000 | ~22
11 Jul 2017 | 25 mA | 5 | 15h 25min | 5 Hz | 5,550,000 | ~22
12 Jul 2017 | 26 mA | 5 | 15h 20min | 5 Hz | 5,520,000 | ~22
13 Jul 2017 | 24 mA | 5 | 12h 35min | 5 Hz | 4,530,000 | ~21
25 Oct 2017 | 39 mA | 6 | 32h 06min | 2.5 Hz | 5,675,740 | ~13
Date |  | D | Scan time | Rep. rate | # points | Average # steps / dim
28 Nov 2016 | 40 mA | 5 | 0h 45min | 5 Hz | 270,000 | ~12
28 Nov 2016 | 40 mA | 5 | 0h 40min | 5 Hz | 240,000 | ~12
29 Nov 2016 | 43 mA | 5 | 3h 55min | 5 Hz | 1,530,000 | ~17
30 Nov 2016 | 41 mA | 5 | 3h 00min | 5 Hz | 1,080,000 | ~16
21 Dec 2016 | 38 mA | 5 | 5h 00min | 5 Hz | 1,800,000 | ~18
3 Mar 2017 | 32 mA | 5 | 2h 50min | 5 Hz | 1,020,000 | ~16
5 Mar 2017 | 30 mA | 5 | 5h 10min | 5 Hz | 1,860,000 | ~18
8 May 2017 | 41 mA | 5 | 20h 05min | 5 Hz | 7,300,000 | ~24
10 May 2017 | 19 mA | 5 | 4h 50min | 5 Hz | 1,740,000 | ~18
12 May 2017 | 30 mA | 5 | 4h 30min | 5 Hz | 1,620,000 | ~17
10 Jul 2017 | 25 mA | 5 | 13h 8min | 5 Hz | 4,730,000 | ~22
11 Jul 2017 | 25 mA | 5 | 15h 25min | 5 Hz | 5,550,000 | ~22
12 Jul 2017 | 26 mA | 5 | 15h 20min | 5 Hz | 5,520,000 | ~22
13 Jul 2017 | 24 mA | 5 | 12h 35min | 5 Hz | 4,530,000 | ~21
25 Oct 2017 | 39 mA | 6 | 32h 06min | 2.5 Hz | 5,675,740 | ~13
* Many more of D=1,2,3,4 scans
and some of D=5,6 but not finished successfully are not listed

## Slide 10: Beam stability during 6D scan
32 hours of 6D scan

## Slide 11: Observed correlation in x’-w partial projection
1
2
3
1
2
3
Horizontal angle [rad]
full projection (energy spectrum)
looks ordinarily

## Slide 12: Similar patterns are observed in beam simulation with strong space charge
6D Gaussian
distribution
1.2 m
Partial projections
energy
x
x’=y=y’=0
energy
y
x=x’=y’=0
2.5 MeV
100 mA
Quadrupole magnets

## Slide 13: Successful demonstration of 6D phase space measurement technique and finding previously unknown correlations already opens new R&D possibilities for training young researchers and engaging small business
Improving speed and resolution of 6D scan
Manipulation of massive 6D data arrays
Methods of finding other correlations
Study of high order correlations in beam distribution function using particle tracking codes

## Slide 14: Focus-Drift-Defocus-Drift (FODO) line experiment
6D phase space measurements
Achromatic 180⁰ bend
Matching section
FODO line of 19
Permanent magnet quadrupoles
Large Dynamic Range emittance scanner
Beam dynamic simulation benchmark facility :
  Measured 6D distribution at input
  FODO transport channel as simulation “benchmark case”
  Large Dynamic Range emittance measurement at exit

## Slide 15: FODO beam line design
permanent magnet quad
permanent magnet quad holding structure
Magnetic measurements
Assembled FODO line

## Slide 16: BTF beam line simulation Graphical User Interface
Based on PyORBIT Particle-In-Cell code
Can use artificial or measured initial particle distribution
Multiple functions to aid in BTF optics setup
  Generation of distribution from measured emittances
  Particles tracking
  Achromat bend tuning, etc.
Test for potential application at SNS accelerator
Courtesy of Z. Zhang, A. Shishlo, A. Zhukov

## Slide 17: High Dynamic Range measurements (halo)
Measure transverse profiles with ~ 107 dynamic range
  - Switched amplifier gain to overcome Analog to Digital Converter (ADC) Bit depth limit
High Dynamic Range 1D scan
Slit-slit High Dynamic Range emittance scanner

## Slide 18: Long Term BTF development
Building wall
Beam dynamics beam line
PPS fence
BTF area expansion would allow two experiments to co-exist and to add other capabilities

## Slide 19: Summary
BTF was used for new RFQ testing. New RFQ successfully integrated to SNS Front End.
BTF operation will be restored by incorporating old SNS RFQ.
BTF will continue to be a test bench for SNS accelerator systems improvement and testing.
BTF provides unique opportunities for general accelerator physics R&D. There is ongoing R&D program for high intensity beam dynamics study.
BTF beam can be used for non-accelerator related R&D as well, e.g. Moderator Demonstration Facility (MDF). This will require the BTF area expansion.

## Slide 20: Scan time reduction opportunities
Maximize sampling rate to 10 Hz: slit speed, data saving, ~x4
2. Use smarter scanning algorithm, ~x2
80% of measured points are zero!
3. Redesign Beam Shape Monitor (BSM) for simultaneous W-ϕ measurement, ~x10
magnet
view screen
camera
RF deflector
φ
W
Notes: 20

## Slide 21: Permanent Magnet FODO line quadrupoles
Courtesy of A. Menshov
Mounting structure allows changing phase advance of FODO line using different combinations of magnets and drift lengths
Courtesy of A. Menshov
Magnet gradient:
G = 5.7367487 kG / 2.25 cm = 2.549666 kG/cm
Magnet strength:
G x L = 2.549666 kG/cm x 3.50 cm = 8.9238 kG

## Slide 22: Moderator Demonstration Facility
MDF layout
space for AP line
Neutron target with test moderator
Neutron beam lines
Laboratory Director Research and Development fund (LDRD) grant in FY15-16 to:
Design proton beam line
Feasibility study of 2.5MeV Li target
Feasibility study of neutronics and instrumentation
Accelerator driven source of neutrons, neutron beam lines and instrumentation for R&D on prospective moderator designs with hands on access
(requires ~ 50W of 2.5Mev protons)
MDF is feasible and of great importance for future source development (STS)