## Slide 1: ESS Experience with Ion Source and LEBT Control System Development and Commissioning
Nick Levchenko
Control Systems Engineer
www.europeanspallationsource.se
2016-09-xx

## Slide 2: Scope

## Slide 3: Stakeholders
INFN LNS (Catania)
CEA (Saclay)
ESS Accelerator Division
ESS ICS Division

## Slide 4: Control System Technical Solutions
VME-based very fast data acquisition and control (Faraday Cup, Magnetron, etc.), later transitioning to uTCA
EtherCAT-based fast data acquisition and control (power supplies, cooling and vacuum systems)
PLC-based local interlocking and control
PC-based IOC’s
MRF-based timing system (VME, PCIe)

## Slide 5: EPICS @ ESS
ESS EPICS Environment (EEE), collection of scripts to:
  Compile and install EPICS resources
  Create/run IOC’s without compilation (dynamic loading, introduced by Dirk Zimoch, PSI)
All machines are network-booted
All IOC’s run using centrally located EPICS modules
IOC’s are managed with IOC Factory

## Slide 6: Example IOC (Architecture)
IOC
Vacuum Controller
PLC
Power Supply
m-epics-mks945
m-epics-plc
m-epics-pstdk
require
require
require

## Slide 7: Module
7
Module version
EPICS versions
Architectures

## Slide 8: Controls Configuration Database (CCDB)
Defines which devices an IOC controls

## Slide 9: Controls Configuration Database (CCDB)
Defines which EPICS modules does IOC need for every controlled device

## Slide 10: IOC Factory
Configures the IOC (EPICS versions, module versions, etc.)

## Slide 11: IOC Factory
Configures the IOC (EPICS versions, module versions, macros)

## Slide 12: Example IOC (Generated by IOC Factory)
Vacuum Controller
PLC

## Slide 13: Advantages of module architecture
Support multiple EPICS versions
Automatic management of dependencies
Easy to manage multi-user work on the same IOC
  Can test individual modules in parallel with iocsh
Easy to reuse modules developed by other people for other IOC’s
Easy to switch between different module versions
Easy to work with remote users

## Slide 14: Modules distribution (m-epics-s7plc)
CEA EEE Server
ESS EEE Server
Lund, Sweden
Saclay, France
make
make install
rsync

## Slide 15: IOC configuration distribution (st.cmd)
CEA EEE Server
ESS EEE Server
Lund, Sweden
Saclay, France
rsync
www
CCDB, IOC Factory

## Slide 16: Current issues (work in progress)
Need for manual import of modules developed in remote locations
16
CEA EEE Server
ESS EEE Server
make
make install
rsync
CCDB, IOC Factory

## Slide 17: Current issues (work in progress)
Need for manual recompile of modules when adding new EPICS version
17
Module version
EPICS versions