## Slide 1: BLUESKY & OPHYD
A lightweight framework for Interactive and automated data collection
Arman Arkilic — NSLS2

## Slide 2
Data collection overview and FRAMEWORK COMPOnents
BLUESKY: Specify and execute experiments
OPHYD: Hardware abstraction layer
MIDDLE-LAYER SERVICES: Asynchronous and semi-structured services + archiver appliance
DATABROKER: Simplified interface to obtain data from middle layer
SUITCASE: Library that provides means to export experimental data from database to file
ARCHIVERAPPLIANCE: For PVs that were not captured by daq
http://nsls-ii.github.io/

## Slide 3
BLUESKY

## Slide 4: Captured and organized to facilitate reproducibility and searchability
RICH Metadata

## Slide 5: Seamlessly reuse a procedure on completely different hardware
Experiment generality
Same experimental procedure (“scan”)…
scan([point_detector], motor, 1, 5, 5)
…different hardware:
scan([area_detector], temp, 273, 283, 10)
There are many other procedures…
relative_scan([area_detector], temp, 273, 283, 10)

## Slide 6: Experiments are “rewindable,” recovering cleanly from interruptions
INTERRUPTION RECOVERY

## Slide 7: Experiments can be run unattended, automatically suspending and resuming if needed
Automated SUSPEND/RESUME

## Slide 8: Export data (live) into any desired format or database*
PLUGGABLE I/O

## Slide 9: CUSTOM EXPERIMENTAL PROCEDURES (“PLANS”) GET FEATURES FOR FREE
INTERRUPTION RECOVERY
Bluesky’s design separates specification from execution. The RunEngine (the executor) handles all of the following:
handling interruptions (Ctrl+C or automatic suspension)
I/O
“cleaning up”, e.g., putting hardware in a safe state at exit
User-defined procedures do not have to do any of this; they get it all “for free”.

## Slide 10: Interface naturally with numpy and Python scientific stack
INTEGRATION WITH SCIENTIFIC PYTHON
[“State of the Stack” by Jake VanderPlas, SciPy Conference 2015]

## Slide 11: Some niceties about bluesky
Key Bluesky Features
Ability to compose and combine complex plans in addition to built-in simple ones
Customizable callbacks: any function that accepts a Python dictionary as its argument can be used as a callback.
Interruptions: all plans can be interrupted
Suspenders: Signal can be monitored and execution suspended for appropriate condition
Asynchronous acquisition: flying and monitoring

## Slide 12
OPHYD

## Slide 13: Allows users to work with devices w/o epics expertise
ABSTRACTION LAYER ON TOP OF EPICS

## Slide 14: DEVICES HAVE Common attributes and methods
UNIFIES HARDWARE BEHIND SET/STOP
All Devices Have:
name -> human-friendly string identifying device
read() -> dict of human-readable names and values
describe() -> dict of metadata about each value
trigger()
stage() and unstage() -> a “context manager,” like arming
subscribe() -> asynchronously monitor
(…and a couple more optional ones)
“Movable / Settable” Devices Have:
set(…)
stop()

## Slide 15: What beamline/accelerator Staff thinks of a device
CLEAR SCOPING

## Slide 16
DECLARATIVE SYNTAX IN PYTHON

## Slide 17
PROVIDES AN INTERFACE FOR BLUESKY and ALIASES FOR PV(S)

## Slide 18
provides specialized classes for specific detectors supported by EPICS Area Detector

## Slide 19
ACKNOwledgements
Thomas Caswell
Dan Allan
Ken Lauer

## Slide 20: SOME NICETIES of ophyd
OPHYD
A Device is composed of Signals or of other Devices. Devices can contain other devices. Some devices map to single pieces of hardware (like a motor). Others group together many different pieces of hardware (like a diffractometer).
In one process, the same PVs might appear in multiple different Devices, so organized for different uses.
The staging process is a “hook” for preparing a device for use. To add custom staging logic to a Device, subclass it and override stage and/or unstage like so.
ophyd provides a high level interface that is used by bluesky: read, describe, trigger, stage, unstage, configure, read_configuration, describe_configuration
ophyd also provides a low level interface for exploration and debugging
ophyd comes with a set of “ready to use” devices: EpicsMotor, EpicsScaler, EpicsMCA/DXP, ‘AreaDetectors’
PVPositioner (explain what position is according to ophyd (we had an example about this somewhere)), Pseudopositioner(aliasing), SoftPositioner(debug)
ophyd provides means to compose custom devices (maybe a simple Cpt example, most likely not)
Difference between signal and device: sig no sub component
AreaDetector and specific hardware (most likely not but we have a list)
Reciprocal space