## Slide 1: areaDetector use and developments at Diamond
Ronaldo Mercado
Epics Collaboration Meeting
Oak Ridge
Sep 2016

## Slide 2: Outline
History
IOC count
Pilatus detectors with PPU
EPICS v4 plugin
Area Detector for ADCs
Computer vision – loop centring - at MX beamlines
Mapping project and SWMR
Conclusions
20 September 2016
Area Detector use and developments at Diamond

## Slide 3
History
Before 2010 All Diamond area detector data was to be handled by our upper level acquisition software (GDA).
  However, speed wasn’t great (Java) and there was no consistent framework.
  Consequently, GDA team selected EPICS area detector as their detector framework.
2010 onwards EPICS team takes over detector interfaces. Many areaDetector drivers and plugins used and developed.
December 2013 at NSLS-II Area detector working group formed.
3
20 September 2016
Area Detector use and developments at Diamond

## Slide 4: IOC count
  About 170 IOCs using areaDetector 1-9
About 40 IOCs using ADCore 2-4
Aravis GigE Camera IOCs ~ 80
Pilatus driver IOCs – 17
Medipix IOCs - 9
Pco camera IOCs – 8
Xspress3 IOCs – 7
Perkin Elmer IOCs - 4
Dxp IOCs (XIA) – 4
Pixium IOCs – 2
quadEM – 3
dtacq - 3
20 September 2016
Area Detector use and developments at Diamond

## Slide 5: Pilatus detectors with PPU
Unmerged changes to Pilatus detector driver, both related to use of PPU “Pilatus Processing Unit”
“Soft trigger” option (Giles Knap)
        Restores step scan performance without additional hardware – 20 Hz step scan vs 5 Hz when PPU is introduced.
        Overcomes extra latency in invoking the area detector pipeline.
CBF template copy (Ronaldo Mercado) Works around detector server and camserver not able to access template from central storage.
scp from ppu to detector server
Furka
/ramdisk to /ramdisk
(modified rsync)
Grimsel (modified rsync)
20 September 2016
Area Detector use and developments at Diamond
Scientific Computing
Detector

## Slide 6: EPICS v4 plugin
NDPvaPlugin
pvaDetector plugin
DLS purpose: mainly move data from Windows to Linux
Future intent: distribute processing to multiple hosts
20 September 2016
Area Detector use and developments at Diamond

## Slide 7: EDM screens for epics v4 plugin
20 September 2016
Area Detector use and developments at Diamond

## Slide 8: Area Detector for ADCs
quadEM (Mark Rivers)
CAENels TetrAMM
D-TACQ ADCs (Adam Bark)
NDReframePlugin (Ed Warrick)
Provides triggering by using an ADC channel.
ADEthercat (Ronaldo Mercado)
NDArrays from Ethercat ADCs
ADIvium (Jon Thompson)
NDArrays from Ivium multi channel potentiostat.
Area detector driver for Panda (Chris Turner)
NDArrays from Panda ADC channels
In development
20 September 2016
Area Detector use and developments at Diamond

## Slide 9: Auto-centring using adPython
Robot loads 75um Mitegen loop
Autocentring brings loop face-on
Zoom 2: Alignment at omega and omega +180 using findCircle and 1st round of rotation axis alignment
Zoom 10: Optimisation of the alignment until it converges to less than 4 pixels (1um)
FindCircle (through area detector)
Focussing through STAT plugin
Python script plugin (Hough circle finding): Tom Cobb and James O’Hea
Results
Tested with rotation axis off by 40um, it brings it back to within 3-4um
Repeatable (within 1um)
Takes few minutes
20 September 2016
Area Detector use and developments at Diamond

## Slide 10: Auto centring using adOpenCv
20 September 2016
Area Detector use and developments at Diamond

## Slide 11: adOpenCv pipeline and results
Camera
Blur (Gaussian)
Edge detect (canny)
Close
Sample locate
Values to GDA
Derivatives to detect sample loop widest point
Centre by moving motors
Results
Hough circle finding with moves, etc., takes minutes – too slow for unattended operation
“Sample locate” processing at 7 to 8 frames/sec
Turnaround time of 10 seconds
Can be used unattended when loop size matches crystal size
“sample locate” could be moved to adPython with no loss of performance
adPython is recommended for new projects.
20 September 2016
Area Detector use and developments at Diamond

## Slide 12: Mapping project and SWMR
Mapping
Work packages
            WP1 SWMR
            Single Write Multiple Read
            Pronounced “swimmer”
20 September 2016
Area Detector use and developments at Diamond

## Slide 13: Mapping
Move sample under focused x-rays
Continuous or trajectory motion (a.k.a. fly scan)
Interactions with the sample are recorded
Process
  Reduce data to create a map (image)
Visualization
  Show map of reduced data
  Click to see raw or detailed data
1 mm
Abs
DPC
DF
C
O
C
O
Fe
Slide Thanks to Mark Basham
20 September 2016
Area Detector use and developments at Diamond

## Slide 14: Mapping project work packages
WP1 - SWMR
WP2 - Visualisation
WP3 – Experimental Parameters
WP2.1 – NXScan
WP4 – EPICS/GDA Middleware
WP2.2 - Processing
Messaging
Data
20 September 2016
Area Detector use and developments at Diamond

## Slide 15: Conclusions
  The architecture works well Big advantage is that it has three data streams: Compressed video via ffmpeg for interactive visualisation Uncompressed frame data via channel access High speed data streaming to disk
  Consistent set of plugins
Many detector types, few of each
SWMR developments and NDPos plugin are a cornerstone of the Mapping Project
Gradually migrating to ADCore, still many IOCs using release 1-9
20 September 2016
Area Detector use and developments at Diamond

## Slide 16: Thank you for your attention
Slides/feedback
James O’Hea
Mark Williams
Alice Douangamath
Mark Basham
Giles Knap
Jon Thompson
Ulrik Pedersen
Chris Turner
James Mudd
Nick Rees
Tom Cobb
Mapping project
Analysis
  Mark Basham
  Alun Ashton
  Peter Chang
  Baha El Kassaby
  Jacob Filik
Science
  Andy Dent
  Paul Quinn
Controls
  Tom Cobb
  Alan Greer
  Ulrik Pedersen
  Gary Yendell
Acquisition
  Matthew Dickie
  Matt Gerring
  Rob Walton
  James Mudd
  Charles Mita
  Keith Ralphs
  Matthew Webber
Project Planning
  Kathryn Poulter
  Steven Launchbury
Acknowledgements
20 September 2016
Area Detector use and developments at Diamond