## Slide 1: JLab Hall B Controls: Infrastructure and IT Integration
Wesley Moore
JLab CNI
EPICS Collaboration Meeting
September 2016 - ORNL

## Slide 2: Overview
Hall B at JLab
Migration to modern software
  EPICS, GUIs, etc
Useful utility scripts
How we leveraged IT and security expertise
  Host Management
  Monitoring
  Remote Access
Future plans
Wesley Moore
wmoore@jlab.org

## Slide 3: Hall B at JLab
Hall B
CEBAF
Google Maps: taken 09/08/2016
Wesley Moore
wmoore@jlab.org

## Slide 4: Hall B at JLab
Torus Magnet
(while under construction)
CLAS12 Detector
Beamline
20-ton Radial Crane
Wesley Moore
wmoore@jlab.org

## Slide 5: Hall B at JLab
Torus Magnet
(commissioning)
CLAS12 Detector
Beam Direction
Torus Magnet
(front view)
Taken 09/08/2016
Wesley Moore
wmoore@jlab.org

## Slide 6: Hall B at JLab
Slow controls supports beamline,
detectors, and experiments
>50 apps/drivers, >65 IOCs
Diverse subsystem support:
Cryogenics (mostly PLC-based)
Detectors, targets
Magnets
Vacuum
Motors (collimators, harps, targets)
Scalers
Gas (He, N, etc)
High/Low voltage
Chillers
Slow Controls Team:
Wesley Moore, Nathan Baltzell (JLab)
Ken Livingston, Bryan McKinnon (Glasgow)
PLC Programming:
Nicholas Sandoval, Pablo Campero (JLab)
HPS
Wesley Moore
wmoore@jlab.org

## Slide 7: EPICS
EPICS R3.13.4
  VME-centric (VxWorks)
MEDM 3.1.9
ALH
No web interfaces
CVS for most code
  Some with no version control
EPICS R3.14.12.5
  softIOC-centric (RHEL7 64-bit)
CS-Studio 4.1.1
  Wrapper script generates tmp workspace
  Open MEDM-style Menu or Alarm Perspective
BEAST/Notifier
  Some script generated configs
WebOPI
  Read-only gateway access
  Used for Management Staff and basic monitoring
Git for all code
  Branching (master, develop, hotfix)
Before…
After…
Archiving done with JLab’s Mya Archiver/Viewer
<2yr migration
Migration
Wesley Moore
wmoore@jlab.org

## Slide 8: CS-Studio
CSS launcher scripts
clascss , opens CSS with MEDM-style.
clascss-alarm, opens CSS in alarm perspective with menu to the left.
Both generate temporary Workspaces, provides consistent behavior and user experience.
Migration
2
1
Wesley Moore
wmoore@jlab.org

## Slide 9: CS-Studio
GUIs a combination of:
Script generation, internal and external to CSS
Image overlays
Hand drawn
Migration
Wesley Moore
wmoore@jlab.org

## Slide 10: WebOPI
Configuration
RHEL7 VM, 8-Core, 8GB
Tomcat reverse proxyed behind Apache for access control.
Firewall rules allow access to Read-only CA Gateway.
Available off-site.
Apache/Tomcat: Marty Wise (JLab)
Migration
Findings
Images with PVs didn’t display.
Have seen linked OPIs not resolve.
Macro inheritance issues.
Had to use relative paths, we copied our full CSS Share to webserver.
font.def still needs tuning.
Wesley Moore
wmoore@jlab.org

## Slide 11: BEAST XML Generator
csv2beast.py
Import/export spreadsheet as CSV for convenience.
CSV converted to BEAST XML.
Sub-elements found by column headers.
Anyone have similar tools?
Utilities
Wesley Moore
wmoore@jlab.org

## Slide 12: softIOC Management
softioc_console*
Uses procServ.conf as “lookup table”
Issues ssh/telnet commands to softIOC host and port number
*Written by: Anthony Cuffe (JLab)
procServMgr*
Launcher for procServ
Uses a simple config file to manage:
  Server hostname
  telnet port number
  IOC enable/disable
  etc...
Key actions:
  start/stop/restart
  check (start if not running)
procServ.conf snippet
ssh –xt <hostname> telnet localhost <port>
Puppet
Installs cronjobs on softIOC servers, for polling procServMgr
Utilities
Wesley Moore
wmoore@jlab.org

## Slide 13: Host Management
Configuration
RHEL6 VM
Puppet
Puppet Dashboard
Facter (system profiling)
All open source
Notes
Host naming scheme makes Puppet config easier, allowing regex matching.
Not used for IOCs. Maybe in the future.
Manages
Installed packages, yum repos
NFS mount points, autofs
Group accounts/passwd
cron jobs for IOC startups
Ensures services running. Ex:
  CA Gateways
  iocLogServer
Logrotate
IT Integration
Puppet Server: Sherman White (JLab)
Wesley Moore
wmoore@jlab.org

## Slide 14: Monitoring
Configuration
RHEL6 VM
Nagios 4.0.6
NRPE 2.15
Apache
All open source
Notes
Sends Email and SMS alerts.
Monitors
Resources including:
CPU load
Disk space
Process count
Services including:
Alarm Server/Notifier
CA Gateways
Verify 2-factor logins
IT Integration
Wesley Moore
wmoore@jlab.org

## Slide 15: Linux VDI
Virtual Desktop Infrastructure
After installing client app:
Login to VDI connection server (password)
Select a VM-pool from list
Login to Linux VM (2-factor)
Hosted on our existing VM infrastructure
Cross-platform clients
Reconnect to existing sessions
Used for remote r/w access
VMs managed by Puppet, monitored by Nagios
IT Integration
Infrastructure: Myung Bang (JLab)
2
3
1
Linux uses VMware Blast protocol
Windows uses PCoIP
RHEL7 VM
Wesley Moore
wmoore@jlab.org

## Slide 16: Linux VDI Mobile
IT Integration
Horizon Toolbar
Samsung s5
Wesley Moore
wmoore@jlab.org

## Slide 17: VDI Misc.
IT Integration
Just to show Windows works fine too....
HTML Access
Connect to Virtual Desktop using only a browser
No client install required
We haven’t configured, but on the TODO list.
Win10, Samsung s5
Win8, Firefox
Credit: labs.vmware.com
Windows
Better support than Linux (No zero-clients yet)
Used for thin-clients and zero-clients at JLab
Wesley Moore
wmoore@jlab.org

## Slide 18: Future Plans
Integrate JLab tools with CS-Studio
  Logbooks
  Mya Archiver
Split alarm configuration
  Provide separate trees for main detectors
Improve deployment of new releases
  CS-Studio
  BEAST
  WebOPI and OPI tree to webserver
Configure VDI HTML access
Wesley Moore
wmoore@jlab.org

## Slide 19: Questions?
Acknowledgements:
Nathan Baltzell (JLab, Hall B)
Myung Bang (JLab, CNI)
Marty Wise (JLab, CNI)
Wesley Moore
wmoore@jlab.org