## Slide 1: New beamline from refurbished NSLS1 components. BDN (NextGen)
Oksana Ivashkevych, Controls’ Engineer
9/22/2016
NSLS1 beamlines, second life.

## Slide 2: BDN project summary
BDN, Beamlines Developed by NSLS2
Ex NextGen

## Slide 3: BDN project summary
BDN, Beamlines Developed by NSLS2
Ex NextGen
Project manager: Julian Adams
CMS is partner with Center of Functional Nanomaterials CFN.
Had First Light:
    CMS - Complex Material Scattering
    TES - Tender X-ray Absorption Spectroscopy
Will be build in 2017
    QAS - Quick X-ray Absorption and Scattering
    XFM - X-ray Fluorescence Microprobe

## Slide 4: Beamline outlook
CMS controls efforts started in March 2016
There were hutches, racks, no power till mid. May.
UHV Slits arrived first week of March.
IRR scheduled for August.

## Slide 5: Optimizing the efforts
Found a server
IOCs and GUIs were developed and tested once.
Independent of construction hiccups.
The server is on the
campus
Lab, beamline identical

## Slide 6: A – Hutch reused components
DMM Monochromator
Focusing mirror
- A Hutch Network Switch

## Slide 7: B – Hutch reused components
Micro-focusing KB mirror
Sample chamber
WAXS detector
SAXS detector
Flight path

## Slide 8: Monochromator
built by FMB Oxford 10 y. ago
Controlled by MCS8 with servo protection unit.

## Slide 9: Was……
EDM GUI

## Slide 10: Monochromator at the end
        ; Homing PLC for Axis 1 (PLC 8)
        OPEN PLC 8 CLEAR
        COMMAND"&1#1->X"
        COMMAND"&1 B1 R"
        DISABLE PLC8
        CLOSE

## Slide 11: KB micro-focusing mirrors
Horizontal x4 + Vertical x4 low current 160mA DC Servos with rotary encoders + 5V limit switches.
Designed by APS Beamline Controls & DAQ group some ~10 years ago.
Controller was a custom made servo drive in VME crate
Electronics and the interface card were designed by James Franck Research Institute University of Chicago.

## Slide 12: KBs with NSLS2 standard controls
  Abandoned old controls.
  Used Delta Tau low current version

## Slide 13: What went wrong….
41 pin horizontal and vertical connectors have different colors uses for the same pins.
Cable termination mistake caused a little smoke.
After fixing everything ……
One motor didn’t and still doesn’t work properly.
Observing bizarre interference between the channels.

## Slide 14: Looking for this board
Still looking for this board, unpopulated PCB, design document.
Planning to solder new part on existing board.
Believe UA9638 is a faulted part

## Slide 15: First Light log…
8/26/16, 6:13 pm
8/26/16, 6:32 pm
8/29/16, 5:16 pm
8/29/16, 5:53 pm
8/29/16, 6:12 pm
From beamline scientists: “Thanks for the Log Book, it is awesome!”
8/29/16, 6:36 pm

## Slide 16: Was is easier to build a beamline from refurbished components?
All major components were previously commissioned: they already worked.
All components were on site, No vendor dependencies, self paced, self planned.
Termination issues due to nonstandard equipment.
Controls efforts needed as usual were underestimated.
EASIER…

## Slide 17: First Light on Aug., 26 2016
Kevin Yager –CFN partner
Masa Fukuto – Lead Beamline Scientist
Lukas Lienhard – mechanical engineer
Rick Greene – beamline tech. coordinator
Oksana Ivashkevych - controls engineer