## Slide 1: MQTT Support for CS Studio
Megan Grodowitz
grodowitzml@ornl.gov

## Slide 2: What is MQTT?
Sensor devices publish messages to topics that describe the device or reading attributes
Applications receive updates to specific topics
A broker retains messages to reduce network traffic and power, while increasing reliability when devices drop out
Servers and storage can be used to log all messages in a central location

## Slide 3: MQTT Concepts
Topic
  A string identifier of the form “a/b/c/d/e”, where slashes separate subtopics
  Clients publish or subscribe to topics
  # is the glob symbol, i.e “a/#” means all subtopics of “a”
Broker
  Server program that receives, buffers, and send messages based on topic
  Each topic may contain up to 1 message value at a time, which may be retained
Client
  Anything that connects to the MQTT broker: serial devices, python scripts, java programs, etc.
  Clients send a unique identifier when they connect to the broker, e.g. MAC address

## Slide 4: MQTT Concepts
QoS
  Level 0: Deliver message at most once (fire and forget)
  Level 1: Deliver message at least once
  Level 2: Deliver message exactly once
  EPICS does not make message guarantee, uses put-callback to verify activity
Images from www.hivemq.com
QoS only describes client/broker guaruntees… No such thing as, say monitor/sensor or controller/motor guaruntee

## Slide 5: MQTT Concepts
Persistent Sessions
  Client can connect to broker with the clean session flag set false
  Messages are retained even if the client disconnects
  Clients must also maintain messages when broker disconnects
  Standard does not define how many or how long (until we run out of resources)
Message Retention
  Individual messages have a retention flag
  Message is retained indefinitely
  EPICS does not have central server, so traffic does not get retained anywhere unless something connects to channels, e.g. archiver
LWT (Last Will & Testament)
  A device can indicate a final message to send when it disconnects from the broker
  Often used to set status to “offline”
  EPICS device that drops out just disappears
No concept of Put-callback
  E.g. I cannot get a set acknowledgement that the servo has moved
  Best effort is to have the servo publish its position back to the same or other topic
  This has room for error/race conditions

## Slide 6: MQTT vs. EPICS Comparison
MQTT always has a broker
  No searching process where we try to discover devices: better for wide area network.
  EPICS does not need a broker, no single point of failure: good for local area network
MQTT broker is the only “connection”
  No such thing as disconnected PV
  To detect whether device is connected to broker, use status topic
MQTT messages are all plain text
  No type information (e.g. double, string, table)
  No meta-data fields (e.g. timestamp, alarm values)

## Slide 7: PVs and Widgets in CS Studio
PVs are attached to widgets using the PV property value
At runtime, PV value automatically updates widget, or can be used in rules or scripts.

## Slide 8: MQTT PV for CS Studio
VType PV plugin provides channel access, pv access, local, and simulated values
Examples values of PVs attached to widgets:
  loc://myvariable
  pva://SOME_CHANNEL
  sim://sine(1, 1, 10)
MQTT PVs are defined as:
  mqtt://topic[<type>]
Examples:
  mqtt://servo/rotation
  mqtt://servo/status<VString>
MQTT type names are the same as local PV values (VDouble, VString, etc)

## Slide 9: Encoding/Decoding PV Values from the Broker
Broker only sends text string
  We would like to maintain type info: Double, String, etc
  Indicated in PV name with <type>
  Default type when not indicated is a Double
What happens when a string arrives from broker?
More robust additions could include metadata
  E.g. timestamping
  Problem: Each device would need to conform to consistent string formatting
  This would require, for example, Python library to format PV metadata to string in a way consistent with CS Studio
  When in doubt, set the PV to type VString and process the input in a script

## Slide 10: MQTT PV for CS Studio
Specify a control widget to publish changes to a topic
Change PV value to publish to specified topic
Monitor status to get update from LWT when device disconnects
Specify a monitor widget to view changes to a topic

## Slide 11: Conclusions
Now CS Studio can open garage doors!
  Actually MQTT is used in a variety of real world applications
    EVERYTHNG, Amazon IoT, OpenStack, Open Geospatial Consortium SensorThings
  Support in many languages, WebSocket for MQTT for browsers
To use:
  Setup broker URL in preferences
  Use PV name mqtt://topic
  Integrates well into existing VType PV plugin
  Type support within CS Studio