## Slide 1: Plans for EPICS Version 4 at ESS
Timo Korhonen
Integrated Control System Division
European Spallation Source ERIC
www.europeanspallationsource.se
20 September 2016

## Slide 2: Outline
Why Version 4
Why at ESS?
The REAL goal is…
Some plans
  Services
  “Big Data”
  Atomic actions
Summary

## Slide 3: Why Version 4?
At the time EPICS was created, computers looked different…
In the past 30 years, capacities have change several orders of magnitude:
  Storage capacities: Mbytes to Gbytes to Tbytes
  Processor speeds from a few MHz to several GHz, multicore
  Software technologies have taken great leaps
  Network speeds 10 Mbit/sec to 10 (or soon 100) Gbit/sec
Our facilities have changed, too – a lot!
Data transport of EPICS, Channel Access has served the community really well
  Even too well? Is there a problem, after all?
  But: we should take advantage of the progress that has taken place

## Slide 4: Why V4 at ESS?
ESS is a facility with a planned lifetime of 40 years
  Starts to produce science in early/mid 2020’s
How often is there a chance to start really from scratch?
  Not very…
  ESS however has almost no legacy constraints
Apart from the technical reasons:
  This is a chance to give a push to move to a new standard that takes us…quite some way into the future. Next 30 years?

## Slide 5: EPICS 4 at ESS
The ESS targets to be fully EPICS 4 compliant
  Use EPICS 4 (pvAccess) for all control system applications
    No Channel Access or “implanted” other protocols
  pvAccess can replace CA functionality today – we think
    Performance, reliability, functionality
    Some enhancements needed
    Interoperability needs to be demonstrated
  IOC development is not (much) affected
    IOCs will work as before, drivers, etc., need no change
    CS-Studio needs some additional work
    Archiver Appliance will/does support V4 structures

## Slide 6: A confession
I do not have a perfect plan for all the things we want to do with V4 in ESS
However, the real goal is that:
  new young people enter the field and implement things that I cannot even imagine today
My ambition is to help to make this happen
  Build an infrastructure that opens new possibilities
Nevertheless, there are a few ideas
  So that I can claim my salary…

## Slide 7: Plans for V4
Use services extensively
  Improve integration of dynamic and static data
Use the new capabilities to improve data quality
  Better handling of measurement data (even in accelerator)
  Rich metadata, synchronous data
Data is the key to performance improvement
  As we heard in the opening talk
  V4 can effortlessly handle big data volumes
    Buzzword array:
      Big data – data mining – machine learning
    Jokes aside, there is potential here
  it does not cost much extra to use the new potential

## Slide 8: Services
What are “services”, after all?
  an IOC is a service that processes the input/output data
  I/O is not the only data that a (modern) control system needs to use or manipulate
Services isolate a certain function
  As long as the interface stays the same, no recompilation or any other changes needed
  Data consumer does not need to know how the data is produced
  For example a service that combines live and archive data; user does not need to know that data sources are different

## Slide 9: Some ideas with services
Uniform access to process and configuration data
  IOC can dynamically access its configuration data
    Magnet field conversion, RF field maps, etc.
Managing of collected data
  Experimental data, accelerator characterization data
  Machine snapshots (e.g. MASAR)
  Consistent storage, indexing and retrieval
  MetaDataStore and HDF5 files
Accelerator online model as a service
  Makes application writing easier

## Slide 10: Modeling example
Transverse
beam offset
Z
“A”
“B”
$ eget -s XCOR:IN20:491:RMAT -a b BPMS:IN20:525
0.669591 0.694604 0 0 -3.08532e-19 2.41325e-19
-0.570851 0.901275 0 0 -1.23627e-19 1.45491e-19
0 0 1.33379 0.966896 0 0
0 0 0.358415 1.00957 0 0
-2.29302e-24 8.92892e-20 0 0 1 1.20724e-05
1.00974e-28 0 0 0 0 1
$ eget XCOR:LI24:900:TWISS
energy 5.00512
psix 37.7625
alphax 13.6562
betax -2.78671
etax -0.00698294
etaxp 0.00107115
psiy 31.9488
alphay 116.762
betay 5.2592
etay 0
etayp 0
z 2438.72
Figure: EPICS V4 modelling service giving orbit response matrices and Twiss parameters for given devices. These are the basis of 95% of emittance minimization applications – feedback, steering, bumps, etc
From N. Delerue, Oxford Univ.
Greg White, Murali Shankar, Ivo List

## Slide 11: Devices, objects and so on
How many definitions of the term “device” you know?
  Depending on your point of view:
  A power supply is a device
  An (accelerator) cell is a device
  The whole accelerator is a device. And so on.
This may sound like stretching a bit but:
  Combining EPICS PVs you can create any device view that you like
    A pvData structure can become a device
    Perhaps even on the fly: use ChannelFinder to get the PVs
Flexible access to infrastructure data can make this possible

## Slide 12: Access to infrastructure & archive data
Greg White, Murali Shankar, Ivo List
$ eget -s LCLS:ELEMENTS
ELEMENT ELEMENT_TYPE EPICS_DEVICE_NAME S_DISPLAY OBSTRUCTION
CATHODE MAD CATH:IN20:111 2014.7 N
SOL1BK MAD SOLN:IN20:111 2014.7 N
CQ01 MAD QUAD:IN20:121 2014.9 N
SOL1 MAD SOLN:IN20:121 2014.9 N
XC00 MAD XCOR:IN20:121 2014.9 N
... (many rows snipped)
Directory Service (based in EPICS V4 channelFinder) examples:
Database example
Figure: Access to Database gives device infrastructure, magnet calibrations, drawing names, etc. Will be used in LCLS-II for cryogenic plant system hierarchy etc.
# The names of PVs, by device name pattern:
$ eget -s ds -a name=XCOR:LI21:135:%
name
XCOR:LI21:135:ABORT
XCOR:LI21:135:ACCESS
XCOR:LI21:135:ALLFUNCGO
XCOR:LI21:135:BACT
XCOR:LI21:135:BACTFO
# Regular expression (restrict to sectors LI25-LI29)
eget -s ds -a regex='XCOR:LI2[5-9]:.*:BDES’
# Device names of the instruments in the laser heater
$ eget -s ds -a etype INST -a tag LSRHTR -a show dname
# A recent search for invalid data in corrector PVs
$ eget -tTs ds -a name %COR:LTU%:%:%DES | \ eget -p ca -f - | grep nan
XCOR:LTU1:558:BDES nan
XCOR:LTU1:558:IDES nan

## Slide 13: “Big data”
V4/pvAccess can effortlessly handle large data volumes
This gives totally new possibilities
  Data that was not possible to collect can be made available for analysis
  Data mining, machine learning
  I am not a big believer of AI imminent success but there is potential to be discovered and used

## Slide 14: Atomic actions
How many times have you had to work around:
  Sending several data items that actually are a unit, and try to make an action
  Getting several pieces of data that belong together
Yes, it is possible to work around
  But you could use that time for something more productive – working on the actual issue!
Recent changes in EPICS make atomic actions possible (3.16)
  See Michael Davidsaver’s talk from Lund EPICS meeting
  Within one IOC – but this is already a lot!
  Cross-IOC atomicity still needs work(arounds)

## Slide 15: From a recent V4 presentation
Performance is excellent
Reliability needs have been met or exceeded
Easy programming and scripting, once you’ve got started
Complex data and RPC enables one, simple, high performance, infrastructure across the whole controls and online scientific system. Utility of this effect previously overlooked, but in practice seen to be key
Normative Types enable systems of narrowly defined services to be applied generally to many experiment user problems
Streaming supports big online data processing. Beats tested alternatives in ease of use and performance.

## Slide 16: Summary
ESS will be going fully for EPICS 4 (or 3+4…)
The foundations are available
  Have to be put into a stress test
Some functionality can be used straight away
  Archiver, CS-Studio, many services
Main issue is to build the potential for
  Modern methods
  Handling large datastreams
  Making things easier
The plan is not clear
  I am looking forward to things we will find out !