## Slide 1: Hazard assessment and the measures on the J-PARC Neutron Source - Short Term Release Modeling -
Yoshimi Kasugai
J-PARC (JAEA/KEK)
Accelerator Safety Workshop 2019
September 10, 2019
Oak Ridge National Laboratory (ORNL), Oak Ridge, Tennessee

## Slide 2: Introduction
Materials & Life Science Experimental Facility (MLF) in J-PARC
  A spallation neutron source using mercury target
  Huge amounts of radioactivity produced and enclosed in the target system.
The hazard assessment on a maximum credible accident was carried out.
  based on a short term release model of radioactive-materials due to loss of the confinement capability for radioactive products.
Radiation monitors and emergency operation processes has been prepared to mitigate the environmental impact.

## Slide 3: Outline of J-PARC
50GeV RCS
3GeV RCS
Liniac
Materials & Life Science Experimental Facility
Neutrino Experimental Facility
Central Control Building
Hadron Experimental Facility
500 m
1000 m
Notes: J-PARCは茨城県東海村にある施設群で、このように差し渡し1000mもあるおおきなものです。
この中に、リニアック、3GeVシンクロトロン、50GeVシンクロトロンの３つの加速器と、我々の関係する物質・生命科学実験施設の他、ニュートリノ、ハドロンの3つの実験施設があります。
ここで何をしているのかと言いますと、まず陽子を光速に近い速度まで加速します。
これを標的原子核にぶつけますと、原子核がバラバラに破砕される核破砕反応が生じて、いろいろな種類の二次粒子が飛び出してきます。これらの二次粒子を用いて様々な実験・計測を行っています。
私共の物質・生命科学実験施設ではこの中性子を用いて、物質科学や生命科学の研究を行っております。
中性子は、軽い元素に敏感であることや、透過力が強く、分子の振動や原子の運動を見ることが出来るなど、従来用いられているX線などによる方法では見えなかった現象の解明が可能であり、新規の科学分野が創成されつつあります。

## Slide 4
Cryogenic Hydrogen Circulation System
Target Trolley
Mercury Circulation System
Neutron Target vessel
Shutter
Protons
Neutrons
Hot Cell
Neutron Target Station

## Slide 5
Outline of the Neutron Target
*Mitigation of cavitation damage by microbubbles
Heat Exchanger
Surge Tank
Mercury Pump
Mercury Circulation System
Length： 12 m
Weight： 315 ton
Mercury Volume： 1.5 m3
Mercury Flow rate： 41m3/hr
Proton Beam
Material：SUS316L
Weight：1.6 t
Length：2m
Neutron Target Vessel
Safety hull cooling water
Mercury
Mercury
Microbubbles
Micro-bubble generator
Flow vanes
Proton Beam
Mercury Vessel

## Slide 6: Concept of the Radioactivity Confinement
Target Vessel
Drain Tank
Collection Tank
Catch Pan
Heat Exchanger
Cooling water
Cooling Water
Helium
Helium Vessel
ＭＬＦ Building
Proton Beam
Hot Cell
Off-gas Treatment System
Gas Monitor
Exhaust Stack
Exhaust System
Neutron Target Station
Mercury
Bubbling System
Gas Holders
2m3×7
Cover Gas (He)
Mercury Circulation System

## Slide 7: Inventory of Radioactivity
Various kinds of radioactive nuclides are produce via spallation reactions.
  The mercury circulation system confines radioactivity with more than 1016 Bq after full beam operation.
Volatile radioactivity
  Tritium (3H): 1015 Bq
  Noble gas (Ar, Kr, Xe): 1013 Bq
  Halogen (Br, I): 1013 Bq
  Mercury: 1016Bq
 might be released due to an leakage accident.
Mass Number of products
Production Yield (Calc.)
Mass Yield for spallation reactions

## Slide 8: Maximum Accident Scenario
The confinement of the mercury circulation system fails destructively, and all contents, mercury and gas products, flows out of the system.
The volatile products, including evaporated mercury, are exhausted and released to the environment.
The gas release stops after 1 hour by stopping and closing the exhaust system.
The radiation dose for the abnormal release at the site boundary are estimated.

## Slide 9: Behavior of Noble and Halogen Gases
Noble gas: Ar, Kr and Xe
  Whole amounts of the products are collected in the cover gas of the mercury tank.
  If the circulation system failed destructively, all of the gas products can be exhausted and released promptly via the exhaust system.
Halogen gas: Br and I
  The halogen products have strong tendency to combine chemically with mercury, and the compounds are solid.
    Hg + 2Br  HgBr2, Hg + 2I  HgI2, etc.
  The compounds, which is contained in the mercury, does not evaporated lower than 200C.
  The halogens does not release to the environment.

## Slide 10: Behavior of Tritium (3H)
Almost whole amount of tritium produced in mercury is absorbed to the stainless steel of the target vessel and the circulation piping.
The absorbed tritium is desorbed from the steel surface via diffusion process after the mercury is removed.
The total desorption rate is not so fast, less than 1011 Bq per hour at maximum, and it seems that desorption continues for a considerable period.
The chemical form of the disrobed tritium is almost HTO.
  The bio effect of HTO is much larger than that of HT by a factor of 104.
As for the accident scenario, we supposed that tritium as HTO is released to the environment with the rate of 1011 Bq for one hour.

## Slide 11: Release of Evaporated Mercury
The whole mercury (1.4 m3) flows out to the catch pan on the trolley.
Evaporation rate of mercury were estimated using one-dimensional plane model.
The decontamination factor of the charcoal filter in the exhaust system is 98%.
16 grams of mercury evaporated for one hour.
2% of the evaporated mercury is released to the environment.
Wind
d: Concentration boundary layer
Mercury

## Slide 12: Total Release
Total released activity
  Tritium（HTO）： 1×1011 Bq
  Noble gas（Ar, Kr, Xe）： 3×1013 Bq
  Mercury(197Hg, 203Hg etc.）： 6×108 Bq
Radiation dose (Inner and external) are estimated by considering the atmospheric dispersion.

## Slide 13: Dose Estimation at the Site Boundary
Internal dose (3T and Hg): DI [mSv]
  DI=KMQ(c/Q)
    K : Committed Effective dose coefficient [mSv/Bq]
    M : Breathing rate [=1.2 m3/h]
    Q : Released radioactivity [Bq]
    c/Q : Dispersion coefficient [(Bq/m3)/(Bq/h)]
External Dose (Ar, Kr, Xe): De [mSv]
  De=EQ(c/Q)
    E : Dose conversion factor for submersion [(mSv/h)/(Bq/m3)]
    Q : Released radioactivity [Bq]
    c/Q : Dispersion coefficient [(Bq/m3)/(Bq/h)]

## Slide 14: Assessment Results
Internal dose
  Tritium: 7×10-4 mSv
  Mercury: 9×10-4 mSv
External dose
  Noble gas: 0.5 mSv
Not exceed 1 mSv, corresponding to the annual dose limit for public, at the site boundary.
However, prevention and mitigation measures should be required for public acceptance.

## Slide 15: Measures for Mitigation
Early detection
  In-cell gas monitor
  Exhaust gas monitor
Emergency operation
  Mercury
    Leakage mercury  on the catch pan  Collection Tank
  Gas products
    Prompt evacuation to the off-gas system
Enclosing the hot cell
The failure progresses in stage.
It is estimated that the released radioactive gases can be controlled less than the amounts corresponding to 0.1 mSv at the site boundary if we start the emergency operation at the alarm level of the exhaust gas monitor.
In addition, the in-cell gas monitors are more sensitive!
We can not miss a precursor of the system failure.

## Slide 16: Summary
The hazard assessment was carried out for the maximum credible accident.
  Even in the worst case scenario, the effective dose at the site boundary is lower than the legal requirement.
We have prepared some equipment and devices to minimize the incident and its impact in the view points of early detection and emergency operations.
  By employing these measures, some kinds of predictor could be found, and the situation could be under control promptly with a sufficient margin.

## Slide 17: Appendix

## Slide 18: Analysis of Atmospheric Dispersion
Gaussian Plume model
Parameters
  Effective height：10 m
  Distance： 380 m
  Wind Speed： 1 m
  Atmospheric Stability： F
330 m
DH
sz