## Slide 1: Integration of USI and CM at NSLS-II 2019 Accelerator Safety Workshop ORNL – Spallation Neutron Source
Robert Lee
NSLSII ESH Manager
September 2019

## Slide 2: Outline
USI Process
  Screening
  Evaluations
USI Training and Qualifications
USI Invoking Processes and Procedures
Significance Determination

## Slide 3: USI Process @ NSLS-II
Basic USI principles:
  SAD/ASE complete
  The USI Process needs to be in place and functional prior to the Commissioning and Operational phases.
  The USI Process must address modifications to the facility, including new activities.
  The USI Process is a key process during facility modification of critical accelerator safety or control systems, or during significant operations changes.
  The purpose of the USI Process is to ensure that the DOE is aware of proposed changes or discoveries that significantly increase risk.
  The USI Process SHOULD allow accelerator management flexibility to make changes to its facilities and experiments and to operate them without additional prior DOE approval as long as said changes do NOT significantly affect the SAD conclusions NOR change the ASE.

## Slide 4: USI Process @ NSLS-II (Cont.)
USI Definitions
  Unreviewed Safety Issue (USI): A significant increase in the probability of, or consequences from: 1) a planned modification that creates a previously unanalyzed postulated accident or condition that could result in a significant adverse impact; or 2) a previously analyzed postulated accident or condition.
  USI Screening: Involves the completion of a simple questionnaire to determine whether a proposed activity has the potential to create a USI, or whether an existing condition potentially constitutes a USI.
  USI Evaluation: Detailed, documented analyses to determine whether a proposed activity or an existing/discovered condition presents a significant increase in risk.

## Slide 5: USI Process @ NSLS-II (Cont.)
Performed via formal procedure:
  NSLS-II Procedure: Unreviewed Safety Issue Determination (NSLSII-ESH-PRC-019) - Process Flow for proposed activity
No further action required
Potential
USI?
No
USI
Evaluation
USI
Disposition
NSLS-II
RSC Review
BNL LESHC
Review
Yes
USI?
No further action required
No
Yes
Proposed Activity:
Experiment
Modification
Procedure
Other…..
USI
Screening
ALD-ESH
Review
DOE
Approval
A similar process for discovered/existing Condition
Distribute determination

## Slide 6: USI Process @ NSLS-II (Cont.)
USI Screening Checklist:
  Does the proposed change or discovered condition impact or potentially impact:
    The Personnel Protection System (PPS)
    ODH Monitoring System
    Radiation Safety Component
    Area Radiation Monitoring System or Component
    Radiological Source Terms from SAD
    Critical Devices
    PS Operating Organization
    Operational Safety Limits
  If any ‘YES’ then Screening fails and an Evaluation required

## Slide 7: USI Process @ NSLS-II (Cont.)
USI Evaluation Format:
  No., Title, Description
  Does the proposed change or discovered condition affect information in SAD or ASE requirements? – Provide Citations
  USI Evaluation Criteria Questions 1. thru 6.
  [YES or NO, with justification]
    Could the change or discovered condition significantly increase the probability of occurrence of an accident previously evaluated in the SAD?
    Could the change or discovered condition significantly increase the consequences of an accident previously evaluated in the SAD?
    Could the change or discovered condition significantly increase the probability of occurrence of a malfunction of equipment important to safety (e.g., engineered credited controls) previously evaluated in the SAD?
    Could the change or discovered condition significantly increase the consequences of a malfunction of equipment important to safety (e.g., engineered credited controls) previously evaluated in the SAD?
    Could the change or discovered condition create the possibility of a different type of accident than any previously evaluated in the SAD that would have potentially significant safety consequences?
    Could the change increase the possibility of a different type of malfunction of equipment important to safety (e.g., engineered credited controls) than any previously evaluated in the SAD?
  USI Determination [YES, if any EC Questions YES]; If ‘YES’ then DOE approval required

## Slide 8: USI Training and Awareness
3 Levels of USI Training
  Awareness Level Training
    General information about USI Process and its functions
    Primarily those whose jobs can warrant a USI Screen
  USI Screener T&Q
    Awareness Level plus Read & Ack. ABDs + USI Proc
    Select Tech Specs who may need USI Screens routinely
  USI Evaluator T&Q
    USI Screener T&Q plus one-on-one training w/ABD Mgr and demonstration of proficiency [Prep of Sample/Example USI Evaluation w/detailed follow-up review]
    Select Tech. Mgmt.

## Slide 9: USI Invoking Processes or Procedures
The Authorization Basis Manager is engaged in all change management processes including:
  Engineering Design
  Engineering Change Orders
  Events/Issues management (ORPS and/or Discovery Events)
  Discrepancy Reports
  Machine Studies (Accelerator Physics and X-ray Beam)
The following procedures invoke a USI screen as a requirement:
  Management of NSLS-II Documents and Records
  Work Planning and Control Procedure
  Authorizing Operations and Performing Maintenance
  Safety System Work Permits
  NSLS-II Radiation Safety Component Configuration Management
  Configuration Management Procedures for ODH, PPS and ARMs
  Procedure for Software Change Control
  Note the ABM is a signatory on all procedures.

## Slide 10: Determination of Significance
Risk Assessment tables from SAD used to determine if the event/issue presents a significant increase in probability or consequence
  Does the event or issue change the risk category presented in the SAD?
Regardless of significance does the event/issue violate a condition of the ASE or is the hazard not addressed in the SAD?
Any other condition determined by Management to present an unacceptable risk to the safety of personnel or the operations of the facility .

## Slide 12: Contacts
NSLS-II Authorization Basis Manager:
Steven Moss
shmoss@bnl.gov
NSLS-II ESH Manager:
Bob Lee
blee@bnl.gov

## Slide 13
Thank You
Questions