## Slide 1: Status of China Spallation Neutron Source
Hesheng Chen
Institute of High Energy Physics, CAS

## Slide 2
CSNS project overview
CSNS design
Commissioning & operation
Users and future plan
Summary
Outline

## Slide 3
CSNS Facility Layout
The phase-I CSNS facility consists of 80-MeV H- linac, 1.6-GeV RCS, beam transport lines, target station, and 3 instruments.
Upgradable to 500kW at 25Hz and 20 instruments
Conducted jointly by IHEP & IOP, CAS
 | CSNS-I | CSNS-II
Beam power (kW) | 100 | 500
Repetition Rate (Hz) | 25 | 25
# of Target | 1 | 1
Average cur. (A) | 62.5 | 312
Proton energy(GeV) | 1.6 | 1.6
Linac energy (MeV) | 80 | 250

## Slide 4
Key Milestones
July 1999 CSNS proposed
June 2005 proposal approved in principle (CD-0)
Jan. 2006-Dec. 2013 Prototyping R&D
Sept. 2008 proposal approved
February 2011 Feasibility study approved (CD-1)
May 2011 preliminary design approved (CD-2)
Sept. 2011 construction start (CD-3)
May 2012 – Jan 2016 civil construction
Sept. 2011–Mar. 2016 component fabrication
Oct. 2014- June 2017 installation & tests
Dec. 2016 RCS commissioning start
Nov. 2017 First beam on target
March 2018 project complete/operation start (6.5Y)
April 2018 First user exp. result paper published

## Slide 5
CSNS Site
The site of CSNS locates at Dongguan, Guangdong Province.
The Dongguan local government provided a land of about 0.67km2 for CSNS campus. 0.27-km2 is used for the phase-I construction.
50 min. by car from the Shenzhen Airport; 2 hours by train & car from Hongkong

## Slide 7
CSNS project overview
CSNS design
Commissioning & operation
Users and future plan
Summary
Outline

## Slide 8
Linac Design

## Slide 9
RCS Design
Lattice of 4-fold symmetry, triplet.
227.92m circumference.
Four long straight sections for injection, acceleration, collimation and extraction.
25Hz, 80~1600MeV

## Slide 10
Neutron scattering hall

## Slide 11
Target station

## Slide 12
Neutron instruments layout
High pressure PND
GPPD
Quasi-elastic spectrometer
Polarized chopper spectrometer
Low-energy chopper spectrometer
MR
SANS
Cold neutron image
Molecular Vibration
MPI total scattering
High energy chopper spectrometer
Single crystal
High energy neutron SEE
Neutron physics
VSANS
Engineering PND
Proton Beam
10B, reserved
Liquid reflectometer
High resolution PND
D+P, LH2 (20K）
C,LH2 (20K)
D, Water (300K)
8A, reserved
D, LH2 20K)
7, reserved
Back scattering

## Slide 13
Neutron instrument: GPPD design
Moderator |  | DPHM（20 K）
Bandwidth(Δλ) |  | 4.5 Å
Max. Beam Size |  | 40(h)×20(w) mm
Flux at sample position |  | ~107 n/cm2/s
Best Resolution(d/d) |  | 0.2 % at 2 =150
Guide |  | Taper focus, m=3
Source to sample distance L1 |  | 30 m
Sample-detector distance L2 | 2 =150 | 1.5 m
 | 2 =90 | 2.0 m
 | 2 =15 | 3.8 m
Performance:
  Determine crystallographic and magnetic structures in general purposes
  Best resolution d/d ~ 0.2 %.
  ~ mimutes for a diffraction histogram used by Rietveld refinement on ~ 1-g-weight sample
  Easily loading the ancillary equipment such as cryostat, furnace and pressure cell

## Slide 14
Neutorn instruments: MR design
Performance:
  Vertical sample geometry: solid film
  Reflectivity/diffraction
  Best resolution Q/Q < 1%
  Polarizing analysis for spinoelectronics.
  In-suit study on growing films
  In-suit MOKE magnetic analysis
  Off-specular scattering
  Grazing-incidence small-angle scattering
Moderator | CHM (20 K)
Bandwidth（Δλ） | 6 Å
Guide | Bender+Sraight+Taper 40 × 60 → 20 × 30 mm²
SS distance L1 | 19.5 m
SD distance L2 | 2 m
Sample table | 6-axis movements
Polarizer/analyzer | Supermirror type
Detector | 2D position-sensitive resolution: 2 mm

## Slide 15
Neutron instruments: SANS design
Moderator | CHM（20K）
MS distance | 14 m
SD distance | 1~5 m
Detector | 
Effective area | 50×50 cm2
Resolution | 1 cm (FWHM)
 | 0.4-8 Å
q range | 0.004-3.4 Å-1
Performance:
  Reliable SANS data between 0.01 ~ 0.5 Å-1 to characterize 1-100 nm particles.
  Instrument resolution better than ~30% around Qmin
  Good dynamic range, sample space
  Variable sample size

## Slide 16
CSNS project overview
CSNS design
Commissioning & operation
Users and future plan
Summary
Outline

## Slide 17
CSNS Site
Birds View of CSNS
August, 2017

## Slide 18
First Neutron @ Aug. 28, 2017

## Slide 19
19
Beam power | Rep. rate | Ave. Curr. | Beam Energy | Neutron Efficiency | Neutron Flux
100 kW | 25Hz | 63μA | 1.6GeV | 0.1(n/p/sr) | 2*107
Beam power | Rep. rate | Ave. Curr. | Beam Energy | Neutron Efficiency | Neutron Flux
10 kW | 25Hz | 6.3μA | 1.6GeV | 0.005(n/p/sr) | 105
23 kW | 25Hz | 14.5μA | 1.6GeV | 0.125 | 2.5*106
In the technical test for official acceptance, all the acceptance goals have been reached, and most of them were exceeded.
On construction schedule!
Acceptance goal
Design goal
Design and Acceptance Goal

## Slide 20
20
Historical curve of beam power
Nov. 2017, First 10kW beam strike on target for a short while;
Mar. 2018, beam power over 20 kW in the test operation;
Jan. 2019, after 4 weeks beam commissioning , beam power was gradually increased to 50kW+ with well controlled beam loss.
Sep. 2019, based on the 6 weeks beam commissioning, the beam power in user operation was increased to 80 kW step by step.
We plan to increase the beam power to 100kW by the first half of 2020.
10kW
20kW
30kW
50kW
80kW

## Slide 21
21
24 hours beam operation (Oct.8,2018)

## Slide 22
22
Beam loss and control
Linac&LRBT
RTBT
RCS

## Slide 23
23
4055 hours was provided to users in the first user operation
The availability is over 92% during the user operation
Machine hours Statistics (18.10-19.6)

## Slide 24
Neutronics Performance of Target Station
  Measured spectra & pulse shape agreed well with simulation.

## Slide 25
Neutronics Performance of Target Station
Wavelength spectra (CHM) Peak brightness (DPHM)
TAV brightness (DWM)
The neutronic performance of the source (and moderators) is excellent, and provides evidence of strong coupling between the target and the moderators.
NTAC10 report, Dec，2018

## Slide 26
Commissioning of GPPD
NIST-640e standard sample Si, refinement Rp = 1.88%、Rwp= 2.89%
GPPD can obtain accurate and reliable information on the determination of crystal structure and magnetic ordered structure, the discrimination of light elements and adjacent transition elements and so on.
GPPD review committee, April, 2018
0.182% for back scattering bank
Better than the design goal
0.164% for one module
@ back scattering

## Slide 27
Commissioning of MR
20 hrs
Function NR：Rmin<10-5 Diffraction: d/d = 0.6% PNR: done

## Slide 28: Glass carbon & Bates-poly，molecular weight: 200 k
Commissioning of SANS
Scattering from steel flange
Beam size diagnostic Background analysis

## Slide 29
GPPD: Li-ion batteries research
Li/Ni exchange ratios in series of LiNixMnyCozO2 materials are precisely determined for the first time
Y.G. Xiao et al. Nano Energy 2018, 49, 77–85
Illustration of a pair of Li/Ni exchange and arrangement of magnetic moments in the TM layer of triangular lattice
Rietveld refinement of the NPD patterns and calculated cations/anions diffraction patterns for the pristine and the corresponding schematic crystal structure.
a) 2D-ordered cation layer; b) 3D-disordered cation framework; c) Schematic representation of the shrinking distance between a pair of O–O ions and the corresponding structure distortion.
E.Y. Zhao et al. Energy Storage Materials 2019, 16, 354–363
E.Y. Zhao et al. Angew. Chem. Int. Ed. 2019, 58, 1–6
The superior structure stability and robust anions framework of LTNNbOF (280 mAh/g) upon (de)lithiation process were experimentally demonstrated.
The structural-dimensionality effect on the l-OR and associated oxygen lattice stability in Li-rich cathodes have been characterized and clarified.

## Slide 30
GPPD: Magnetic skyrmions research
X.Y. Li, et al. Adv. Mater. 2019, 1900264
a–c) Structural parameters describing a C2v biskyrmion; d–f) The simulated magnetic form factors corresponding to (a–c), respectively; g) An in-plane magnetization of the biskyrmion configuration. h) The MnNiGa single-crystalline sample is checked using a single-crystal X-ray diffractometer; i,j) The refinement result of high-resolution neutron powder diffraction data.
The structural parameters of the biskyrmion state in MnNiGa bulk crystals was determined
Notes: 1. Biskyrmions do not assemble into a long-range-ordered lattice. Instead, their correlation length always remains comparable to the periodicity of the stripe domains, and increases with increasing magnetic field.
2. Although biskyrmions do not order into periodic lattices on a large length scale, they are in-plane rotationally ordered, with the rotation direction being locked to certain crystallographic directions.
These polar molecular properties of the biskyrmion system suggest an intricate energy balance in MnNiGa, which is fundamentally different from chiral skyrmion systems. Such anisotropic nature, representing an extra degree of freedom for this type of skyrmions, may be exploited as information carrier. In this case, the two binary states are encoded within the same topological state, which reduces the energy consumption that is required for the state switching, demonstrating advanced device scheme for skyrmion-based memories.

## Slide 31
MR: Multipurpose Reflectometer
Interface Induced Enhancement of Inverse Spin Hall Voltage in NiFe/Pt Bilayers Capped by MgO layer
Probe the deep inside a film
Zhu et al 2018 Neutron News, 29(2), 11
Zhu et al 2019 J. Phys.: Condens. Matter https://doi.org/10.1088/1361-648X/ab172a
The SLD profile shows an interface between pure Pt and MgO layers with their nominal SLDs, which supporting an interfacial induced ISHE enhancement.
First PNR data
@ CSNS

## Slide 32
MR: Multipurpose Reflectometer
H.C. Chen et al. Appl. Phys. Surf. (in press)
Sensitivity to reveal the complicated
magnetic structure in the film.
X.Z. Zhan et al. 2019 Sci. Rep. 9, 6708
Probing the Transfer of the Exchange Bias Effect by Polarized Neutron Reflectometry
The behavior of helium atoms in He+ ion implanted W/Ni bilayer nanocomposite

## Slide 33
SANS: Metal glass
W.X. Dong, et al. Acta Materials (Under Review) CityU & NUST team lead by X.L. Wang
In-situ observation of an unusual phase transformation pathway with Guinier-Preston zone-like precipitates in Zr-based bulk metallic glasses
The pathway of amorphous-to-crystalline phase transformation in Zr-, Fe- and Pd-based bulk metallic glasses
Notes: 采用中子小角散射技术研究了Zr-基BMG由非晶到结晶的动力学问题，提出了一种基于短程原子输运的相分离机理。

## Slide 34
Running Scheme in 2019
System /Instrument | Planed Hour | Included Hour |  |  |  | Running Data of Similar International Advanced Facilities
 |  | Preparation | Beam Time(for User Experiments) | Instrument Development | Downtime | 
Accelerator | 6000 | 1000 | 3600 | 1000 | 400 | 5900
Target | 5600 | 1000 | 3600 | 800 | 200 | 3980
Instruments |  |  |  |  |  | 
GPPD | 3600 | 50 | 2800 | 600 | 150 | 
MR | 3600 | 50 | 2600 | 800 | 150 | 
SANS | 3600 | 50 | 2600 | 800 | 150 | 

## Slide 35
CSNS project overview
CSNS design
Commissioning & operation
Users and future plan
Summary
Outline

## Slide 36
User service
https://user.csns.ihep.ac.cn (in both Chinese and English）
International users are welcomed
Register an account
Submit a proposal
Proposal type：
1.Direct access
2.Rapid access
Third call for proposal:
2019.06
For third round operation
2019.09-2020. 01

## Slide 37
First operation year（Sept. 2018-June. 2019）:
    performed 101 (included 11 from oversea and HK) (acceptance 50%)
    Research fields: energy material, structural material， magnetic, film, alloy, polymer, nano, biology material, hydrogen storage, drug et. al.
Next operation period（Sept. 2019 - Jan. 2020）:
  regular application 164, 35% accepted
  approved 57 proposals (included 7 from oversea, HK and Macao)
37
User Proposals
Chinese publications in neutron scattering

## Slide 38
User Instruments
Multiple Physics Instrument by Dongguan Institute of Technology, and CityU (HK) under construction
Engineering Diffractometer by Center for Excellent Advanced Materials (Dongguan) under construction
High Pressure Diffractometer by South China Univ. of Sciences and Technology (Shenzhen),
Atmosphere Neutron Irradiation by China Electronic Product Reliability and Testing Inst. under construction
High energy chopper spectrometer by SUN YAT-SEN Univ.
Guangdong Province Government Donation:
Very small angle neutron scattering
Energy resolved neutron imaging

## Slide 39
Neutron instruments layout
High pressure PND
GPPD
Quasi-elastic spectrometer
Polarized chopper spectrometer
Low-energy chopper spectrometer
MR
SANS
Cold neutron image
Molecular Vibration
MPI total scattering
High energy chopper spectrometer
Single crystal
High energy neutron SEE
Neutron physics
VSANS
Engineering PND
Proton Beam
10B, reserved
Liquid reflectometer
High resolution PND
D+P, LH2 (20K）
C,LH2 (20K)
D, Water (300K)
8A, reserved
D, LH2 20K)
7, reserved
Back scattering

## Slide 40
Future Plan
  CSNS Phase II (14th 5 year plan from 2021 ) :
  More neutron Instruments (10 instruments)
  More sample environment and user lab.
  Beam power upgrade to 500kW ：
    LINAC beam energy upgrading to 300MeV by superconducting cavities. The tunnel is available.
    RCS works for 500kW with minor upgrade
    Target upgrading to 500kW: new target and modulators. (shielding and utility fulfill 500kW)
    Long term
    Second target stations
    Muon beams
  ……

## Slide 41
Summary
CSNS finished construction and reached the specifications on schedule, and passed the national acceptance on Aug. 2018 and was opened to users.
CSNS is the operation: stable running with high efficiency, improving performance.
The design and construction of user instruments are underway.
The phase-II instrument construction and the power upgrade will be started rather soon.
Thanks advices and helps from Foreign Lab.’s and scientists during the design, construction and commissioning of CSNS
CSNS welcomes intl. users and looks forwarded for cooperation in the neutron scattering and applications..

## Slide 42
Thank you ！