## Slide 1: Bubble Generation using a Micro-Orifice Nozzle in Liquid Cross-Flow
Charlotte Barbier
Volkan Yildirim
Elvis Dominguez-Ontiveros
10/16/2019
ICANS 2019

## Slide 2: Introduction
The Spallation Neutron Source (SNS) at ORNL uses a liquid mercury target
Due to the short proton beam pulse, heat is deposited rapidly in the liquid mercury, resulting in strong pressure wave due to rapid thermal expansion.
These pressure waves cause high stresses and cavitation damage. To mitigate them, SNS has been injecting small Helium bubbles in the target.
Although satisfying results were observed, more mitigation is desired to increase target reliability.

## Slide 3: Gas Injection at SNS: Inlet Orifice Bubbler (IOB)
The orifices work under “choked flow” conditions. Gas flow rate is constant when gas reaches sonic velocity going through the outlet orifice.
  operating at 100 psig
mercury flowing at ~100GPM
IOB
Proton beam
1/16” diameter nozzle
1.8” diameter
1/8” length

## Slide 4: Strain Reduction
Courtesy of W. Blockland/Y. Liu/D.Winder
% strain reduction caused by gas injection
Strain reduction across the target vessel was observed even at low gas flow rate injection (~0.5 SLPM)

## Slide 5: More gas seems to lead to less strain!
Courtesy of W. Blockland/Y. Liu/D.Winder

## Slide 6: More gas less cavitation damage!
Target 18 – Inner Wall
(Jet-flow design)
Qavg = 0.31 SLPM
Pavg = 1121 kW
Etotal = 1260MW-hr
Target 19 – Inner Wall
(Jet-flow design)
Qavg = 0.45 SLPM
Pavg = 1187 kW
Etotal = 1987 MW-hr
Target 20 – Inner Wall
(Jet-flow design)
Qavg = 0.57 SLPM
Pavg = 1287 kW
Etotal = 2231 MW-hr
Courtesy of D. McClintock

## Slide 7: IOB headaches: Fabrication and Operation Issues
Fabrication challenges
  nozzles get clogged during welding process
  labor intensive (60 small nozzles to weld)
Unable to achieve design flow rates
Performance degradation
  Flow rate decreases during operation
T18
0.45 SLPM
0.25 SLPM
OE limit
0.71 SLPM
0.45 SLPM
OE limit
OE limit
0.8 SLPM
0.6 SLPM

## Slide 8: Pressure Wave Mitigation Theory
=30mm
Peak pressure decrease is a function of:
  bubble size
  void fraction (total number of bubbles)
At the wall  VF matters the most
  1% VF with 300 mm diam bubble: 25 MPa  0.6 Mpa
  0.05% with 40 mm diam bubbles: 25 Mpa 6 Mpa
Higher pressure wave mitigation when the wave propagates through a liquid-bubble mixture.
1D simulation in a cylinder, monodisperse population, no bubble-bubble interaction
At the center
At the wall
SNS: VF<0.05%
Okita, K., Takagi, S. and Matsumoto, Y., 2008. Propagation of pressure waves, caused by a thermal shock, in liquid metals containing gas bubbles. Journal of Fluid Science and Technology, 3(1), pp.116-128.

## Slide 9: Next IOB Generation at SNS
Use larger orifices and operate them at lower pressure:
  flow is still under choked conditions
  if orifices get clogged, pressure can be increased to maintain constant mass flow rate
How increasing the orifice size impact the bubble size?

## Slide 10: Experimental Setup
Acrylic section with flat outside surface to avoid optical distortion
Inner diameter of test section = 2”
Nozzle: 1/16” tubing with orifice diameter of 8 to 18 micron diameter.
Water flow rate: 10 to 30 GPM
High Speed Movies (4k fps) with telecentric lens:
  18.0 mm/px
water
10-30 GPM
mass flowmeter
0.5 mm filter
Helium
GPM | Vave (m/s) | Re
10 | 0.31 | 1.6E+04
20 | 0.62 | 3.2E+04
30 | 0.93 | 4.7E+04

## Slide 11: Example of Videos
10 micron
PHe = 100 psig
QH2O = 30 GPM
18 micron
PHe = 100 psig
QH2O = 30 GPM

## Slide 12: 8 micron clogging
10 GPM, 40 psi
<d>=428 micron
Est. flow rate = 0.75 ccm
10 GPM, 40 psi (43 min later)
<d>=209 micron
Est. flow rate = 0.04 ccm
Expected flow rate = 6.4 sccm
The measured gas flow rate corresponds to the one expected from a 2. 8 micron diameter orifice

## Slide 13
He pressure (psi)
40
60
80
100
“8 µm” [1.9 µm]
Water (GPM) | 10 | 20 | 30

## Slide 14
He pressure (psi)
40
60
80
100
Water (GPM) | 10 | 20 | 30
“10 µm” [9.6 µm]

## Slide 15
He pressure (psi)
40
60
80
100
Water (GPM) | 10 | 20 | 30
“12 µm” [8.9 µm]

## Slide 16
He pressure (psi)
40
60
80
100
Water (GPM) | 10 | 20 | 30
“16 µm” [10.7 µm]

## Slide 17
He pressure (psi)
40
60
80
100
Water (GPM) | 10 | 20 | 30
“18 µm” [16.3 µm]

## Slide 18: Modes of Bubble Formation
Single bubbling:
  very low gas injection rate
  spherical bubble
Pulse bubbling:
  Bubble are less spherical
  Bubble formed from necking
Jetting:
  bubble size independent of orifice size
Single bubbling
Pulse bubbling
Jetting
Cavity formation
Increasing gas injection
orifice flow rate
liquid velocity
Forrester, S. E., and C. D. Rielly. "Bubble formation from cylindrical, flat and concave sections exposed to a strong liquid cross-flow." Chemical Engineering Science 53.8 (1998): 1517-1527.

## Slide 19
Higher gas injection flow rate generally lead to slightly larger bubbles
Increasing water velocity strongly reduced bubble size

## Slide 20: Bubble Generation Frequency

## Slide 21: Gathering all the data together:
100 GPM? Orifice diameter impact relatively low

## Slide 22: CFD: All Experiments in Same Flow Regime
Power law velocity profile
P=0
Smooth surface no-slip walls
Perfect similarity: all the experiments are in the same flow regime.

## Slide 23: Bubbles are mainly following streamlines+gravity

## Slide 24: Scaling From Water to Mercury
 | Ratio Mercury/Water
Density | 13.6 (!)
Surface tension | 6.7
Dynamic viscosity | 1.7
Shear strain rate > 750 s-1

## Slide 25: Scaling From Water to Mercury
 | Ratio Mercury/Water
Density | 13.6 (!)
Surface tension | 6.7
Dynamic viscosity | 1.7
Shear strain rate > 750 s-1
smaller diameter
Mirsandi, H., et al. "Bubble formation from an orifice in liquid cross-flow." Chemical Engineering Journal (2019).

## Slide 26: Scaling From Water to Mercury
 | Ratio Mercury/Water
Density | 13.6 (!)
Surface tension | 6.7
Dynamic viscosity | 1.7
Shear strain rate > 750 s-1
larger diameter but not too bad since high shear rate
Mirsandi, H., et al. "Bubble formation from an orifice in liquid cross-flow." Chemical Engineering Journal (2019).

## Slide 27: Scaling From Water to Mercury
 | Ratio Mercury/Water
Density | 13.6 (!)
Surface tension | 6.7
Dynamic viscosity | 1.7
Shear strain rate > 750 s-1
Small impact
Mirsandi, H., et al. "Bubble formation from an orifice in liquid cross-flow." Chemical Engineering Journal (2019).

## Slide 28: Conclusions from the single orifice experiments in water
At high liquid flow rates (higher shear rate), the impact of the nozzle diameter is expected to be negligible.
Bubbles in mercury are expected to have smaller average diameters
  higher density
  higher turbulence

## Slide 29: Experiments using Liquid Mercury
8 micron orifices
0.85 SLPM
18 micron orifices
2.8 SLPM
Comparison between 8 and 18 micron IOB: qualitative

## Slide 30: Comparison between 8 and 18 micron IOB: quantitative
8 micron IOB-Bubble Size Distribution (BSD) slightly more skewed towards smaller bubble diameter, but BSD are otherwise very similar.
* the BSD was normalized such that the total number of bubble was 1000 for both measurement

## Slide 31: Conclusions
Experiments demonstrate the same difficulties than experiments: small orifices clog easily!
At 100 GPM, the expected shear rate at the nozzle is large enough that the orifice size has a relatively mild impact on the bubble size.
Both 8 and 18 micron IOB demonstrated at TTF (mercury loop) their abilities to generate bubbles with diameters less than 300 mm.
As the orifices are clogging during operation, the bubble size distribution is also affected. Keeping the same bubble size distribution during the target lifetime is challenging with the IOB.  SNS will switch to swirl bubbler for the PPU project.