## Slide 1: Shielding development for VENUS instrument
ICANS XXIII
Chattanooga, TN, October 17, 2019
I. I. Popova and F.X. Gallmeier

## Slide 2: Outline
Introduction
Geometry description
Source definition
Methods
Results
Conclusion

## Slide 3: Introduction
VENUS - Versatile Neutron Imaging Instrument – in process to be built and is expected to be completed in 2022 and ready for scientific use by 2023
Instrument is based on time-of-flight technique across a range of energies from cold/thermal to epithermal
Beam footprint at the sample position is as high as 28 by 28 cm2
High-energy beam in combination with large beam footprint on the sample position are challenges for shielding and budget

## Slide 4: Introduction
Instrument to be built on beam line 10 and will face decoupled poisoned H2 moderator
For cost reasons VENUS will be built in a downsized enclosure version at beam restrictions to 20x20 cm2 with T0-chopper and 4x4 cm2 with white beam
Shielding is upgradable (about doubling shielding side walls) at later time to allow 28x28 cm2 white beam originally envisioned
Beamline shielding is designed for on full white beam.

## Slide 5: Geometry description
Shielding analyses are performed for:
  Beam line shielding
  Enclosure and beamstop shielding
Beam line shielding starts from the target monolith
Enclosure follows the beam line shielding

## Slide 6: Requirements
Dose rates in generally accessible areas of 0.25 mrem/hr
Shielding height off floor of 4.45 m (2.4 m off centerline) to 7.4 m radius from monolith center
Shielding height off floor of 3.96 m (1.9 m off centerline) to 11.4 meter radius

## Slide 7: Geometry description – beam line
Beam optics starts 1 meter downstream of moderator
Optical components are comprised of a series of selected apertures, T0 and bandwidth choppers, beam scrapers and a fast shutter
Moderator
Pinhole
+20cm
+10cm
-10cm
-20cm
1m 4.5m 7m 14.5m
Flexible aperture
T0 chopper
BW chopper
BW chopper
Full 28x28 cm2 beam
20x20 cm2 beam
4x4 cm2 beam

## Slide 8: Geometry description – beam line
Beam path is shielded by:
high-density concrete, which extends to 2.90 m from the beam centerline to the top and to the side
high-density concrete, which extend to 2.14 m on the bottom followed by instrument floor from regular density concrete
1m 4.5m 7m 14.5m
+4m
+2m
+0m
-2m
-4m
-6m
+6m

## Slide 9: Geometry description – enclosure
Beam line enclosure is made from HD concrete
Enclosure thickness on the side is 40-cm and on the top is 75-cm
Enclosure thickness on the downstream wall is 55 cm
Sample in the analyses is 2.45cm thick steel and 32cm by 32cm.
Additional analyses are performed for case, when sample is slanted 45 degrees towards hot cell.

## Slide 10: Geometry description – enclosure
75
55
90
68

## Slide 11: Source definition
Beam line shielding
  Source terms based on 1.0 GeV, 2MW operation
  as a neutron beam with intensity of 4.47 1012 n/s, starting at core vessel insert nose
  0-0.5 degree, 0.5-1 degree and 1-2 degree angular segments
Enclosure shielding
  The source for PPU assuming a 1.3 GeV proton beam at 2 MW power
  0-0.5 degree, 0.5-1 degree and 1-2 degree angular segments
  The new 0.5-0 deg bin has a softer spectrum than the original most forward bin.
  The acting T0 chopper was figured into a modified source description accounting for:
    Timing of chopper causing a energy-dependent opening
    Attenuation of beam by 30 cm of Inconel

## Slide 12: Source term description
The effect of the T0 chopper is:
Suppressing epithermal spectral components (E=1-500eV)
Eliminating fast component (1keV-10MeV)
Suppressing high-energy component (>10MeV)
dashed-
modified
solid -original

## Slide 13: Methods
Analyses are performed with the Monte Carlo code MCNPX version 2.7.0
Shielding is modeled in 5 cm increments to use geometry splitting
2D mesh-tallies are defined in Cartesian coordinate
Thickness of the slice is 20 cm and mesh size is 5 cm x 5cm
Dose rate are obtained by folding fluxes with flux to dose conversion coefficients

## Slide 14: Beam line shielding analyses
Five sets of analyses are performed:
White beam, beam line shielding is from high-density concrete ;
White beam, beam line shielding is from high-density concrete, with steel in first 55 cm from the beam center line;
T0 chopper intercepting the beam, beam line shielding is from high-density concrete;
White beam, regular-density concrete;
White beam, regular-density concrete with steel in first 55 cm from the beam center line.

## Slide 15: Beam line shielding results

## Slide 16: Enclosure shielding results
Three sets of analyses are performed:
  Beam areas at sample position defined by collimator/scrapers to be 20x20 cm with T0 chopper acting;
  Beam areas at sample position defined by collimator/scrapers to be 4x4 cm with white beam;
  Beam area at sample position is 28x28cm, there is no collimator scrapers

## Slide 17: 4x4cm white beam with 40-cm HD enclosure, no sample
White beam
Analyses for beam stop
Dose rate contours at 0.25, 10, 100mrem/h, red color
Enclosure contours are in white color

## Slide 18: 4x4cm white beam with 40-cm HD enclosure, sample
White beam
Dose rate contours at 0.25, 10, 100mrem/h, red color
Enclosure contours are in white color

## Slide 19: 4x4cm white beam with 40-cm HD enclosure, slanted sample
White beam
Dose rate contours at 0.25, 10, 100mrem/h, red color
Sample is slanted 45 deg towards hot cell, beam passing path is 2.54cm
Dose rates elevated outside the enclosure upto 0.5 mrem/r

## Slide 20: 20x20 cm beam, acting T0 chopper in 40cm HD enclosure
Analyses for beam stop
Dose rate contours at 0.25, 10, 100mrem/h, red color
Enclosure contours are in white color

## Slide 21: 20x20 cm beam, acting T0 chopper in 40cm HD enclosure
Dose rate contours at 0.25, 10, 100mrem/h, red color
Enclosure contours are in white color

## Slide 22: White beam, no collimator/scrapers, sample
White beam
Dose rate contours at 0.25, 10, 100mrem/h, red color
Enclosure contours are in white color

## Slide 23: Conclusions
Five sets of analyses are performed to help define beamline shielding:
  Dimensions
  Materials
Three sets of analyses for the enclosure are performed to define:
  Enclosure thickness
  Enclosure material – high-density concrete
  Beam stop shielding thickness