## Slide 1: Technique Development Beamlines at the High Flux Isotope Reactor
Lowell Crow
Neutron Optics and Polarization Team
Neutron Technologies Division
ICANS XXIII October 2019 – Chattanooga, Tennessee

## Slide 2: Why do we need development beams?
We need moderators, guides, filters, shutters, choppers, monochromators, analyzers, focusing devices, sample environments, detectors, shielding , etc. All need testing
Prototyping of new techniques using neutrons may require configuration changes, novel apparatus, or long preparation times
This is difficult to schedule on busy, oversubscribed user instruments
We maintain development beamlines at HFIR, which support our efforts at both HFIR and SNS – these were constructed on existing locations with operating funds (ORNL-NScD Instrument Improvement for CG4B)

## Slide 3: Work with Indiana University Group Roger Pynn, Steven Parnell (now at TU Delft), Steve Kuhn
Neutron Optics and Polarization Team
Lee Robertson (lead)
Lowell Crow
Peter Jiang (3He polarizers)
Josh Pierce (Dynamical Nuclear Polarization)
Fankang Li
Ryan Dadisman
Dante Quirinale
Nicolas Silva
Ann Jennings
Landen Mcdonald
David Wasilko
Jillian Ruff
HB-2D Polarized Development Beamline at HFIR
Past members: Bill Hamilton, Jinkui Zhao, Xin Tony Tong, Tianhao Wang
CG1A (Detectors): Rick Riedel, Jason Hodges, Kevin Berry, Loren Funk
CG1B (NSD): Jaime Fernandez-Baca, Mike Cox, Spectroscopy Group, Diffraction Group

## Slide 4: A short overview of HFIR
HB-2 – radial beam tube in a Beryllium reflected reactor
+ very high thermal flux
- very high fast flux
Use a cooled Sapphire filter
Supports 4 beamlines, including
HB-2D Polarization Development
High Flux Isotope Reactor – since 1965
Flux trap flux : 2.5 x 1015 thermal
Beam tube flux : 1.2 x 1015 thermal
Cold Source and Guide Hall – Commissioned 2007
CG4B area
CG1A
CG1B

## Slide 5: We currently have four development beamlines at HFIR
Detector Test Station CG1A
Alignment Diffractometer CG1B
Cold Neutron Polarization Development Beamline CG4B
Polarized Neutron Development Beamline HB-2D

## Slide 6
CG1A Detector Test Station Wavelength 4.22 Å
Flexible rail mount with about 3 m of operational space
Flux is > 106 n/cm2 s
Parallel plate monitor test 2011
Detector Calibration (e. g. Anger Cameras)
Detector Prototype Tests
Contact: Rick Riedel

## Slide 7
CG1B Alignment and Utility Diffractometer 2.417 Å, 14.0 meV
Flux is about 1.4 x 106 n/cm2 s
Beam is up to 8 × 8 cm2 at about 4 m from the flat graphite monochromator
Monochromator/analyzer tests
Sample alignment (saves time on user instruments)
Optics and components tests (e.g. sample cans)
Alignment of
CTAX Monochromator
Alignment of new HB-1A M1 monochromator before 2018 installation
Contact: Jaime Fernandez-Baca, Mike Cox (NSD)

## Slide 8: HB-2D Polarization Development Beamline – in HFIR Beamroom
The beamline is configured for each measurement; the only fixed components are the monochromator drum, shutter, and beamstop. Variable-height lift tables allow us to position components. We have a variety of polarizers, flippers, stages, and detectors available
HB-2D Polarized Development Beamline at HFIR
With Graphite: 4.25 Å (use Be filter or accept harmonics)
Cryoflipper with 3He analyzer
3D Polarimetry with Indiana University
Double cell 3He measurement
MICE Demonstration
Diffractometer Arm

## Slide 9
Modulated Intensity by Combined Effort (MICE)
Neutron Intensity Modulation and Time-Focusing with Integrated Larmor and rf Techniques
J. Zhao, W. A. Hamilton, S.-W. Lee, L. Robertson, L. Crow, Y. W. Kang Applied Physics Letters
HB-2D Polarized Development Beamline at HFIR
Larmor rf encoding (like NRSE or MIEZE)
Modulation is before any sample (like MIEZE)
Neutrons travel through an adjustable-current solenoid between the RF flippers; since it does not rely on a zero-field region, the performance should be robust in moderate magnetic field environments
First measurements demonstrate frequency time-focusing
Demonstration experiment on HB-2D

## Slide 10: New Last Year: CG-4B Cold Neutron Polarization Development Beamline
This new beamline allows a longer wavelength, 5.48 Å, and a longer flight path length (about 6.5 m ) than in our previous development positions at HB-2D or CG1A.
This yields enough space for Larmor spin encoding techniques which require significant flight path distance, such as SERGIS, SESANS, MIEZE, or MICE. It also provides space for the power supplies, refrigerators, electronics, and cooling required for these methods.
Polarized Development Beamlines at HFIR

## Slide 11
First Experiment on CG4B: Helium Turbulence
To be submitted:
Imaging fluorescence of excimers created by neutron capture in liquid He II—an alternative for turbulent flow research
X. Wen, Shiran Bao, L. McDonald, J. Pierce, G.L. Greene, Lowell Crow, Xin (Tony) Tong, A. Mezzacappa, R. Glasby, W. Guo, and M.R. Fitzsimmons

## Slide 12: Transverse Resonant Spin Echo – Fankang Li, Ryan Dadisman, David Wasilko, Steve Kuhn
Note: since HFIR was down this year, we borrowed 2XC at MURR (Columbia, Missouri)
Next Experiments at CG4B
Transverse Resonant Spin Echo (Fankang Li)
Quantum Entanglement with Wollaston Prisms (with Jaime Fernandez-Baca)
Revisit Turbulence ( with Mike Fitzsimmons)
SANS with Dynamical Nuclear Polarization (Josh Pierce)
Spherical Polarimetry – Peter Jiang, Tianhao Wang, Nicolas Silva, Jillian Ruff
Other projects – Lowell Crow, Lee Robertson, Jodi Camino
Detector tests – Rick Riedel, Su Ann Chong
and HB-2D
Spherical Polarimetry (Peter Jiang)

## Slide 13: In about 2023, all HFIR instruments come out, and we have to reinstall all of them!
HB-2 tunnel in beam room will be modified
Do we keep HB-2D, and if so in what form?
Planning is already in progress
Where are development locations?
New Guide Hall Layout
“MANTA” new Cold 3-Axis
Imaging
IMAGINE
Spin Echo
Extend the building
Move both SANS downstream
New locations for IMAGINE and Imaging
New guide supports Larmor, Spin Echo
Alignment is satellite of Spin Echo
Alignment