## Slide 1: Precision absolute polarimeter development for the 3He++ ion beam at 5.0-6.0 MeV energy
Workshop on Polarized Sources, Targets, and Polarimetry
Grigor Atoian, A.Poblaguev, A.Zelenski
Brookhaven National Laboratory
Sep 26, 2018

## Slide 2: Polarized 3He++ ion source development in EBIS BNL-MIT collaboration
2
Proposal of production of polarized 3He++ beam in EBIS. A.Zelenski, J.Alessi, ICFA Beam Dynamics Newsletter 30, p.39, (2003)
… A doubly polarized electron-ion collider (EIC) is the best way to examine the internal structure of the proton and neutron. The technology to accelerate polarized proton beams has been well established at RHIC. However, studying the structure of the neutron requires the acceleration of polarized 3He++, which carries ~90% of its polarization in the neutron, and to match the unprecedented statistical precision an EIC will provide, it is indispensable to have high precision measurements of the hadron beam polarization. For this reason, development of a polarized 3He ion beam has been identified as an R&D priority by the EIC Advisory Committee in 2009 and the Office of Nuclear Physics Community Review in 2017.
U. S. Department of Energy
Office of Science | Nuclear Physics FY 2018
Research and Development for Next Generation Nuclear Physics Accelerator Facilities
Polarized 3He++ production is important part of the ongoing extended EBIS “upgrade" project. Completion-2021
The 3He++ spin-rotator and polarimeter is funded by DOE grant Research and Development for Next Generation Nuclear Physics Accelerator Facilities. Completion-2020.

## Slide 3
The development of the 3He polarizing apparatuses, the spin-rotator, and the nuclear polarimeter at the 3He++ ion beam energy 6.0 MeV is funded by the DOE Research and Development Funds for the Next Generation Nuclear Physics Accelerators Facilities.
“Extended” EBIS upgrade with new “injector” solenoid spin rotator and polarimeter for polarized 3He++ ion production
Holder 3He-cell
with filling and injection valves
Transition region

## Slide 4: Optically-pumped 3He in the high magnetic field
Drift tube -20-40 kV
Insulator
Pulsed valve
3He-cell
D 216mm
D 175mm
beam
beam
Holder 3He-cell with filling and injection valves inside the EBIS SC solenoid at 5.0T magnetic field
Purification system of 3He gas into cell by modified creo-pump and absorbed cartridge pump;
Polarization 1Torr 3He gas inside glass-cell by MEOP technique;
Measurement and control polarization by optical probe polarimeter;
Injection of polarized 3He into drift tube (beam line) by pulsed valve ( ~2-3*1012 atoms/pulse);
10 Amp electron beam completely ionizes the polarized atoms;
Accelerate to 6 MeV by RFQ-LINAC system;
Rotate a spin from the longitudinal to the vertical direction by bunsher-1;
Measurement polarization of 3He beam by 6MeV polarimeter;

## Slide 5
3He optically-pumped cell in the high magnetic field
3He-cell
3He filling valve
3He injection valve
HV isolator
Inputs& outputs:
RF- discharge cable;
pumping laser high power optic fiber;
probe laser optic fiber;
3He spectra control fiber;
filling valve pulse cable;
Injection valve pulse cable;
PD output cable;
3He gas filling line
Drift tube
A long drift tube with a small diameter (~10-15mm) acts like a 3He storage cell, which reduces gas load of the EBIS vacuum system.

## Slide 6
After EBIS LINAC the polarized 3He beam will have an energy 6MeV and a longitudinal spin direction. Before it will transport to the Booster the spin will be rotated to the vertical direction by dipole. With additional enable spin-flip we can measure polarization of the beam by a standard configuration of left/right symmetric Si strip detectors like proton-carbon polarimeters in AGS and RHIC, and H-jet polarimeters in RHIC.
“Extended” EBIS upgrade with new “injector” solenoid spin rotator and polarimeter for polarized 3He++ ion production
Linac
dipole
dipole
dipole
dipole
quad
quad
buncher2
Existing line
polarimeter
21.5 deg
Booster
solenoid
FC
FC
3H++

## Slide 7
We will measure the spin correlated asymmetry of scattering on the gas target to determine the polarization of beam.
The asymmetry could be find from the number of detected scattered particles in left/right (L/R) detectors depending on the beam spin ():
and ,
where is the beam polarization, - analyzing power and - statistical accuracy.
The square root formula strongly suppress systematic errors associated with left/right detectors acceptance asymmetry and the beam spin up/down luminosity asymmetry.
The precise measurement of the beam polarization depends on:
well knowledge the effective analyzing power in the measured area;
accuracy of calibration and control of the measured energy;
energy and time resolution of detectors;
control the detector dead-time and pileup;
data collection rate
3He-4He scattering polarimeter at 6.0 MeV beam energy

## Slide 8
The analyzing power for elastic 3He-4He scattering is a function of the beam kinetic energy and the CM scattering angle - 𝐴𝑁(𝐸𝑏𝑒𝑎𝑚,𝜃𝐶𝑀) and can reach 100% at several points (𝐸,𝜃) [1].
Analyzing power of 3He-4He scattering
[1] D.M. HARDY et al. “POLARIZATION IN 3He + 4He ELASTIC SCATTERING”, Pys. Let. Vol.31B, #6, 16 March 1970, p. 355-357

## Slide 9
There is no inelastic contribution in 3He-4He scattering at energy of beam. One of point is 𝐸𝑏𝑒𝑎𝑚≈5.3 MeV and 𝜃𝐶𝑀≈91° [1]. The exact location of this point was not well determined. Late the location of this point was evaluated as 𝐸𝑏𝑒𝑎𝑚≈5.4 MeV,𝜃𝐶𝑀≈ 79° (Ref. [2]).
[1] G.R. PLATTNER et al. “ABSOLUTE CALIBRATION OF SPIN -1/2 POLARIZATION”, Pys. Let. Vol. 36B, #3, 6 Sep 1971, page 211-214 [2] W.R.Boykin, S.D.Baker, D.M.Hardy, “Scattering of 3He and 4He from polarized 3He between 4 and 10 MeV,” Nucl. Phys. A 195, 241 (1972).
Analyzing power of 3He-4He scattering

## Slide 10
Chart: Range of He4 in Si
| 0.93433476394849779 | 1.0454935622317596 | 1.146351931330472 | 1.2403433476394849 | 1.3291845493562231 | 1.4150214592274675 | 1.497854077253219 | 1.5785407725321887 | 1.6579399141630899 | 1.8133047210300428 | 1.9660944206008586 | 2.1175965665236052 | 2.2686695278969955 | 2.4201716738197425 | 2.5721030042918454 | 2.7248927038626602 | 2.8789699570815452 | 3.0347639484978544 | 3.1918454935622318 | 3.3506437768240342 | 3.5111587982832617 | 3.6738197424892705 | 3.83862660944206 | 4.6909871244635193 | 5.600858369098713 | 6.562231759656652 | 7.5836909871244629 | 8.6566523605150216 | 9.7896995708154488 | 10.97854077253219 | 12.223175965665234 | 14.884120171673819 | 17.7725321888412 | 20.896995708154506 | 24.253218884120169 | 27.841201716738194 | 31.652360515021453 | 35.682403433476395 | 39.927038626609445 | 44.377682403433475 | 49.055793991416301 | 53.905579399141629 | 59.012875536480685 | 64.291845493562235 | 69.742489270386272
 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10
Chart: Range of He3 in Si
| 5.600858369098713 | 6.562231759656652 | 7.5836909871244629 | 8.6566523605150216 | 9.7896995708154488 | 10.97854077253219 | 12.223175965665234 | 14.884120171673819 | 17.7725321888412 | 20.896995708154506 | 24.253218884120169 | 27.841201716738194 | 31.652360515021453 | 35.682403433476395 | 39.927038626609445 | 44.377682403433475 | 49.055793991416301
 | 1.1364 | 1.3258 | 1.5152 | 1.7045 | 1.8939 | 2.0833 | 2.2727 | 2.6515 | 3.0303 | 3.4091 | 3.7879 | 4.1667 | 4.5455 | 4.9242 | 5.303 | 5.6818 | 6.0606
Analyzing power of 3He-4He scattering at 6MeV

## Slide 11
The requirement of the range and an accuracy of measured energy can be satisfied by Hamamatsu Si-photodiode array S4114-35Q.
Detector
Hamamatsu Si-photodiode array S4114-35Q:
Number of channels: 35
Channel size: 0.9mm x 4.4mm
Depletion region >30mkm
Hamamatsu photodiode array S4114-35Q mounted on the ceramic board and connect with D-sub vacuum thru connector on the flange.

## Slide 12
3He-4He scattering polarimeter at 6.0 MeV beam energy
4He
Valve-2
Valve-1
Top view

## Slide 13
Side view
Top view
3He-4He scattering polarimeter at 6.0 MeV beam energy
LED
collimator
Si-array

## Slide 14
Calibration and monitoring of energy and time
The time resolution of alpha at E > 1MeV range is beater then σt ≲ 0.2 ns.
Difference time of flight for scattered 3He and recoil 4He of left/right arm:
(
allows us to strongly recognize an elastic scattered 3He 4He pair and suppress systematic errors.
Two α-sources ( -3.183 MeV and 5.486 MeV) will be used for energy calibration and monitoring.
Both, dead-layer and gain can be determined in such a way. The method was well proved in the RHIC polarimeters.
Same way we will calibrate and monitor a time. By flashing a blue LED on all channels of the silicon array. A short pulse of light can provide a good imitation of the particle .

## Slide 15
 | Be (z=4) | (z=13) | (z=28) | 
 | ~580 |  |  | 
, | ~555 |  |  | 
 | ~530 |  |  | 
 | 1.848 |  |  | 
, cm |  |  |  | 
 | Be (z=4) |  |  | 
 | ~580 |  |  | 
 | ~555 |  |  | 
 | ~530 |  |  | 
 | 1.848 |  |  | 
Multiple scattering:
To reduce beam energy , we need
6 of Be - or
of Al - or
of Ni -
if distance to detector is
10 mm “target length” gives .
 |  |  | ~
 | 3 (9.5) | (17.3) | (27.7)
Vacuum window

## Slide 16
Vacuum window
Chart: Energy loss of 6 MeV 3He vs. thickness of foils
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Al | 125 | 250 | 375 | 500 | 625 | 750 | 875 | 1000 | 1125 | 1250
Be | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
Cu | 290 | 580 | 870 | 1160 | 1450 | 1740 | 2030 | 2320 | 2610 | 2900
Absorber | Vacuum window | Al foil-1 | Al foil-2 | Al foil-3 | Al foil-4 | Al foil-5
Thickness, um | 2 | +1 | +1 | +1 | +0.5 | +0.5
Beam energy, MeV | 5.75 | 5.625 | 5.50 | 5.375 | 5.25 | 5.125
The energy of the 3He beam can be increased or decreased by up to 140 keV in total by the buncher.

## Slide 17
We studied:
mechanical and vacuum properties of thin foil for window;
safe procedure of filling 5Toor 4He-gas in chamber;
electronics: amplifier , shaper and DAQ;
the time and energy resolution of the detector;
energy absorption in thin window vs. thickness and 4He gas;
…
Test setup for 6 MeV polarimeter
Vacuum gauge1
Vacuum gauge2
4He filling system

## Slide 18
Test setup for 6 MeV polarimeter
Dry scroll pump
Pfeiffer Vacuum
Leak detector

## Slide 19
Test setup for 6 MeV polarimeter
Vacuum gauge1
Vacuum gauge1
Chamber 1 (5Torr 4He)
Chamber 2
4He filling system
α-sources: ,
12 ch. preamplifie

## Slide 20
Spectra of 148Gd after and 241Am before ~7mkm Al-foil by Hamamatsu Si array detector (S4114-35N)+preamplifier(charge)+shaper(CNI).
Sigma noise ~15keV; energy resolution of 148Gd (3.184MeV) ~18keV
and 241Am (+7mkm of Al) ~80keV; full-width of the signal ~130nsec

## Slide 21
 | 148Gd | 241Am | 5 Torr, 12.5cm | 5 Torr, 12.5cm
10-5 Torr, 20cm | 274.6 ch. | 397.6 ch. |  | 
10 Torr, 20cm | 270.9 ch. | 392.5 ch. |  | 
Delta | ~50keV | ~60keV | ~15keV | ~13keV
Absorption energy of alpha in 4He gas

## Slide 22
Spectra of 241Am (5.388-1.6%, 5.443-13%, 5.486-84%, 5.511, 5.545MeV) and 148Gd (3.184MeV) by Hamamatsu Si array detector (S4114-35N)+preamplifier(charge)+shaper.
sigma noise ~21keV;
energy resolution of alpha (148Gd) ~35keV;
full-width of the signal ~60nsec.

## Slide 23
Beam parameters:
beam polarization
beam energy
total intensity
intensity in polarimeter ~
bunch frequency 1 Hz
bunch duration to Buster (to the polarimeter can be extend 200 )
The expected characteristics of the 6 MeV polarimeter based at the following parameters of the beam:
covered of center mass angle: 70-950
available energy range: 5.0-6.0 MeV
detector noise (PED) ~ 15keV
energy resolution (no window) ~ 20keV
time resolution ~ 0.2 ns
signal full width ~ 130 ns
energy spread (after ~7mkm Al) ≲ 80keV
expected rate ~100 event/pulse
Expected Characteristics of the beam and Polarimeter

## Slide 24
Summary
Development of a polarimeter at the end of October 2019
  Mechanical and vacuum tests of the polarimeter.
Complete test of polarimeter on the BNL Tandem non polarized 3He and 4He continuous beam in December 2019:
  study of the signal coincidence in two arms:
    background;
    3He /4He separation;
    energy and time resolution of detector
  absorption energy in the vacuum window;
  absorption energy on the Al foil vs. thickness and deposited energy in 4He gas vs. pressure;
  …
Prepare the polarimeter for installation on the EBIS line in early 2020

## Slide 25
E. Beebe, S. Ikeda, T.Lehn, S. Kondrashev, M. Musgrave, J. Maxwell,
R. Milner, M. Okamura, D. Raparia, J. Ritter, S. Trabocchi
Acknowledgements
Thank you

## Slide 26
Backup

## Slide 27
Chart: Flow He-4 thru 1.8 Al foil
| 5.0000000000000001E-3 | 0.01 | 0.1 | 0.5 | 1 | 2 | 3 | 4 | 5 | 6
Presure in ch2 | 4.5e-05 | 4.5e-05 | 4.5e-05 | 4.5e-05 | 4.6e-05 | 4.8e-05 | 5e-05 | 5.1e-05 | 5.3e-05 | 6e-05
He flow | 4e-12 | 1.4e-07 | 5.5e-06 | 2.4e-05 | 4.9e-05 | 9e-05 | 0.00013 | 0.00016 | 0.0002 | 0.0003

## Slide 28
Chart: Number of the He-atoms vs. width of pulse on the valve at SCS= 2.0T and D(hole)~100mkm
| 500 | 750 | 1000 | 1250 | 1500 | 1750 | 2000 | 2250 | 2500 | 3000
Valve curr.11A | 0.0175 | 0.2744 | 0.5894 | 1.0969 | 1.3944 | 1.3594 | 1.3244
Valve curr.13A | 0.1925 | 0.91 | 1.75 | 2.52 | 2.835 | 3.22 | 3.5 | 3.5 | 3.36 | 3.01