## Slide 1: Instrumentation of SNS Target Module
M. W. Wendel
SNS Accelerator Advisory Committee Meeting
February 16–18, 2016
Key contributors:
Wim Blokland, Jeff Bryan, Yun Liu, Bob Sangrey, Bernie Riemer, Drew Winder

## Slide 2: Contents
Purpose of instrumentation
Plan for instrumentation
Report on first data
Upcoming developments

## Slide 3: Sensors are now routinely installed on the target mercury vessels
Motivation is to improve target reliability by understanding mercury vessel dynamic response
  Improve structural analyses to extrapolate new designs
  Discover unaccounted-for vulnerabilities (e.g., structural mode excitation)
  Evaluate gas injection system
Intent is to improve and extend the instrumentation suite
  Stainless steel vessel (strain, temperature, acceleration)
  Mercury (temperature, pressure, flow)
  Dosimetry and materials irradiation
Goal is to fully understand the response of the target to beam pulse

## Slide 4: On-vessel instruments will provide understanding of actual target response
FEM predictions
Analysis has uncertainties in the EOS
  Liquid, vapor, non-condensable gas
Measurements can improve analytical predictions
  Strain
  Temperature, velocity and pressure
October 8, 2015
Successful measurements of target strain

## Slide 5: With gas injection, reduction in pressure pulse loads should be evident in reduced strain
Gas injection
Gas bubbler
A similar benefit: the success of some design changes can be confirmed by measurement

## Slide 6: Strict requirements for addition of instrumentation are established
Zero impacts to beam operations due to functional failure of instrumentation hardware (including installation, removal, and disposal)
No impacts on leak detector function throughout the target lifetime
Seal on cable through target flange must be tight
Hardware must be connected by Remote Handling
Nominal target installation, removal, and disposal can not be precluded
In-beam testing plan must be coordinated with SNS operators

## Slide 7: Strain sensor measurements from in-beam experiments at Los Alamos helped jump-start the effort
Six in-beam damage test campaigns were conducted since 2000 investigating cavitation damage on mercury targets:
2011 experiment

## Slide 8: Strain sensors were installed at the target manufacturer by SNS staff
Eight strain sensors
Transmission test run of single-mode fiber
Two accelerometers

## Slide 9: Leads are coiled up on back of target module for connection after install
Unfurling/handling the fiberoptic cable
Making the connection in the cell with MSM
Cutting the fiberoptic cable

## Slide 10: Target T13 with cables ready for installation
Connector Box and spool
Fiber bundle

## Slide 11: First instrumented target (T13) provided valuable data
Strain sensors on target front
Accelerometers on piping
Collaboration involving many SNS groups
Obtained data for single pulses and bursts of 10
Engineers monitor target data acquisition system during pulse-on-demand
PROTONS
Strain Sensors
Accelerometers
Instrumented Target Installed into Core Vessel

## Slide 12: Data were collected for the following conditions before
Internal pressure (positive and negative)
Dead weight with and without mercury
Flowing mercury at various pump speeds (vibrations)
Single beam pulses
Cycled beam pulses

## Slide 13: Generally, the target responded as predicted with FEA
PROTONS
1 MW equivalent pulse

## Slide 14: Best agreement between predicted and observed response in forward region
1
2
Positioned between ribs
Calculated
Calculated

## Slide 15: Sensors 1 & 5 should have similar responses – the data validate this
Vertical offset should be corrected
Calculated
Calculated

## Slide 16: Sensor 8
Sensor 8
Pulse 19 at 25µC
Pulse 1 at 10µC
Calculated

## Slide 17: With burst of 10 pulses, no build-up is observed
Sensor 4
Sensor 7

## Slide 18: R&D of rad-hard optical strain sensors
  Radiation up to 1010 Rem/hr neutron and 108 Rem/hr gamma for 5000 hrs
  No commercial solution for high radiation optical strain sensors
~850 kW beam

## Slide 19: Instrumented target MTX-009 results
Data were obtained for 83 pulses
FEA evaluation showed agreement in timing and quality
  Prompt response right at the beam was the best-predicted
  Underestimated damping of the media (sensor 2 is interesting)
  Overestimated strains in the transition section
Strains do not change with ten 60 Hz pulses
  Single pulse assumption for FEA simulation is applicable
  15 years of in-beam scaled experiments can be used more confidently
No under-damped resonance modes were observed
Responses are linear with pulse charge
Instrumentation on future targets will investigate the unexpected results

## Slide 20: MTX-010 has been received with sensors installed
Same sensor locations
High-rad multimode option for the fiber strain sensors
Prototypes for single mode sensor (4)
Robust connector for remote-handling fiber-optic connection
Thermocouples near the back of the target

## Slide 21: Future developments
Longer life strain sensors to track changes
  High rad multi-mode
  Single mode
  Metal foil
Mercury flow and temperature
Vessel temperatures
Irradiation tests

## Slide 22: Summary
MTX-009 (T13) strain sensor results are already useful
MTX-010 (T14) has been received with improved sensor array
Plan is to grow the extent of the diagnostics to fully understand the target response