## Slide 1: Advances in Accumulator Ring Beam Damping
N.J. Evans

## Slide 2: Overview
Motivation
Damper System Status and Overview
Damping Results and Recent Advancements
Summary

## Slide 3: Motivation
E-p instability – interaction of beam with a cloud of electrons in the beam pipe generated by low levels of beam loss, amplified by secondary electron generation
Image credit: Zaipeng Xie

## Slide 4: Motivation – E-P Manifestation
Broadband (80-120MHz) betatron oscillation:
10.0μC
5.0μC
2.5μC
Spectrogram of Difference Signal
Rise time ~10’s of turns
Turn
300
1000
Turn
300
1000
Freq[MHz]
40
200
Extraction
Turn
300
1000
Freq[MHz]
40
200
2008 Study by Cousineau et. al.

## Slide 5: Motivation – E-P During Operation
E-p produces <1mm oscillation near the end of accumulation – No detectable losses associated with e-p – but:
  Onset will be fast – rise times typically 10s of turns
  Complicated dependence on many parameters – bunch shape, current, momentum spread, etc.
  Could be a problem as we move to 2.8 MW
Mitigation measures include: Beam pipe coating, up to 15 kV 2nd harmonic RF, large apertures (low losses), and active feedback

## Slide 6: Making the Damper System Work
By Dec 2014 | Hardware in place, tested, sporadic damping
Jan-Feb 2015 | Hardware Knowledge Transfer*
Mar-Jun 2015 | BTF Studies w/ damper hardware
Jul-Aug 2015 | Software & Operation Knowledge Transfer**
Aug-Sep 2015 | Consistent, Reliable Damping Achieved, Conducted Damper Performance Experiments
Oct 2015 - Present | Data Analysis, Write-up, Documentation, etc.
*Special thanks to *Jeff Bryan, *Craig Deibele, **Zaipeng Xie, ** Eric Breeding

## Slide 7: Damper System Overview
LLRF
Analog
Delay
FPGAs
Switch
Stripline
Pickup
Power
Amps
User
Interface
Stripline
Kicker
Sampling Clock
RF Ref

## Slide 8: Damper System Overview
Pickup and kicker are identical 0.49m striplines
beam
Pickup
Kicker
e-p

## Slide 9: Damper System DSP
1 QuiXilica Triton-V5 Board/plane
  10-bit ADC (up to 2GHz)
  3 Xilinx Virtex-5 FPGAs per board:
    Delay
    Comb Filters
    FIR EQ
    Digital Gain
  12-bit DAC

## Slide 10: Damper System Interface
Damper Interface
Analog Delay Interface
Works well but not user friendly

## Slide 11: Damper System In Action
Broadband signature of e-p signature on spectrogram fall 2015
Damper effectively suppresses e-p
*Note that upper and lower sidebands have been separated
Horizontal Plane

## Slide 12: Damper System In Action
Total oscillation amplitude is only about 0.5mm at the moment
Vertical oscillation not as pronounced
Vertical Plane

## Slide 13: Damper System – Delay
Multi-turn delay is a big hit to performance
Minimum delay > 2 turns
≥2146 ns
955 ns

## Slide 14: Damper System – Delay
Damping is most effective when we kick at odd integers of π/2 phase shift
Minimum delay (red) >2 turns
Optimal delay is longer
X’
X

## Slide 15: Damper System – Delay
First choose N to satisfy the phase advance
Then adjust Tadd
Total Phase Advance
Total Delay
Delay must satisfy:

## Slide 16: Damper System – Delay
Actual delays are:
  Hor = 6 turns
  Ver = 4 turns
Delay must satisfy:
Total Phase Advance
Total Delay

## Slide 17: Damper System Performance
Power in the 10-300 MHz band of difference signal
Once timing is set, gain is tuned to minimize total oscillation
Note the small rise near the end of the cycle
Horizontal
Vertical

## Slide 18: Damper System – Delay
If N gets too big trying to meet these conditions, why not change Q?
Delay must satisfy:
Total Phase Advance
Total Delay

## Slide 19: Delay Reduction Study
Change delay required to damp by changing tune
Find optimal gain for short delay
Changing back to long delay, optimal short delay setting is too large

## Slide 20: Gain Limitation
As we increase gain eventually beam is driven
Max gain changes throughout the cycle

## Slide 21: Gain Limitation
Momentum spread, beam current increase (dipole = y×I, effective gain increase) through cycle
Both could be responsible for some growth

## Slide 22: Gain Limitation
Currently gain setting at any time is limited by the trying to minimize oscillation throughout cycle

## Slide 23: Gain Scheduling
Gain should be a function of time
We tested this with a two stage gain schedule

## Slide 24: Gain Scheduling
With our large gain, growth occurs in higher modes, and late in the cycle
Gain schedule does help damp e-p and reduce growth late in cycle

## Slide 25: Summary
Damper works.
If losses due to e-p are detected damper will provide headroom
We have a lot of power, but we could use it more effectively
We have two specific tasks to improve damper:
  Implement gain scheduling
  Explore delay reduction through tune choice

## Slide 26: Summary
Understand physics behind e-p onset better to identify better working point in a complicated parameter space – delay, tune, momentum spread, gain, bunch shape, etc. – to minimize loss
  Beam based experiments
  Understand BTF measurements – simulation underway
Understand limitations of a multi-turn system
  Analytic work and simulation
The software, and documentation need to be polished

## Slide 27: Thanks
I want to thank the AP and BI teams for support throughout the last year
I especially want to thank Jeff Bryan, Craig Deibele, and Zaipeng Xie for all their help (and patience) getting the damper up and running

## Slide 28: Additional Slides

## Slide 29: Damping Rates
We can drive beam, and then damp – timing is good
Difference signal during drive-damp test
Sign of the gain is flipped at turn ~550

## Slide 30: Damping Rates
Horizontal Plane, N=6
gain too large for optimal damping
Exponential fit to dipole signal gives growth/damp times

## Slide 31: Damper System Overview
Digital Signal Processing: 1 Quixilica Board/plane 10-bit ADC (2GS/sec) 2 Xilinx FPGAs per board: Coarse Delay Comb Filters FIR EQ Digital Gain 12-bit DAC
LLRF
Analog
Delay
Switch
FPGAs

## Slide 32: Damper System – Delay Breakdown
Source | Delay[ns]
Cable ~170m | 560.1
Comb Filters | 955.0 (1 turn)
LLRF thru Amps | 631.1
Total Minimum Delay | 2146.2
>2146 ns
955 ns

## Slide 33: Damper System – Delay Breakdown
≥2189 ns
955 ns
Delay Control | Total Delay[ns] | Precision[ns]
Analog Delay | 15.75 | 0.25
Digital Delay | 1600 | ~8.0

## Slide 34: Damper System Overview
Damper system: Pickup, Signal Processing, Kicker