## Slide 1: Progress to 1.4 MW Reliable Operations
AAC, February 16-18, 2016
by Mike Plum
Ring Area Manager & Accelerator Physics Team Leader

## Slide 2: Outline
Beam power history, limitations
RFQ transmission update
Smart chopping update
Ring injection at high beam power
Activation levels, path to further improvements
Maximum beam energy for today’s accelerator

## Slide 3: Recent beam power history
Beam power on target
Jan. 1, 2013 to Dec. 31, 2015
1.0 MW
1.2 MW
1.4 MW
*0.85 MW is target conservation
0.85 MW*
Damaged RFQ RF couplers
Damaged DTL5 ceramic RF window
Damaged RFQ RF couplers
Ion source Edump
OE limit restriction
Planned power ramp up
Target replacement
Target replacement
MEBT water leak Target replacement
Target replacement
Target replacement
1.4 MW 1st time
Notes: Fall 2013 the RFQ couplers were damaged after a long period of abuse (vacuum event during a power outage, high hydrogen flow). They showed multipacting signatures and high temperature.
Spring 2014 had good RFQ couplers and ion source performance which allowed power increase to 1.4 MW.
July 2014 there were two vacuum events that released water vapor into the RFQ. RFQ couplers showed multipacting signatures and heating after those events. Increased heat load required reducing the field to allow for stable RFQ operation.
Fall 2014 there were two target failures and the MEBT water leak.
April 2015 DTL5 window failed during RF conditioning, and the replacement window had a leak that prohibited running above 1.3 MW.
Fall 2015 the OE limit restricted running below 1.4 MW. There were ion source edump issues with voltage decay and bad insulators before the target failure in September 2015. The ion source edump insulator issues continued throughout the fall. The voltage decay issue was resolved by increasing the cesium collar temperature before the target failure in September 2015. The ion source edump issues also degraded the RFQ performance by increasing beam loss and using up cooling capacity for the RFQ.

## Slide 4: Beam power limitations
Plasma processing will increase SCL cavity gradients (M. Doleans talk)
65 keV
Peak current limitation:
RFQ has poor beam transmission
60 – 75%
Energy limitation:
SCL cavity gradients limit max beam energy to ~957 MeV
Chopper improvement:
Rise/fall time improvements, longer minipulse length, smart chopping help overcome power limitations
Plan to install new RFQ Jan. 2017
Peak current and beam energy limitations are offset by the chopper improvements, but we need more margin

## Slide 5: Beam availability limitations
Overall availability is good
Biggest sources of availability limitation are linac high power RF and the associated High Voltage Converter Modulators
No correlation with high beam power
LINAC
Front-End
Accumulator Ring
RTBT
HEBT
Injection
Extraction
RF
Collimators
Downtimes by system |  |  | 
System | Subsystem | CY14 [hours] | CY15 [hours]
RF | High power | 132 | 145
Electrical | HVCM | 77 | 74
Electrical | Power supplies | 34 | 43
Electrical | AC distribution | 10 | 76
Ion source | RF | 24 | 15

## Slide 6: RFQ transmission vs. RFQ field
Due to thermal (resonance) instability we cannot operate the RFQ at the design field
Measured transmission is 12 – 30% less than design
This is the primary limitation in 1.4 MW margin
Absolute RF field measurements are difficult, and there is uncertainty in the actual fields
We know they are low, but how low?
Courtesy A. Shishlo
Oct. 27, 2015
Typical operating point today
Potential current increase

## Slide 7: RFQ absolute field measurement (S. Aleksandrov)
Measure x-ray spectrum emanating from center of RFQ
Gives absolute measurement of maximum voltage between vane tips, and thus absolute measurement of RFQ field amplitude
98%
1.5%
0.5%
Energy, keV
Counts/s
Maximum Energy
Courtesy S. Zhukov, Y. Kang

## Slide 8: RFQ inter-vane voltage (field) vs. setpoint
Absolute field measurements suggest the voltage is low by about 15%
Courtesy S. Zhukov, Y. Kang
Setpoint
Energy, keV
Design voltage = 83 kV
Today’s operating voltage
Preliminary data!
During the next few months these measurements will be improved by calibrating the x-ray detector and by determining the optimum detector position

## Slide 9: Smart chopping
10% increase in “average un-chopped” fraction may be possible
1 turn
Relatively large un-chopped flattop most of injection
Longitudinal “tricks” to recover big gap at extraction time
Ramp-up
Flat-top
Ramp-down
Store
New features

## Slide 10: Smart chopping
Status:
  Installed summer 2015
  Basic testing fall 2015
  Now needs careful study (planned for this run cycle)

## Slide 11: Path to high power, high availability operations
Replace RFQ
  Plan to install Jan. 2017
Increase SCL cavity gradients See talk by Marc Doleans
  Started Jan. 2016
Smart chopping
  Started Fall 2015
AIP program to address reliability issues See talk by George Dodson
  In progress

## Slide 12: SNS injection at high beam power
Stripper foil mount and bracket damage
Electron collector damage

## Slide 13: Ti vs TZM bracket comparison
New TZM bracket tested Nov. – Dec. 2015
  Almost zero damage at full 1.4 MW beam power
Advantages: high sublimation temperature, low sputtering yield, high sputtering threshold
Disadvantages: Heavy, long-lived radio-activation
Will test three more TZM brackets during Feb – May 2016 run
#BW-18,
~24 days at ~1.2 MW
#1872,
3 months at 1.1 to 1.4 MW.
Photos by C. Luck
#2199, TZM bracket, ~16 days at 1.4 MW
All brackets and mounts are Ti except this one

## Slide 14: Stripper foil sublimation
If our stripper foils are getting hot enough to sublimate we need to know that now
In 2015 we developed a new method to measure and monitor stripping efficiency
Results to date: maximum observed efficiency drop is 1.3% but errors are large and thinning could easily be due to effects other than sublimation

## Slide 15: Electron collector erosion
Electron collector is becoming eroded away due to impact of convoy electrons
Design on a new collector should start soon
We are considering different shapes and ability to adjust stripper foil position w.r.t. collector position
1/15/16
Photos by C. Luck
Committee advice on the urgency of this issue would be appreciated!

## Slide 16: 7/28/15 1188

## Slide 17: 1/15/16 3086

## Slide 18: Activation levels
1.3 MW until 3 to 5 hours before survey
Sept. 22, 2015
All numbers are mrem/h at 30 cm
100 mrem/h = 1 mSv/h
90
LEDP
50
After SCL-1
90
DH25
1000
strip foil
1000
inj kicker
90
coll. straight
80
Extr Sptm
DTL
2 – 30
CCL
8 – 60
SCL mb
5 – 40
SCL hb
5 – 45
5 – 35
70
Slot 32
Ring
5 – 40
50*
DH13
150*
QH26
RTBT
5 – 25*
* 3 days after 1.3 MW
** No survey near this time, indicated does rates are typical
Except for a few hot spots, the dose rates are relatively low
HEBT
<5**

## Slide 19: Recent beam power history for 2015
Beam power on target
Jan. 1, 2015 to Dec. 31, 2015
1.0 MW
1.2 MW
1.4 MW
Activation measurements
Target replacement
Planned outage
Planned outage

## Slide 20: Path to lower activation levels
Beam loss reduction to date has been almost entirely empirical
  Beam loss per Coulomb of beam charge has been steady for years (i.e. beam loss is linear with beam power)
  Possible that we are in a local minimum
  rms Twiss parameters are highly mismatched throughout linac and HEBT
  Possible that the BLMs are minimized, but the beam loss is not
Ideal route to minimum loss is accurate simulation code that will tell us how to set all parameters required
Plot courtesy of C. Peters

## Slide 21: Path to lower activation levels (cont.)
Need accurate input distribution for simulation codes
Need good linac simulation code
Need accurate SNS linac lattice
Simulation determines parameters for minimum beam loss
6D phase space measurement on Integrated Test Stand
Add linac simulation capability to PyORBIT
Beam-based measurement of lattice parameters
Benchmark simulations with measurements
* S. Cousineau talk
* A. Shishlo talk
* A. Shishlo talk

## Slide 22: Beam energy limit
Maximum beam energy today is limited to ~957 MeV by SCL cavity gradients
If the gradient limitation is removed (e.g. by plasma processing and cavity repairs) the new linac beam energy limit would be from SCL klystron power
PPU project will install new cavities before ring injection area is upgraded
What is the maximum energy?
SCL gradients March 2015

## Slide 23: Magnetic field stripping limits ring injection energy
Lorentz-transformed magnetic field looks like electric field in rest frame of beam particles Eion [V/m] = bgcBlab [T]
Loosely-bound electrons on H− particles can be stripped off
A1 = 2.47E-6 V sec/m A2 = 4.49E9 V/m
B(s) = magnetic field
b, g, c = relativistic factors
Beam energy (0.5 to 2 GeV)
0.5 T case
Frac. loss (10-6 to 101)
(A. Jason et al., PAC 1981, p. 2704)
Double jeopardy for ring injection Both beam energy and required B field are higher
Fractional loss per meter:

## Slide 24
Assume limit on additional beam loss is 1 W (i.e. adds ~1 mSv/h (100 mrem/h))
to dose rate in injection section. Also assume 1.4 MW beam power.
Beam energy (0.8 to 1.4 GeV)
Beam power lost [W]
Beam energy must be less than 1.1 GeV to limit additional beam loss to 1 W
(Magnet power supply is only at ~75% for 1.1 GeV)
Beam energy limit due to ring chicane

## Slide 25: Summary
Accelerator today can usually reach 1.4 MW, but need more margin for routine high power delivery
  RFQ replacement, plasma processing
Convoy electron damage to stripper foil brackets at high beam power is mitigated by new bracket material (TZM)
Convoy electron collector damage rate is increasing due to high beam power. Need to redesign & replace.
We have an active program to further improve beam losses and better understand beam dynamics
Maximum practical beam energy is ~1.1 GeV, limited by magnetic stripping at ring injection

## Slide 26
Thank you for your attention!

## Slide 27
Back up slides

## Slide 28: SNS Linac Structure
Length: 330 m (Superconducting part 230 m)
Production parameters:
Peak current: 38 mA
Repetition rate: 60 Hz
Macro-pulse length: 1 ms
Final Energy: 940 MeV (1000 MeV design)
Average power: 1.4 MW
65 keV

## Slide 29: Ti vs TZM bracket comparison
#2024, pos’n 9, used for 4 days, beam high on foil due to positioning error. ~2 days at ~1.3 MW.
BW-18, pos’n 4. ~24 days at ~1.2 MW
#1872, pos’n 7, up to 1.4 MW. 3 months at 1.1 to 1.4 MW.
Photos by C. Luck
#1937 pos’n #11, Foil in 5.1 mm dnstr position. ~7 days at 1.20 – 1.33 MW, ~13 days at 1.0 to 1.2 MW.
TZM bracket, ~16 days at 1.4 MW, Nov. 15 – Dec. 9, 2016
All brackets and mounts are Ti except this one

## Slide 30: SNS injection schematic
Multi-Turn Charge-Exchange Injection to accumulate high intensity
Stripping foil removes 2 electrons, injected protons merged with previously accumulated beam.
The Secondary foil strips residual H- and H0 which survive the first foil.

## Slide 31: Electron Catcher Design
Field tilt directs electrons downward
Nominally, electrons should impact underside of electron catcher wedges
Electron Catcher
1 GeV H− convoy electrons
545 keV energy
~ 2 kW
Gyroradius: 12 mm,
Period: 0.29 ns,
Pitch: ~16 – 23 mm
Efficient electron catching: catcher and foil need to be properly aligned

## Slide 32: Electron catcher is not at the proper location w.r.t. the foil
 | As built error [mm] | Tolerance [mm]**
Horizontal | 8 | A few
Vertical | 3 | ±6.5
Longitudinal | 6.4 | 6.5
Initial installation was misaligned. Foil moved three times to address injection loss and bracket damage issues.
The catcher is not and has never been positioned within design tolerance.
Design at catcher
As-built, at catcher
14
4

## Slide 33: Example Convoy Electron Simulated Trajectories
foil
bracket leg
bracket arm
Electron caught at catcher !
Reflected electron hits vacuum vessel top
Reflected electron hits bracket arm
Reflected electron hits foil again

## Slide 34: Electron catcher: Electrons striking top?
July 2014 Damage to top of wedge #3 shows circular electron trajectory. Electrons also appear to be striking underside of wedge #3 (as they should), and top edge of wedge #4.
August 2009
Carbon-carbon wedges coated by aluminum from foil brackets, then sputtered / evaporated off by convoy electrons. Electrons appear to be striking tops of wedges #3 and #4.
1
2
3
5
4
Photo by C. Luck
3