## Slide 1: Laser Stripping Experiment Status
Sarah Cousineau
AAC Review
February 17, 2016

## Slide 2: Outline
Motivation
Reminder of concept
Project structure (funding, timing, etc)
Status of 10 μs stripping project
Status of power recycling cavity effort

## Slide 3: Foil Issues at SNS: Foil Damage, Radiation
#1872, up to 1.4 MW. 3 months
Bracket damage from convoy electrons
Foil used for entire run cycle
#1073
Typical Beam Loss Pattern SNS Ring, 1.3 MW
Highest loss point in accelerator – 800 mrem/hr @ 30 cm.
Requires dual plane injection painting to minimize loss.
New foil
Nanocrystalline diamond

## Slide 4: The Price of Higher Beam Power Density (A Quick Experiment)
Chart: Horizontal RMS Emittance (pi mm mrad))
| 29.5829 | 25.6244 | 21.9501 | 17.870525
Nominal Painting | 1 | 1.097 | 1.2529 | 1.8871
Flattop | 10.8878 | 4.7878
Shallow Painting | 10.2062 | 4.3382
Nominal case
Injection radiation limit for experiment
Unexplored
Cutting the emittance by half increases injection beam loss by factor 10 - 30

## Slide 5: Laser Assisted Stripping Concept
?
H-
H0
Step 1:
Lorentz Stripping
H-  H0 + e-
e
e
e
e
Step 2:
Laser Excitation
H0 +   H0*

H0*
Laser field
e
p+
e
Step 3:
Lorentz Stripping
H0*  p + e-
Experiment conducted with
10 MW UV laser.
Diverging laser
Laser in tunnel
Straightforward scaling to 1 ms requires: ~600 kW average UV laser power (way too much!)
6 ns
H-
p
2006 Proof of Principal Experiment

## Slide 6: The Laser Stripping Collaboration
$825K
3 Years: 04/2013 – 04/2016
Goals:
Demonstrate laser assisted stripping for 10 μs
Develop laser power amplification scheme with power recycling cavity.
DOE HEP Grant:
“Laser-Assisted H- Stripping for High Intensity Synchrotrons”
BES and HEP share the injection foil problems.
There is common interest in developing laser stripping.
$250K
2 Years: 04/2016 – 04/2018
Goals
Demonstrate laser stripping for 1 ms using power recycling cavity
Develop conceptual design of operation system
Status: Almost Complete
Status: Just Awarded
1st Grant
2nd Grant

## Slide 7: Progress on 10 μs Experiment This Year
All equipment for 10μs experiment installed
Laser transported from remote to local station
Laser parameters at IP measured
Laser timed-in with beam
All necessary ion beam parameters verified at IP
Last year reported on successful demonstration ion and laser beam techniques aimed at required power.
This year’s focus was on finalization of the experimental configuration:
WE ARE READY

## Slide 8: Configuration of 10 μs Experiment
Experiment is in the transport line to the ring (HEBT)
Laser is located remotely in Ring Service Building (RSB)
Laser
in Ring Service Building
Interaction point
Major concerns:
Laser power loss in transport
Pointing stability
Safety of laser in RSB
Complexity of installation
~70 m

## Slide 9: Engineering View of Experimental Vessel (you saw it last year)
Current monitor
Movable Permanent Magnets
Wire scanner
Interaction point
Courtesy Menshov

## Slide 10: Installed Experimental Vessel
Demonstrated 100% conversion H- to H0
No interference with high power operations

## Slide 11: Laser Transport Line Design
Specs: 70 meters; 9 mirrors; 4 windows
Courtesy Menshov

## Slide 12: Laser Transport Line
Installed July 2015, January 2016
From RSB
Local optics table
Final optics table

## Slide 13: Laser Beam Spots on Monitors
Courtesy Liu, Rakhman

## Slide 14: Laser Spot and Jitter at Local Station
At exit of laser transport line
At IP
Laser jitter
Laser Spot
Laser Spot
Laser jitter
Courtesy Liu, Rakhman
Position (mm)
Position (mm)
Point # (~0.5 seconds/sample)
Point # (~0.5 seconds/sample)

## Slide 15: Final Measured Laser Parameters at IP
Parameter | Required (Design) | Delivered
Remote Station Laser Parameters |  | 
Macropulse length | 10 us | 10 us
Micropulse width | > 30 ps | 30 – 50 ps (adjustable)
Peak Power in RSB | 1.5 MW | 2.5 MW (at 35 ps)
In Tunnel Laser Parameters |  | 
Transmission Efficiency | 60% | 70%
Maximum Peak Power | 1 MW | 1.7 MW (limit to 1 MW for experiment)
Pointing stability at IP |  | ±0.10 mm (H) ×±0.11 mm (V)
Horizontal divergence at IP | 2 mrad | 2.6 mrad
Vertical size at IP | 0.8 mm | 1.1 mm

## Slide 16: Experimental Plan and Risk Mitigation
Mitigation Plan:
Windows have tested against baseline laser power.
Interlocks placed on laser size, divergence.
Experiments to be conducted only when recovery time available.
Will step laser power up slowly.
Primary Risk: Window break / vacuum leak.
Chart: Laser Peak Power (MW)
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.900000000000001 | 2.0
 | 0.44 | 0.69 | 0.83 | 0.9 | 0.93 | 0.947 | 0.95 | 0.951 | 0.952 | 0.954 | 0.957 | 0.961 | 0.966 | 0.97 | 0.974 | 0.977 | 0.979 | 0.98 | 0.981 | 0.9812
Courtesy Gorlov
Model-Calculated Stripping Efficiency vs. Power
Tuning

## Slide 17: Next Step: Extending to 1 ms Stripping
H- beam
Extending to 1 ms will require a laser power recycling cavity.
The concept is to start out with a 1 ms, low power laser pulse and amplify to ~1 MW peak in cavity power.
The experimental vessel was designed to accommodate a future cavity.

## Slide 18: Laser Power Amplification Scheme
Courtesy Liu, Rakhman

## Slide 19: Recycling Cavity Status
Cavity
Burst-mode UV beam
Cavity locking beam
Status:
Cavity lock achieved in May 2015.
Demonstrated 50 times power enhancement (goal was 30).
Courtesy Liu, Rakhman
Challenge: Mirror damage threshold too low. Can’t run high power in cavity.
Plan forward centered on investigating high damage threshold mirrors using single wavelength.

## Slide 20: Summary
We are ready to begin stripping experiments.
First experiments will commence in early March.
The laser power recycling cavity has achieved 50 times power amplification.
New grant will allow further development of power recycling cavity / amplification scheme for future 1ms stripping experiments.