## Slide 1: Beam Dynamics Studies at the ITS and Collaborative Accelerator R&D
Sarah Cousineau
AAC Review
February 16, 2016

## Slide 2: Education, Outreach, Community Service
Community Service:
Review panels: ESS, Fermilab, CSNS, JParc, FRIB
PRSTAB Editorial Board, reviewers.
Conference Organization: IPAC, NAPAC, ICFA HB, ICAP.
Education Outreach:
Host 4-8 undergraduate interns per year
Host 3 graduate students, rolling
USPAS: 5 instructors, curriculum committee chair
University of Tennessee Collaboration
Supports education and research in accelerator physics.

## Slide 3: University of Tennessee Collaboration
Research funding:
  Laser Assisted H- Stripping (DOE HEP + SNS)
  6D Beam Dynamics at ITSF (NSF HEP + SNS)
UT program currently supporting:
  2 UT postdocs
  3 UT graduate students
  1-2 undergraduate interns per year
Rely on USPAS for coursework.
Partnership with University of Tennessee to provide Accelerator Science education.

## Slide 4: The Laser Stripping Project
DOE HEP Grant: “Laser-Assisted H- Stripping for High Intensity Synchrotrons”
Educational Support
4 undergraduate internships
1 graduate student
1 postdoc
Postdoc/Student Projects
Technical details in break-out session tomorrow.
Terms of Initial Award
3 years: 05/2013 – 04/2016
$825K
Renewal Award
2 years: 04/2016 – 04/2018
$250K
Lutrell
Liu, Rakhman
Liu, Rakhman

## Slide 5: 6D Beam Dynamics at the ITS
NSF Grant: “Six Dimensional Experimental Characterization of High Intensity Hadron Beams in Front End Systems”
Terms:
$600K
3 Years 09/2015 – 09/2018
Educational Support
1 postdoc (hired)
1 graduate student (in place)
1 undergraduate per year
Student/Postdoc Projects
Diagnostics design optimization
Design of lattice
Data acquisition software
Optimization of data processing
Simulations of beam halo

## Slide 6: Motivation
A common conclusion: “Our code doesn’t reproduce the measured beam distribution because we don’t have an accurate initial distribution.”
Is it true? We want to find out.
Typically, measure
projections:
The Goal:
x’
x
y’
y
φ
z
Combine assuming no other relationships between variables

## Slide 7: Motivation
But this is not a complete 6D distribution:
Assumes all cross-terms = 0
Includes cross-terms:
Possible sources of non-zero cross terms:
Solenoidal focusing in LEBT
Space charge forces
Non axially symmetric fields in ion source
Q: Are these terms significant enough to affect the beam dynamics?
A: We think so…

## Slide 8: The Impact of Cross-Terms
Example: Start with 2 distributions whose typically measured properties look the same, but which differ in the underlying cross-terms.
Uncorrelated in cross terms
(all cross-terms = 0)
Correlated in cross terms (KV)
FODO
transport

## Slide 9: The “Curse of Dimensionality”
Traditional diagnostics can be used to measure all projections.
The limiting problem is scan time.
Problem compounded by need to average over multiple samples.
Times are not reasonable for operational accelerators.
1 2 …….. m
For a course measurement:
Scan rate 1 step/sec: 106 sec = 280 hrs
Scan rate 10 step/sec: 105 sec = 28 hrs

## Slide 10: 6D Beam Dynamics Studies at the ITSF
Full 6D diagnostics suite
A transport lattice with variable matching
Students, postdocs!
Integrated Test Stand
Goals of this project:
Complete the first direct 6D phase space measurement of beam exiting RFQ.
Measure and simulate beam halo formation.
Identify important phase space correlations.
Required Infrastructure:
  Finally, we have the critical ingredient!
  Does it help?
  Can we alter diagnostics in operational machines to provide this information?
Upcoming additions
NSF HEP award
Operational-style front end
High beam current (for space charge)
LOTS OF BEAM TIME (main limitation)

## Slide 11: Integrated Test Stand Facility
Ion Source
RFQ
MEBT
Particles | H-
Energy | 2.5 MeV
Current | < 50 mA
Pulse width | < 1 ms
Rep rate | ≤ 60 Hz
Power | < 7.5 kW
Future Extension for Neutron Moderator Studies
Menshov

## Slide 12: From 2D to 4D Transverse Measurements
FARADAY CUP
BEAM
FARADAY CUP
BEAM
4D system is part of original ITSF diagnostic suite
Menshov

## Slide 13: Direct 6D Measurement Scheme
dxdy
BEAMLET
dxdydx´dy´
BEAMLET
RF DEFLECTOR
(BSM)
BENDING MAGNET
(Magnetic Spectrometer)
FARADAY CUP
These are all well-established diagnostics techniques
Note the intensity is cut at each step. What is left at the Faraday Cup?
Energy Selection
Phase Selection
Menshov

## Slide 14: The Issue of Signal Strength
Equal sampling in all planes
Example:
Beam Extent (r=n*σ) | N remaining
r = 1σ | 3.5×106
r = 3σ | 2.9×104
r = 5σ | 9.7
Faraday cup sufficient for at least 3σ
B. Cathey

## Slide 15: Layout of 6D Measurement Diagnostics
Slit Pair 2
Slit Pair 1
Slit Pair 3
BSM
From RFQ
Menshov

## Slide 16: Reducing the z-φ Scan Time
Magnet
Energy selection slit
Time selection slit
Faraday Cup or
other detector
RF deflector
  Advantage:
  Faster
  Disadvantage: Smaller dynamics range of charge to light conversion.
Magnet
View screen
Digital camera
φ
W
100 × faster
RF deflector
Optimization is a graduate student project.

## Slide 17: Lattice for Halo Studies
Option 1
Option 2
Design of lattice is postdoc project.
New postdoc, Z. Zhang, arriving May, 2016.
Menshov

## Slide 18: Schedule
09/2015
-
09/2016
Hire graduate student, postdoc.
Optimize diagnostics.
Design lattice.
Develop data acquisition software.
09/2016
-
09/2017
Install diagnostics.
Fabricate and install lattice.
Perform 6D phase space measurement.
09/2017
-
09/2018
Perform beam dynamics experiments.
Simulate and benchmark halo with pyORBIT.
Evaluate cross correlations and diagnostics.

## Slide 19: Summary
Accelerator physics, diagnostics, and ion source group very active in external community.
Strong accelerator physics education collaboration with UT, supported by DOE and NSF HEP grants that allow “hands-on” research for postdocs, students.
Beam dynamics at ITSF will attempt the first direct 6D measurement of beam in a front end.
Will use 6D distribution to study halo development and benchmark codes.
Schedule for 6D project is very aggressive.