## Slide 1: STS Neutron Beamline Interfaces
Van Graves STS Instrument Engineer
STS Fundamental Physics Workshop July 26, 2019

## Slide 2: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Instruments

## Slide 3: Site Plan

## Slide 6: STS Facilities
STS divided into 4 joined buildings
Instrument buildings named by nominal instrument length from monolith center
Avg STS instrument length is 30% longer than avg FTS instrument length
Target Building
40M Building
50M Building
90M Building
90 m
40 m
50 m
FTS
STS

## Slide 7: STS Initial Planning Instrument Suite
STS will support 22 instruments
Currently all end stations fit within building envelopes
  Left two empty ports for additional long instruments, hope to limit building punch-throughs to these instruments
  STS site best supports long instruments in the ST18-ST22 quadrant
ST22
IMAGING
ST21
MENUS
ST20
EWALD
ST19
TBD
ST18
TBD
ST17
CHESS
ST16
NESCRY
ST15
TBD
ST14
HERTZ
ST13
VERDI
ST12
NSE
ST01
SANS2
ST02
ZEEMANS
ST03
CYGNUS
ST04
TBD
ST05
VBPR
ST06
SANS1
ST07
BWAVES
ST08
WASABI
ST09
QIKR
ST10
TBD
ST11
SANS3

## Slide 8: STS Day One Instruments
Eight initial instruments in current project scope have been developed to conceptual level
Final instrument suite and port locations will be selected post-CD1
ST21
MENUS
ST20
EWALD
ST17
CHESS
ST13
VERDI
ST02
ZEEMANS
ST03
CYGNUS
ST06
SANS1
ST09
QIKR

## Slide 9: STS Beam Line Arrangement
Top (Cylindrical) Moderator Beams
Bottom (Tube) Moderator Beams
Proton Beam
Beam lines 1-11
Beam lines 12-22

## Slide 10: Instruments by Moderator
Tube moderator provides broader pulses than cylinder moderator at the same pulse peaks
2 of 6 tube moderator beam ports currently occupied by Day One instruments (SANS1 & CHESS)
ST22
IMAGING
ST21
MENUS
ST20
EWALD
ST19
TBD
ST18
TBD
ST17
CHESS
ST16
NESCRY
ST15
TBD
ST14
HERTZ
ST13
VERDI
ST12
NSE
ST01
SANS2
ST02
ZEEMANS
ST03
CYGNUS
ST04
TBD
ST05
VBPR
ST06
SANS1
ST07
BWAVES
ST08
WASABI
ST09
QIKR
ST10
TBD
ST11
SANS3
Moderator/Reflector Assembly

## Slide 11: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Instruments

## Slide 12: STS Incorporates Neutron Beamline Bunkers
Heavily shielded rooms near monolith where choppers and other beamline components are located
  Personnel-accessible during beam-off without unstacking significant amounts of shielding
Bunker implementation motivated by
  the desire to reduce background radiation by providing an integrated shielding design near the target monolith.
  the observation that the high brightness STS moderators are smaller than their FTS counterparts, requiring greater alignment precision of the in-monolith optics packages.
  the desire for straightforward and flexible installation of the near-monolith beamline components and required services (vacuum, cooling water, and electrical).
Bunkers require significant integration and interface definitions between Instrument Systems, Target Systems, and Conventional Facilities

## Slide 13: Neutron Beam Line Bunkers are Beam-off Accessible
Provide closest locations for hands-on accessible beam line optics & choppers
  Maintaining personnel accessibility during beam-off for life of facility is a fundamental design requirement and assumption
  This assumption is based on chopper activation experience at FTS & will be continually reviewed as neutronics analyses are completed
Houses facility Maintenance Shutters
Radial depth (~5.6 m) adequate for monolith insert handling equipment
Provides utilities for choppers, shutters, & monolith inserts
Removable shielding roof panels (~1.5m thick high-density concrete) & floor level access door
Monolith Insert Remote Handling Device
STS neutron bunkers will be more crowded than this!

## Slide 14: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Instruments
Monolith insert with optical guide module
STS Neutron Factory & Monolith Inserts

## Slide 15: All 22 Monolith Inserts Installed During STS Construction
Reentrant, water-cooled, stainless housing which allows installation of neutron optics in close proximity to the moderators
  ~5 m long, ~2 tons
  Can also accommodate shield plugs
All Inserts installed during facility construction, assumed to be life-of-facility components (but can be replaced)
  Unpopulated beamlines will have shield plugs within Monolith Inserts
Seals against nozzle flange
Provides cooling environment for guide optics
Incorporates permanent upstream beam window
Exterior steps block neutron streaming paths and minimize upstream width
Monolith Insert
Maintenance Shutter
Nozzle Extension
Insert Seal Surface
Insert Utility Connections
Upstream Beam Window
Downstream Beam Window
Insert with shield plug
Guide Module

## Slide 16: Moderator Approach Distance
Nozzles extend the vessel environment through the monolith shielding to the bunker
Nozzles will be matched to scientific and facility layout requirements (angles, sizes, slopes, etc.)
  Currently all except QIKR are standardized
Delivering the best science requires ability to place guide as close as possible to moderator
All moderator views are 3x3 cm, but Monolith Inserts are standardized with 5x5 cm openings to account for diverging optics
Approach distances determined by beam port location and moderator
  Tube moderator inserts don't have adjacent neighbors, can extend further into monolith
Horizontal section through upper moderator
Beamline | Approach Distance (cm) | Beamline | Approach Distance (cm)
ST01 | 95 | ST22 | 95
ST02 | 98 | ST21 | 98
ST03 | 98 | ST20 | 98
ST04 | 98 | ST19 | 98
ST05 | 98 | ST18 | 98
ST06 | 78 | ST17 | 78
ST07 | 98 | ST16 | 98
ST08 | 98 | ST15 | 98
ST09 | 104 | ST14 | 98
ST10 | 98 | ST13 | 98
ST11 | 108 | ST12 | 108
Upper moderator approach distances
Lower moderator approach distances

## Slide 17: Guide Modules Aligned within Inserts
Most guide modules installations will be semi-remote because target will be in place
Guide alignment shims pre-configured based on mapped monolith insert geometry
Downstream beam window & shield plug removed prior to installation
Guide module pushed into kinematic locating features, gravity holds in place
Downstream window installed semi-remotely
Monolith Insert & Guide Module alignment mockup proposed
Guide Module
Monolith Insert
Downstream alignment features
Upstream alignment feature (insert & guide cut for visibility)

## Slide 18: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Instruments

## Slide 19: STS Shutter Philosophy
FTS uses large primary shutters for all beam lines
  Only a few beam lines use their primary shutter for experimental operations (some don’t have secondary shutters), most only used during weekly or run-cycle shutdowns
  Shutters are highly activated and heavily shielded
Since STS facility shutters are in personnel-accessible bunker, shutter activation can’t be allowed
STS approach is to provide Maintenance Shutters in bunkers, with each beam line responsible for their own Operations Shutter(s) downstream
FTS Beam Line | Primary Shutter Operations | Ops/Week
3 | 347 | 26.9
18 | 133 | 10.3
12 | 94 | 7.3
17 | 57 | 4.4
5 | 37 | 2.9
14 | 13 | 1.0
13 | 11 | 0.9
1 | 7 | 0.5
2 | 6 | 0.5
4 | 6 | 0.5
16 | 3 | 0.2
6 | 1 | 0.1
7 | 1 | 0.1
11 | 1 | 0.1
15 | 1 | 0.1
FTS Shutter use during beam-on ops Jan 21 – Apr 21, 2015 (~13 wks)
Maintenance Shutter

## Slide 20: Maintenance Shutters have 3 Functional Positions – Open, Gamma Blocking, and Neutron Absorbing
Primarily used to block gamma radiation during maintenance outages
  Current concept: 20 cm tungsten
  Not used as neutron blockers due to activation limitations
Neutron absorber reduces activation of failed downstream components (choppers) during beam-on operations but does not allow their extraction from the beam line
  Constructed from material which does not activate strongly
  Will likely not block all neutrons, so components between Maintenance & Operations Shutters can only be accessed during facility shutdowns
Optical guides can be accommodated
Shutter cavity widths driven by requirement to extract monolith inserts
Shutter gates installed with beam lines
  Unused beam lines will have shield plugs within Monolith Inserts
Gamma Blocker
Optional Guide
Neutron Absorber
Guide Carrier with kinematic alignment features

## Slide 21: Neutron-Blocking Operations Shutters Required by all Beam Lines
Each beam line responsible for its own operations shutter(s) for daily experimental operations
  Curved lines may only require thin neutron absorbers
  Straight lines will require heavy tungsten shutter, early estimates suggest 1m tungsten
Plan to provide standard designs suitable for majority of beamlines, based on proven FTS secondary shutters
Operations shutters will allow personnel access for sample changes and failed downstream components
  Personnel can’t access beam line components upstream of operations shutters except during maintenance periods
1m
Guide
Tungsten
Neutron absorber
Operations shutter

## Slide 22: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Instruments

## Slide 23: Day One Instruments
EWALD – Enhanced Wide-Angle Laue Diffractometer
CHESS – Chopper Spectrometer for Small Samples
ZEEMANS – High Magnetic Field Instrument
CYGNUS - SWANS
SANS1
QIKR – Quite Intense Kinetics Reflectometer
VERDI – Versatile Diffractometer
MENUS – Materials Engineering by Neutron Scattering

## Slide 24: QIKR Requires Several Facility Customizations
Two independent views of same moderator to support liquid-liquid interfaces from both directions
  5° vertical separation, 2° horizontal separation between dual end stations
  Single chopper supports both beams
Diverging beams from moderator significantly complicate monolith optics
  Custom handling equipment needed
Custom Nozzle Extension and Maintenance Shutter required

## Slide 25: Summary
Neutron bunker operational philosophy drives the design of STS beamlines and interfaces with Target and Conventional Systems
Initial beamline concepts fit within current building boundaries, empty beam ports can accommodate two future long beamlines
FTS shutter experience led to adoption of maintenance / operations shutter scheme
Customizations to accommodate science requirements, within some limits, can occur for those needs which are known early in the design process

## Slide 26: Questions?

## Slide 27: FTS/STS Comparison – Sections Perpendicular to Proton Beam
Core Vessel
Core Vessel Insert / Monolith Insert
Shutter Insert / Maintenance Shutter Insert
Target Building Boundary
Primary Shutter / Maintenance Shutter
STS Core Vessel Environment extends further outward
STS monolith optics & shutters are much different than FTS
  STS Monolith Inserts combine FTS CV & Shutter Inserts
STS bunker diameter and Target Building width are linked
Core Vessel Environment

## Slide 28: Bunker Interfaces & Scope
Conventional Facilities
  Permanent concrete
  Conventional utilities
Target Systems
  Core Vessel & Nozzle extensions
  Monolith shielding
  Monolith Insert utilities
Instrument Systems
  Bunker Roof Panels
  Monolith Inserts
  Maintenance Shutters
  Beamline technical equipment & shared utilities

## Slide 29: Conventional Facilities Must Support Compact Neutron Source Optics
Target and Instrument Building designs must provide stable platforms for both initial and future beamline installations
Requirement given to Conventional regarding monolith & instrument floor deflection
  1mm initial settlement + 1mm live load (temporary) deflection
  Preventing relative movement between monolith and instrument floors is critical
Initial structural design incorporates micro-pile spacing of 10ft
Small amount of basement space under 40M/50M Buildings, mostly slab-on-grade

## Slide 30: Alignment – Neutron Beam Lines to Moderators
Core vessel nozzles attached on site
  Nozzle ends supported by monolith structure (not shown)
Vessel beam port face & nozzle flange fabrication and installation tolerances must be considered in adjustment range of inserts & guides
Large component fabricator indicates positional tolerances on pins ±0.1 mm and perpendicularity tolerance of ±0.02 mm (0.004° on the faces) plus ±0.2 mm installation tolerance
  Leads to a positional error of ±0.9 mm at the downstream end of the nozzles (~5 m)
  Remote installation of inserts & guides imposes a 6 mm gap around components, so fabrication error does not impact design
Nozzle installation must be well mapped for insert installation
  Monolith bulk shielding will be in place during survey, expect entire monolith to move as single entity
Core Vessel and Nozzle Extensions

## Slide 31: Alignment – Neutron Beamlines to Moderators (cont'd)
Precisely defining beamline misalignment tolerances requires understanding of their impact on instrument performance
  Sensitivity analyses (neutron simulations) needed to fully define these tolerances
  Expect cylindrical moderator more forgiving than tube moderator with 1 beamline viewing each tube end
Preliminary study of tube moderator misalignment completed
  Initial conclusion is beamlines should be aligned within 0.5 degrees of tube axis
Brightness changes at neutron emission for off-axis angles for brightness of 3-cm-diameter tube moderator. The effect on the time-integrated brightness is shown on the left plot, and peak brightness is on the right plot.
"A Liquid Hydrogen Tube Moderator Arrangement for STS,” F.X. Gallmeier, STS document STS03-31-TR0005-R00, January 2018

## Slide 32: Monolith Insert Utilities
Cooling utilities provided by Target Systems as in FTS
  Helium supply / hot off-gas
  Seal vacuum port
  Water supply / return
Floor trench shields water pipes and provides drain location for monolith insert leaks
Hot off-gas
Helium supply &
insert seal vacuum check port
Insert cooling water supply & return
Gas valve panel
Feedthrough box into monolith inserts
Insert utilties
Insert internal water cooling paths

## Slide 33: Initial Bunker Wall Penetration Shielding
Create ample penetrations in bunker wall to aid in beamline component installation and future needs
Must fill in openings with shielding (1.5m-thick bunker walls)
Considering a drawer-style concept to facilitate such installation
  Details are beamline-specific
Would require partial beamline disassembly and auxiliary support structure to pull drawers into bunker
  Prefer to put only passive optics in bunker wall, but this would not be a hard requirement
Inner bunker wall serves as SCE boundary, will require some sort of air barrier
Drawers extended into bunker

## Slide 34: Outline
Facility layout
Neutron beamline bunkers
Monolith optics & alignment
Shutters
Choppers & beamline shielding
Instruments

## Slide 35: Choppers Concepts Based on FTS Choppers
Basis for STS chopper concept: when chopper speed equals source frequency, the edges of STS neutron pulses exiting chopper have the same rise & fall time as the FTS exiting edges
  Chopper diameters increase from 0.58m (FTS/60Hz) to 1.25m (STS/15Hz)
  Smaller choppers (0.7m dia) are possible which require two disks to meet the STS Chopper Specification but function as a single disk chopper
  STS chopper library developed based on FTS designs for commonly used choppers
Large diameter choppers fit better in the bunker, but can be anywhere along the beamlines
Magnetic bearing T0 choppers are being strongly considered since they will impose no vibration on sensitive optics
Large diameter T0 choppers in bunker
STS 15Hz chopper library

## Slide 36: Beam Line Shielding Estimates Completed
Preliminary beam line shielding estimates developed from McStas calculation for 15 Hz / 700 kW operation / multiple moderator sizes
  Constant cross section guides matching moderator view face sizes
  Straight & curved (2000m radius) beam lines
Results
  1m regular density concrete (RDC) around beam lines out to ~30m
  ~1.5m high density concrete (HDC) bunker roof panels & wall
Intend to implement consistent method for precast concrete shield blocks
  Fabrication tolerances from different techniques caused fit-up problems on FTS beam lines
As neutronics analyses are performed, streaming shield requirements along the beam lines will be developed
Estimated 1m shielding around choppers
Bunker outer wall
Estimated 1.5m shielding around bunker