## Slide 1
The decade long transition from a custom control system to EPICS
Edmund Blomley on behalf of the KIT team
Copyright M. Breig

## Slide 2: Karlsruhe Research Accelerator (KARA)
KIT synchrotron lightsource & accelerator test facility
  until 2015 known as „ANKA“
Key parameters
  Build 2001
  Circumference: 110.4 m
  Ramped storage ring: 0.5 - 2.5 GeV
Image: U. Herberger
1 Hz injection scheme at 0.5 GeV
accumulation for 30-45 minutes once per day

## Slide 3: The Original Control System: ACS
ACS
  ALMA common software (https://ascl.net/1302.003)
  Advanced control system
Motivation
  Object-oriented interface abstraction layer
  Provide same interface for all power supplies independent of manufacturer
Custom extensions for ANKA
  LonWorks bus (at that time, cheap and efficient for the amount of data)
  Special hardware control cards
First Control System

## Slide 4: ACS & LonWorks Layout
Server
LonWorks PCI Card
LonWorks Bus
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
Device
Custom Interface Card
LonWorks bus system
Worked well for original setup
Over time maintenance more tricky
Challenge of adding any new device

## Slide 5: Migration to a new Control System?
Issues with ACS in regard to scale– and extendability
Around 2007 looking for an alternative control system
No dedicated controls group
  “What is CERN doing?”
Decision was made to introduce to PVSS/WinCC
  GUI(!)
support for PLCs
Integration of MRF timing system via UDP
  By choice to avoid VME
Second Control System

## Slide 6: EPICS: First Contact
3-4 years of investment into PVSS
  Spoiler alert: PVSS didn’t get much traction on the accelerator side
Around 2010: Tango or EPICS?
New BPM electronics
  Comparing Tango and EPICS implementation
Decision was made to switch to EPICS
Control System Studio (CSS) as the new GUI
Third Control System

## Slide 7: Design Decisions
Ubuntu desktop and server as main OS
  Use virtual machines as much as possible
Custom EPICS build toolchain creating Debian packages
  Only build modules we need
  Add local patches as needed
Cassandra database for archiving raw data
Naming conventions…
  <accelerator>:<location>:<device group>:<device name/number>:<properties>
  Avoid too many abbreviations
  Local patch of EPICS base to allow PV length up to 255 characters

## Slide 8: Migration Plan
Ethernet or serial communication directly possible?
  Beam current DCCT: create IOC to read out serial interface
Possible to exchange hardware interface?
  Storage ring quadrupole magnets: replaced controls interface
Exchange individual devices
  Ideally commercially available (no custom power supplies)
  TCP/UDP (or serial) interface mandatory
No migration of complex systems
  Analog LLRF: replace whole system

## Slide 9: Gateways
EPICS
PVSS
ACS
OPC
CAS
Implement gateways while “waiting“ for native implementation
At least basic access
  Status, on, off, set value
Allow GUI control, alarming, archiving via EPICS/CSS

## Slide 10: Migration Milestones
2023
2012
2018
2015
2021
First EPICS devices
First IOC
LLRF system
First family of power supplies
Shutdown of PVSS
Replacement of large power supplies
Shutdown of ACS
First insertion device
Second family of power supplies

## Slide 11: Status
Recent focus on Python-based IOCs and AI integrations
Centralised IOC management via Salt
Next in line:
  Migration to Phoebus
  Fully transition to OPCUA (for PLCs)
  Bluesky?
~80,000 PVs
~700 IP devices
~94 IOCs
TUPDP030
THPDP020
~30 PLCs
More accelerators!
  FLUTE
  cStart
  Laser Wakefield Accelerator…

## Slide 12: Community Contribution?
Working on new controls website
Open access to our internal EPICS repositories and/or build products
  Lots of automated workflows (CI/CD using GitLab)
  EPICS Debian tool chain
  Python-to-Debian tool chain (pyepics, softIOC, caproto, etc…)
  IOCs for commercial devices
  Establish documentation workflow (GitLab -> Readthedocs)
Make our EPICS developments more visible
  OPCUA, MRF, …
  Execute Device Support

## Slide 13: Not just changing Control Systems…
2001
2023
2012
2006
2019
Karlsruhe Research Center (FZK)
Karlsruhe Institute of Technology (KIT)
Institute for Synchrotron Radiation (ISS)
Institute for Beam Physics and Technology (IBPT)
Institute for Photon Science (IPS)
ANKA
KARA
ACS
PVSS
EPICS