## Slide 1: Review of the open source EtherCAT Motion Control Framework
Alvin Acerbo :: Controls Engineer :: Paul Scherrer Institute
EPICS Collaboration Meeting 2023, 8 October, Cape Town

## Slide 2: EtherCAT: an Ethernet-based fieldbus
EtherCAT = Ethernet for Control Automation Technology
Open fieldbus standard originally developed by Beckhoff GmbH.
Maintained by EtherCAT Technology Group.
Hardware requirements:
  Master: standard computer hardware (NIC)
  Slaves: dedicated hardware, EtherCAT Slave Controller (ESC)
Masters: Commercial (e.g. Beckhoff TwinCAT) and open source masters available.
Slaves: Several 100 manufacturers of slaves (drives, I/O, sensors, robots).
Topologies: Line, Star, Ring.
Media: Cat 5 cable, plastic fiber, glass fiber.
Bandwidth utilization: 80%-97% (100 Mbit/s , Ethernet, Full-Duplex) .
Supports Distributed Clock (DC) in slaves with a max. of 100 ns synch error.
Cycle times > 50μs.
Applications: Motion, large or long distance systems, synchronized systems.

## Slide 3: Previous work and status at SLS-2
Diamond Light source “dls-ethercat” driver:
  Data acquisition and control
Paul Scherrer Institute “ecat2” driver:
  Data acquisition and control
Other facilities are using EtherCAT as well but based on commercial software / hardware platforms.
At SLS-2.0:
  Chosen as a medium performance platform for data acquisition and control.
  Chosen for motion control in accelerator applications.
  ECMC with EtherLab driver.

## Slide 4: ECMC: EtherCAT Motion Control
ECMC is an open source motion control framework for EPICS environment.
Functionalities:
Motion (with EPICS Motor Record support):
  Positioning (absolute, relative)
  Constant speed
  Referencing sequences
Motion (extension to Motor Record)
  Motion interlocks
  Triggering, latching positions
  Synchronization axis to axis
  Synchronization to external source (timing system,…)
General
  Data acquisition (analogue <100 kHz, digital <1 MHz)
  General I/O + low level control

## Slide 5: Architecture
Linux Controller
EtherCAT master / User space
Iocsh conf. cmd:
“ecmcConfigOrDie()”
ECMC Core
Real Time Thread (1kHz)
Axis 1
Axis 2
PLC 1
Axis n
EtherCAT process image
PLC n
asynPortDriver
Interfaces
asynoctet
asynfloat64
asynarrayxxx
asynint32
command parser
Kernel
EPICS motor records
EPICS records
EthercatMC
Motor model 3 drv.

## Slide 6: Real Time Thread Execution
EtherCAT
Axis 1
Axis PLC 1
Axis 2
Axis PLC 2
Axis n
Axis PLC n
PLC 1
PLC 2
PLC n
Read from EC
Write to EC
Sleep (next ms)
EtherCAT
Motion
General PLC

## Slide 7: Axis class
14
Encoder
PID-Control
Monitor
Drive
Axis
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
ECPdoEntry
EC master
EC master
EC master
Axis object executes and links objects:
  Encoder
  Trajectory Generation
  PID-Controller
  Monitor
  Drive
Sequences
  Homing (different types)
“Cfg.CreateAxis(…)”
Types: Normal / Virtual
Optional Axis PLC for synchronization / control (executed in sync with axis object)
Trajectory
Normal, Virtual
Normal, Virtual
Normal, Virtual
Normal
Normal

## Slide 8: Configuration in EPICS
All configuration in EPICS startup file:
ECMC configurations
(speed, acceleration…..)
Terminal configurations
(Service Data Object access:
max current, mode…)

## Slide 9: Configuration continued
Configuration iocsh command:
ecmcConfigOrDie “command” : Exits if return code !=0
ecmcConfig “command” : Accepts return codes !=0
Returns: 0 for success or otherwise error code.
Example 1: Create Axis 1 object:
ecmcConfigOrDie ”Cfg.CreateDefaultAxis(1)”
Example 2: Set position controller gain for axis 1 to 0.1
ecmcConfigOrDie ”Cfg.SetAxisCntrlKp(1,0.1)”
Example 3: Read max current of EL7041 drive at bus position 1:
ecmcConfig ”EcReadSdo(1,0x8010,0x1)”

## Slide 10: Configuration with ecmccfg
Configuration is made by adding commands to the ioc startup file.
In order to simplify, a configuration framework called ecmccfg have been developed (originally at PSI):
  Main repo: https://github.com/paulscherrerinstitute/ecmccfg
  Local fork: https://github.com/icshwi/ecmccfg.
ecmccfg contains:
  Hardware configuration files for:
    EtherCAT slaves
    Motors, encoders, and sensors
  Default database files
  Extensive set of examples for different hardware's and applications

## Slide 11: Synchronization
Synchronization of axes is handled by a axis synchronous PLC:
  ax<id>.traj.setpos = Trajectory generated setpoint for axis <id>
  ax<id>.enc.actpos = Actual position of axis <id>
  ax<id>.drv.enable = Enable amplifier of axis <id>
  ax<id>.mon.ilock = Motion interlock of axis <id> (allowed to move if 1)
  ax<id>.mon.ilockfwd = Motion interlock of axis fwd <id> (allowed to move if 1)
  ax<id>.mon.ilockfwd = Motion interlock of axis bwd <id> (allowed to move if 1)
  ….. Any plc expression can be entered.
Axis PLCs are recalculated / refreshed in 1kHz
Examples:
Slaving: ax2.traj.setpos := ax1.enc.actpos;
Synchronization: ax2.traj.setpos := ax1.traj.setpos;
Gearing: ax2.traj.setpos := 0.5 * ax1.traj.setpos;
Phasing: ax3.traj.setpos := ax1.traj.setpos + ax2.traj.setpos;
Advanced: ax1.traj.setpos := 10*sin(ax2.traj.setpos + ec0.s3.VALUE);
Timing system: ax1.traj.setpos := ec0.s3.VALUE * 0.5 + ec0.s4.AO_1;
Interlocks: ax1.mon.ilock := ax2.mon.ilock and ax5.mon.ilock and ax4.enc.actpos > ax3.enc.actpos;
Enable: ax2.drv.enable := ax1.drv.enable;
Enable alternative: mc_power(1,ax1.drv.enable);
Axis 1
Axis PLC 1
Axis 2
Axis PLC 2
Axis n
Axis PLC n
PLC 1
PLC 2
PLC n
Read from EC
Write to EC
Execution flow:

## Slide 12: ECMC data access over Asyn: EtherCAT
Record INP/OUTP field syntax:
"@asyn(<asynPort>,<address>,<timeout>)ecmcInfoStr)”
ecmcInfoStr:
CMD=<cmd>/T_SMP_MS=<sampletime>/TYPE=<type>/<parameter name><read/write>"
CMD (optional):
  “UINT64TOFLOAT64”: Converts 64bit uint data to float64 before push to EPICS (64 bit positions and time)
  “FLOAT64TOINT32”: Converts float 64 to int32 before push to epics (binary PLC values)
T_SMP_MS (optional): Record update rate in milliseconds
TYPE (mandatory): Type of data to transfer (asynInt32, asynFloat64, asynInt32ArrayIn..)
<parameter name> (mandatory):
  Example for Ec data: “ec<master index>.s<slave index>.<data alias>”
  Use “ecmcReport 3” to see available parameter names
<read/write> (mandatory)
read “?”
write “=”

## Slide 13: Example: 2-Axes slit
2 virtual axes
  Slit center position
  Slit gap/opening
2 normal axes (blade positions)
Forward Kinematics:
ax3.traj.setpos:=ax1.traj.setpos - ax2.traj.setpos/2;
ax4.traj.setpos:=ax1.traj.setpos + ax2.traj.setpos/2;
Inverse Kinematics:
ax1.enc.actpos:=(ax3.enc.actpos+ax4.enc.actpos )/2;
ax2.enc.actpos:=(ax4.enc.actpos – ax3.enc.actpos);
Amplifier enable:
ax3.drv.enable:=ax1.drv.enable or ax2.drv.enable;
ax4.drv.enable:=ax1.drv.enable or ax2.drv.enable;
Or:
mc_power(3, ax1.drv.enable or ax2.drv.enable);
mc_power(4, ax1.drv.enable or ax2.drv.enable);
Blade
Axis 3
Blade
Axis 4
Axis 4 (Normal: Blade position)
Axis 3 (Normal: Blade position)
Axis 1 (Virt: Center position)
Axis 2 (Virt: Gap)

## Slide 14: Summary
EtherCAT:
  Hardware portfolio supporting EtherCAT is large.
EMCC:
  ECMC built on OS EtherLab driver.
  ECMC has a well-developed interface to EPICS.
SLS-2.0:
  ECMC is being adopted for motion, DAQ, I/O at SLS-2.0 beamlines girders, RF.
    Served mid-tier performance applications, highly customizable.
    Potential for more complex scenarios (i.e. complex kinematics, fly-scan)

## Slide 15: Wir schaffen Wissen – heute für morgen
My thanks go to
ECMC developers
Anders Sandstrom
Igh open source EtherCAT master (www.etherlab.org)
Questions?