## Slide 1: Warm and cold SNS LINAC commissioning
A. Aleksandrov
9/25/2021
Spallation Neutron Source,
Oak Ridge National Laboratory, TN USA
Test Beams at SNS

## Slide 2: Outline
SNS accelerator overview
Test beam options at SNS accelerator
  Linac Dump
  Momentum Dump
  Injection Dump
  Extraction Dump
SNS Beam Test facility

## Slide 3: SNS Accelerator Complex
H- stripped to protons
Current
1ms
Front-End: Produce a 1-msec long, chopped, low-energy H- beam
LINAC: Accelerate the beam to 1 GeV
Accumulator Ring: Compress 1 msec long pulse to 700 nsec
Deliver beam to Target
Ion Source
2.5 MeV
1000 MeV
86.8 MeV
CCL
SRF, b=0.61
SRF, b=0.81
186 MeV
387 MeV
DTL
RFQ
P beam on target : 1.44MW
I beam average: 1.44mA
Maximum Beam energy: 1 GeV
Duty factor: 6%
Rep. rate: 60Hz
Pulse width: 1ms

## Slide 4
2.4845 ns (1/402.5 MHz)
260 micro-pulses
645 ns
300 ns
945 ns (1/1.059 MHz)
1ms
16.7ms (1/60 Hz)
15.7ms
Macro-pulse
structure (made by the Ion Source)
Mini-pulse
modulation (made by the chopper)
Micro-pulse
structure
(made by the RFQ)
SNS linac beam pulse temporal structure
~50mA
~40mA

## Slide 5
SNS ring and target beam temporal structure
700ns
16.7ms (1/60 Hz)
Beam pulse structure at neutron target
~33A
Current
1ms
Beam pulse structure in accumulator ring
~33GW
peak power
~23kJ per pulse

## Slide 6: Beam access opportunities
Ion Source
2.5 MeV
1000 MeV
86.8 MeV
CCL
SRF, b=0.61
SRF, b=0.81
186 MeV
387 MeV
DTL
RFQ
Very dense equipment placement
no access
Linac Dump
Momentum Dump
Extraction Dump
Injection Dump

## Slide 7: Beam modes
Neutron production
  4500 – 5000 hours per year
  Beam parameters and trajectory strictly controlled
    Small beam fraction can be diverted at several locations
Beam study
  <800 hours per year
  Beam parameters are variable
  Bam can be sent to different destinations

## Slide 8: Linac Dump beam line
7.5kW average beam power
Any temporal structure
  40mA, 1ms , .3Hz
  40mA, 5us, 60Hz
Passively cooled
Beam energy
  .2-1. GeV in beam study mode
  1 GeV in production mode
Can be used during production
  laser stripper to divert beam

## Slide 9: Nonintrusive 1-GeV H0/p+ beam extraction at the SNS linac dump
1-GeV/1.3-GeV H0 beam can be extracted to the linac dump using laser beam
Beam extraction can be conducted at 1 Hz to 60 Hz
Temperal structure of H0 beam is variable from a few micro bunches to the entire macropulse
Estimated extraction charge is 5 nC per macropulse with the current laser system and can be increased by an order of magnitude with more amplifiers or power recycling setup. (300W – 3kW)
Laser-based beam extraction scheme
Example of temporal structure
Developed laser system
Courtesy Yun Liu

## Slide 10: 1GeV, 2kW shielded beam absorber
~ 6’ x 6’ x 6’
Closed loop water cooling

## Slide 11: Momentum Dump
5kW average beam power
Any temporal structure
  40mA, 1ms , .2Hz
  40mA, 3us, 60Hz
Forced air cooled
Beam energy
  .2-1. GeV in beam study mode
  1 GeV in production mode
Can be used during production
  Foil stripper to divert beam

## Slide 12: Injection Beam Dump
150kW average beam power
Any temporal structure
  40mA, 1ms , 6 Hz
  40mA, 100us, 60Hz
water cooled
Beam energy
  .2-1. GeV in beam study mode
  1 GeV in production mode
Can be used during production
  ~1mA peak current

## Slide 13: Extraction Beam Dump
7.5kW average beam power
Short pulse temporal structure
  40mA-40A
Passively cooled
Beam energy
  .8-1. GeV in beam study mode
Can not be used during production

## Slide 14: Current BTF layout in RFTF Annex building (8320)
Particles | H- | H-,p
Energy | 2.5 MeV | 2.5MeV
Current | < 50 mA | <50mA
Pulse width | < 1 ms | <50us
Rep rate | < 60 Hz | <10Hz
Beam Power | < 7.5 kW | <65W
High Power
mode
Low Power
mode

## Slide 15: BTF beam line straight line layout
6-D scan
FODO
HDR
emittance
High power
beam stop
Moderator Test Stand (MTS)

## Slide 16: Feasibility of BTF upgrade for higher energy, more high-power test stations
Pros
  Significant infrastructure available: RF power, cooling water, cryogenics
Cons
  Radiation shielding will be required for whole facility

## Slide 17: Summary
High energy test proton beam can be available for experiments at several locations in SNS accelerator tunnel
  There is no existing infrastructure for test stations
Low energy test proton beam can be available for experiments at Beam Test Facility