## Slide 1: Accelerator Perspective for ADS (internal use only)
Presented at the
ADS Workshop 2021
ORNL
September 24, 2021
Sang-ho Kim
Accelerator Systems Section
Research Accelerator Division, NScD

## Slide 2: Outline
High power hadron machines
  State of the art is superconducting linear accelerator (SCL)
Beam power/beam energy for ADS
  Achievable with existing technologies
Beam trip frequency requirement for ADS
  Need more studies and assessment
What are the ‘REAL’ benefits of accelerator driven sub-critical reactors?
  May need separate assessment for strong case(s)
Summary

## Slide 3: High power hadron machines
Chart: Beam Energy (GeV)
| 0.8 | 0.8 | 24
Existing (SP) | 0.1 | 0.2 | 0.0050973
Existing (LP) | 0.5 | 1.25 | 2.2 | 0.25 | 100 | 120
Design (SP) | 1.44 | 0.0027 | 0.33 | 0.015049 | 0.0012816
Design (LP) | 1.6 | 100
 | 1000 | 0.001
 | 100 | 0.0001
 | 1000 | 0.01
Upgrade (SP) | 2.35 | 0.3 | 0.0058888
Upgrade (LP) | 3
Planned (SP) | 0.065 | 1.2 | 0.0168 | 0.4
Leg Existing (SP) | 500
Existing (LP) | 200
Fusion Material Irradiation
ADS
Neutron scattering
High energy physics

## Slide 4: Modern high power linacs
Most (all) of high-power machines under construction/design are based on Superconducting RF (SRF) technology
  Higher efficiency (grid power to beam)
  Smaller beam loss (large bore)
  Operational flexibility (large energy acceptance)
  Shorter linac length (high gradient)
Availability/reliability is machine (application) specific
  Most of machines aims at > 90 % availability
  ADS requirement is tougher (will discuss later)
Notes: One of kind…

## Slide 5: SNS Superconducting Linac (SCL)
FE
DTL
CCL
SRF, b=0.61
SRF, b=0.81
1000 MeV
upgrade
Accumulator Ring
Liquid Hg Target
259 m
157 m (SCL)
71 m
Empty slots
for upgrade
Cryomodules
in the tunnel
SNS SCL is the world first mega-watt class hadron linear accelerator using SRF technology
  Successful deployment of SRF technology and highly reliable operation of SNS SCL encouraged other high power accelerator projects around world to adopt SRF technology
1300 MeV
SNS SCL system (including all supporting systems) is routinely running at 98 % availability
186 MeV

## Slide 6: SRF accelerating structures
SRF applications are expanding to lower beam velocities ( =v/c)
=0
=1
0.05
0.1
0.25
0.5
0.8
SNS SCL range

## Slide 7: High-power hadron SCLs under development
PIP-II: CW capable, H-, 0.8 GeV, 2 mA chopped, > 1 MW capable
ESS: pulsed (4% beam duty), proton, 14 Hz, 2 GeV, 62.5 mA peak, 2.5 mA average, 5 MW
FRIB: CW, p to U, >200 MeV/u, 0.7 emA (U-238), 0.4 MW

## Slide 8: High power CW proton accelerator for ADS
Beam power (at 1 – 2 GeV), , Pth: reactor thermal power
Cyclotron
  A few MW is limit: multiple cyclotrons for high beam power
  Beam energy is limited to 500 ~ 600 MeV
Linac
  Accelerator design for ADS in 1990s: based on normal conducting structures
  Recent advances in superconducting RF cavities
    SCL is the generally accepted technology of choice for ADS accelerator
  Some variations under study, e.g. recirculation concept (new LDRD)

## Slide 9: Comparisons of NC based linac with SCL
 | ATW-1 | ATW-2 | SNS old design | SNS | PIP-II
Structure type | All normal conducting | All normal conducting | All normal conducting | NC + SC | All SC except RFQ
Beam energy | 1.6 GeV | 0.8 GeV | 1.0 GeV | 1.0 GeV 1.3 GeV | 0.8 GeV
Beam mode | CW | CW | pulse | pulse | Pulse to CW
Linac length | 1900 m | 1000 m | 465 m | 260 m 330 m | 215 m
Notes: Just to give an idea….

## Slide 10: ADS roadmap
Test/prototype/demo.
  Dedicated demo machine (e.g. MYRRAH) will provide a real proof
  Some test can be done utilizing existing machines (e.g. JPARC TEF)
Industrial scale
  CW proton beam: 10 to 30 MW (e.g. JAEA, EFIT, C-ADS)
Demonstration/
Experiment
-Tech./comp. test/development
-Fuel studies
-System Avail. >50%
Industrial scale transmutation
-Transmutation of minor Actinide, Am
-Use process heat
-System Avail. >70%
Industrial scale power generation w/ energy storage
-Deliver power to the grid
-System Avail. >80%
Industrial scale power generation w/o energy storage
-System Avail. >85%
1 – 2 MW beam
0.5 – 3 GeV
10 – 75 MW beam
1 – 2 GeV (CW)
10 – 75 MW beam
1 – 2 GeV (CW)
10 – 75 MW beam
1 – 2 GeV (CW)
Summary from White paper ‘Accelerator and Target Technology for Accelerator Driven Transmutation and Energy Production’ (2010)
Notes: TEF: Transmutation Experimental Facility
EFIT: European Facility for Industrial Transmutation of Minor Actinides
MYRRAH:

## Slide 11: General remark on beam energy and beam power for CW operation
All critical aspects of physics and technologies for accelerator have been demonstrated but not collectively
  No showstopper regarding beam energy and beam power
Next slides will discuss about beam trip requirements

## Slide 12: Beam trip frequency requirement
Data from MYRRAH, JAEA (both LBE Target/coolant)
Mechanical integrity: thermo-mechanical, fatigue, interaction with LBE
System availability
MYRRAH reactor
JAEA reactor

## Slide 13: Beam trip frequency requirement – MYRRHA
Mechanical integrity issues on window, fuel cladding, reactor structure, etc.
Long beam interruption causing reactor shutdowns: restart will take 20~40 hours
Beam trip > 3 sec: 10 times during 3-month of operating cycle ~ about 0.1 trips/day
T. Junquera, Accelerator Reliability requirements for ADS: the MYRRHA project goals, presented at 4th international workshop on ADSR systems and Thorium, 8/31 – 9/2, 2016
  cf. FY20 SNS 95% availability:
    No. of trips > 3 s: 14.3 trips/day
    (SNS data from Charles Peters)

## Slide 14: Beam trip frequency requirement - JAEA
t < 10 s: 20,000/yr (beam window)
10 s < t < 5 min: 2,000/yr (Inner barrel)
T > 5 min: 42/yr (system availability)
  0.14 times/day
    Plant restart (20 hours / trip)
    70% yearly system availability or 85% during run
H. Takei, et. al, Estimation of acceptable beam-trip frequencies of accelerators for accelerator-driven systems and comparison with existing performance data, J. Nucl. Sci. Tech., Vol 49, No. 4, April (2012), pp. 384 – 397
No. of trips per day
JAEA requirement
SNS FY20
(Charles Peters)

## Slide 15: Remark on beam trip requirement
It is THE major challenge!
Need balanced and goal-oriented machine philosophy. General approach should include
  Simple design (less parts/equipment, more passive)
  Over design/LARGE margin
  Highly modular design
  Redundant design (serial and/or parallel)
  Or Innovative breakthroughs
SNS provides one of best opportunities for this study/analysis (New LDRD program started this year)
  ADS community has been analyzing SNS statistics with positive feedbacks
Other important challenge for industrial ADS
  Number of staff
Notes: One of kind… R&D nature….

## Slide 16: Molten salt reactor for Minor Actinide (and W-Pu) transmutation
ORNL has a long history and unique experience with molten salt reactor
Molten salt reactor may relax beam trip requirement
  ???
Transmutation: More interest than energy production in US
  Electricity production can be the next goal, which requires more reliable and highly available system

## Slide 17: What are the ‘REAL’ benefits of accelerator driven sub-critical reactors?
ADS is mainly driven by accelerator community so far….
Turning-off accelerator will immediately shut reactor down, which is true, but argument seems weak
  safety?: maybe good for public acceptance
Notes: Three mile island (human-computer interaction, human error, etc), Chernobyl (design obsolete), Fukushima Daiichi (due to decay heat)….
May not be technical solution for the previous incidents.

## Slide 18: Are we on the same page?
Perspectives can be different

## Slide 19: Minor Actinide burning rate?
If so, would be strong case for ADS
From H. Abderrahim presentation at 4th international workshop on ADS & Thorium
*EFIT: European Facility for Industrial Transmutation of Minor Actinides

## Slide 20: Is accelerator really needed for breeder reactor?
Time (hours)
For self-contained breeder reactors (nf=nb=1), operation of breeder reactor with just control rod is difficult
R. Barlow presentation at 4th international workshop on ADS & Thorium

## Slide 21: Summary
High power hadron machines
  Technology of choice is superconducting linear accelerator (SCL)
Beam power/beam energy for ADS
  Achievable with existing technologies
Beam trip frequency requirement for ADS
  Accelerator: Need studies for Large-scale INDUSTRIAL accelerator
  Reactor: Need assessment for molten-salt reactor
Benefits of accelerator driven sub-critical reactors
  Need separate assessment for strong case(s)