## Slide 1: ML Data Infrastructure
S. Zhukov
W. Blokland
https://www.pnnl.gov/

## Slide 2: Data Infrastructure Challenges
Data volume
Data format mismatch LabVIEW/C++ vs Python
Data transfer
  Internal firewall and external collaborators – two firewalls to cross with terabytes of data
  Network speed: ICS network was never meant to transfer lots of data, obsolete.
All ML project activity should not affect neutron production – all data producing IOCs should run normally
BPM | DCM | HVCM | Target
3.8 Tb | 2.5 Tb | 0.12 Tb | 0.11 Tb

## Slide 3: Data Format
Need to write in LabVIEW and C
Need to read in python
Must be binary
Must have random access (not sequential)
Records should support arbitrary number of fields
File creation should not affect IOC’s resources
Requirements
HDF5 – scientific “standard” for large files
NPYX – numpy internal
TDMS - LabVIEW internal
Custom
Possible candidates

## Slide 4: Data Transfer
ORNL enterprise network
SNS ICS network
Oracle DB
ThinLinc
Errant Beam Server
BIGMAC file storage
EB storage
Globus
Thinlinc client
Receiving script
Sending script
GitLab version control
Git client
Internet
ORNL user
External User
Instruments
1G/100Mbit
100Mbit
X Mbit
Feels real fast
1G
1G

## Slide 5: Data Transfer
DCM
BPM
BPM
BPM
BPM
BPM
BPM
BPM
BPM
BPM
BIGMAC file storage
Errant Beam file storage
Firewall
Automated transfer across firewall
Linear accelerator
Oracle DB
Event
Timestamp
BPM1
BPM2
DCM
Python library for browsing events (development frozen)
Python library for reading data files
Processing files and
exporting to Oracle
and tagging (development frozen)
Before
After

## Slide 6: Expected workflow vs reality
All code is shared over GitLab
  Worked but more as a transfer mechanism, not collaboration tool
Code is runnable on Errant Beam server
  Initially worked to familiarize themselves with the data and test libraries but not widely used recently. ThinLinc is not responsive enough to work comfortably
Sophisticated data selection uses Oracle and runs on EB server
  Failed. Some test implementations exist but specs are too vague and takes a lot of effort to implement with unclear benefits.
Trained models are shared over GitLab
  Worked
Data transfer is transparent and efficient
  Transfer process is still clunky and mostly used by Beam Based… HVCM?

## Slide 7: Running inference live for DCM
Training on DCM Data
Compiling TF model
Generating C++ code to run inference
LabVIEW IOC runs inference on RT data
Siamese Twins
Deploy model and code to IOC
Training on DCM Data
Compiling RF model to VHDL
Generating LV FPGA bitfile
Random Forest
Deploy bitfile to IOC
Every is now a well documented process hopefully!

## Slide 8: Streaming ALL DCM data and running analysis inference on a separate server
LabVIEW DCM IOC
Standalone Linux Server Lots of RAM to store several hours of WFs @60Hz
BIGMAC file storage
1Gbit
1Gbit/100Mbit
Possible use cases
Store all WF for a long continuous period of time for later analysis
Running several inference in parallel
Running “auto-correlation”: applying Siamese model using time shifted WF as a reference

## Slide 9: Discussion
How to better integrate with JLAB?
Who can use the data streaming server?
Do we still want to use oracle database for data selection?
  Pros, cons