## Slide 1: Overview of Methods
Method | Advantage | Drawback | SNS Use Case | Comments
Non-NN ML | More interpretability | Poor performance on large dataset | BB/Target | 
Gaussian Process | Easy implementation | Non-scalable | BB/Target | 
Multi-layer Perceptrons | Simple input-output mapping | Structural redundancy | BB/Target | 
Convolutional Neural Networks | Automatic feature extraction | Data hungry | BB/HVCM | 
Recurrent Neural Networks | Ability to model time-series | Vanishing/exploding gradient | BB/HVCM/ CMS | 
AutoEncoders | Data representation in reduced dimension | Destroys interpretability of data | BB/HVCM | 
Siamese Networks | Can work with imbalanced data | Sensitive to input variations | BB | 
Generative Adversarial Networks | Useful when more data needed | Unstable training | HVCM | 
Customized Neural Networks | Customizable | Specific models | HVCM | 
Physics-informed Neural Networks | Reduced data need | Some physics needed | CMS | 
Reinforcement Learning | Dynamic control adaptation | Expensive training | All | 

## Slide 2: Multi-layer Perceptron

## Slide 3: Multi-layer Perceptrons (MLPs)
Single neuron: linear regression
Activation function: introduce nonlinearity
Fully connected multi-layered neural networks
Sigmoid
Rectified Linear Unit (ReLU)
How it works:

## Slide 4: Multi-layer Perceptrons (MLPs)
Advantages:
Simple input-output mapping
Customizable with a wide range of non-linear activation functions to model complex relations
Drawbacks:
Pure black-box model
Redundancy due to fully-connected framework
Architecture selection (Neural Architecture Search)
Application Fields:
Data visualization
Data compression
Encryption
Image/text/speech recognition
Machine translation
Jack of all trades, master of none!
SNS Use Cases:
Anomaly detection using BPM phase data
Upstream BPM
Downstream BPM
…
…
…
…
…
MLPs were a popular machine learning solution in the 1980s

## Slide 5: Recurrent Neural Networks

## Slide 6: Recurrent Neural Networks (RNNs)
Model sequences (time-series) through repeated cells
How it works:
Cell
Cell
…
Cell
Cell
Structure:
Unrolled RNN:
Popular cell designs:
Math behind:
transition

## Slide 7: Recurrent Neural Networks (RNNs)
Advantages :
Ability to learn from long sequences
Mitigate vanishing-gradient problem in deep networks
Drawbacks :
Suffers from short sequences
Require state value at each timestamp for efficient training
Application Fields:
Failure prognostics
Market (financial) predictions
Text/speech recognition
Semantic parsing
SNS Use Cases:
Equipment prognosis using beam-based signals
HVCM failure prediction
LSTMs include “Forget Gates” that decides whether a previous state should be used

## Slide 8: Customized Neural Network Architectures

## Slide 9: Convolutional LSTM (ConvLSTM)
Convolution operation applied to inputs and states @ each timestamp
Tailored to discover spatiotemporal pattern in data
ConvLSTM: matrix multiplication of inputs and states replaced by convolution operation
CNN-LSTM: two layers stacked
Application Fields:
Predict next-frame in a video
Precipitation nowcasting
Classical LSTM architecture
SNS Use Cases:
ConvLSTM-AutoEncoders for High Voltage Converter Modulators (HVCM) anomaly detection

## Slide 10: ConvLSTM AutoEncoders
Conv
LSTM
Conv
LSTM
Conv
LSTM
ConvLSTM
ConvLSTM
ConvLSTM
MaxPool
MaxPool
UpSample
UpSample
Seq2Seq model
Machine translation
Text summarization
Bi-directional LSTM
Process sequences in both directions
Speech recognition
Semantic parsing
SNS Use Cases:
HVCM/Beam-based anomaly detection
SNS Use Cases:
Prediction with time-series data
  HVCM
  Beam-based

## Slide 11: Physics-informed Neural Networks

## Slide 12: Physics-informed Neural Networks (PINNs)
Underlying physics guides data-driven nodes
Reduce need for data greatly
Collocation methods:
  PDEs to constrain NN solution
Hybrid methods
  Graph models where physics and data-driven kernels coexist
F. A. C. Viana, R. G. Nascimento, A. Dourado, and Y. A. Yucesan (2021), "Estimating model inadequacy in ordinary differential equations with physics-informed neural networks," Computers and Structures, Vol. 245, pp. 106458, 2021. (DOI: 10.1016/j.compstruc.2020.106458).
Raissi, M. (2018). Deep hidden physics models: Deep learning of nonlinear partial differential equations. The Journal of Machine Learning Research, 19(1), 932-955.
SNS Use Cases:
Multi-fidelity modeling for CMS

## Slide 13: Collocation Methods
https://developer.nvidia.com/modulus
Raissi, M., Perdikaris, P., & Karniadakis, G. E. (2019). Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations. Journal of Computational physics, 378, 686-707.

## Slide 14: Hybrid Physics-informed Neural Networks (PINNs)
Euler Cell
Physics-based Cell
Hybrid Cell
Actual Output
Available Data
Predictions
Physics kernels
Data-driven kernels

## Slide 15: Hybrid Physics-informed Neural Networks (PINNs)
Application Fields:
Wind Turbine Main Bearing Fatigue
(Prognosis)
Model:
Results:
Lithium-ion Battery Aging Model
(Prognosis)
Model:
Challenge
Unbalanced data
Calibrated with visual inspections
Small subset of farm sampled
Data
Load history of 30 years of 100 turbines
Visual grease inspections once a month for 6 months
Results:
Y. A. Yucesan and F. A. C. Viana, "Hybrid physics-informed neural networks for main bearing fatigue prognosis with visual grease inspection," Computers in Industry, Vol. 125, pp. 103386, 2021. (DOI: 10.1016/j.compind.2020.103386).
R. G. Nascimento, M. Corbetta, C. S. Kulkarni, and F. A. C. Viana, "Hybrid physics-informed neural networks for lithium-ion battery modeling and prognosis," Journal of Power Sources, Vol. 513, pp. 230526, 2021. (DOI: 10.1016/j.jpowsour.2021.230526).
Challenge
Prognosis models depend on several empirically adjusted factors

## Slide 16: Hybrid Physics-informed Neural Networks (PINNs)
Application Fields:
Torsional vibration damper
(System ID)
Model:
Results:
Model-form uncertainty in corrosion fatigue (Prognosis)
Model:
Challenge
Assumed: pure mechanical fatigue
Reality: Corrosion-fatigue
Data
Load history of 5 years of 150 aircraft
Crack length of 15 aircraft @ 5th year.
Results:
Y. A. Yucesan, F. A. C. Viana, L. Manin, and J. Mahfoud, "Adjusting a torsional vibration damper model with physics-informed neural networks," Mechanical Systems and Signal Processing, Vol. 154, pp.107552, 2021. (DOI: 10.1016/j. ymssp.2020.107552).
A. Dourado and F. A. C. Viana, “Physics-informed neural networks for missing physics estimation in
cumulative damage models: a case study in corrosion fatigue,” ASME Journal of Computing and Information Science in Engineering, Vol. 20 (6), 10 pages, 2020.