## Slide 1: Exploring Initial Distributions at the Beam Test Facility
Kiersten Ruisard
5th ICFA mini-workshop on Space Charge Oct 25, 2022

## Slide 2: Background and Motivation
Broad goals:
predictive modeling for beam distribution with halo
better understanding of beam losses
Beam Test Facility (BTF)

## Slide 3: After RFQ, beam core is hollowed
y
x
This is dependent on charge:
Full projection:
Slices in y:

## Slide 4: In simulation of MEBT, we predict that neglecting correlations will affect rms sizes and beam shoulders/tails
PyORBIT simulation of SNS linac (MEBT+DTL) with/without interplane correlation:
Initial simulation bunch from Parmteq simulation:
Fully correlated,
Not fully correlated
Full projections:
Phase distribution for y=0,x’=0,y’=0 and x=xi

## Slide 5: For BTF experiment, we expect effect at 3 orders of magnitude below core density
Initial bunch
from PARMTEQ,
8M particles
output
Contours at 10%, 1%, .1%, .01% of peak
Fully correlated,
Not fully correlated
xrms, yrms [cm]
Density [au]
x’ [mrad]
Notes: This was highlighted in 2019 SC workshop talk; I didn’t imagine we’d be in this boat today.
2 reasons: Focus on high-dim over lattice benchmarking due to impending configuration (some questions about dipoles raised….so get rid of dipoles?)

## Slide 6: Right now, lattice errors far exceed sensitivity needed to examine effect of 6D
Fully correlated,
Not fully correlated

## Slide 7: High chromaticity in BTF causes sensitivity to RFQ output energy
Per FODO cell,
For 50 keV RMS width and 9.5 cell FODO,
Full projection phase spaces:
Phase space for different energy slices:
* measurements
Notes: * We will be sensitive to 10’s of keV offset in output energy from RFQ

## Slide 8: Current benchmark status: there is no RMS agreement
viewscreens (collimated beam)
2D phase spaces
Slits (full beam)
X rms, Y rms
RMS size [mm]
Notes: Why is this so hard?
High phase advance (103 deg/cell)
Initially low diagnostics per cell.

## Slide 9: Soft-edged field profiles matters for permanent magnets in FODO section
9”
Halbach permanent magnet quad
We still (mostly) trust hard-edged model for electro-magnet quads! Are we wrong?
Implemented,
Not implemented
Contours:
60%,
10%,
1%,
.1% of peak

## Slide 10: Py-orbit multi-bunch solver is required to get space charge right,
T=2.48 ns
Implemented,
Not implemented
Beam rms width at FODO entrance >
RFQ
FODO

## Slide 11: Residual vertical dispersion explains asymmetry in vertical phase space
orbit=0
orbit≠0
Orbit error,
No error
vertical dispersion [m]

## Slide 12: Summary #1
Motivation: predicting halo extent
Initial bunch: core-hollowed due to nonlinear space charge
Status: Lattice model errors exceed distribution errors
Ranked importance:
  Field profile for PM quads
  Overlapping bunches
  Dipole model?
  Residual dispersion
  Energy, via chromaticity
  Field profile for electromagnet quads
  6D initial distribution

## Slide 13
Summary:
This talk presented a study of the initial distribution and transport of (up to) 50 mA, 402.5 MHz H- bunches at the SNS Beam Test Facility. The purpose of this work is to demonstrate prediction of beam halo + halo losses
From your perspective, where is the gap regarding space charge effects?
The gap is in our ability to predict beam evolution with space charge with desired accuracy
What is needed to bridge this gap?
Careful validation of models, including initial beam distribution
  Sufficient diagnostics
  efficient methods for calibration and error identification
Responsive simulation development (e.g., multi-bunch solver)
Other effects for linacs: Cavity models, longitudinal dynamics
Summary slide, 5th ICFA mini-workshop on Space Charge
Theme: Bridging the gap in space charge dynamics
Notes: Other things: cavity modeling;

## Slide 14: Backup

## Slide 15: Project Status
Shutdown August 2022
New RFQ commissioning
  ~Nov 2022
Straight BTF in 2023
Species | H-
Energy (MEBT) | 2.5 MeV
Energy (LEBT) | 65 keV
RFQ | 449 cells 402.5 MHz
Beam current | Up to 50 mA

## Slide 16: Energy error (chromatic effect)
Orange is 2.5 MeV-20 keV
Blue is 2.5 MeV

## Slide 17: 5D method
dipole
beam
viewscreen
Notes: We always get asked about repeatability, stability;

## Slide 18: 6D apparatus
dipole
beam
RF
grid 9x 9 x 9 x 9 x 9 x 512, ~24 hours

## Slide 19: Beam current during 7.6-hour scan
average BCM current = -26.73 +- 0.06 mA
Notes: Gap is a software bug, not a machine fault

## Slide 20
Comparison of 2 datasets taken 2 weeks apart
5D scan (integrated along other 3 dimensions)
7.6 hours
2D scan
~15 minutes
X [mm]
X’ [mrad]

## Slide 21: BTF follows footsteps of earlier attempts to benchmark medium-energy beam evolution
Qiang, J., Colestock, P. L., Gilpatrick, D., Smith, H. V., Wangler, T. P., & Schulze, M. E. (2002). Macroparticle simulation studies of a proton beam halo experiment. Phys Rev ST-AB, 5(12), 35–47 .
mismatched
matched
Simulations of high-intensity ion front-ends benchmarked to RMS agreement but cannot reproduce tails/halo.
Hypothesis: Limited knowledge of initial distribution to blame for discrepancies
LEDA @ LANL: extensive simulations aimed at benchmarking halo evolution measurements
Notes: IMPACT simulations; distributions simulated starting at plasma boundary of source

## Slide 22: Typical input distribution based on 2D projections
MeV
Assumption:

## Slide 23: After RFQ, core is hollowed
y
x

## Slide 24: Right now, lattice errors far exceed sensitivity needed to examine effect of 6D
Correlated,
De-correlated
Initial bunch
from PARMTEQ,
8M particles
output
Notes: This was highlighted in 2019 SC workshop talk; I didn’t imagine we’d be in this boat today.
2 reasons: Focus on high-dim over lattice benchmarking due to impending configuration (some questions about dipoles raised….so get rid of dipoles?)

## Slide 25: High-dimensional benchmark at end of beamline
Simulation
Measurement
Notes: * Simulation includes dispersion, Orbit offset at HZ04:
Y0 = 6.17 mm
Y0’ = -2.2 mrad

## Slide 26: 2D projected phase space viewed at energy slices
Measurement
Simulation

## Slide 27: 2D projected phase space viewed at energy slices
Measurement
Simulation

## Slide 28
collimate
Notes: Why is this so hard?
High phase advance (103 deg/cell)
Initially low diagnostics per cell.

## Slide 29: Chromaticity in FODO line
Per FODO cell, C = -0.00007 / keV
For 50 keV RMS width and 9.5 cell FODO,
8 mm ~ ?? keV

## Slide 30: RFQ Benchmark, full-projection
Measured
Simulated

## Slide 31: RFQ Benchmark, slices
measured
simulated
y, mm
x, mm
Notes: * Scaes are the same