## Slide 1: Nuclear Batteries: Possible Applications for SNS-produced Radioisotopes
OFFICIAL USE ONLY
May be exempt from public release under the Freedom of Information Act (5 U.S.C. 552), exemption number and category: 5, Privileged Information
Department of Energy Review required before public release
Name/Org: B. R. Johnson. Date: April 18, 2022
Guidance (if applicable): ORNL Isotope Science & Engineering Office
Brad Johnson, PhD
Isotope Science and Engineering Directorate
Program Manager, Nuclear Batteries
Oak Ridge National Laboratory
865-574-1333
johnsonbr1@ornl.gov
Chris Duke,
National Security Sciences Directorate
National Security Program Manager
Oak Ridge National Laboratory Commercial/STE: 865-241-3310 Secure: 361-8500 dukecm@ornl.gov

## Slide 2: Nuclear Battery (NB) Overview
NB
Baseline
NBs = constant current power supplies.
NB advantages:
  Long-lived (months – decades)
  Rugged, durable
  Silent
  Temperature insensitive
Challenges:
  Traditional NB SWAP ≠ current mission needs
  Supply chain
  Economics
D-Cell sized
Nuclear
Battery

## Slide 3: Nuclear Battery Concepts:
Radioisotope
Electricity
Output
Input
Transducer
Energy Source:
Radioisotope decay energy
• Pu-238: alpha particle
• Sr-90: high energy beta
• Am-241: alpha
• Ni-63: low energy beta
Transducers:
RTG: Thermoelectric (PbTe, SiGe, etc.), Stirling engine
BV: Semiconductor (SiC, GaN, Si, etc.)
BPV: Scintillator + photovoltaic

## Slide 4: Types of Nuclear Batteries:
Adams_2015_Rsrch-Dev-and-Eval-Cap-for-Betavoltaic-Pwr-Sources_ ASEE#13983
Radio-isotope
Scintillator
PV
RTGs
BVs
BPVs
Radioisotope Thermoelectric
Generators
Betavoltaics
Beta-Photovoltaics
NASA RTG heat source
Pu-238
Thermoelectric Transducer
Beta particle source
Semiconductor
Transducer

## Slide 5: Different ways to convert radioactivity into electricity
NB Type | Energy Source | Transducer | Power Level | Application | Usage
RTG | a, b → Thermal DT | TE semiconductors | 1-100’s W | Mini-satellites Maritime Sensing UAV Deep earth | High
BV | b → e-h pairs | Voltaic semiconductors | 1-1000µW | Remote wireless sensors Medical | Low
BPV | b → photons | Luminescent + PV | 0.1-10mW | Hybrid NB-CB systems Remote wireless sensors | Low
Isotope
Scintillator
Scintillator
PV
PV
Adams_2015_Rsrch-Dev-and-Eval-Cap-for-Betavoltaic-Pwr-Sources ASEE#13983

## Slide 6: Nuclear Battery Power Ranges
Betavoltaic (BV)
RTG-hybrid concept
BV-hybrid concept
µW
mW
W
kW
MW
100µW
Power Mgmt Unit
10mW peak
NASA GPHS
292W
BUP-500: 650W
NASA MMRTG
110W
Betacel®
400µW
Fission 10kW
LANL - ”KRUSTY”
Power Mgmt Unit
RTG
1.5kW peak

## Slide 7: Example BV Nuclear Battery:
Radioisotope
Electricity
Output
Input
Transducer
Ni-63
Textured SiC
Ni-63: Pure beta emitter
~ 17 keV/decay
~ 100y half-life

## Slide 8: Example RTG Nuclear Battery:
Radioisotope
Electricity
Output
Input
Transducer
Pu-238
NASA high temp thermoelectric
NASA heat source
Pu-238: alpha emitter
~ 5.5 MeV/decay
~ 88y half-life

## Slide 9: ORNL: Heritage Nuclear Battery Expertise
Prime supplier of RTGs from the 1950’s – 1970’s
SNAP-7B, Light Buoy, Baltimore, MD
Name | Watts, Electric | Date | Buyer | Use | Place
Sentry (Weather Bureau) | 5 | 1961 | Weather Bureau | Weather Station | Axel-Heiberg Island
SNAP7A | 10 | 1962 | US Coast Guard | Buoy Light | Curtis Bay, MD
SNAP7B | 60 | 1964 | US Coast Guard | Lighthouse | Baltimore, MD
SNAP 7C | 10 | 1962 | US Navy | Weather Station | Antarctic Mainland
SNAP7D | 60 | 1964 | US Navy | Barge weather station | Gulf of Mexico
SNAP 7E | 7.5 | 1964 | US Navy | Sonic beacon | Undersea near FL
SNAP 7F | 60 | 1965 | Philips Petroleum | Buoy warning and control station | Gulf of Mexico
URlPS (P1-1002) | 1 | 1966 | US Navy | Deep sea | Port Hueneme, CA
URIPS (PI-1001A) | 1 | 1967 | US Navy | Deep sea | Port Hueneme, CA
NUMEC (2) | 7 | 1966 | Israel | Undersea or surface | 
U1-1001 | 1 | 1967 | AGN-BMI-Bendix | Geodetic benchmark | Pacific Ocean near Anacupa, Is
NUMEC 100MA (2) milli TRACS | 0.1 | 1967 | US Navy | Deep sea | Port Hueneme, CA
NUMEC TRACS-25A | 20 | 1968 | US Navy | Tidal wave warning system | Bahamas
RlPPLE III | 0.7 | 1967 | US Navy (Loan) | Undersea test | Port Hueneme, CA
RlPPLE IV | 2 | 1967 | US Navy | Submarine cable repeater | 
RlPPLE IX | 4 | 1967 |  | Aircraft ground beacon | 
MW-3000A | 2.5 | 1967 | US Navy | Deep sea | 
SNAP-21 (5) | 10 | 1969 | US Navy | Undersee | Offshore San Clemente Is, CA
LCG 25A | 25 | 1966 | US Navy | Oceanographic Instruments | Fairway Rock, AK
LCG 25B | 25 | 1967 | US Navy |  | Port Hueneme, CA
SNAP 23A | 60 | 1969 | US Navy | Terrestrial | 
Sentinel 25E (11, 12, 13) | 25 | MAR 1969 | US Navy | Oceanographic data stations | 
Sentinel 25D (8, 9, 10) | 25 | JUN 1969 | US Navy | Terrestrial and to 1000 ft undersea buoys | 
LCG 25C1 | 25 | 1968 | NASA | Interrogation, recording, and location system | Puerto Rico coast sub-surface buoy
P1-1003 P1-1004 P1-1005 P1-1006 | 1.2 | 1970 | US Navy | Deep ocean | Port Hueneme, CA
33 RTGs
24 USN
Fuel: Sr-90 from Hanford

## Slide 10: ORNL: Current Key Contributor to NASA RTGs
MMRTG used on Mars Perseverance Rover
Fuel: Pu-238 from SRS + ORNL

## Slide 11: NASA General Purpose Heat Source RTGs: Modular Design
General Purpose Heat Source Module

## Slide 12: ORNL: Integrated Nuclear Battery Technology Provider
Isotope production
Materials processing
Packaging and encapsulation
Energy conversion
Device design & fab

## Slide 13: Nuclear Battery Challenges:
Electricity
Output
Input
Transducer
2. Energy conversion: Advanced, high efficiency technologies
Fuel: Need efficient, large scale radioisotope production
Thermoelectric Unicouple:
5% 20% (?)
3. Power Control: Low-loss, hybrid power management

## Slide 14: Solving nuclear battery challenges:
Efficient fuel production
  Isotopes with long decay chains
Efficient energy conversion:
  Improved transducers
227Ac 227Th 223Ra 219Rn 215Po 211Pb 211Bi 207Tl 207Pb
(32.9 MeV/decay)
238Pu 234U : (5.5 MeV/decay)
Power Management Unit
RTG
• Efficient use of radioisotopes:
  - Hybrid Power Supplies

## Slide 15: Nuclear Battery Energy Economics:
Isotopes of Interest | Type of NB | Example Size NB | #g @ BOL for 20y NB* | #Ci @ BOL for 20y NB*
Pu-238 | RTG | 10W | 420.7 | 7,202
Am-241 | RTG | 10W | 1854.4 | 6,357
Sr-90 | RTG | 10W | 350.3 | 48,340
Ac-227 | RTG | 10W | 26.8 | 1,941
Pm147 | BV/BPV | 10mW | .98 | 910
Eu-155 | BV | 3mW | .74 | 360
Ni63 | BV | 1mW | 5.8 | 330
H-3 | BV | 100µW | 0.01 | 100
*BOL = Beginning of life; Assuming 5% Efficient RTG; 3% Efficient BV
Sr-90 Example:
1.13 E 6 eV/decay
1 Ci = 3.7 E 10 decays/sec
1 J = 6.24 E18 eV
1 W = 1J/s
∴149 Ci Sr90 for1 Wth energy
For 5% efficient RTG:
2,987 Ci Sr90/We
Key Facts:
NBs need an abundant supply of radioisotope fuel
Radioisotopes are difficult to make and expensive
NBs must use radioisotope fuel efficiently
Modest improvements in energy conversion have significant impact on size, weight & cost

## Slide 16: Nuclear Battery Isotope Wish List:
Isotope | Half-Life (y) | Specific Activity (Ci/g) | Mean Energy @ Secular Equilibrium (KeV) | Specific Power @ Secular Equilibrium (W/g) | mW/Ci | W/g compared to Pu-238 | Grams for 10W thermal | Ci for 10W thermal
Pu-238 | 87.70 | 17.12 | 5,487 | 0.557 | 32.53 | 1.00 | 17.96 | 307.43
Sr-90 | 28.79 | 138.0 | 1,129.6 | 0.924 | 6.70 | 1.66 | 10.82 | 1,493.33
H-3 | 12.30 | 9,618.9 | 5.7 | 0.324 | 0.034 | 0.58 | 30.87 | 296,899.15
Pb-210 | 22.20 | 76.3 | 6,472.7 | 2.928 | 38.37 | 5.26 | 3.42 | 260.62
Si-32* | 153.00 | 73.05 | 764 | 0.331 | 4.53 | 0.59 | 30.22 | 2,207.97
Ac-227 | 21.77 | 72.3 | 3.3E+04 | 14.085 | 194.78 | 25.29 | 0.71 | 51.34
U-232 | 68.9 | 22.36 | 4.1E+04 | 5.422 | 242.47 | 9.74 | 1.84 | 41.24
Cm-244 | 18.11 | 78.97 | 5,796.4 | 2.714 | 34.36 | 4.87 | 3.69 | 291.02
32Si -> 32P -> 32S; betas < 1MeV; min shielding; excellent T1/2 ; more vol efficient than 3H; not SNM
3H: Low energy beta; No shielding
210Pb -> 210Bi -> 210Po: Mass efficient heat source; good T1/2 ; high energy beta req’s shielding
227Ac & 232U: Excellent W/g, but high energy g’s
244Cm: Neutron emitter

## Slide 17
Efficient Fuel Production: Power Output of Various Isotopes

## Slide 18: Efficient Production: Co-Produced Radioisotopes
12 Full Length Rods, (1,923 Pellets), 3 Cycles = 100Ci Ac-227
10We, 5% h, 20-yr RTG needs 1,941 Ci Ac-227 ~ 20 HFIR cycles ~ 3+ yr
* Calculations by Justin Griswold & Victor Bautista, ORNL
NOTE: Th-229 is the parent isotope for Ac-225, a very valuable medical isotope for cancer therapy

## Slide 19: Nuclear Battery Significance & Opportunity:
National needs for advanced NBs
Adv. technology is able to create NB breakthroughs
The infrastructure, talent & team exists to develop & commercialize adv. NB technology
ORNL has already committed internal R&D $$ on advanced NB technology