## Slide 1
Secondary Neutron Production Evidence in TREND Experiments
Catherine Apgar
Department of Nuclear Engineering
University of California, Berkeley

## Slide 2: Overview
A Tri-lab collaboration has been formed between LBNL, LANL, and BNL to measure (p,x) reactions relevant to isotope production from threshold to 200 MeV for primary isotopes of interest and their impurities.
LBNL 88-Inch Cyclotron Ep,max = 60 MeV
BNL BLIP Ep,max = 200 MeV
LANL IPF Ep,max = 100 MeV
2

## Slide 3: Isotope Production Motivation for Sb(p,x) Experiments
3
Cross section measurements of 117mSn and 119mTe (a cow for 119Sb) to optimize production for high SA with minimal impurities
Primary Isotopes:
119m,119gTe, 117mSn
Potential Impurities:
116,117,118,121m,121g,123mTe, 113,119m,121m,121gSn
These Auger emitters a promising candidate for OA via RSV and potentially small mass tumors.
Notes: 117mSn colloid has shown promising results in preclinical trials for the treatment of arthritis.
  Undergoes electron conversion, very low energy gamma given the large difference in the spin/parity between the isomer and the ground state
  14 day half life simplifies its distribution logistics
  Decays to stable Sn-117
  Tends to migrate to the bones, and specifically where there is more disease in the bone.
  It is currently being used for the treatment of joint pain in canines and is in clinical trials in humans
119mTe is also being investigated as an isotope generator for 119Sb, an auger emitter for targeted radiotherapy of small tumors.
  119mTe has a half life of 4.7d, compared to the 16hr half life of its ground state (again, another 11/2-1/2+ ground state
117mSn – similar gamma emission (158keV vs 140keV) to 99mTe for imaging
Properties of Sn – tend to goes where the disease is in bone, less disease, less tin, more tin
Short range relative to beta emitters,
Low energy conversion electron emission

## Slide 4
4
Irradiation via traditional natSb foils placed with monitor foils and degradiers to determine current using IAEA charged particle monitor reactions (2017)
A. Hermanne et al., Nucl. Data Sheets 148 (2018) 338-382
IAEA Monitor Reactions
natCu(p,x)62Zn
natCu(p,x)63Zn
natCu(p,x)65Zn
natCu(p,x)56Co
natCu(p,x)58Co
natTi(p,x)46Sc
natTi(p,x)48V
Experiments included preliminary cross section measurements for the natNb(p,4n)90Mo proposed monitor reaction
Experimental Setup
Notes: The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where is initial activity at end of irradiation, is areal density, is the average cross section based on incident energy and energy loss within the foil, is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial
The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where 𝐴_0 is initial activity at end of irradiation, 𝜌Δ𝑥 is areal density, ∫1▒〖𝜎(𝐸) 𝑑𝜙/𝑑𝐸 𝑑𝐸〗 is the average cross section based on incident energy and energy loss within the foil, 𝜆 is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial

## Slide 5
5
Nuclear Data Motivation for Sb(p,x) Experiments
Evaluation for high-energy (p,x) reactions and improvements to existing reaction models
Iterative approach in TALYS
  Select level density model
  Adjust level density models
  Adjust pre-equilibrium parameters
  Adjust optical model potential parameters
  Sensitivity review on previous adjustments
Variable | Default | Adjusted
Rspincut | 1 | 0.4
 | 1 | 1.5
 | 1 | 1
 | 1 | 1.5
 | 1.5 | 1.5
W1adjust n | 1 | 2.5
W2adjust n | 1 | 0.6
Variable | Default | Adjusted
Rspincut | 1 | 0.4
 | 1 | 1.5
 | 1 | 1
 | 1 | 1.5
 | 1.5 | 1.5
W1adjust n | 1 | 2.5
W2adjust n | 1 | 0.6
*Other adjusted parameters include ldmodel, strength, equidistant, m2constant, m2limit, m2shift, spincutmodel, preeqmode, mpreeqmode, preeqspin.
Notes:   These adjustments greatly improved fitting for pre-equilibrium tail for higher incident energies

## Slide 6: Another Interesting Finding from these Experiments:
Sb
As
Cu
Jπ=8-
no isomer
We see evidence of (n,2n) on targets run at BNL where incident energies are highest
6
Notes: Bottom line up front

## Slide 7
Note: Data was not observed during the June 2020 run, Oct 2022 run analysis in progress
TREND Experimental Results
ENDF 65Cu(n,2n) 64Cu
TENDL 65Cu(n,2n) 64Cu
(n,2n) reaction on 65Cu peaks at ~20MeV at nearly 1 barn!
7
65Cu(p,pn) vs. (n,2n)
Can we use this information to extract the secondary neutron spectrum?

## Slide 8: Can we use this information to extract the secondary neutron spectrum?
TREND Experimental Results
ENDF 75As(n,2n)74As
TENDL 75As(n,2n)74As
(n,2n) reaction on 75As peaks in a similar energy range at a similar magnitude
Similar result was seen in M. Fox et al.
Source: Measurement and modeling of proton-induced reactions on arsenic from 35 to 200 MeV, 2021
8
75As(p,pn)74As

## Slide 9: Can we use this information to extract the secondary neutron spectrum?
TREND Experimental Results
TENDL 121Sb(n,x) 120Sb (total)
CAVEAT: This would require a lot more rigorous analysis than a simple subtraction, I’m only including it because we see a similar pattern.
TENDL 121Sb(n,x) 120Sb (gs)
Calculated difference between total and gs
Jπ=8-
9
121Sb(p,pn)120mSb

## Slide 10: Can we use this information to extract the secondary neutron spectrum?
TREND Experimental Results
ENDF 123Sb(n,2n) 122Sb
TENDL 123Sb(n,2n) 122Sb
(n,2n) reaction on 123Sb peaks in a similar energy range at but is ~50% greater cross section
This reaction channel is off by a larger order of magnitude than prior results
As much yield here
As here
A 200 MeV proton drops to 100 MeV in 4.4 cm of Sb
The nuclear areal density of 4.4 cm of Sb is ≈4x1023
This corresponds to a sreactionrR≈0.8
10
123Sb(p,pn)122Sb

## Slide 11
Additional Indicators
Indications of natSb(n,g) seen in observations of 124Sb at BNL (limited amount at LANL as well)
Note this is not an absolute cross section as the neutron energy/flux is unknown
124Sb can only be produced via incident neutrons on natSb
1690.983 keV ,
No known competing gammas from other sources including polyester backing, adhesive
11

## Slide 12
Additional Indicators
Large discrepancies between sites are not seen in all reaction channels
This indicates that it is likely not the result of systematic error in calculations
12

## Slide 13: The adjustments we made to the Pre-eq model parameters have a significant influence on the secondary neutron spectrum
Chart: Neutron Energy (MeV)
Range of (n,2n) peak
What are the implications for 226Ra(n,2n)?
13

## Slide 14: Thank You!
This research was supported by the Isotope Program within the U.S. Department of Energy’s Office of Science, carried out under Lawrence Berkeley National Laboratory (Contract No. DE-AC02-05CH11231), Los Alamos National Laboratory (Contract No. 89233218CNA000001) and Brookhaven National Laboratory (Contract No. DEAC02-98CH10886)
14
Special thanks to the members of the
Tri-Lab Evaluated Data Collaboration:
Lee Bernstein
Dmitri Medvedev
Etienne Vermeulen
Jon Batchelder
Eva Birnbaum
Cathy Cutler
Morgan Fox
Yun-Hsuan Lee
Jonathan Morrell
Meiring Nortier
Ellen O’Brien
Michael Skulski
Andrew Voyles

## Slide 15
15
Nominally varying the areal density of the stack materials provides a better representation of current and energy in each bin reduces systematic uncertainty due to range straggling and limitations in stopping power characterization.
This variance minimization technique has been utilized in Graves et al., Voyles et al., Fox et al., and Morrell et al.
Varying the range of resulted in local minima at the various sites
Experimental Analysis
Notes: The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where is initial activity at end of irradiation, is areal density, is the average cross section based on incident energy and energy loss within the foil, is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial
The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where 𝐴_0 is initial activity at end of irradiation, 𝜌Δ𝑥 is areal density, ∫1▒〖𝜎(𝐸) 𝑑𝜙/𝑑𝐸 𝑑𝐸〗 is the average cross section based on incident energy and energy loss within the foil, 𝜆 is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial

## Slide 16: Experimental Setup
16
Irradiation via traditional natSb foils placed with monitor foils and degradiers to determine current using IAEA charged particle monitor reactions (2017)
A. Hermanne et al., Nucl. Data Sheets 148 (2018) 338-382
IAEA Monitor Reactions
natCu(p,x)62Zn
natCu(p,x)63Zn
natCu(p,x)65Zn
natCu(p,x)56Co
natCu(p,x)58Co
natTi(p,x)46Sc
natTi(p,x)48V
A preliminary cross section measurement for the natNb(p,4n)90Mo proposed monitor reaction
Notes: The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where is initial activity at end of irradiation, is areal density, is the average cross section based on incident energy and energy loss within the foil, is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial
The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where 𝐴_0 is initial activity at end of irradiation, 𝜌Δ𝑥 is areal density, ∫1▒〖𝜎(𝐸) 𝑑𝜙/𝑑𝐸 𝑑𝐸〗 is the average cross section based on incident energy and energy loss within the foil, 𝜆 is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial

## Slide 17: Energy Differential natSb(p,x) Cross Section Measurements up to 200 MeV
17
Nominally varying the areal density of the stack materials provides a better representation of current and energy in each bin reduces systematic uncertainty due to range straggling and limitations in stopping power characterization.
This variance minimization technique has been utilized in Graves et al., Voyles et al., Fox et al., and Morrell et al.
Varying the range of resulted in local minima at the various sites
Notes: The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where is initial activity at end of irradiation, is areal density, is the average cross section based on incident energy and energy loss within the foil, is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial
The use of monitor foils in each compartment provides us with the opportunity to not only more accurately characterize the current, but the energy within each stack too. This is done by a technique demonstrated in previous work, where density is treated as a free parameter and adjusted to minimize the variance of the reaction cross sections across the stack.
(This is especially useful for parts of the stack where one or more monitor cross section is changing drastically, and definitely more pronounced towards the back of the stack,
You can see in this video how the measured values fall in line with IAEA cross sections up to ~104.8%. After this point they diverge again.
IAEA data is represented by the solid line with uncertainty, measurements from the 100 MeV irradiation are the data points
A correction for range straggling and limited stopping power characterization involved treating the density of degraders as a variable to minimize systemic uncertainty in the current.
Again, this is not physically suggesting a change in density, but more to account for any potential limitations in stopping power calculations.
This weighted energy and current for each compartment can then be used to determine the cross sections for the isotopes of interest. This was implemented using a python code written by a former PhD student in the group, Jon, Morrell and uses an Anderson and Ziegler-based Monte Carlo code.
Where 𝐴_0 is initial activity at end of irradiation, 𝜌Δ𝑥 is areal density, ∫1▒〖𝜎(𝐸) 𝑑𝜙/𝑑𝐸 𝑑𝐸〗 is the average cross section based on incident energy and energy loss within the foil, 𝜆 is the decay constant, and t is irradiation time.
In addition to using Cu and Ti for monitor reactions, Nb was used as well in the 55 Mev, 100MeV, and 200 MeV stacked targets. Although this is not yet an established monitor xs by the IAEA, the (p,4n) reaction to produce 90Mo is a strong independent channel in the energy ranges we frequently look at, has a reasonably long half-life of 5.5 h, and has several strong gamma lines.
As it stands currently, only 58Co has established monitor cross section energies above 100 MeV and up to our 200 MeV range, so additional monitor cross sections are very beneficial

## Slide 18: Motivations for Sb(p,x) Experiments
18
Cross section measurements of 117mSn and 119mTe (a cow for 119Sb) to optimize production for high SA with minimal impurities
99mTc 117mSn
Imaging with 117mSn compared to 99mTc
[Swailem et al. 1998]
Primary Isotopes:
119m,119gTe, 117mSn
Potential Impurities:
116,117,118,121m,121g,123mTe, 113,119m,121m,121gSn
These Auger emitters a promising candidate for OA via RSV and potentially small mass tumors.
Notes: 117mSn colloid has shown promising results in preclinical trials for the treatment of arthritis.
  Undergoes electron conversion, very low energy gamma given the large difference in the spin/parity between the isomer and the ground state
  14 day half life simplifies its distribution logistics
  Decays to stable Sn-117
  Tends to migrate to the bones, and specifically where there is more disease in the bone.
  It is currently being used for the treatment of joint pain in canines and is in clinical trials in humans
119mTe is also being investigated as an isotope generator for 119Sb, an auger emitter for targeted radiotherapy of small tumors.
  119mTe has a half life of 4.7d, compared to the 16hr half life of its ground state (again, another 11/2-1/2+ ground state
117mSn – similar gamma emission (158keV vs 140keV) to 99mTe for imaging
Properties of Sn – tend to goes where the disease is in bone, less disease, less tin, more tin
Short range relative to beta emitters,
Low energy conversion electron emission

## Slide 19: TALYS Modeling: Additional Parameter Adjustments
19
Notes:   These adjustments greatly improved fitting for pre-equilibrium tail for higher incident energies

## Slide 20: Cross Section Measurements for Medical Radioisotopes 117mSn and 119mTe
Preliminary cross section measurements have been calculated for 117mSn and 119mTe (a cow for 119Sb) up to 200 MeV via proton bombardment
Auger-Meitner therapy with 117mSn is currently used to treat canine OA and companies are pursuing clinical trials for human treatment.
The high LET and short range makes Auger-Meitner emitters a promising candidate for small mass tumor treatment as well.
20
Notes: 117mSn
Potential Therapeutic Radionuclide – Radiosynoviorthesis (RSO)
t1/2=13.76d
  Logistically easy to handle
  Will not be an ongoing issue in the body
Isomeric Transition, emitting 158.56keV photon
  Similar energy to 99mTc, meaning similar gamma imaging techniques in hospitals
CE with 140 KeV discrete energy for therapy have an average range of ~300 μm in tissue
  High radiotoxicity in localized area
  Unlikely to damage surrounding healthy tissue
In preclinical tests, it remains localized, safe
Tests have been conducted in mice and dogs
Te-119m (4.7d)
Potential Therapeutic Radionuclide Generator – 119Sb (t1/2=38h)
Low energy auger electrons
High dose, high radiotoxicity, minimum damage to normal tissue
Current production in cyclotron facilities using 119Sn(p,n)119Sb
Using a radionuclide generator expands treatment options