## Slide 1: Radioisotope Production at Los Alamos National Laboratory
Etienne Vermeulen
LANL Isotope Program
September 26th, 2023
ORNL RIPS Workshop
LA-UR-20-28653, 22-28729

## Slide 2
“I realize, of course, that DID budgets are not enormous. I believe, in fact, that the national interest demands that they be substantially increased. The way to do this is by not only vigorously supporting those activities which are of proven value but also by exploring new activities which offer unusual promise....Thus, with the support of the DID for this proposal, we can assist in obtaining additional funds for an isotope production facility at LAMPF.”
L.Rosen – Presentation to the AEC Division of Isotopes Development
15 December 1970

## Slide 3: Isotopes
We make can make a wide range of radioactive isotopes that have a huge range of application spaces for many different end users.
Isotope | Half-life
82Sr | 25.5 d
68Ge | 270 d
134Ce | 75.9 h
44Ti | 58.9 a
225Ac | 10 d
230U | 20.8 d
119mTe | 4.71 d
Isotope | Half-life
32Si | 153 a
73As | 80.3 d
109Cd | 462.6 d
22Na | 2.6 a
236Np | 1.5 105 a
Medical applications
Cancer therapy
Environmental Applications
Industrial Applications
Nuclear Forensics

## Slide 4: LANSCE & The LANL Isotope Production Facility (IPF)
Area A
Line D
pRAD & UCN
800 MeV
Side Coupled Cavity Linac
805 MHz
H+
H-
Drift Tube Linac
201.25 MHz
100 MeV Transition Region
750 keV
H+
H-
H-
Proton Injectors
SCCL is 90% of accelerator length
Proton Storage Ring
Weapons Neutron Research Facility
100 MeV proton beam routinely used at 250 mA for isotope production
Notes: So where do we make these isotopes?
We use the Isotope Production Facility, located at the Los Alamos Neutron Science Center linear proton accelerator. We are located at the front end, where we extract protons at an energy of 100 MeV. You can see that the accelerator is able to continue to accelerate protons up to 800 MeV which are utilized by the other downstream facilities.

## Slide 5: IPF v1 Location
Beam
Stop
Line D
Line X
Line A
800 MeV
Side Couple Cavity Linac
805 MHz
H+
H-
Transition
Region
Drift Tube Linac
201.25 MHz
100 MeV
750 keV
H+
H-
Proton
Injectors
Existing
Isotope Production
Station
SCCL is 90% of accelerator length
LANSCE Accelerator Complex
Proton Storage Ring
Weapons Neutron Research Facility
Manuel Lujan, Jr. Neutron Scattering Center

## Slide 6
Targets

## Slide 7
Isotope Production Facility (IPF)
100 MeV
Main beam Line
Hot Cell
Monorail Crane
40’ Water
Target Cooling System
In front of the Hot Cell
Manipulators
Target system 3D model
IPF

## Slide 8: 100 MeV Proton Beam at IPF
100 MeV pulsed proton beam (100 Hz) on hockey puck-sized targets
~250 µA proton beam current = 1.6e15 protons/s!
Protons
(100 MeV)
RbCl
Beam
Average target size
Swept in circle(s) to produce a concentric ring-shaped profile, reducing peak power density on the target
5-circle raster pattern
Notes: Now HOW do we make these isotopes?!
We use a 100 MeV pulse proton beam. When I say pulsed I mean that our beam is not constant, it has a specific pulse structure and is delivered at a rate of 100 Hz, meaning we receive proton pulses 100 times per second. We use an average beam current of ~250 uA, which corresponds to about 1.6 *10^15 protons /second. In addition, our proton beam is very rapidly swept in a series of concentric circles to distribute the heat more evenly on the target. You can see the image of our five circle raster pattern here, and this is distributed on a target about the size of a hockey puck.
We use a three-stacked target configuration (3 targets in a row), separated by small gaps, to allow us to force cooling water along the front and back faces to remove the pretty substantial amounts of heat we are dumping into these targets with our proton beam.

## Slide 9
IPF Beam Window Assembly
Notes: To provide more context, while the beam window itself is no bigger than the palm of my hand in surface area (or as this pictures indicates, smaller in area than a box of scotch magic tape). and only half a mm thick, this beam window is not an independent component, easily replaced in the event of failure.
nickel alloy, welded onto a beam pipe containing active adjustable collimator segments. This beam window assemb
This beam window is actually weleded on to a stainless steel flange, and then welded onto a section of beam pipe containing 4 fixed and 4 adjustable collimator segments, capable of moving from aperature diameters of 1.4 to 2.3” via a flexure mechanisms. These collimator segments are active, in that they are installed with connections for both temperature and current (beam spill) feedback), and they have cooling lines running through them.
This assembly is contained withing a nearly 7 foot (2m) section of beam pipe that is welded together and enclosed inside of a larger pipe through which our cooling water returns.
2m (6.5 ft)

## Slide 10
IPF Beam Window Assembly
Shielding
IPF beam window
IPF target station
6.5’
IPF beam window assembly
Notes: Here I have shown the entire beam window & collimator assembly, as it is installed relative to the IPF target station You can see that this section of pipe must be inserted into the concrete shielding block surrounding the IPF target station, and that once installed, the majority of this assembly is inside of the shielding.

## Slide 11
Indications of Beam Window Failure
Rapid/nearly instantaneous degradation of beamline vacuum.
  Fast valves upstream closed due to increase in vacuum.
When the vacuum team was trying to recover IPF beamline vacuum, they noticed water coming out of the vacuum pump.
Opening the beamline revealed water in the vacuum pump, and other beamline diagnostic components.
Camera inspection clearly showed a puncture hole in the beam window.
Notes: Rapid/nearly instantaneous degradation of beamline vacuum.
  Fast valves upstream closed due to increase in vacuum.
When the vacuum team was trying to recover IPF beamline vacuum, they noticed water coming out of the vacuum pump.
Opening the beamline revealed water in the vacuum pump, and other beamline diagnostic components.
Camera inspection clearly showed a puncture hole in the beam window, looks very similar to the hole that we saw in our plastic beam imaging foil.

## Slide 12
IPF Beam Window Assembly Removal Process
Notes: To give a sense of the effort and planning involved in removal and replacement of this beam window assembly, I have shown two pictures here.
The picture on the left shows an image pulled from video taken during the beam window assembly removal – due to the contamination, full PPE and respiratory protection is required.
In addition, the dose rate associated with this assembly can be quite significant, so planning for this to ensure worker protection took a significant amount of effort and planning.
Once this assembly is removed, the picture on the right shows just how difficult it is to transport this assembly and the unusual shipping cask (of which there is only one) required to safely move and store it.
Transported on flat bed trucka n dmoved with crane.

## Slide 13: Computational Multi-Physics Modeling
Influence of thermal hydraulic behavior?
What are the protons doing?
Temperature
Velocity
Molten Rb Metal Target
Boiling in Cooling Water System
Bubbles
Bulk water flow
Temperature
Liquid Fraction
Velocity
RbCl Target Melting Front
Notes: All this experimental data informs our models so that we can have better predictive tools (that we now have more confidence in!) to tell us what our system is doing!!
Now how are we able to create a model to capture this multi-physics system and what can we gain by using this model? By applying two-way coupling between a particle transport code (to determine what the protons are doing) and a thermal hydraulics code, it is possible to determine how this highly interdependent system behaves.
Rb melting point – 103 F
RbCl melting point = 1324 F
Computational Coupling
This video shows the model-predicted time-dependent temperatures and velocities in a molten production target. In addition to understanding our targets better, another tangible benefit of modeling was the discovery of boiling in our cooling water – something that we must understand in order to push the limits of our system.
Ultimately, developing a computational model will allow us to not only understand our system and its limits, but to safely push the bounds of large scale radioisotope production as we know it while avoiding high consequence events like target failures. This work focuses on the front end of radioisotope production, but this first step is essential, and everything that happens downstream is dependent on our ability to safely and successfully make these radioisotopes.

## Slide 14
P
G
Target A
B
C
Flow
(Inconel target capsule)
IPF cooling system – 1st channel
Experimental flow loop
Flow loop
5
Experiment
Mirror
TOutlet
TInlet
Inconel
Test Section
Induction heating
High-speed camera
(40000 fps)
Operating conditions
10~12 GPM flow rate
85 K subcooling
2 bar pressure
Channel geometry
Non-fully developed
IPF’s specific conditions
Optical access
window
Inconel
T
Flow
Flow

## Slide 15
 Uniform heat deliver to Inconel window
 Enable to calculate heat flux
 Off the shelf Inconel window
Limited applied heat flux (0.9MW/m2)
due to poor thermal contact between
different metals.
(IPF ~3MW/m2)
7
Experiment
Test section design
D50mm Pancake coil
Inconel
T
T
T
T
S-coil
Inconel test section
Original test section design
Aluminum
frame
Steel
cap
Copper
rod
T

## Slide 16
Experiment
Twall – Tsaturation
10 GPM flow rate
85 K subcooling
2 bar pressure
IPF conditions
5 mm
At IPF: Bubbles are small and fast departure – early stage of boiling
Boiling heat transfer coefficient of
~48000 W/m2/s
CHF
*
5 mm
Burn mark
30 mm
1.5 GPM flow rate
45 K subcooling
2 bar pressure
Reduced conditions
Critical Heat Flux
(CHF)
IPF avg. power
What would be the boiling crisis ?
(CHF)