## Slide 1: MicroTCA Working Group
Alan Justice
Controls Hardware System Engineer
Oak Ridge National Laboratory
Spallation Neutron Source
EPICS Meeting
MicroTCA Working Group
September 16-20, 2024

## Slide 2: Schedule
13:10 - 13:30 Introduction/MicroTCA at SNS
13:30 - 13:50 MicroTCA at FRIB
13:50 - 14:10 MicroTCA at FNAL
14:10 - 14:30 MicroTCA at APS
14:30 - 14:50 MicroTCA at ESS
14:50 - 15:00 Questions/Discussion
15:00 - 15:30 Break
15:30 - 15:50 SNS IPMI EPICS Tool
15:50 – 17:00 Open Discussion

## Slide 3: MicroTCA Applications at the Spallation Neutron Source
Alan Justice
Controls Hardware System Engineer
Oak Ridge National Laboratory
Spallation Neutron Source
EPICS Meeting
MicroTCA Working Group
September 16-20, 2024

## Slide 4: MicroTCA future at SNS
VME to MicroTCA upgrades are part of the Integrated Controls Section modernization strategy at SNS
Extensive in-house hardware & firmware expertise
Improving the reliability through extensive component health monitoring (IPMI)
Vadatech VT814
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 5: MicroTCA Applications at SNS
Low Level RF
  Ring LLRF
  LINAC LLRF
Machine Protection System(MPS)
Magnet Power Supplies(PS) - Injection Kickers
  Waveform Monitor
  Waveform Generator
Personnel Protection System(PPS)
  Beam Power Limiting System

## Slide 6: MicroTCA Hardware in production at SNS
MicroTCA Systems in Production(69)
  Crates
    VT815(3), VT811(19), VT819(47)
  FPGA cards
    AMC523(92), AMC502(32), AMC560(4)
  MCH
    UTC002(25), UTC006(1)
  Processors
    AMC726(22)

## Slide 7: Ring Low Level RF
Upgrade from VME in 2016
First MicroTCA production deployment at SNS
Total of 4 LLRF systems in use
Hardware
  Vadatech VT811 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC502 carrier cards
  Vadatech AMC726 Processor
  Custom FMC Timing Receiver
  Custom FMC ADC/DAC
Ring LLRF Station 1
Notes: Preventative Maintenance
Spares

## Slide 8: LINAC LLRF
Upgrade from VXi
Began as part of the Proton Power Upgrade Project
Total of 14 LLRF systems in use
Will be extended to all LINAC LLRF over the next 3 years
Hardware
  Vadatech VT811 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC523 with custom RTMs
  Vadatech AMC726 Processor
  Vadatech AMC502
  Custom FMC Timing Receiver

## Slide 9: Upgraded Machine Protection System
Largest deployment so far with a total of 48 systems
Master Hardware
  Vadatech VT815 Chassis
  Vadatech UTC002 MCH
  Vadatech UTC006 Crossbar/MCH
  Vadatech AMC502 carrier cards
  Vadatech FMC105 SFP transceivers
  Vadatech AMC726 Processor
Field Node Hardware
  Vadatech VT819 Chassis
  Vadatech AMC523
  Custom RTM
SNS MPS Master and Trigger Control
Notes: Crossbar reference at the bottom

## Slide 10: Magnet Power Supplies – Injection Kickers
Waveform Monitor Hardware
  Vadatech VT811 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC502 carrier cards
  Vadatech AMC726 Processor
  Custom FMC ADC
Waveform Generator Hardware
  Vadatech VT811 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC502 carrier cards
  Vadatech AMC726 Processor
  Custom FMC DACs
Injection Kicker Waveform Monitor
Injection Kicker Waveform Generator

## Slide 11: Beam Power Limiting System
Personnel Protection System and Machine Protection System functions
Limit Beam Power on First Target Station
Hardware
  Vadatech VT815 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC560 carrier cards
  Vadatech AMC726 Processor
  FMC 155 – RS485
  FMC265 - ADC
  Custom FMC Timing Receiver

## Slide 12: Current and Future Development
Current Developments
  LINAC HPRF
  Extraction Kicker Monitor
Future Developments
  LEBT Chopper
  Timing Master