## Slide 1: EPICS Software Development of the Fast Event System for APS-U
Ran Hong
Controls Engineer
Advanced Photon Source
Argonne National Laboratory
Sep 16, 2024

## Slide 2: Outline
Fast Event System for SR and Linac
Device support development for the MRF VME-300 series cards
  Delay compensation
  Virtual gate generation
  Timestamp generation
System Integration at APS:
  User interface PVs and Legacy PVs
  GUI development
On-going development
  Merging with the main repository
  Run the EPICS IOCs on RTEMS

## Slide 3: Timing and Event Systems for APS
Fast event system for the new storage ring
  Providing timing signals to event-based devices: BPMs, DAQ aggregators, …
  Providing edge triggers to conventional devices
  Hardware components made by Micro-Research Finland (MRF) (VME based 300-series)
Legacy timing and event system for the injection complex
  Booster, Particle Accumulation Ring (PAR) and part of the Linac
  Providing edge triggers and events (legacy APS Event system components)
Refurbished timing system for the Linac
  Providing edge triggers to existing devices
  MRF event system components (VME based 300-series)
APS-U Storage Ring
Booster
PAR
Linac

## Slide 4: Fast Event System for SR and Linac
EVM
EVM
SR RF/3, ~117MHz
EVM
EVM
EVM
EVM
EVM
…
SR Double-sectors
BTS
…
MCR
EVM
Fan-out module
Fan-out module
EVR
Embedded EVRs
LB+ BPMs
MPS BPLD
TBT DAQ Aggregator
PS DAQ Aggregator
…
Edge-triggered devices
Typical Double-sector
From MCR
EVM
Fan-out module
EVR
Edge-triggered devices
Linac
Linac RF/24, ~119 MHz
EVR
EVR
EVR x6
Edge-triggered devices
Edge-triggered devices
Edge-triggered devices
Event generation
Edge triggers from the legacy timing system
Internal frequency divider
Software command
Edge trigger examples
Pulsed septum
Cerenkov Beam Loss monitor
BPMs
…

## Slide 5: EPICS Device Support Development
Main repository: https://github.com/epics-modules/mrfioc2
  Evolved from the device supports of the 230-series hardware
  Leverage some developments from mTCA-300-series EVM/EVR by ESS to VME64x platform
  Providing the API functions, database template, CSS/Phoebus screens
APS Local repository
  Forked from the main repository
  Adapted to VME-300-series EVM and EVR
  Features in recent firmware releases are supported
  Merging to the main repository in progress

## Slide 6: Device Support Development: Delay Compensation
Delay compensation development
  Previously, EVMs only measure the delay, but not able to adjust its FIFO to introduce delay
  Delays introduced by EVMs are crucial for embedded EVRs not having the delay compensation support
  Firmware updated to allow EVMs to adjust FIFO depth to introduce delay
    Supports both static delay or dynamic delay
  APS Configuration
    Static delays for EVMs in local stations
    Delays to local stations are measured by MRF EVRs
    Delay variance among local stations: 300ps, 3 months after the initial configuration.
EVM
EVM
Fan-out module
Embedded EVR
EVR
EVM
EVM
EVM
EVM
Embedded EVR
Embedded EVR
Embedded EVR
Most of the embedded EVRs do not support delay compensation yet
Must be able to adjust its delay to cover the major delay for the end-component not supporting delay compensation

## Slide 7: Screen Enhancement for Delay Compensation
Top-level EVM
Leaf-level EVM
EVR

## Slide 8: Device Support Development: Virtual Gate Generation
Virtual gates: pulse generator (ID = 28 – 31) in MRF EVR dedicated to enable-gates or masks for other pulse generators.
Before: virtual gates configured with the set and reset function.
Firmware update: virtual gates can also be generated as a triggered pulse with specified delay and width after the trigger event
  Only for EVR-VME-300, not the embedded EVRs in EVM boards.
Example usage:
  For SR, a typical use is to gate the P0 signals upon injection
Registries, API functions and GUI are available for setting a triggered pulse for the virtual gates, but previous firmware does not support this feature.

## Slide 9: Device Support Development: Timestamp Configuration
Timestamp configuration for EVG-230
  1 PPS source (interrupt source): second increment input (1 PPS GPS)
  One trigger event configured for code 0x7d upon the 1PPS source
  Event 0x70 and 0x71 generated by software
Timestamp configuration for EVM-300
  DBus5: second increment input (1 PPS GPS)
  DBus4: fast timestamp clock input (10MHz the GPS)
  1 PPS source (interrupt source): same as DBus5
  Event 0x7d, 0x70 and 0x71 generated by hardware automatically
Device support update
  User can select either modes above
  When the EVM-300 mode is chosen, software stops generating 0x70 and 0x71

## Slide 10: System Integration at APS: User-interface PVs and GUI
Relevant PVs are grouped together for pulse set up
Coarse and fine delays calculated in software
PVs for user interface are published and accessible to the users.
Device-interface PVs from the device support are protected by access security.

## Slide 11: System Integration at APS: User-interface PVs and GUI
MCR

## Slide 12: System Integration at APS: User-interface PVs and GUI
SR Local Station

## Slide 13: System Integration at APS: User-interface PVs and GUI
Linac Timing Screen
User PVs from old timing system are hosted in a soft IOC, and linked to the PVs of the new timing system
Minimized the changes on the client IOC and GUI.

## Slide 14: Current Status at APS
Finished recently
  EVM-300 and EVR-300 initialization and configuration
  PLL Bandwidth selection
  More options for the AC main trigger Synchronization source
  EVR event clock mode selection
  Flash I/O support
  EVM delay compensation action
  Multiplexed counter external reset
  Hardware timestamp generation
  Database substitution files for EVM-VME-300
Functions merged to upstream repo

## Slide 15: Current Status at APS
Work in progress
  Making the database template file compatible with both mTCA and VME cards
  EVR-VME-300 CML/GTX mode word order fix: waiting for ESS to verify that the mTCA systems are not affected.
  EVM reset button
  EVR rear transition board fine delay
  CSS/Phoebus screens for VME-300-series hardware
Merging to upstream repo ongoing
  Merge requests submitted for the first 2 and under review
  The rest on the way

## Slide 16: Backups

## Slide 17: MRF event system components
Event system components by Micro-Research Finland Oy
  MRF Event master (EVM-VME-300): event generation and fan-out and concentration
  MRF Event Receiver (EVR-VME-300)
  FOUT-12 event fan-out card (EVF): 12 way-event fan-out, 1 receiver port, 11 transmitter ports.
  Universal I/O transition board: more I/O slots for EVM and EVR
  MRF also provides components in other form factors (mTCA, PCIe, …)
MRF EVM-VME-300
MRF EVR-VME-300
MRF FOUT-12
Universal I/O Transition Board

## Slide 18: MRF Event System at APS
The Fast Event System is a distributed timing and trigger system.
  Synchronized clocks
  Codes and data encoded in the clock signal for trigger distribution and synchronous frequency generation
The event system acts as a global timebase for applying timestamps to collected data and performed actions.
Some major components used at APS (VME64x based):
  Event generator (EVM-300): generates event codes, programmable, can be daisy-chained
  Event receiver (EVR-300): receives event codes and perform actions, programmable
  Event fan-out module: duplicates event links
Event Generator
(EVG)
Event Receiver
(EVR)
Event Link
…
…
…
Event clock tick, 16-bit word
EVM
EVM
Fan-out module
Fan-out module
Fan-out module
Fan-out module
EVR
EVR
EVR
EVR
EVR
Signals in the event link
Typical event system

## Slide 19: Delay Compensation
Code compatibility
  Shared across VME, mTCA, PCIe, etc:
    Registry addresses: shared register map
    EPICS record interface mechanism: object + function
    Low-level API (event generation, pulser configuration, delay compensation, etc)
        Shared database template
  Unique features of each platform:
    Initialization functions
    Number of I/O ports, available bits for delay and pulse width, etc.
        Different substitution files for each platform/hardware variance
        Valid PV value ranges are different
  User interfaces on different sites
    The main repository development makes sure the existing systems are not broken upon updates
    Site-specific records are maintained locally

## Slide 20: Device Support Development: Delay Compensation
Delay compensation mechanism
  Upstream EVM measures the delay to each downstream components using beacon event time difference
  Measured delay values are sent to the downstream components via the data transfer channel in the event link (8 bits every 2 clock cycles)
  EVM/EVRs measure their own delays
  Additional delays are introduced by adjusting the FIFO depth
  Operation modes
    Static: Fix the delay introduced by an EVM/EVR
    Dynamic: Set a delay target for EVM/EVR and let it adjust its own delay to reach the target delay
Top-level EVM
Generating Beacon event 0x7e
Fan-out ch1
Fan-out ch2
Fan-out ch8
Beacon back
Beacon out, delay value out
EVM
EVM or EVR
Fan-out ch1
Fan-out ch8
…
…
Uplink
Uplink
Beacon back
Beacon out, delay value out

## Slide 21: Device Support Development: Timestamp Configuration
Timestamp construction at EVR
  Use 0x70 and 0x71 events to construct the next second value in the buffer
  Upon event 0x7d, the buffer value is loaded as the current second value
  Fast timestamp (nanosecond counter)
    Nanosecond counter choices:
        Event clock tick: fastest, but affected by reference frequency change (e.g. RF ramping studies)
        Dbus4 (10MHz): constant frequency locked to GPS
        Event 0x7c: older style, may introduced more event collisions
      The clock tick frequency value can be set via an EPICS PV.
        If too high: timestamp gap upon whole-second increment
        If too low: overflow upon whole-second increment
      RF Frequency are measured, and the TS clock tick frequency is updated
  Event timestamp
    Only events registered as FIFO events have timestamps recorded
    For an EPICs record, to use the event time, the TSE should be set as the event code