## Slide 1: QIKR Shielding PDR: Mechanical Overview
D. Wilson, Lead Engineer
March 03, 2025

## Slide 2: Outline
Model Changes Following Neutronic Analysis
  Target Area Shielding
  Monolith Optics Insert
  Bunker Feed-Through Shielding
  Cave
Components Not Neutronically Analyzed
  Background Shield Wall
Component Acquisition, Manufacturing, Installation Strategies & Costs

## Slide 3: Target Area Shielding/ Monolith Optics Insert

## Slide 4
Monolith Shielding, Upstream & Optics
Monolith Insert
Optics Insert (Shielding)
Monolith Wall
Core Vessel
Additional Shielding
(not shown)
Upstream Shielding Area
Neutrons
Bunker
Area

## Slide 5: Monolith Shielding, Upstream & Optics
Monolith Upstream Shielding (Steel, owned by Target)
Optics Insert (Steel)
Monolith Insert
(Steel)
Nozzle Extension (Steel, owned by Target)
Core Vessel
(Steel)
Belt Line
(Steel)
Neutrons

## Slide 6
Monolith Upstream Shielding – Current vs. Neutronics Model
Empty Space
Neutrons
Version initially used in Neutronics Analysis
One variant was to fill the space completely with steel with circular openings circumscribing the guide path dimensions… this led to the design shown at right
Neutrons
Filled Space
Original Design
Current Design
Current Design
Target shielding includes two water-cooled sections of steel (upstream) and one non-cooled section of steel attached to the nozzle extension
Guide paths pass through oversized (60mm) circular openings in the steel (guide paths = 30mm x 26.5mm)
water-cooled
water-cooled
not cooled

## Slide 7: Monolith Upstream Shielding – Current Design
Nozzle Flange
Steel shielding surrounds gun-drilled circular beam paths ( 60mm)
(desired guide path dimensions: 30mm W x 26.5mm H)
Surrounding belt line shielding is not shown here
Nozzle Flange
Beltline
Shielding with circular beam paths
X-sec through both beam paths simultaneously
Core Vessel
Core Vessel
Neutrons
Neutrons
This section is not cooled, the other sections are water-cooled

## Slide 8
Monolith Optics Shielding
Steel layers, combined upper and lower insert… built as a single assembly in layers
Upstream section is separate but attached in layers along with the downstream section
Entire assembly inserted into monolith in one operation
Fewer gaps & streaming paths compared to original version
New Design
Previous, Neutronics Analysis Design
Upper Optics Insert
Lower Optics Insert
Anti-streaming block
Steel layers, separate upper and lower insert… each built and installed separately
Anti-streaming block installed separately (after inserts) to compensate for the very small chicane between the optics inserts and the monolith insert shelf that separates them (see next slide)
Significant streaming paths seen in neutronics analysis
Design credit: Ryan Butz
Design credit: Cameron Hart
Upper Optics Insert
Lower Optics Insert
Upstream section
Small anti-streaming chicane

## Slide 9
Monolith Optics Shielding – Old Design
Previous Design, Used in Neutronics Analysis
Anti-streaming block, provides more of a chicane than the 9mm step upstream
Upper Optics Insert
Lower Optics Insert
Thin sections (difficult to manufacture)
The anti-streaming chicane
9mm step each side
6mm gaps b/w optics & monolith inserts
Monolith Insert
Monolith Insert Shelf

## Slide 10
Monolith Optics Shielding – New Design
New Design, not yet analyzed
Handler attachment features (likely no significant shielding benefit)
Upper Optics Insert (yellow)
Lower Optics Insert (green)
Thicker sections
Two anti-streaming chicanes with no nominal gaps (12mm upstream, 11mm downstream)
Monolith Insert

## Slide 11
Monolith Optics Shielding
New Design, not yet analyzed
Significant Gaps (red)…
fewer for the new design
Previous Design, Used in Neutronics Analysis

## Slide 12
Neutronics Analysis with Upstream Steel
Neutron dose rate
(mrem/hr)
No upstream steel insert
Upstream steel insert, with chicane
Upstream steel insert, no chicane
Upstream steel insert with chicane is neutronically best (better shielding performance)
Removing chicane will introduce straight streaming pathways along the monolith insert!
Therefore, relatively higher dose rates on the bunker wall face
Vertical cut-view at the bunker wall (view from the monolith)
Screenshots taken from Kursat Bekar’s analysis of QIKR
Current design now most closely matches this scenario

## Slide 13: Guide Installation

## Slide 14
Guide Shielding – Reminder
Horizontal cross-section of an in-bunker guide housing, shows change in shielding layer thickness due to guide curving/angling
Guide Glass (float or borofloat glass)
Steel Shielding Layer
Stainless Steel Vacuum Jacket
Vertical cross-section of the last in-cave guide housing (QIKR-U), shows change in shielding layer thickness due to guide taper
Neutronics analysis used the same guide construction except for a steel vacuum jacket… current design is stainless steel
Plan view
Elevation view

## Slide 15
Guide Shielding – Installation
Cradle Assy
Sled Assy
Crank Assy
A
Guide & Shielding are assembled on Cradle Assy
B
The guide segments and shielding layers are assembled, guide segments aligned. Wheeled “trucks” are attached to the ends.
Guide/shielding assembly is lifted and placed on the sled assembly
The crank assembly is used to pull the guide/shielding assembly (rolling on the truck wheels) into the vacuum housing sleeve
The trucks are removed, and flange covers & windows are installed; the guide housing is ready for transport.
C
Optics Module is placed on Sled Assy and inserted into Vacuum Housing with Crank Assy
Standard In-Bunker Guide Housing Assembly
(QIKR will use the same process)
D
Flange and Window covers are installed before transport
Windows installed
Slide modified from Cristina Boone & Pete Torres’ presentation: “20241204 STS In-Bunker Guide Housings for Scientists.pptx”

## Slide 16: Bunker Wall & Feed-Through Shielding

## Slide 17
Bunker Wall – New
7’4” = 6’8” bunker wall + 8” cave-side protrusion
QIKR-B cross-section
Exterior bunker wall
QIKR-U
QIKR-L
Cave-side protrusion
Standard guide and shielding
Grout layer
Baseplate
Sled on Hilman rollers
Lower and upper shielding
Baseplate
Sled
Upper shielding
Hilman rollers
Lower shielding
QIKR follows the standard design for bunker wall shielding and chicanes (steel)
  Shielding is layered with no nominal gaps between layers, each section of shielding is staggered relative to the next to prevent streaming paths
  The feedthrough frame is wider on the bunker side than on the cave side to provide an anti-streaming chicane
  Gaps are cut into the center of the shielding to fit the guide and its anti-streaming bands
Embedded frame supplied by CF
Shielding mating surfaces are staggered between sections
Anti-streaming bands
Current Design
Screenshot taken from Cristina Boone & Pete Torres’ presentation: “20241204 STS In-Bunker Guide Housings for Scientists.pptx”

## Slide 18
Bunker Wall – Shielding & Cable Channels Used in Analysis
Stepped Cable Passages
Cable Passages removed from the inner sides to avoid overlap with monolith optics insert streaming neutrons
Stepped frame and shielding
Solid shielding (not layered), chicaned
Similar baseplate, sled, rollers, grout layer (not shown)
The current standard design was based on the one shown here, which was used in QIKR’s neutronic analysis… the current standard design is expected to have a similar neutronic performance
The standard design has the inner cable passages in place. QIKR may remove those again, but the new optics insert may help eliminate the need for that

## Slide 19
Bunker Wall – Cable Channels (New)
Smaller Cable Passages
Larger Cable Passages
Cable Passage Covers
QIKR-U
QIKR-L
Current Design
Screenshots taken from Cristina Boone & Pete Torres’ presentation: “20241204 STS In-Bunker Guide Housings for Scientists.pptx”
Cable Passages are stepped in “y” to avoid streaming
y
New design is very similar to the old design. Rather than remove the inner cable channels though, QIKR would fill them with steel

## Slide 20
Bunker Wall – Shielding and Guide Installation
Bunker Wall
Bunker Wall Feedthrough
Bunker Wall Feedthrough Insertion Tool (BFIT)
Optics/Shielding Package
(guide not shown)
BFIT is aligned to the BWF
The sled is placed on the BFIT, the guide housing and shielding layers are built up
The BFIT is then used to transfer the optics/shielding package into the BWF
All components are placed in the bunker with the 50-ton high bay overhead crane
Modified slide taken from Cristina Boone & Pete Torres’ presentation: “20241204 STS In-Bunker Guide Housings for Scientists.pptx”

## Slide 21: Cave

## Slide 22: Cave Exterior – Design Updates
HDC
RWC
HDC
HDC
RWC
HDC
HDC
HDC
HDC
RWC
Original (analyzed) Design
Current (un-analyzed) Design
QIKR-L roof is lower
  Improves cave structure, reduces cost
Cable pass-thrus added to the roof
QIKR-U RWC section shortened, end portion of center wall converted to RWC
  Reduces cost; dose rates are very low on this section of the center wall
600cm
520cm
RWC ST01-side
RWC ST01-side

## Slide 23: Cave Interior – Design Updates
HDC
HDC
HDC
Original (analyzed) Design
Current (un-analyzed) Design
QIKR-U
QIKR-L
QIKR-U
QIKR-L
Single dog-leg to accommodate components
Two center wall dog-legs to accommodate components & QIKR-U monorail hoist
Background shield walls
Center wall has 2 dog-leg features instead of 1
  Allows additional room for components and QIKR-U monorail hoist motor
Background shield walls added
  Their presence was known at the time of neutronic analysis, but they were not included because they are not intended to provide radiation shielding for personnel safety

## Slide 24: Cave – Cubby Spaces
QIKR-U “cubby” space
QIKR-L “cubby” space
Original (analyzed) Design
QIKR-U “cubby” space
QIKR-L “cubby” space
Current (un-analyzed) Design
Additional RWC concrete to fill in space up to the background shield wall (prevents personnel from going behind the wall through the cubby space)
Cubby spaces are all ~4ft in height

## Slide 25
Cave – QIKR-U View of Cubby Spaces
QIKR-U cubby
QIKR-U cable access to end station
QIKR-L cubby
Regular weight concrete
High density concrete
QIKR-L cable channel

## Slide 26: Cave Installation
Cave will be pour-in-place (PIP) concrete, poured in sections
The current thickness of the walls may not support the current wall height, particularly for QIKR-U
  If this is confirmed, the plan will be to install a steel girder skeleton first, then pour the concrete around it… the skeleton will provide additional structural support

## Slide 27: Background Shield Walls

## Slide 28
Background Shield Wall (for Detector Background Reduction)
Movable Shield Walls
QIKR-U
QIKR-L
Background Shield Walls are placed at the end of the guides in each of the QIKR-U and QIKR-L caves
  One half of the wall is fixed, the other is hinged to allow personnel access to the in-cave portion of the guides
  The hinged half is configuration-controlled and remains manually locked unless either both beamlines are inactive, or the proton beam is off
  The QIKR-U wall is slightly wider and shorter than the QIKR-L version because of the different detector locations in the cave and the detectors’ different view angles (QIKR-U looks more downward, QIKR-L looks more upward)
The primary purpose of the background shield walls is to fill the detector’s view with B4C (ZHIP mix panels) to reduce background noise from concrete surfaces (cave walls and floor)
The walls are not intended as radiation shielding for personnel but do block personnel access to areas of the cave that may have higher dose rates in certain operating conditions.
QIKR cave
Bunker wall

## Slide 29
Background Shield Wall – QIKR-L (mirrored for QIKR-U)
Movable Side (downstream view)
Fixed Side
80/20 aluminum extrusion rail, 30-series, 3”x3”
Hilti anchors
Hinges (2x)
Steel, 2000lb capacity
Braces (2x)
80/20 aluminum
Hilti anchors (for hinges)
Hilti anchors
Attachment for swivel hoist ring
(steel, custom)
Hilti anchors
Lock for configuration control
80/20 corner brackets, aluminum
Custom SS 90° L-brackets (4x)
Swing open
Opening for guide end

## Slide 30
Background Shield Wall – QIKR-L
Each background shield walls is built in three sections for easier installation around the guide
  The larger sections have plate to attach a swivel hoist ring for crane transport
  All sections are intended to be assembled in-cave by ORNL staff. If built elsewhere, the two heaviest sections may be transported by crane using swivel hoist ring lift points.
  Construction is an aluminum 80/20 frame with ZHIP mix panels mounted to the downstream side
The ZHIP mix panels have an aluminum backing plate with threaded studs pre-installed by Dielectric Sciences
  Panels are attached to the 80/20 frame using two COTS L-backets… this method keeps the attachment hardware from being visible to the detector
The hinged side of the door (500lbs) is supported by 2000lb capacity hinges & padlocked to the fixed side & configuration controlled
All attachment to the concrete walls & floor is done with Hilti anchors
200lbs/ 156lbs
465lbs/ 202lbs
500lbs/ 375lbs
Weights of QIKR-U version shown in red

## Slide 31
Movable Shield Wall – ZHIP mix panels
ZHIP mix panels are procured from Dielectric Sciences (single source)
  The vendor provides the ZHIP mix on an aluminum backing panel with threaded studs pre-installed
  ZHIP mix layer is 11mm thick, aluminum layer is 3mm thick (may need to increase the aluminum layer to 6mm, waiting for vendor feedback)
Panels are attached to the 80/20 frame with COTS aluminum L-bracket & 80/20 spring-loaded T-nuts
  T-nuts are spring loaded to stay in place if the panel is removed & replaced (may need to be done if panel becomes damaged
Highest ZHIP mix panel weight = 34lbs (QIKR-U)
Spring-loaded T-nut (80/20)
Pre-installed threaded PEM stud (PENN Engineering)

## Slide 32
Background Shield Wall – ZHIP mix panels
Additional ZHIP mix panels are installed on the QIKR-L cave walls to block the detector’s view of concrete surfaces
Panels are attached via Hilti anchors at their corners (ZHIP mix is not present on the corners)
Heaviest panel = 34lbs
QIKR-L
QIKR-U
QIKR-U needs more extra panels on the center cave wall
Extra ZHIP mix panels
QIKR-U

## Slide 33
Background Shield Wall – ZHIP Mix Panels Attachment to Wall
Similar to the background wall panels, threaded studs are inserted into the ZHIP mix aluminum backing panels
Panels attach to Unistrut on the cave wall along their top edges (in-cave manual installation, ORNL labor)
Panels attach to the previous panel with pre-tightened fender washer on their bottom edges (in-cave manual installation, ORNL labor)
Threaded studs with nuts
Fender washer with nut
Unistrut
Nut plate
Screw

## Slide 34: Acquisition, Manufacturing, Installation

## Slide 35: Acquisition strategy
Shielding component | Competitive Bid or Sole Source | Vendor Location | Exotic Mat’ls | Supplier Constraints/ Comments
Lower Beam Stop | Competitive | Domestic | No | 
Bunker Wall Feed-Through (QIKR-L & QIKR-U) | Competitive/ Sole Source | Domestic | No | Rollers are sole sourced from Hilman, steel shielding is competitively bid
QIKR-L Background Shield Wall | Sole Source | Domestic | No | ZHIP mix panels are sole source, frame is sourced from 80/20
Cave, RWC | Competitive | Domestic | No | 
Cave, HDC | Competitive | Domestic | No | 
Note: not currently planning to purchase an upper beam stop or background shield wall unless contingency allows

## Slide 36: Manufacturing strategy
Optics component | Manufacturing Strategy
Lower Beam Stop | Beam Stop Panel: Build-to-print Hardware & PPS Switches: COTS In-house assembly of some components (e.g. hinges, PPS switches, latches)
Bunker Wall Feed-Through (QIKR-L & QIKR-U) | Build-to-print fabrication, in-house assembly
QIKR-L Background Shield Wall | Build-to-print ZHIP mix panels, wall-attach brackets All other components are COTS or modified-to-print COTS (hinges, 80/20 frame) In-house assembly of all components
Cave, RWC | Design/build subcontract with specifications supplied by ORNL
Cave, HDC | Design/build subcontract with specifications supplied by ORNL

## Slide 37: Installation Plan
Optics component | Installation Plan
Lower Beam Stop | The beam stop/ B4C sub-asm supplied by a vendor, final installation done by in-house SNS technicians
Bunker Wall Feed-Through (QIKR-L & QIKR-U) | Installed in-house by SNS technicians and SAM team
QIKR-L Background Shield Wall | Installed in-house by SNS technicians
Cave, RWC | Installed on-site by subcontractors
Cave, HDC | Installed on-site by subcontractors

## Slide 38: Costs

## Slide 39: Total Costs – Original P6 Estimate vs. Current Design
Component | Original P6 Estimate | Current Cost
Lower Beam Stop | $109,724 | $75,267
Bunker Wall Feed-Through | $318,352 | $224,828
QIKR-L Background Shield Wall | $383,424 | $50,754
Cave, RWC | $55,441* | $65,056*
Cave, HDC | $1,503,422 | $1,405,691
Year 2030 dollars
*Cost does not include installation
Includes labor costs

## Slide 40: Summary

## Slide 41: Summary
Neutronics analysis shows that the dose rates within the analyzed cave design are below the limits set in S04080400-DCD10000-R00 in most cases
  Some exceptions in certain accident scenarios… may be dealt with using radiation monitors
Design changes since neutronic analysis will need follow-up analysis prior to FDR
  Some changes are expected to be an improvement:
    Additional steel upstream of the monolith insert
    Conversion of the optics insert from two separate components to one combined assembly
    Reduction in volume of the QIKR-L cubby
  Some changes are expected to have the same shielding performance
    Guide shielding unchanged from first round of analysis
    Bunker feed-through shielding very similar to the analyzed design
  Some changes may be detrimental
    Lowering of QIKR-L roof
    Additional of cable openings in both the QIKR-U and QIKR-L roof
    Conversion of some HDC to RDC, shortening of QIKR-U RDC section

## Slide 42: Questions?