## Slide 1: QIKR Shielding PDR: Mechanical Overview
D. Wilson, Lead Engineer
March 03, 2025

## Slide 2: Outline
QIKR Overview
  Review Scope
  Documentation
  High level QIKR description
Shielding Components
  Monolith Shielding
  Optics Insert
  Guide Shielding
  Shutter
  Bunker Wall and Wall Insert Shielding
  Cave
  Beam Stop

## Slide 3: QIKR Overview

## Slide 4: Review Scope
Included
Description of model used in Neutronics Analysis (safety shielding components only)
  Monolith & guide shielding (Overview)
  Shutter beam blocker thickness
  Bunker wall shielding (Overview)
  QIKR cave (shielding functionality only, no discussion of structural design)
  In-cave beam stop
Neutronic Analysis Results
Discussion of current state of design (design evolution beyond what was analyzed)
  Changes to monolith shielding, shutter, bunker wall, cave
  Background Reduction Shield Wall
Not Included
Details of the monolith wall shielding (installation, cost, etc.)… this is part of Target design reviews
Details of the monolith optics & guide shielding… this will be part of the QIKR Optics FDR
Details of the bunker wall shielding… this will be part of the Bunker Shielding PDR
Cave structural analysis will be done at FDR & will not be discussed at PDR

## Slide 5: Requirements, CQLD, Interface, FMEA Documents
Requirements Documents:
  QIKR Instrument Requirements: S04080100-SRD10000-R02 (not released)
    The latest revision (R02) has not been released yet, awaiting optics alignment updates
CQLD Biological Radiation Shielding:
  Quality Level 2, Configuration Level 2: S04080400-QAI10000-R00 (released)
    Quality Level 2 is because of radiation safety impact of shielding failure, Configuration Level 2 is because radiation shielding is defined as a Configuration Item which requires a Level 2 rating
CQLD Non-Safety Related Shielding:
  Quality Level 3, Configuration Level 3: S04080400-QAI10001-R00 (released)
Interface Documents:
  Interface CF to Bunker wall feedthrough: S01020500-IST10023-R00 (not released)
  Interface to CF (pits in the cave): S04010100-C8U-8800-A10000 r5 (updates not released)
FMEA for Shielding: S04080400-FMA10000-R00 (not released)

## Slide 6: Requirements, CQLD, Interface, FMEA Documents
Neutronics Analysis:
  Bunker Wall, in-Bunker Guide Shielding, Shutter Beam Blocker, Monolith Wall Shielding: TBD (WIP)
  Cave, Beam Stop, In-Cave Guide Shielding: TBD (WIP)
    Cave analysis includes operating and accident scenarios using input conditions from analyses done for the upstream areas of QIKR (monolith, bunker, etc.)
    The data from this document & the one above is presented in this PDR in the Neutronics slides
QIKR Cave Acceptable Dose Rates: S04080400-DCD10000-R00 (released)
  This also defines the approved normal use and accident case scenarios

## Slide 7: STS Instrument Suite
ST01
EXPANSE
ST02
QIKR
ST03
CUPI2D
ST04
BWAVES
ST05
CHESS
ST06
Future
ST07
VERDI
ST08
PIONEER
ST09
CENTAUR
Monolith Region
South Hall
(ST01-ST09)
Target Bay
North Hall
(ST10-ST18)
Proton Beam

## Slide 8: QIKR Instrument Sections
QIKR-U
QIKR-L
Bunker
Cave
Hutch
Lintel
ST02

## Slide 9: QIKR – Schematic View
The maintenance shield does not perform a beam blocking function
The End Station consists of the Incident Table with Slits and Frame Overlap Mirror, the Sample Table, the Detector Table, and the Sample Changer
As oriented in this view, QIKR-U occupies the back half of the instrument wedge & cave, and QIKR-L occupies the front half
QIKR-U End Station
QIKR-L End Station
QIKR-U
QIKR-L
Neutrons
ST02

## Slide 10: QIKR –3D Model View
Neutrons
Maintenance Shield
Shutters
Incident Table with Slits & Frame Overlap Mirror
Sample and Detector Tables, Sample Changer
QIKR-U
QIKR-L
Once in the cave the two beam paths are shielded from each other by a central cave wall
End Station
Beam stops
Bunker wall pass-thrus & shielding
Shielded guides (both in-bunker and in-cave)
Monolith Insert
Raised QIKR-U cave floor

## Slide 11: Installation of Components
2-ton monorail in each cave for component installation, & sample environment changes
All QIKR in-bunker components will be installed by removing the bunker roof panels and using the 50-ton high bay gantry crane
Most QIKR in-cave components will be installed by bringing the components into each cave on a cart, then carrying them to their final location with a 2-ton monorail hoist
The monorail will also be used during operations to swap sample environments and to service end station components
Beam stops are hinged and swing out of the way to allow user or component access when needed

## Slide 12: Need for a QIKR-L Pit
QIKR-L requires a pit for the end station because of the downward sloping beam
The pit is two-level to allow a reasonable height for the user to stand & to wheel in equipment carts
The end station pit is combined with a cable channel to route motion cables into the upper cave (QIKR-U), then out to the control racks through the QIKR-U roof
Cable Channel from QIKR-U into QIKR-L
End station pit, allows room for a grout plate and 2” of grout for end station installation
Ramp for user and cart access
User will need to step up 6” to access the incident table

## Slide 13: Component Details – QIKR-L Shown (QIKR-U is Similar)
Cave Roof (HD)
Background Shield Wall
Exterior Cave Walls (HD)
Bunker Wall Shielding
Guide with Steel Shielding
Dividing Wall Between QIKR-U and QIKR-L
Cave Roof (RW)

## Slide 14: Component Details – QIKR-L Shown (QIKR-U Similar)
Guide narrows, steel shielding increases to fill in the space
Steel guide shielding

## Slide 15: Component Details – QIKR-L Shown (QIKR-U is Similar)
Slits (Locked in place)
Guide & Housing
Incident Table
Sample Table
Hexapod
Configuration controlled hood
Detector Arm
Location of Sample (not shown)

## Slide 16: QIKR Shielding Requirements (S04080100-SRD10000-R02)

## Slide 17: Monolith Shielding

## Slide 18
Monolith and Optics Inserts
Credit: Cameron Hart
QIKR Monolith Insert Assembly
Window
Optics Modules
Monolith Insert
Nozzle Extension
Guide Glass
Neutrons
Both upper and lower beam paths will be contained together within the monolith section. They will be installed (and can be removed) using a bunker-designed handler.
The monolith section consists of:
  One Nozzle Extension (provided by Target, vacuum env)
  One Monolith Insert, 1x (Bunker-designed, QIKR-owned, helium env)
  Two Optics inserts (QIKR-designed & owned, helium env)
Monolith insert will be removable, even after Operations begin

## Slide 19
The monolith insert has two windows to isolate the guide environment (helium) from either the target environment (vacuum) or the bunker environment (air)
The monolith insert has a center shelf to allow the lower and upper optics inserts to be separate from each other
  It was originally though that combined optics inserts would be too heavy for the bunker’s insert handler to manage
The center shelf has a downstream cutout to allow for an anti-streaming block
Shelf to separate upper and lower optics inserts
Cutout for anti-streaming block
Credit: Cameron Hart
Upstream window (aluminum)
Downstream window
(aluminum)
Monolith Insert
Small upstream anti-streaming chicane

## Slide 20
Each insert consists of four pieces: a floor, a roof, and two side walls Material = anti-corrosion coated steel, custom fabricated
  Pieces generally mate to each other along a +2.5° ramped surface except in areas where monolith insert contact pads are located
  Pieces could be split up along the z-dir to aid in fabrication, but ORNL manufacturing confirms they can handle 3.25m as a single length
The anti-streaming block compensates for having very limited space for chicane features between the monolith and optics inserts
Guide routing is constrained by available width for the optics inserts… guides cannot curve or angle in a way that causes them to be outside the optics insert boundaries
Guide support surfaces
Upper insert
Lower insert
Anti-streaming block
Downstream end
31mm
Monolith insert contact pads
64.4mm
Rectangular outer geometry, inner geometry tailored to the guide
Credit: Cameron Hart
Optics Inserts
Small upstream anti-streaming chicane

## Slide 21
Monolith/ Optics Insert Assembly
Anti-streaming block, provides more of a chicane than the 9mm step upstream
Upper Optics Insert
Lower Optics Insert
Thin sections (difficult to manufacture)
The anti-streaming chicane
9mm step each side
6mm gaps b/w optics & monolith inserts
Monolith Insert
Monolith Insert Shelf
Elevation (Side) View
Neutrons

## Slide 22
6mm gaps (red) allow neutron streaming
Monolith/ Optics Insert Streaming Paths
6mm
50.45mm
6mm
The 6mm gaps along the insert sides are long and have only a single chicane

## Slide 23
Monolith Shielding
QIKR’s segment of the monolith wall
QIKR monolith & optics inserts
QIKR-U guide glass
QIKR-L guide glass
Target’s Core Vessel, Belt Line, and Shielding
ST02 moderator location
Core Vessel
Core Vessel Shielding
Beltline

## Slide 24
Monolith Shielding – Upstream Empty Space (Vacuum)
Empty space (vacuum) upstream of the monolith insert window. No shielding.
Neutrons

## Slide 25: Guide Shielding

## Slide 26
Guide Shielding
The QIKR guides are enclosed in two-layer housings from the bunker start to the guide ends
Vacuum environment inside the housings
The outer housing layer (steel) provides the vacuum boundary
The inner housing layer is steel and provides shielding around the guide glass… 3mm gaps surrounding each layer
Shielded Guide Housings

## Slide 27
Guide Shielding
Horizontal cross-section of an in-bunker guide housing, shows change in shielding layer thickness due to guide curving/angling
Guide Glass (float glass in the bunker, borofloat glass in the cave)
Steel Shielding Layer
Stainless Steel Vacuum Jacket
Vertical cross-section of the last in-cave guide housing (QIKR-U), shows change in shielding layer thickness due to guide taper
Plan (Top) view
Elevation (Side) view

## Slide 28: Shutter

## Slide 29
The Shutter blocks the neutron beam to allow personnel access to the cave… there is one shutter per beamline (two total)
The QIKR shutter follows the standard design for failsafe operation, support structure, and control & PPS switches
  The beam blocker will drop into position to block the beam if there is a loss of power or compressed air
The composition of the beam blocker is 10cm of tungsten (upstream) followed by 1cm of boron carbide
Upper beamline (QIKR-U) Shutter
Lower beamline (QIKR-L) Shutter
Beam Blocker
Beam Open (with optional attenuation)
Beam Monitor
Downstream side (looking upstream)
Design credit: Rudy Thermer
Shutter – Description
The 10cm tungsten thickness is more conservative than required by neutronic analysis… 8.11cm is sufficient for QIKR-U, 6.52cm is sufficient for QIKR-L

## Slide 30
Shutter – Beam Blocker
12-gauge aluminum sheet metal (2 places)
1cm thick B4C
Setscrew holes to help secure the tungsten, if needed
10cm thick tungsten
Machined aluminum housing
Machined aluminum carrier plate
M6 shoulder screws (2x)
M6 socket cap screws (6x)
Beam blocker is 10cm of tungsten followed by 1cm B4C
  Produces <.25mrem/h dose rate from the blocked beam at the sample location
The tungsten and B4C are placed in a housing and secured with aluminum sheet metal end caps and (if needed) setscrews
The housing is attached to the shutter carrier plate by two brackets & M6 screws
  Top bracket is attached to carrier plate by shoulder screws to provide good vertical location
  Side bracket and housing are attached by socket cap screws
Blocker can removed/ replaced/adjusted while installed in the beamline
M3 flat head screws (8x)

## Slide 31: Bunker Wall and Feed-Through Shielding

## Slide 32
Bunker Wall & Feed-Throughs
The bunker wall contains feed-through openings to allow the guide to pass from the bunker into the cave
On either side of the feed-through, there are chicaned channels to allow cables to pass between the bunker & cave (needed for shutter and chopper power & signals)
Steel shielding is placed between the guide housing and walls of the feed-throughs
Both the steel shielding and cable channels are chicaned to minimize neutron streaming
Bunker wall feed-throughs
Cable channels
Steel shielding
Bunker Wall = 203.2cm thick HDC
353.8cm above the cylindrical moderator center (RWC above that) --HDC = High Density Concrete --RWC = Regular Weight Concrete

## Slide 33
Feed-Through Shielding & Optics
Sled / Shielding
Rails and pillow blocks (old design, see next slide)
Steel bands serve as anti-streaming features
Steel bands encircling the housings serve as anti-streaming features
Exterior of the shielding is rectangular, interior is contoured to fit the guide path
Mounting base plate is leveled with a regular weight concrete (RWC) grout layer (not shown) underneath
Housing and shielding assembly is slid into the bunker feed-through opening on rails attached to the mounting base plate
Upper beam
Lower beam
Upper beam
Lower beam
Shielding
Shielding (A36 Steel, Corrosion coated)
Credit: Art Diaz
Leveled mounting plate (yellow) with grout layer (not shown) beneath
Shielding chicanes

## Slide 34
Original (pillow block bearings and rails)
Hilman
Change in Feed-Through Rollers
Benefits of Hilman rollers:
  allow for easier rail alignment
  Less empty space, better anti-streaming
Empty space (non-shielded)
Shielded space
Rails on both sides need good alignment to each other
Only one side of the Hilman roller system provides lateral motion constraint… the two rails do not need to be tightly aligned to each other
Alignment rollers on one side only
Original Design
Neutronic Analysis Design
There are gaps, but no unobstructed streaming paths except at the Hilman roller corners (white)

## Slide 35: Cave

## Slide 36
Cave – Exterior
QIKR-U
QIKR-L
HDC
RWC
HDC
HDC
HDC
Cave dimensions and materials match those used in the neutronics analysis
Cave doors (not shown) are 70mm thick steel, PPS interlocked
600cm
2500cm to moderator
2100cm to moderator
400cm
RWC ST01-side

## Slide 37
Cave – Interior
Elevation View
Plan View
QIKR-U
QIKR-L
Bunker Wall
Shutter locations
Upper Guide
Lower Guide
Cave
Center wall is 350mm thick HDC
Outer walls are 300mm thick HDC or RWC (see previous slide)
QIKR-U has an elevated floor to hold the guide supports and end station equipment
  User will stand on the elevated floor to access the QIKR-U sample environments and end station
Space beneath the QIKR-U floor is accessible to QIKR-L for sample environment equipment (called the QIKR-L “cubby”)
Space beneath the QIKR-U on the downstream end is used for QIKR-U sample environment equipment
  Also used to route cables from both the QIKR-U and QIKR-L end stations
Personnel access to the guides upstream of both end stations is blocked by a movable but locked & configuration-controlled wall
  These walls were not part of the neutronics analysis… they play no role in radiation shielding except to create personnel-inaccessible areas where dose rates are allowed to be unlimited
Configuration-controlled walls
Cave
Elevated QIKR-U floor
Elevated QIKR-U floor

## Slide 38
Cave – Cubby spaces
Cubby spaces are both ~4ft in height
Space beneath the QIKR-U floor on the upstream end is accessible to QIKR-L for sample environment equipment (called the QIKR-L “cubby”)
Space beneath the QIKR-U on the downstream end is used for QIKR-U sample environment equipment
  Also used to route cables from both the QIKR-U and QIKR-L end stations
QIKR-U “cubby” space
QIKR-L “cubby” space

## Slide 39
Discussion of Allowable Dose Rates in the Cave
S04080400-DCD10000-R00 describes the reasonable normal operating and accident scenarios to be evaluated for the QIKR cave
Normal operating scenario:
  Slits present and open to the max values used in an experiment
  Water sample present at the sample location
Accident scenarios:
  Slits present and open to their max widths & heights
  Water sample present at the sample location
  Stainless steel sample present at the sample location
Acceptable max dose rates in the cave during both operating and accident scenarios:
  No limit inside the cave in areas where personnel cannot access
  2mrem/h in personnel-occupied spaces inside the cave
  Up to 5rem/h at the sample location within a 30cm radius of the sample
  Up to 2mrem/h outside the cave with no need for signage where personnel access is limited
  Up to 5rem/h outside the cave with radiation area signage in place

## Slide 40
Discussion of Allowable Dose Rates In & Above the Cave
Personnel-inaccessible (red)
No dose rate limits
Locked wall
Locked wall
User & staff accessible (blue)
Dose rate max =
-- 2mrem/h generally
-- 5mrem/h inside 30cm radius of the sample
Inaccessible or staff-only access (magenta)
Dose rate max =
-- 2mrem/h without need for action
-- 5mrem/h with radiation area markings
Generally-inaccessible (green)
Dose rate max = 0.25mrem/h
Cave roof = staff-only access

## Slide 41: Summary: Normal Operation
normal operation (QIKR-L active and QIKR-U active) |  |  | 
Cave | Location |  | maximum total dose rate (mrem/h)
QIKR-L | Outer wall, ST03 side | Upstream (HDC) | 0.72
 |  | Downstream (RDC) | 0.28
 | Back Wall |  | < 0.25
 | Roof | Upstream (HDC) | < 0.25
 |  | Downstream (RDC) | 0.43
QIKR-U | Outer wall, ST01 side | Upstream (HDC) | 0.64
 |  | Downstream (RDC) | 0.34
 | Back Wall |  | < 0.25
 | Roof | Upstream (HDC) | 0.31
 |  | Downstream (RDC) | 0.51
normal operation (only QIKR-U active) |  |  | 
QIKR-L | in-beam |  | 0.27
 | bisector wall (inside cave) | Upstream (HDC) | 1.02
 |  | Downstream (RDC) | 0.49
normal operation (only QIKR-L active) |  |  | 
QIKR-U | in-beam |  | 0.28
 | bisector wall (inside cave) | Upstream (HDC) | 0.71
 |  | Downstream (RDC) | 0.29
No significant elevated dose rates inside/outside the QIKR instrument cave enclosure
Data table from Kursat Bekar’s analysis
The normal operating scenarios here use slits at max aperture… more conservative than required

## Slide 42: Summary: Accident Conditions
This dose rate is in a personnel- occupied section of the QIKR-L cave & is above the allowed max of 2mrem/h, but is located high on the wall where users would not be (see next slide)
accident condition (QIKR-L normal operating and QIKR-U accident) |  |  | 
Cave | Location |  | maximum total dose
 |  |  | rate (mrem/h)
QIKR-L | Outer wall, ST03 side | Upstream (HDC) | 0.72
 |  | Downstream (RDC) | 0.31
 | Back Wall |  | < 0.25
 | Roof | Upstream (HDC) | < 0.25
 |  | Downstream (RDC) | 0.43
QIKR-U | Outer wall, ST01 side | Upstream (HDC) | 1.79
 |  | Downstream (RDC) | 0.30
 | Back Wall |  | < 0.25
 | Roof | Upstream (HDC) | 0.65
 |  | Downstream (RDC) | 0.88
accident condition (QIKR-L accident and QIKR-U normal operating) |  |  | 
QIKR-L | Outer wall, ST03 side | Upstream (HDC) | 2.70
 |  | Downstream (RDC) | < 0.25
 | Back Wall |  | 0.31
 | Roof | Upstream (HDC) | 0.38
 |  | Downstream (RDC) | 0.71
QIKR-U | Outer wall, ST01 side | Upstream (HDC) | 0.94
 |  | Downstream (RDC) | 0.34
 | Back Wall |  | < 0.25
 | Roof | Upstream (HDC) | 0.31
 |  | Downstream (RDC) | 0.51
accident condition (QIKR-L inactive and QIKR-U accident) |  |  | 
QIKR-L | in beam |  | 0.28
 | bisector wall | Upstream (HDC) | 1.01
 |  | Downstream (HDC) | 2.76
accident condition (QIKR-L accident and QIKR-U inactive) |  |  | 
QIKR-U | in beam |  | 0.27
 | bisector wall | Upstream (HDC) | 2.35
 |  | Downstream (HDC) | 0.35
Data table from Kursat Bekar’s analysis
normal
accident
This area outside the cave may need radiation area markings, depending on which beamline is on ST03. Currently, this area is blocked by CUPI2D & is inaccessible to personnel. Is it a concern for beamline cross-talk?
This dose rate is in an area inaccessible to personnel while either beamline is operating.

## Slide 43
Figure from Kursat Bekar’s analysis
Discussion of Allowable Dose Rates In & Above the Cave
Location of 2.76mrem/h dose rate in QIKR-L

## Slide 44: Beam Stop

## Slide 45
Beam Stops – Overview
QIKR-U
QIKR-L
Both QIKR-L and QIKR-U beam stops are hinged to allow easier access to the back side of the end stations when needed (expected to be infrequent)
Beam stops are manually moved and manually latched in the “open” and “closed” positions
  “closed” position is for “beam on” condition & is indicated to IPPS via magnetic sensor (two sensors for redundancy)
Hinge weight capacity: 8000lbs axial
3500lbs radial
Beam stop weight: 2860lbs
Beam stop weight: 1970lbs

## Slide 46
Beam Stop – Construction
HD Concrete 100mm thick
Steel rebar .375” diameter
~12” spacing
3 B4C Panels, 5mm thick, with 2mm thick aluminum backing
H=1450mm, W=600mm
Screwed-together steel frame with Nelson studs
Aluminum face plate, ~3mm thick
Steel block 200mm square 50mm thick
Creates a can for containing the HDC
Screwed-together steel frame construction
Aluminum face plate is screwed to the steel frame in multiple locations
Neutronics analysis model for the beam stop has the same B4C, HDC, and steel block thicknesses & HxW dimensions
Steel frame, Nelson studs, aluminum face plate, and reinforcing steel rods (rebar) are departures from the MCNP model
  Changed made to make the beam stop manufacturable
Because of concerns the HDC concrete may crack when suspended from one side by the hinges, beam stop construction may change to only B4C + steel
  Will need re-evaluation by neutronics at FD

## Slide 47: Beam Stop – QIKR-L
Beam stop is hinged to swing up against the cave wall when needed.
Steel frame contains lift attachments on the top, Nelson studs along the inside surfaces, and attachments for a latching rod and a magnetic sensor on the bottom
Hinges, Brookfield W125HD-RH (same as used for cave door)
Steel frame
Aluminum sheet face
B4C panels
Steel block
HD Concrete
Rebar
Nelson studs

## Slide 48: Beam Stop – QIKR-L
Two latching/stop blocks that stop the beam stop in the correct position (open or closed) and provide a means of latching the beam stop in place
In the closed position, there are two magnetic PPS sensors on the bottom edge, one on the back, one in the front.
  The non-wired halves of the sensors are attached on adjustable brackets on the beam stop steel frame
  The wired halves are attached to an aluminum sheet metal box, the cables run along the floor to the center cave wall
Cable cover
Non-wired magnetic sensor half
Latching rod
Sheet metal box with wired sensor half
Latching/stop blocks

## Slide 49: Beam Stops – QIKR-L
Cable cover
Magnetic sensor
Latching rod, top portion
Latching/stop block
Latching rod, bottom portion
Chamfer ramp

## Slide 50
Beam Stop – QIKR-U Safety
The upper beamline version is the same as the lower except mirrored and taller, with the stops shifted inboard
  Inward shift of the stops is because of the length of the upper floor relative to the length of the beam stop
  Additional vertical length is because of the upward angle of the beam that shifts the beam stop upward away from the floor
The sensor is shifted inboard as well here, but could actually be shifted outward to the free end of the beam stop
The section of railing behind the beam stop would be lifted and rotated out when the beam stop is swung open… can be rotated back into place once the beam stop is open (railing = 37lbs)
Railing weight = 37lbs
Railing closed
Railing open

## Slide 51: Questions?