## Slide 1: Vessel Systems and Target Station Shielding Preliminary Design
Chris Anton
Cam Eiland
Hogan Knott
Darren Dugan
Mike Strong
April 21, 2025

## Slide 2: S.03.06 Vessel Systems and S.03.07 Target Station Shielding
Vessel Systems
Target Station Shielding

## Slide 3: Vessel Systems Scope
Core Vessel Shielding Assembly
Gamma Gate Assembly
Nozzle Extension Assemblies
Core Vessel Assembly

## Slide 4: Core Vessel Assembly
CV Lower Weldment
CV Primary Lid
MRA Access Hatch
Target Segment
Access Hatch
CV Upper Weldment
CV Lid Tent
Utility Hatch
Utility Hatch

## Slide 5: Core Vessel Lower Weldment Details
CV Center Split Flange
CV Bottom Plate
CV Skirt
CV Bottom Flange
CV Beltline
CV Drain
Lower Weldment Lower Shell
Lower Weldment Upper Shell
Key Features:
Contain CV environment (vacuum or helium)
Support internal shielding and technical components
Leak collection and draining
Allow passing of proton beam
Support and alignment of monolith inserts containing guide optics
Minimal thermal deflection due to beam operation required to maintain guide optic alignment
Design for manufacturability to reduce procurement cost and schedule

## Slide 6: Core Vessel Lower Weldment Details
100 mm thick flange bolts to CV Baseplate
Alignment Notches set orientation of CV in monolith
Clearance holes allow for CV fine alignment
Core Vessel drain hole
100 mm thick rolled and welded shell
Weight of internal shielding supported here
Drainage grooves
Sits below tan skirt shelf
25 mm rolled and welded vacuum shell
Laminated east and west beltline quadrants
Proton Beam Clearance Opening
PBW Sealing Interface
Dual Channel and QIKR nozzle extensions weld to ID of beltline
Monolith insert alignment shim mounting holes
Flood cooled north and south beltline quadrants
25 mm rolled and welded vacuum shell
CV Split Flange with weld prep and o-ring groove

## Slide 7: Core Vessel Beltline Details
Forged cooling block design
Laminated cooling block design
Pros
Much less welding
  Less weld distortion
  Less post-weld machining
  Greater reliability
Greater flexibility in cooling designs
Cons
Raw material cost is higher
Limited suppliers for large forgings
Pros
316 plates are easy to source
Cons
Complex welding required
Extensive post-weld machining
Reduced reliability

## Slide 8: Core Vessel Upper Weldment Details
Thick top flange to reduce vacuum induced deflections
CV Split Flange allows for factory leak testing, installation via high bay crane, and welded final seal
Steps in sidewall to reduce radiation shine
Top step allows for utility lines to clear shield blocks during vertical removal
Utility nozzles accommodate water cooling, helium filling and sensor passthroughs
Key Characteristics:
Contain CV environment (vacuum or helium)
Minimize radiation shine up CV side walls
Leak collection and draining
Minimal thermal deflection due to beam operation required to maintain target alignment
Design for manufacturability to reduce procurement cost and schedule
Accommodate all utility feedthroughs with spares for flexibility during operational life

## Slide 9: Core Vessel Lid Assembly Details
MRA Hatch
Utility Hatch
Primary Lid
Lid Tent
Target Hatch
Utility Hatch
Key Characteristics:
Contain CV environment (vacuum or helium)
Support target assembly mass
Minimize all target flange deflections
Design for manufacturability to reduce procurement cost and schedule
Enable MRA, Target segment and TVP removal
Provide access to CV interior utility connections

## Slide 10: Core Vessel Primary Lid Details
TVP, tent and hatch covers with bolt patterns and sealing surfaces
Stiffening ribs to reduce lid deflections under gravitational and vacuum loading

## Slide 11: Core Vessel Lid Tent Details
Stiffening ribs to reduce lid deflections under gravitational and vacuum loading
Target outrigger supports
Target Assembly mounting flange
Target segment removal hatch
MRA removal hatch
***Tent is captured by the target shaft

## Slide 12: Core Vessel Lid Hatch Details
MRA Access Hatch
Target Segment Access Hatch
Utility Hatches
Stiffening ribs to resist vacuum induced deflections

## Slide 13: Core Vessel Shielding
Target Segment
Removable Shield
Block
Layer 4 Uncooled
Shielding
Lower Ring
Uncooled Shielding
MRA Removable
Shield Block
Upper Ring Uncooled Shielding
Layer 1 Cooled Shielding
Layer 5 Uncooled Shielding
MRA Utility Line
Shielding
Key Characteristics:
Provide radiation shielding
Minimize thermal deflection of surfaces interfacing with technical components
Allow for vertical extraction of the target segments, MRA and TVP
Allow for vertical extraction of target shaft
Minimize radiation streaming
Protect the MRA hydrogen lines from physical damage
Provide clear neutron flight paths between MRA and guide optics
Provide clear proton flight path
Restrain target during seismic event
Support and align MRA

## Slide 14: CV Shield Block #1 Details
Previous laminated plate design
Current gun drilled forged design
Gun-drilled vertical cooling holes
Water plenums
Current design is transitioning from stacked plate design to machine forging design
  Superior pressure-bearing performance
  Significantly less welding
MRA supported off of this shield block

## Slide 15: CV Cooled Shield Block Layer 2 Details
Current design is transitioning from stacked plate design to machine forging design
  Superior pressure-bearing performance
  Significantly less welding
Target snubber ring mounted to these shield blocks
Lower neutron beams (6x total) pass through these shield blocks
High heat loads require complex cooling scheme
Target wheel cutout
Neutron beam clearance
MRA Cutout

## Slide 16: CV Cooled Shield Block Layer 3 Details
Uncooled carbon steel
Cooled stainless steel
Current design is transitioning from stacked plate design to machine forging design
Development of layer 3 shielding has intentionally lagged behind layer 2 due to their similar thermal profiles
Target and MRA are surrounded by these shield blocks
Upper neutron beams (12x total) pass through these shield blocks
High heat loads require complex cooling scheme
TVP clearance notch
MRA clearance
Target clearance
Neutron beam clearance

## Slide 17: CV Lower Ring Shielding Details
Utility line galleries
Monolith Insert clearance holes
Carbon steel ring shields serve two primary purposes:
  Facilitate extraction of a fully populated target assembly that is unable to rotate
  Reduce the volume of cooled shielding, reducing CV shielding costs

## Slide 18: CV Upper Ring Shielding Details
Carbon steel ring shields serve two primary purposes:
  Facilitate extraction of a fully populated target assembly that is unable to rotate
  Reduce the volume of cooled shielding, reducing CV shielding costs
Utility line galleries
Monolith Insert clearance holes
QIKR neutron beam clearance

## Slide 19: CV Layer 4 Shielding Details
Utility line galleries
TVP clearance
MRA clearance
Target shaft clearance

## Slide 20: CV Layer 5 Shielding Details
Utility line galleries
TVP clearance
MRA clearance
Target shaft clearance
Target segment clearance

## Slide 21: CV Removable Shielding Details
MRA removable shield block
Target segment removable shield block

## Slide 22: CV MRA Utility Shielding Details
MRA utility line shine shield
Hydrogen transfer line shine shield

## Slide 23: Core Vessel Shielding Restraint System

## Slide 24: Standard Nozzle Extension Assembly Details
Lower Bracket Assembly
Upper Bracket Assembly
Transition Flange
12’’ Sq Tubing
10’’ Sq. Tubing
Rear Flange
Mounting Bars

## Slide 25: QIKR Nozzle Extension Assembly Details
Round Nose
Front Flange
Small Boxed
Section
Large Boxed
Section
Rear Flange
Transition Flange
Screw Caps
(welded)
Seal Welds
Welded to CV
Inside Diameter

## Slide 26: Dual Channel Nozzle Extension Assembly Details
Dual Channel Nozzle Extension
Bracket Assemblies
Round Nose
Front Flange
Small Boxed
Section
Large Boxed
Section
Rear Flange
Transition Flange
Welded to CV
Inside Diameter
Mounting
Bar

## Slide 27: Nozzle Extension Seal Welds and Monolith Insert shims
Seal Weld to ID
Seal Weld
Monolith Insert
Shims

## Slide 28: MRA Utility Jumpers
Connect MRA flanged connections to corresponding flanged connections on CV side walls
Each line will include a flex line portion
Flex lines allow for MRA connections to be broken and the jumper lines moved during MRA removal and installation

## Slide 29: Gamma Gate Assembly
Actuator Arm
Lead filled stainless steel
Rail Mounts
Linear Rails
Locking Pins
Rollers
The gamma gate provides radiation protection during target maintenance activities
Remote actuation is required
Facilitates hands-on target maintenance

## Slide 30
Pipe Pan
Removable Shielding
PBW Removable Shield
PBW Shielding
Removable Shield
PBTA Remote Clamp
Removable Shield
Layer 2
Bulk shielding
Layer 1
Bulk shielding
Layer 3
Bulk shielding
Layer 4
Bulk shielding
Layer 5
Bulk shielding
Layer 6
Bulk shielding
Target Station Shielding Scope
Pipe Pan

## Slide 31: Bulk Shielding Scope
Layer 2
Bulk shielding
Nozzle extension
clearance ports
Layer 1
Bulk shielding
Layer 3
Bulk shielding
Layer 4
Bulk shielding
Layer 5
Bulk shielding
Layer 6
Bulk shielding

## Slide 32: Core Vessel Baseplate Details
Grout Holes
CV Mounting Holes
Water drain grooves
TSS Mounting Holes
CV Baseplate Anchors
Water Drain Port
Leveling Assembly
Welded Covers Over CV Baseplate Anchors

## Slide 33: Bulk Shielding Liner Details
Grout Holes
PBW Bump-Out
Bulk Shielding Liner
Anchor Holes
TSS Mounting Holes
Bulk Shielding Liner Anchors
Leveling Pucks

## Slide 34: Bulk Shielding Layer 1 Details
CV Drain Pipe Clearance Channel
PBW Alignment Plate
Clearance
Leveling Pucks
Nozzle Extension
Bracket Notch
Anchor Tie Rods
4x Shield Blocks
Under CV
Anchor Tie Rods

## Slide 35: Bulk Shielding Layer 2 Details
Bolt to the next layer of shield block
L shaped blocks are slid underneath each installed nozzle extension

## Slide 36: Bulk Shielding Layer 3 Details

## Slide 37: Bulk Shielding Layer 4 Details

## Slide 38: Bulk Shielding Layer 5 Details

## Slide 39: Bulk Shielding Layer 6 Details
Forms support for removable shield plates above pipe pans

## Slide 40: Pipe Pan Details

## Slide 41: Pipe Pan Removable Shielding Details

## Slide 42: AIC Removable Shielding Details
PBTA Clamp
Shield Block
PBW Shield
Block
PBW Shielding
Shield Block

## Slide 43: BACKUP SLIDES

## Slide 44: BACKUP SLIDES

## Slide 45: BACKUP SLIDES

## Slide 46: BACKUP SLIDES

## Slide 47: BACKUP SLIDES