## Slide 1: Reflectometry Software
Bogdan Vacaliuc
Reflectometry Group, LSS Section
Neutron Scattering Division
Reflectometry - Instrument Review, NSD ORNL, Oak Ridge, TN 10 February 2026 V1.1

## Slide 2: How this talk is organized.
Aim: Answer specific questions regarding software development process and provide details on future development.
Notes: Charge questions.
Stock image

## Slide 3: Overview
Recap: Experiment Process thru Analysis
  Planning, Experiment, Reduction, Analysis, Insight
“Be a Defect, be a Story…”
  How the reduction software development lifecycle operates
“Be a Bug, be a Feature…”
  How data acquisition software development works
Challenges
Future Development

## Slide 4: Recap: Experiment Process thru Analysis
Idea
Proposal
Pre-Experiment
Experiment/Data Collection
Analysis
Paper
Reduction
Notes: Some software out of scope (make the picture gray for out-of-scope SW)
Software hits all these places, bits we will talk about are analysis and reduction and data collection sw
Ideal: doing analysis while still doing the experiment, feedback on what sample is doing, you can optimize your experiment (part of what AI/automation is trying to achieve)
Also while live reduction is so valuable

## Slide 5: Be a Defect …, Be a Story… [Reduction Software Dev]
Reduction software is maintained and supported by a dedicated team of software engineers
13 + 1 mgr / 32 inst
Point of Contact:
  Focus Team Leads
30min meetings daily
2 week “iterations” – periods of work that is pre-planned, then evaluated in a retrospective held on Wednesday mornings
Notes: Addi requested removal of org chart, and clarified that only 13 persons are working on reduction software not 17.

## Slide 6: Be a Defect …, Be a Story… [“The Process”]
Notes: Add stick figures (as animation?) to show progress in how each step of the process needs people to “move it along…”

## Slide 7: Be a Defect …, Be a Story… [”The Backlog”]
As of Jan 15, 2026
8 Capabilities/”EPIC”
  Those features that require multiple “Stories”
24 Defects (3 critical, 10 high, 6 in-testing)
46 Stories (17 high, 8 in-development, 11 in-testing)
Average completion time of any Defect/Story is ~40days
  (from a compilation of data spanning activity back to 2023)
At current metrics, 24*46*40 = 2800 days of activity (+10yrs)
(*) As a reference: SANS reduction software development was allotted 20FTE
Notes: Slide 28-29 have alternate views where Accumulated is divided by number of tickets to record mean defect/story/task completion rate.

## Slide 8: Be a Defect …, Be a Story… [”A New Hope”]
The software engineering group is going to revise this process over the next 18-24 months*
  Doing research, accepting feedback now
  Considering the open-source development model more closely
Reviewing for the next development thrust project now
(*) communicated to the CIS weekly meeting on Feb 6, 2026
Notes: Notes on “Fair Use” and the reference to Star Wars (copyright Lucasfilm) in the graphic. Parody acceptable [1], “using a book as a prop in a stage performance” favors fair use [2] and the many derivative works that were acceptable to Lucasfilm [3]. Fair use definition in US Copyright Law [4]
[1] https://www.kleinlitigation.com/that-one-time-when-lucasfilm-sued-president-reagans-star-wars-program/
[2] https://guides.nyu.edu/fairuse#:~:text=What%20is%20Fair%20Use?,use%20falls%20under%20fair%20use.
[3] https://blogs.library.unt.edu/copyright/2018/03/02/star-wars-the-copyright-question/
[4] https://www.copyright.gov/fair-use/

## Slide 9: Be a Bug …, Be a Feature… [Data AcQuisition Side]
Instrument software and hardware are maintained and supported by three dedicated teams of engineers
25 + 3 mgr / 32 inst
60 min weekly “On Call Support”
Continuous Presence*
Notes: * Bogdan is a former member, and the arrangement now is that he be primary POC for the two reflectometry instruments

## Slide 10: Be a Bug…, Be a Feature [“The Process”]
Urgent
  Call IHC*: DAQ on-call triages, identifies subject-matter expert who can help
Non-Urgent
  Email support during business hours
New Capability
  Use the “Redmine” System for project management
(*) Instrument Hall Coordinator (IHC) – 24hr on-site personnel for immediate response and coordination ~ 911 for the facility
Notes: This is the official guidance – consider putting this into a picture slide, keep bullets simple. Key is 3 routes: urgent, non-urgent, new capability important takeaway is that there are different routes
Concern :top half – rapid response. Bottom half not so much but you can get things done

## Slide 11: Be a Bug…, Be a Feature [The “Redmine” System]
Triage with SA GLs every two weeks
Priority-based tasking
Subject-Matter-Expert-based assignments
Heroic Efforts are Common!
Notes: Often a target date for the experiment and proximity to the required date are required to obtain attention

## Slide 12: Be a Bug…, Be a Feature [Parting Thoughts]
IHC have visibility into control system
Problems are triaged by DAQ on-call
DAQ personnel are empowered to resolve issues
Process is setup to optimize for problem solving over long-term development

## Slide 13: Challenges: REF_L Keyence Rangefinder Integration
Laser Rangefinder to determine liquid surface
2025-06-06 Project Entered
2025-09-25 Discussion
  Experiment Date assigned
  Developer assigned
2025-10-09 In Test
2025-10-15 In Use
2025-10-17 Completed
Notes: Example of a challenge that ended in a success and achievement
Some challenges arose in testing due to behavioral discrepancy just prior to use. They got sorted out and it’s was a successful integration! Total development time recorded: 22hrs

## Slide 14: Challenges: REF_M reproducibility (pol/non-pol)
Motion Control Electronics (MCE) Refresh at REF_M
  Solve instrument configuration repeatability issue
    Problem: switching from polarized to unpolarized mode requires 1-2 days of instrument re-alignment due to non-repeatability, aging control hardware*
    Control system struggles with coordinated movements at this scale…
    Progress: refresh of MCE, careful reprogramming and extensive repeatability tests
(*) True nature of the root cause is currently under investigation as part of the MCE electronics refresh
Notes: Example of more complex DAQ-side challenge
Instrument team records that the reproducibility became an issue in 2017 following the control system conversion…

## Slide 15: Challenges: Reduction
Instrument staff is heavily involved in reduction
  Generally, reduction is complete by the end of the experiment
Partial reduction with instrument staff support is enough to guide the experiment along
Goal: reduction step to be seamless
  high throughput, no problems in reduction
  reduced data is available continuously and correct
Notes: Key points: often its IS that is heavily involved in reduction process. Also who is doing it and how long it is taking. Positive: what our plan is. We have a plan, bigger picture of why we need to solve the problem
There are several cases where we are doing the loop – not really the data we will act upon, but its close enough to guide us (better confidence)
Whole theme about the loop (if that loop is seamless – instrument running fast, high throughput, no problems in that loop, must be flawless – then the AI can accelerate it…)
Scientist is an educator – teaching the technique, but hampered by issues in the reduction codes. 1st intro in person is much better than in teams later
If were really next on the list – talk about possibility of a requirements document to get that level of support from the software engineers. This gives the team a lot of hope. We want the review committee to latch on and tell them “you have to invest in this”…

## Slide 16: Challenges: Cybersecurity patching causes glitches
Cybersecurity requires monthly updates
  Frequent [documented] breakage that requires efforts on the part of instrument staff
  Our software is too fragile to cope with this condition at the moment
Solution: verify proposed patches in advance of deployment
  Patching of development DAQ machines occurs 1 week in advance of deployment
  Data acquisition and Reduction software need automated validation testing on these systems
Progress: Virtual Twin, Automated reduction and comparison with “golden” datasets
Notes: Stock image(s)
There is some “friction” with the current Redhat Support Model: we do not pay for workstation licenses, so we are not entitled to our own patch schedule – the patching process gets “whatever” the RedHat versions are on the date/time of the patch operation. Discussions with the Linux team have indicated that there are options, but they require more $$$ or complex configurations to achieve.

## Slide 17: Near term Future Development: REF_L DAQ
Integrating “2D” Detector operation into UI
  Standalone python scripting in regular use for 2 cycles
  Cd filters for direct beam attenuation (commissioning in 2026A)
  Beam footprint calculator
  New alignment method (chi motor, solid theta motor alignment, …)
Notes: Erik left a thread – here is where we are in the technique – demonstrated that, now 2yrs and are going to be integrating these tools in to roll out to users.
Started from nice workflows and tools and a good user experience. Now the focus is to get these new flexibilities are integrated into a nice workflow again (see upper right plot)

## Slide 18: Mid term Future Development
Improve live data reduction
Eliminate elements that make the software fragile
  Complex configuration files
  Complex pre-existing/assumed values
Improved testing of reduction codes
  daily automated reduction that compares outputs of deployed codes with established known-good
Notes: Important part of this is that it’s about improving the live data reduction. Step back from the details and think at long term levels. Keep going back to the feedback loop motif.

## Slide 19: Laboratory Directed Research and Development
“Materials by Design”
  Predictive Theory
  Autonomous Synthesis
  Multimodal Characterization
  Agentic AI determines next steps based on results
Molecular Beam Epitaxy
Angle Resolved Photoemission Spectroscopy
X-Ray Diffraction
Polarized Neutron Scattering
Validation
Notes: Every software part of this system is generated with AI assistance: the control of the MBE are all Raspberry-PI components with digital/analog conversion hats and control software written in conjunction with ChatGPT.
It is a requirement of the project to use AI assistance in developing the codes used.
TODO: add feedback (vacuum) and theory inform loops (make it clear not in tight loop). Part is to verify theory of distribution of magnetism of thin film
Image credits: Bogdan Vacaliuc (photos), Intersect presentations,

## Slide 20: Research / Development Plan
Agent AI augmented software development
Successful Examples
  Movie generator for scattering with T dependency
  Refactoring of control interface for RHEED* device
  QuickNXSv1 adaptation
  Solve constraint layer modeling in Refl1d
(*) Reflected High Energy Electron Diffraction
Notes: go/no-go decision on QuickNXSv1 adaptation once this pilot project results are demonstrated
Put movie into extra slides
Image Credit: https://deanhallpass.wordpress.com/2013/08/29/hello-computer/ (scotty), Copyright Paramount Pictures, acceptable under fair use principles

## Slide 21: Summary
Reflectometry software has a vision
Improving Reduction is central
Investment at ~20FTE is requested
Notes: Does agent AI live up to promise of 5x productivity gain? Still need 4FTE in that case…
Do we hope to get half of what we ask: 10FTE (2 FTE+agent AI)?

## Slide 22
Acknowledgements
DAQ Hardware & Firmware: B. Avery, M. Bobrek, O. Fajardo-Osorio, S. Giles, P. Hansen, M. Harrington, H. Harvey, S. Hicks, C. Ndo, S. Wall
Detector Hardware & Firmware: J. Beal, V. Sedov
Mechanical: C. Sabens
This manuscript has been authored by UT-Battelle, LLC, under contract DE-AC05-00OR22725 with the US Department of Energy (DOE). The US government retains and the publisher, by accepting the article for publication, acknowledges that the US government retains a nonexclusive, paid-up, irrevocable, worldwide license to publish or reproduce the published form of this manuscript, or allow others to do so, for US government purposes. DOE will provide public access to these results of federally sponsored research in accordance with the DOE Public Access Plan (https://www.energy.gov/doe-public-access-plan).
Software: X. Geng, K. Gofron, R. Gregory, G. Guyotte, J. Kohl, B. Krishna, M. Ruiz-Rodriguez, A. Sobhani, G. Taufer, Z. Thurman, K. Vodopivec, M. Waddel
Computing aka Linux Team: M. Bedynek, B. Conway, R. Crompton, J. Hale
Computational: M. Doucet, M. Guthrie, A. Hicks, M. McDonnel
Scientific: R. Anderson, T. Charlton, G. Ehlers, E. Watkins
Notes: From the 2024 November Friday Forum.
Added key CIS folks now as well.
Image Credit: Bogdan Vacaliuc, personal archive

## Slide 23: Supplementary slides

## Slide 24: Overall Software Architecture
Beam line Workstations
Sample Environment,
Beam Line Equipment
Detector
NeXus
EPICS IOCs
Scan Server
nED
Streaming Translation Client
ADARA
EPICS
Mantid
CS-Studio
MantidPlot
Streaming Message Service
PVStreamer
ADnED Neutron Statistics
Service
Mantid
Framework
w/AutoReduction
Mantid (Neutron data analysis software)
HDF5 file with standard structure for neutron data.
Credit: Matt Pearson
Notes: From the 2024 November Friday Forum.
This slide to be adjusted to describe {lr,mr}_reduction, quicknxs and refred

## Slide 25: Remote experiments successfully deployed on all beamlines
Accomplishment
  Directorate goal achieved: remote experiments deployed on all beamlines in the user program
Significance
  Allows external users to control experiment as if they were at the beamline
  Instrument Teams control access in real time with EPICS IOC tools
  EPICS infrastructure installed on SpICE instruments, enables hybrid EPICS/SpICE functionality
Credit: Harley Skorpenske, Janell Thompson, Klemen Vodopivec, Jaimie Werner and David Cashion
Notes: From the 2024 November Friday Forum
Developed during the pandemic years 2020-2021
Call out: flexibility to local users to not have to spend night at the beamline, increase size of experiment team [sentence or two]
Mention how many people in directorate participated to make this possible: user management, training, sample handling. Very much a whole-facility effort.

## Slide 26: AI/ML closed loop experiment steering framework developed
External Instrument Control (EIC) enables automated control of experiments from a location beyond the extent of the instrument’s own network
Authenticated
Observable
Enables streamlined Advanced Computing collaboration
Credit: Ray Gregory, Jean-Christophe Bilheux
Notes: From the 2024 November Friday Forum.
Built upon the implementations of ScanTools, EPICS, and the core instrument control system architecture at SNS+HFIR
Allows for *SAFE* manipulation of the instrument control system by arbitrary software *OUTSIDE* the beamline control system using a series of indirect operations. Changes to the ICS are "suggestions" that can be acted upon by automation processes withing the beamline control system that determine if the changes are a) safe, b) appropriate, c) authorized.

## Slide 27
ADARA
Data Fiber (2.125Gbps)
Network Fiber (25-100Gbps)
Network Cat5 (1-10Gbps)
PCIe over Fiber (2.5Gbps)
CTRL/
STATUS
PCIe
A30X
Converged
Accelerator
BLxx-ai1
EPICS PVs
Instrument Position Feedback
(drive experiment autonomously)
Modular DSP
STC
Analysis
PCIe
PCIe
DPU Card
(2 port)
PCIe
OCP3.0
DPU Card
(2 port)
nED
SMS
BLxx-daq1
Switched Network
DETECTOR
Side-by-side comparison with
modeled behavior and
immediate refinement
Direct visualization of
Sample behavior in scientific coordinates
Xiaojian Bai, Et. Al.,"Hybridized quadrupolar excitations in the spin-anisotropic frustrated magnet FeI2", Nature Physics Letters 17, April 2021
https://neutrons.ornl.gov/content/neutrons-piece-together-40-year-puzzle-behind-iron-iodide%E2%80%99s-mysterious-magnetism
10-year Plan
Alternate Ecosystems for DPU/Accelerator
(selection to be determined, pros/cons defined)
Notes: From the 2024 November Friday Forum.
Didn’t get adapted for reflectivity analysis and detector (but gives an idea of what it could be…)
Desire to show hardware-assisted reduction, analysis and feedback operating *at the beamline* vs. the development of federated and cross-facility efforts also described.

## Slide 28: Be a Defect …, Be a Story… [”Data of The Backlog #1”]
The composite of Defect + Story + Task = Accumulated Time
For the defects/stories completed in the period, this is the accumulated time in each process step.
Notes: Need to add slides

## Slide 29: Be a Defect …, Be a Story… [” Data of The Backlog #2”]
Tyipcal Defect/Story Completion delay approx. 40 days
Divide total accumulated time by the total number of defects/stories/tasks that completed in that interval
Notes: Slide 23 has an alternate view where Accumulated is divided by number of tickets to record mean defect/story/task completion rate.
For periods 3, 6, 9 only defects and stories were sampled (future automation is pending, the graph may be fully rendered by the time of the review…)

## Slide 30: Event Movie

## Slide 31: LR Analysis Tools
refl1d
  Brian Benjamin Maranville, et al. Reflectometry/refl1d: V1.0.1a1. v1.0.1a1, Zenodo, 19 Nov. 2025, doi:10.5281/zenodo.17651288
  Integrated with experiment file system and reduced data files produced by both ‘quicknxs’ and ‘refred’
genx
  A. Glavic and M. Björck, “GenX 3: the latest generation of an established tool”, J. Appl. Cryst. (2022). 55, 1063-1071, doi:10.1107/S1600576722006653
BornAgain
  Pospelov, Gennady et al. “BornAgain: software for simulating and fitting grazing-incidence small-angle scattering.” J. Appl. Cryst. (2020). 53,Pt 1 262-276, doi:10.1107/S1600576719016789
Notes: G.L Payne, P.L. Von Behren, “Fortran program to calculate finite-range no-recoil DWBA transfer cross sections
“, Computer Physics Communications
Volume 7, Issue 1, January 1974, Pages 13-37, available=http://doi.org/10.1016/0010-4655(74)90054-x, https://elsevier.digitalcommonsdata.com/datasets/y2848yskcp/1