## Slide 1: MARS Imaging Instrument Suite Review from 2020 to 2025
February 3-4, 2026
Yuxuan Zhang, on behalf of the neutron imaging team
Notes: Accessing Title Slide Options The standard ORNL presentation template includes five branded title slide layouts:
  Title | Standard. The preferred layout for lab-wide and general presentations. Features a default aerial photograph of the lab.
  Title | Custom Image. Allows replacement of the default background with a custom full-slide image (16:9 or 4:3 landscape format).
  Title | Custom Portrait Image. Supports inclusion of a custom 4:3 portrait image positioned next to the introductory text.
  Title | Custom Landscape Image. Supports inclusion of a custom 16:9 landscape image positioned next to the introductory text.
  Title | Text Only. Offers additional space for longer titles and multiple presenters.
Additional Lab-approved title slides specific to directorates and user facilities are available in PowerPoint under the following folders: Custom Title Slides and User Facility Templates, located in Presentation Templates.
Custom Title Slide Guidelines
  Image Rights. Any custom images, graphics, or photography must be owned by ORNL or used with documented permission from the original creator or source.
  Appropriate Image Use. Select images that work well with the layout. Ensure the focal point of the image is not obscured by the title text and white overlay box.
  Relevance and Impact. Visuals are a key element of effective communication. Whenever possible, use imagery that enhances the message of your presentation and reflects ORNL’s mission and values.
  Quality and Clarity. Use high-resolution images for clarity on large screens. Avoid overly complex or dark images that may conflict with the title text.
  Text-Only Option. If no appropriate or approved imagery is available, or if imagery is not permitted for the subject matter, the Title | Text Only layout provides a clean, professional alternative.
Learn more about ORNL presentations
  https://ornl.sharepoint.com/sites/branding/SitePages/presentations.aspx

## Slide 2: The MARS User Support Core Team (2020-2025)
Yuxuan Zhang
Instrument Scientist
James Torres
Instrument Scientist
Jean Bilheux
Computational Instrument Scientist
Roger Hobbs
Scientific Associate
Since 2023.7
Since 2024.2
Erik Stringfellow
Scientific Associate
 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Yuxuan (IS) | 1 FTE | 1 FTE | 1 FTE | 1 FTE | 1 FTE | 1 FTE
Erik (SA) | 1 FTE | 1 FTE | 1 FTE | 1 FTE | .5 FTE | 
Jean (CIS) | .5 FTE | .5 FTE | .5 FTE | .5 FTE | <.5 FTE | <.5 FTE
Chen (CS) |  | .4 FTE | .4 FTE | .4 FTE | .4 FTE | .4 FTE
James (IS) |  |  |  | 1 FTE | 1 FTE | 1 FTE
Roger (SA) |  |  |  |  | .5 FTE | 1 FTE
Total | 2.5 FTE | 2.9 FTE | 2.9 FTE | 3.9 FTE | 3.9 FTE | 3.9 FTE
2019-2024
Since 2019.3
Chen Zhang
Computational Scientist
Since 2021.6
Notes: This research used resources at the High Flux Isotope Reactor and Spallation Neutron Source, a DOE Office of Science User Facility operated by the
Oak Ridge National Laboratory. This work is based upon research sponsored by the Laboratory Directed Research and Development Program of Oak Ridge National Laboratory, managed by UT-Battelle LLC for the US Department of Energy.

## Slide 3: The MARS User Support Core Team (2026)
Saurabh Kabra
Instrument Scientist
 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Yuxuan (IS) | 1 FTE | 1 FTE | 1 FTE | 1 FTE | 1 FTE | 1 FTE | .5 FTE
Saurabh (IS) |  |  |  |  |  |  | .5 FTE
Erik (SA) | 1 FTE | 1 FTE | 1 FTE | 1 FTE | .5 FTE |  | 
Jean (CIS) | .5 FTE | .5 FTE | .5 FTE | .5 FTE | <.5 FTE | <.5 FTE | .5 FTE
Chen (CS) |  | .4 FTE | .4 FTE | .4 FTE | .4 FTE | .4 FTE | .4 FTE
James (IS) |  |  |  | 1 FTE | 1 FTE | 1 FTE | 1 FTE
Roger (SA) |  |  |  |  | .5 FTE | 1 FTE | 1 FTE
Total | 2.5 FTE | 2.9 FTE | 2.9 FTE | 3.9 FTE | 3.9 FTE | 3.9 FTE | 3.9 FTE
2026.2
Yuxuan Zhang
Instrument Scientist
James Torres
Instrument Scientist
Jean Bilheux
Computational Instrument Scientist
Roger Hobbs
Scientific Associate
Since 2023.7
Since 2024.2
Since 2019.3
Chen Zhang
Computational Scientist
Since 2021.6
Notes: This research used resources at the High Flux Isotope Reactor and Spallation Neutron Source, a DOE Office of Science User Facility operated by the
Oak Ridge National Laboratory. This work is based upon research sponsored by the Laboratory Directed Research and Development Program of Oak Ridge National Laboratory, managed by UT-Battelle LLC for the US Department of Energy.

## Slide 4: The Multimodal Advanced Radiography Station

## Slide 5: Oversubscription rate, average ≈ 2.96
The lowest score was 3.5

## Slide 6: Research diversity at MARS

## Slide 7: Since FY20, MARS users = 12-16% of HFIR users

## Slide 8: Sample environments
Current
Custom user-supplied equipment
  Chiller and shielding (polarization)
  Concrete freezing stage
  H2 pressure cell
  Fuel cells
  Molten salt furnace
  TGA
  Battery cells
Biologic potentiostat
Shared SE
  Pressure (EAP) cells
  IR lamps
  Hot-A vacuum furnace
  Polarization (supermirror polarizer and 3He analyzer)
Amteco furnace: Molten salts
Plant growth chamber
Future
Expanded-cavity for Amteco furnace for larger samples
Replace aging plant growth chamber
Mechanical load frame(s)

## Slide 9: MARS Highlights

## Slide 10: Effort in improving spatial resolution since 2021 (supported by instrument M&S)
25 μm setup
7 um
Routine setup
(before upgrade)
High-res setups with achievable resolution of 7, 15 and 25 μm are routinely available

## Slide 11: Upgrade of detector gantry and sample table (May 21, 2024)
Detector x 3
New Sample Table
(XYZ)
z
y
x
Detector
Sample Table
(XYZ)
z
y
x
Travel:
x: 400 mm
y: 50 mm
z: 200 mm
Travel:
x: 400 mm
y: 230 mm
z: 300 mm
Max. load capacity: 200 kg
Notes: Note: this new table has vastly increased the space underneath the detector, allowing for larger and/or more complex materials to be placed against the detector

## Slide 12: Multiple imaging detector systems tailored for different needs (at the downstream main sample pos.)
1
2
3
5
future

## Slide 13: Upstream sample pos. also has a dedicated detector for high-speed imaging
High-speed imaging of molten salt dynamics at the upstream sample pos.
Steel
container
1st melt
Gas bubbling
70 Hz
700 °C
70 Hz
500 °C
4
Upstream sample position for higher flux
Imaging furnace

## Slide 14: Development of neutron grating interferometry (nGI) (supported by division mid-scale investment)
G1
G2 & G2
Imaging Detector
Source
Sample
Flight tube #1
Flight tube #2
G1
G0 & G0
Symm. and Asymm. nGI setup

## Slide 15: Demonstration using suspended nano PMMA spheres
Chart: Autocorrelation length (nm)
| 44 | 66 | 88 | 110 | 132 | 154 | 176 | 198 | 220 | 242 | 264 | 286 | 308 | 330 | 352 | 374 | 396 | 418 | 440 | 462 | 484 | 506 | 528 | 550 | 572 | 594 | 616 | 638 | 660 | 682 | 704 | 726 | 748 | 770 | 792
ROI#1 | 0.65847 | 0.56998 | 0.51113 | 0.4862 | 0.48174 | 0.48608 | 0.50542 | 0.52067 | 0.51835 | 0.52563 | 0.51643 | 0.51787 | 0.51538 | 0.51438 | 0.51608 | 0.51698 | 0.51821 | 0.52778 | 0.53 | 0.52567 | 0.5254 | 0.52502 | 0.52521 | 0.52744 | 0.51678 | 0.53278 | 0.535 | 0.53094 | 0.52929 | 0.52913 | 0.53801 | 0.5255 | 0.52871 | 0.53064 | 0.53639
ROI#2 | 0.86371 | 0.8186 | 0.79836 | 0.7619 | 0.73969 | 0.72599 | 0.72386 | 0.71578 | 0.71811 | 0.71106 | 0.72079 | 0.72048 | 0.71898 | 0.71142 | 0.72261 | 0.71399 | 0.71539 | 0.71235 | 0.71868 | 0.71242 | 0.71861 | 0.7159 | 0.72281 | 0.71226 | 0.72084 | 0.71893 | 0.71152 | 0.71395 | 0.71752 | 0.71838 | 0.72523 | 0.71659 | 0.7187 | 0.71688 | 0.71315
ROI#2 | 0.76101 | 0.67861 | 0.61046 | 0.56778 | 0.5353 | 0.51543 | 0.4998 | 0.50606 | 0.49901 | 0.51227 | 0.51072 | 0.51858 | 0.52023 | 0.5197 | 0.52146 | 0.52785 | 0.51831 | 0.51523 | 0.5256 | 0.5147 | 0.51964 | 0.51154 | 0.51777 | 0.52361 | 0.51706 | 0.52574 | 0.52088 | 0.52255 | 0.51755 | 0.51984 | 0.51762 | 0.51498 | 0.52012 | 0.52218 | 0.52307
The curves indicate the size of the PMMA spheres,which match well with the spec. (~100 nm in the top cell, ~150 nm in the bottom cell)
Some settling observed in the bottom cell, resulted difference in number density of PMMA can be observed
TI
DFI
(Sample courtesy of Dr. Fankang Li)

## Slide 16: Applying nGI to study AM materials
Indicating different microstructures between selected ROIs
(Sample courtesy of Dr. Chris Fancher)
Chart: Autocorrelation length (nm)
| 119 | 207 | 296 | 384 | 473 | 561 | 650 | 738 | 827 | 915 | 973
ROI#1 | 0.90005 | 0.84186 | 0.81203 | 0.77403 | 0.74714 | 0.73046 | 0.71311 | 0.69458 | 0.68627 | 0.67655 | 0.66688
ROI#2 | 0.88509 | 0.8318 | 0.76691 | 0.73068 | 0.69465 | 0.65229 | 0.61751 | 0.58536 | 0.56662 | 0.54067 | 0.52107
ROI#1 | 0.82703 | 0.77267 | 0.73745 | 0.71892 | 0.69848 | 0.67993 | 0.66987 | 0.65324 | 0.64091 | 0.63355 | 0.62704 | 0.61998 | 0.6072 | 0.60675 | 0.5843 | 0.58253 | 0.57661 | 0.56795 | 0.56842 | 0.55806 | 0.55027 | 0.53892 | 0.53542 | 0.52989 | 0.52204 | 0.51266 | 0.51467 | 0.50692 | 0.49985
ROI#2 | 0.8041 | 0.74065 | 0.67603 | 0.61799 | 0.58124 | 0.53594 | 0.50514 | 0.47315 | 0.45253 | 0.42976 | 0.41044 | 0.40241 | 0.38046 | 0.37534 | 0.34826 | 0.33675 | 0.33822 | 0.32589 | 0.32304 | 0.31414 | 0.30859 | 0.29807 | 0.29824 | 0.2899 | 0.28409 | 0.28593 | 0.27366 | 0.27638 | 0.26645
  Two setups (Symm. and Asymm.) to cover ACL ranges from ~40 nm to ~3400 nm, push-button transition between setups
  Only has a monochromator fixed at 2.53Å
  Currently, no velocity selector (VS) to perform quantitative nGI efficiently. Usage is limited to studies only aim to get qualitative contrast.
  VS is proposed at the future MARS NB-4 location after HBRR
Dark-field revealing micro-/nano- scale structures
3D printing Inconel with two cooling regions
Microstructures revealed by Electron backscatter diffraction

## Slide 17: Addressing previous suite reviews

## Slide 18
Given these successes, it was disappointing to learn from the team that ORNL plans to eliminate imaging from the CG1-1D and repurpose that beamline for another single-crystal spectrometer.
Furthermore, this decision is hard for the present committee to understand, given the potential and given the large number of neutron spectrometers that already exist at ORNL.
Concerns were raised by the committee about the need to have a plan for long term staffing and talent retention
team was challenged to think hard about expanding the user community, beyond the expert user. We believe there are many potential users within the communities of the ASNT, ASM, and TMS societies.
The need for improved spatial resolution is emphasized, since the user community is begging for it, and the neutron imaging community is falling further behind. make impactful demonstrations of what can be achieved with the highest resolution neutron imaging capabilities available. opportunities for battery and fuel cell applications of interest to the ORNL team

## Slide 19
Current status
Status update
Maintained a diverse research program and user community
Achieved 7 μm spatial resolution
Increased number of staff
Made investments towards a mail-in program
Developed a pre-conceptual design of NB-4 with much improved instrument performance
Recruited scientists from National Museum of Natural History that expanded our existing user community
1 pub in 2022 collaborated with Vulcan team and GE, another work collaborating with industrial is planned in 2026
2017
2020
Greatest area of opportunity, supporting a diverse research program
Complex research projects
Recent beamline upgrades
Extensive software development
Scientific diversity and productivity
Software and novel ‘notebooks’ concept
Cross-institute collaboration
Notable strengths
Recommendations
Increase flight path
Add shielding and beam stop
Improve spatial resolution
Streamline & speed up data workflow
Increase staffing
Add Wavelength Resolved Tomography (WRT)
Long-term staffing & talent retention
Improve spatial resolution, opportunities for battery and fuel cell applications
Streamline 3D analysis flow with tutorials
Consider a remote experiment program
Expand user community especially with VENUS coming online
MCP integration into EPICS
Enhance collaboration with VULCAN team

## Slide 20: Operando Imaging-Guided Gradient Design for High-Mass-loading Cathodes
Scientific Achievement
Directly visualized Li reaction gradients in thick, high-mass-loading all solid-state batteries (ASSBs) cathodes. A Li⁺ flux–guided gradient catholyte design was developed, enabling superior rate capability.
Research Details
A 33 mg/cm² NMC811 cathode was monitored using operando neutron imaging. Lithiation inhomogeneity from the solid electrolyte (SE) side to the current collector was observed. A three-layer cathode—graded in SE content from high to low—significantly improved rate performance for NMC811 and LCO cathodes, with up to 171% capacity gain at high current.
Significance and Impact
This work provides the first direct evidence of Li⁺ flux mismatch in thick solid-state cathodes and offers a scalable design principle to overcome it.
T. Ji , Y. Zhang , J. Torres , A. Mijailovic , Y. Tang , X. Zhao , J. Bilheux , J. Wang , B. Sheldon , O. Oyedeji and H. Zhu, Nature Communication, 16, 7667 (2025)., doi: 10.1038/s41467-025-62518-y.
Work was performed at MARS, HFIR CG-1D
(a) Position vs. time plots with the averaged neutron transmission (trans.) changes (Trt/Tr0) represented in color. Trt/Tr0<1 indicates reduced trans. due to Li increase or natLi replaced by 6Li, Trt/Tr0>1 indicates increased trans. due to delithiation.
(b) Zoomed in on the cathode side. Colormap has been slightly changed to enhance the contrast for better visualization. Voltage vs. time curve is overlayed in white color.
(a)
(b)
Notes: Operando neutron imaging is deployed on a high-mass-loading NMC 811 cathode of 33 mg/cm2 (5.0 mAh/cm2) and directly visualizes the lithiation prioritization of the cathode active material (CAM) from the solid electrolyte membrane side to the current collector side.
In addition to the tortuosity, another key limitation on ion transfer in the cathode arises from the mismatch between the uniform distribution of the solid electrolyte (catholyte) in the conventional composite cathode and the non-uniform Li+ flux generated by the faradaic reaction of CAMs.
A gradient in the catholyte concentration is engineered to match the Li+ flux distribution as a means of eliminating the ion transfer obstacle.
This approach demonstrates enhanced rate performance, even with high-mass-loading cathodes. A LiCoO2 composite cathode with 100 mg/cm2 high-mass-loading exhibits an areal capacity of 10.4 mAh/cm2 at a current density of 2.25 mA/cm2.
This work provides insight into the ion-transport limitation in thick cathodes and demonstrates an effective gradient design to overcome the kinetic barrier and achieve high battery performance.
Researchers: A. Mijailovic and B. Sheldon (Brown University); Y. Tang (Dartmouth College); T. Ji, J. Wang, and H. Zhu (Northeastern University); Y. Zhang, J. Torres, X. Zhao, J. Bilheux, and O. Oyedeji (Oak Ridge National Laboratory)
Acknowledgements: This research used resources at the High Flux Isotope Reactor, a DOE Office of Science User Facility operated by the Oak Ridge National Laboratory. H.Z. acknowledges the primary support of the US Department of Energy (DOE), Office of Science, Office of Basic Energy Sciences under award number DESC0024528. The authors would like to acknowledge support from the US Department of Energy (DOE) Bioenergy Technologies Office (BETO) Projects under contract with UT-Battelle LLC. This manuscript was partially authored by UT-Battelle LLC under contract DE-AC05-00OR22725 with DOE. The beam time was allocated to MARS on proposal number IPTS-30750.1.
Publication/ press releases/ related links:
“Operando Neutron Imaging-Guided Gradient Design of Li-ion Solid Conductor for High-Mass-loading Cathodes,“ Nature Communications, 16(7667) (2025)
https://doi.org/10.1038/s41467-025-62518-y

## Slide 21: Summary

## Slide 22: Instrument experiments vs. publications (since 2011)
HFIR unplanned outage (2018.11 – 2019.10)
COVID-19
Heat exchanger outage

## Slide 23: Instrument experiments vs. publications (since 2019)
Increasing pub # with JIF>7
HFIR unplanned outage (2018.11 – 2019.10)
COVID-19
Heat exchanger outage

## Slide 24: Publication # is comparable with a few selected world class imaging instruments
*FRM-II has been down for the recent years.

## Slide 25: Near-term instrument upgrades
Cobot installation
 | Upgrade | Funding | Timeframe
Active projects | Dedicated computing resource | NScD | Completed
 | Collaborative robot (cobot) | BRaVE midscale | 2024-2026
 | Detector active water cooling | MARS M&S | 2025-2027
 | Image intensifier | NScD midscale | 2025-2027
 | Slit apertures for interfaces | MARS M&S | 2025-2026
 | High-res., infinity-corrected optics | MARS M&S | 2026-2027
 | HFIR 20 kN load frame | NScD midscale | 2026-2027
 | Multipurpose sample environment chamber | MARS M&S | 2026+
Proposed/planed | Optimized imaging instrument at NB-4 | NScD | ASAP after HBRR
 | Simultaneous Neutron and X-ray (SNAX) | ICE (under final review) | 
 | Amteco extended cavity | TBD | 
 | Black-body grids (scattering corr.) | TBD | 
 | Sparse-view, AI/ML-assisted acquisition | TBD | 

## Slide 26: Future of MARS
HBRR starts Sep. 2029
MARS at CG-1D is a repurposed instrument, has evolved through various upgrades over the years
MARS at NB-4 will be the first purposely designed/optimized imaging instrument at HFIR
Optimized guide design shows improved flux

## Slide 27: Vision of MARS
Complete the conceptual and preliminary designs of NB-4
Successfully rebuild with equivalent or better capability at NB-4 after HBRR with minimum delay
Further improve the capabilities in spatial and temporal resolutions, and quantitative studies
Implement AI assisted sparse-view smart acquisition
Implement automated data reduction and tomographic reconstruction algorithms
Launch a mail-in/rapid-access program with automated sample changes and data acquisition
Commission samples environments, including a load frame and multi-atmosphere chamber
Following NB-4, MARS will be fully optimized for cold-neutron imaging on par with world-leading instruments
Integrate simultaneous X-ray imaging (SNAX concept) if funded
Near-term (1-3 years)
Long-term (3+ years)

## Slide 28: Acknowledgments
Thank you for your time in reviewing our imaging program!!!!
This research used resources at the High Flux Isotope Reactor, a DOE Office of Science User Facility operated by the Oak Ridge National Laboratory.
Operations support teams
ORNL User office
The ORNL neutron imaging team
The diverse imaging community that trusted us and helped us to improve

## Slide 29: SWOT Analysis – MARS
A wide variety of detectors, motion control systems, and setup hardware
Possible to reconfigure instrument flight tubes for complex experiments
Highly diverse research and unique users
User-friendly software and online tools
Healthy funding and support for software and beamline improvements
Unique, large scale user experiments, including in-situ/in-operando device and material characterizations (batteries, fuel cells, molten salts) using shared SE equipment
Only 1 CIS for MARS and VENUS
CG-1 neutron guide was built for a spectrometer, not imaging, leading to suboptimal white-beam flux and beam uniformity
Lacking sufficient sample environment for soft matter and high pressure
X-ray imaging capability is lacking/weak
No velocity selector as needed for quantitative nGI measurements; monochromator upgrade needed
User guidance/instructions for proposal preparation and advertisement of nGI capabilities
Space limited for equipment, difficulties in returning user supplied equipment
MARS (NB-4) conceptual design is delayed, lead to unknown delay of HFIR neutron imaging after HBRR
High complexity of user experiments that creates elevated risk for accidents and materials mishandling
Dependence on additional funding for outsourced and expensive visualization (Amira) and data-correction (BM3D) software
Auto data reduction for standard processes (2D normalization, CT reconstruction)
Mail-in/rapid access program
AI/ML tools for data acquisition, reduction, and analysis
Widen slits/collimation and assemble larger detector to leverage large ~17cm diameter beam
Upgrade/optimization inside the CG1 optics box for reliable operation
Development of the neutron microscope (custom lens system and vibration-free platform)
Development of advanced optics for beam focusing and magnification
Strengths
Weaknesses
Opportunities
Threats