## Slide 1: Bio-SANS: Current Status–Future Goals
PRESENTED BY
FEBRUARY 09,2026 | OAK RIDGE, TENNESSEE
Venky (Sai Venkatesh) Pingali
Center for Structural Molecular Biology

## Slide 2: Bio-SANS Team
Instrument Scientist
Instrument Development
Plant cell wall (Assemb. & Deconst.)
Bio-Environmental
Biomembranes
Biomaterials
Biomacromolecular Complexes
Venky Pingali
Computational Instrument Scientist
Real-time Data Reduction (Live)
AI-driven Automation Capability
Flexible Proteins (MD)
Protein/Nucleic Acid Complexes
Deuterium Incorporation
Alan Hicks
Instrument Scientist
Sample Environment Development
Data Analysis
Biomacromolecular Complexes
Lipid Nanoparticles
Nucleic Acid Complexes
Biomembranes
Biomaterials
Wellington Leite
Scientific Associate
Instrument Operations
User Training
Testing Sample Environments
Coordinate maintenance jobs
Maintain Safe Procedures
Felicia Gilliland

## Slide 3: Bio-SANS Instrument (Charge Q1)
Monochromation:
6–25 Å
Collimation System:
8 M1 Guides (2 m each)
Detection System:
3He Linear Position Sensitive Detectors (LPSD) – 256 Pixels
Staggered arrangement of tubes – (H x V: 5.5mm x 4.5mm)
Main ~ 1m x 1.0m (192 tubes) – (2012)
Mid-range ~ 1m x 0.4m (64 tubes) – (2024)
Wing ~ 1m x 0.9m (160 tubes) – (2016)
Main
Wing
Midrange
Main
Midrange
Wing
Vacuum Tank
Sample
Monochromator, l
Guides (Passive Collimation)
Neutron Beam Direction
Mid-Range
Main
Wing
Ө
3He Tube Detectors
Semi-Transparent Beam Trap

## Slide 4: Unique capabilities of Bio-SANS (Charge Q1)
Semi-transparent beam trap:
  simultaneous ‘Scattering’ & ‘Transmission’ measurements
Multi-array detector system:
  provides a dynamic q-range factor of 280
Specialized for biological community:
  Size Exclusion Chromatography (SEC) SANS of biomolecules
  Freeze-thaw protein solutions for pharma & biology
  Data analysis for intrinsically disordered protein (ALS collab.)
  Live reaction cell for thermochemical deconstruction of plants
  In-vivo whole cell studies for biofuels

## Slide 5: Bio-SANS sample environment suite developed for the biological community (Charge Q1)
4-Position Tumbler
Robot w/84 Positions
Chromatography SANS
4-Position Reaction Cell Holder
CryoTemp Solutions

## Slide 6: Suite Review 2020
REVIEW COMMENTS/SUGGESTIONS | RESOLUTION
Publication areas - 50% Soft Matter/40% Biology The number of "bio-users" is low, but focusing on team expertise suggests to concentration on biosciences | Dr. Wellington Leite was hired in 2021 Distribution: 9% Soft Matter/81% Biology (Biomacromolecular Complexes + Biomembranes + Biomass/Biofuels + Biomaterials )
Output lower than GP-SANS and EQ-SANS. The team should consider why? | Contributing factors: Lower staffing level 2 vs. 3 Instrument scientists for Bio-SANS vs. GP-& EQ-SANS Inexperienced user community, need IS collaboration for success
Beamline staff are over-stretched as the beamline becomes high throughput | Developed interactive SANS solution sample data analysis to relieve some burden on IS
Data analysis is a bottleneck | Dr. Alan Hicks was hired in 2024 as computational instrument scientist for biology
It is ideal to focus beam at detector to improve low-Q capabilities, which would be beneficial to RNA and bio complex studies and complement EQ-SANS | Instrument development: Increase low-Q access to Q ~ 5 x 10–4 Å–1
Low demand for SEC-SAXS at synchrotrons; Discuss with counterparts at other facilities to determine SEC-SANS demand and invest instead for auto-samplers (robotics) | The team discussed with neutron facility: D22 (ILL), and synchrotron facilities: Bio-CAT (APS), LiX (NSLS-II), BL4-2 (SSRL) before committing to develop SEC-SANS capability. In addition, the team was the trend-setter in developing robotic auto-samplers.

## Slide 7: Complex Hierarchical Biosystems – Venky Pingali
Plant Cell Wall
Environmental Process
Astner et al. Environ. Sci.: Nano (2025) DOI: 10.1039/D4EN01199F
DOE BER funded Biofuels SFA (ORNL)
Biomacromolecular Complexes
Armbruster et al. Biomac. (2024) DOI: 10.1021/acs.biomac.4c01829
Ribosome Structure during Transcription
NSD Go! Student
Yang et al. ACS Sus. Chem. Eng. (2022) DOI: 10.1021/acssuschemeng.1c06276
4
Plant cell wall Deconstruction
Biomembranes
Tan et al. Langmuir (2025)
DOI: 10.1021/acs.langmuir.4c03677
Biomembrane Disruption
DOE BER funded Biofuels SFA (ORNL)
Senanayake et al. Biomac. (2024)
DOI: 10.1021/acs.biomac.4c00187
Plant cell wall Assembly

## Slide 8: Biomacromolecules – Wellington Leite
Proteins
RNA:RNA Complex
Munsayac et al. Structure (2025) DOI: 10.1016/j.str.2025.01.017
Electron Transfer Flavoproteins
Khan et al. Chem. Sci. (2024) DOI: 10.1039/D4SC04544K
NSD Go! Student
Thomas et al. Biophys. J. (2024)
DOI: 10.1016/j.bpj.2024.05.029
SEC-SANS
Membrane Proteins
Edwards et al. ACS Measurement Science Au (2025) DOI: 10.1021/acsmeasuresciau.5c00099

## Slide 9: Future Goals (Charge Q6)
INSTRUMENT DEVELOPMENT
Develop Focusing Optics System to access Lower-Q (d~1.6 mm)
Establish Laser Alignment Capability
SAMPLE ENVIRONMENT DEVELOPMENT
Develop Multi-Position Cryo-Temp Solution Sample Capability
Collaborative Development Projects with NCNR (NIST)
  Automated Liquid Handling System for Autonomous Experiments
  High-throughput High-pressure/Freezing-temperature Capability
  Rapid-Mixing for Studying Fast Transient States
Automated Liquid Handling System for Autonomous Experiments
In Sample Environment Talk (Luke Heroux)

## Slide 10: McStas Model of Qmin Extension by Insertion of Lenses, Prisms, and High-Resolution Detector (Charge Q6)
Three main components to Model in McStas:
Lens to focus beam at the detector
Prisms to eliminate beam elongation
High Resolution Detector to resolve small-angles finely
(~1 mm pixels)
Qmin = 4 x 10–4 Å–1 (Improvement of ~2.5x )
max. length scale ~ 1.6 mm
High Resolution
Detector
Adapted from Schaefer, D.W, Material Research. Society Symposium Proceeding,(1987)
1.6 mm
0.6 mm
In technical support by John Barker, NIST

## Slide 11: Determine Number of Lenses to Optimize Beam Size and Intensity of Focused Beam (Charge Q6)
Lens
HiRes-DET
We will measure beam size and beam intensity at the detector position by varying
Number of lenses
Neutron wavelength
Lens diameters (12.7mm, 25.4 mm) or sample aperture
Qmin ~ 4 x 10–4 Å–1
Adapted from Iwase et al. J. Appl. Cryst. (2011)
DOI: 10.1107/S0021889811007527
Source
Sample
l
L1=18m
L2=14.5m
D1=15 m
D2=17.5 m
A0=𝛟6mm
As=𝛟10mm
Ad=𝛟14mm
=10 Å
~10–4 Å–1

## Slide 12: Expanding Capability for Studying Solution Samples at Freezing/Cryo Temperatures (Charge Q6)
25
T(°C)
–30
–80
–100
–20
Quantum NorthWest
Biological ice Nucleation
Biological ice Antifreeze
Gharib et al. (2021)
DOI: 10.3389/fbioe.2021.770588
ORNL (in-house)
Meister, Boise State

## Slide 13: Automated Liquid Handling System (Charge Q6/Q7)
DOE BRaVE Initiative funded project
Robot arm (UR 5)
Electronic pipettor
Pressure controller
Wash solutions
containers
Main distribution valve
waste container
Path control valves
Flow-
cell
Nozzle and funnel
Air flow distribution valve
Actuator arm
Load samples from 96-well plates
For the next experiment, the cell is emptied and cleaned by sequential washes with water, detergent, ethanol, and dry air
Mix (1-8) stock solutions to prepare next sample
Enable
AI-driven Experiments
Details in Sample Environment Talk by Luke Heroux

## Slide 14: AI-Driven Experiment Capability Status (Charge Q7)
AI-Driven
Experiments
Beam trap Upgrade:
Semi-transparent
Detector Upgrade-1: Modular Design
12
13
24
Detector Upgrade-3:
Midrange
Data Processing/Analysis:
– Interactive Solvent Background Subtraction
– Automated Basic Data Analysis for Solutions
20
22
Automation-1:
1st Gen. Robot SE
Automation-2:
2nd Gen. Robot SE
15
16
Detector Upgrade-2: West Wing
Sample Area Upgrade:
– Open Scaffolding
– Sample flushed to Tank Window
25
Data AI-Ready?:
Metadata Storage Robustness (LAMBDA)
Data Reduction/Processing:
– 1st Gen. Auto-reduced Data
– ML-driven Prediction of Empty Cell Data
26
Sample Environment: Commission of
Automated Liquid Handling
2007
1st Beam through Bio-SANS
Collimator Vessel Upgrade:
Spacious/Flexibility
DAS Upgrade:
EPICS
Data Reduction:
DRTSANS
19
Large dynamic q-range
Simultaneous ‘Trans.’ & ‘Scatt.’
Basic auto-reduction of data
Basic data analysis (solutions)
Metadata storage (improve)
Auto-empty cell subtraction

## Slide 15: Synergistic Collaborative Efforts (Q6)
Sample environment development and commissioning by NIST-NCNR scientists that will be useful for the broader Bio-SANS user community
https://www.biologic.net/products/sfm2000-3000-4000-stopped-flow/
Umbilical Link
Beam on sample
1.5 cm
Rectangular Cell
Time: 10 – 300s
Rapid-Mixing System
High-Throughput High-Pressure/Freezing-Temperature
NIST SBIR 70NANB21H130 (Patent Pending)
Pressure: 0 – 2.2 kbar
Temperature: –20 – +65 °C

## Slide 16: Conclusion
Pave the path to access length scales > 1 mm
Optimize Lens Configuration
Enable freezing & cryo-temperature capabilities
Develop Automation and AI-driven experimental capability
Leverage collaborations for development of complex sample environments
Lipid Nanoparticles
Nanoplastics/Soil Systems
Membrane Protein
Assembly & Deconstruction of Plant Cell Wall
Flexible Protein Domains
Cellular Components in Living Cells
mRNA + Lipid Nanoparticles

## Slide 17: Questions
Thank you for taking the time to review and provide your valuable suggestions

## Slide 18: Laser System will Streamline Alignment of Sample Environments
Laser spot on sample will provide a quick visual check without the need for neutrons

## Slide 19: HFIR will Undergo Major Maintenance in FY29 Q3
HFIR Beryllium Reflector Replacement (HBRR)
CSMB FY 26–28 funding cycle
Cold Guide Hall Instruments Layout

## Slide 20: Bio-SANS Instrument will Maintain Capability Post-HBRR
Post-HBRR (2030 Q3)
New Beam Delivery Guide System
Beam bending by an additional 3°
Airbus Velocity Selector (higher transmission)
Access to 4.5 Å
Qmax = 1.2 Å–1 (from 1.0 Å–1)
4.5 Å
Current Instrument Planned Upgrade
Microbial Nanoparticles
Soliman et al. Environmental Science: Nano (2022)
DOI: 10.1039/D2EN00263A
7.22°
NB3 Beamline Centerline
Instrument Centerline
9°
Beam Centerline
Neutron
Reactor

## Slide 21: Protein Complex/RNA/RNA-LNP – Wellington Leite
RNA–Lipid Nanoparticle
Thelen et al. ACS Nano (2024) DOI: 10.1021/acsnano.3c08014
Method Development
Edwards et al. ACS Measurement Science Au (2025) DOI: 10.1021/acsmeasuresciau.5c00099
Molecular Condensates
Gibbs, E.,et al. Nat Commun 15, 9531 (2024) DOI: 10.1038/s41467-024-53904-z