## Slide 1
Manufacturing
Galen Aymar
SLAC National Accelerator Lab

## Slide 2: Common Themes
Ceramics: long lead times due to the small relative size of the tube. Material properties are often unknown at the desired frequencies. The makeup of TiN coating maybe questionable after exposure to air and bakeout. BeO is hard to source, known vendors are in Japan and Wales.
Cathodes: hard to source and the quality is variable, leading many vendors to bring production back in house.
HV Connectors: these can end up causing many headaches for sourcing or quality. Vendors prefer the end-users either provide the connectors or allow for flying leads.
Rare earth materials: an ongoing issue that may only be solved by domestic mines being reopened.
Tungsten wire: this issue appears to be solved by government intervention.
Testing tubes at the end-user: this presents a host or both pros and cons (risk, fault, shipping, allowable work, etc.). Having a central testing facility may be useful.

## Slide 3: Common Themes
Capital equipment: this can be funded and procured by end-users and placed at the vendor, with the end-user having priority access to the equipment.
Additive manufacturing: this has been proven in RF loads and cold testing, but not in klystron parts themselves. Ceramics are doable, but still require more development still.
Advanced manufacturing: 5- or 6-axis milling may reduce need for additive manufacturing. Blue laser welding should be pursued to avoid brazing.
Sourcing materials: having a central lab sourcing large quantities of material for use by vendors could be useful.
Lack of expertise: allowing for more prototype testing may help train new engineers.
Knowledge of what tubes are available: a database of currently available and planned requirements for tubes would improve planning or users and vendors.

## Slide 4: Recommendations & Potential Actions
Vendors and end users should be discussing the following:
HV connectors early in the specification process.
Testing tubes at the vendor or lab.
Procurement of capital equipment by labs for use at the vendor factories.
Allowance for more prototype cycles to establish a goal design and train up engineers and technicians.
Working groups or topics of regular discussion at workshops:
Tracking of high-risk materials similar to how tungsten wires were addressed.
Sourcing of high-risk materials by labs to be used as a source for vendors.
Developing a centralized laboratory facility for testing or emergency build capacity.
Continued push on additive manufacturing for all material types
A database of currently maintained tubes and forecasts for tube needs. Used by vendors for planning and by labs for optimizing timing of procurements.