## Slide 1: Example of GSAS-II refinement of magnetic structure from TOF data
July 23, 2026
Keith TAddei
11-ID-D Lead Instrument Scientist
Advanced Photon Source
Argonne National Lab

## Slide 2: Example system: Co5(TeO3)4Cl2
Data collected on POWGEN

## Slide 3: Magnetic structure of Co5(TeO3)4Cl2

## Slide 4: Installing GSAS-II (on Github now)
https://advancedphotonsource.github.io/GSAS-II-tutorials/install.html
You can also create a GSAS-II environment and install with a python manager like Anaconda
Easy installation (will duplicate python)
Windows: https://advancedphotonsource.github.io/GSAS-II-tutorials/install-g2f-win.html
Mac: https://advancedphotonsource.github.io/GSAS-II-tutorials/install-g2f-mac.html
Notes: This slide is included for those who wish to run through this ahead of time. Installation will not be covered in the lecture. More information on GSAS-II will be covered in Brian Toby’s presentation.

## Slide 5: Before starting your refinement:
POWGEN
Be sure to have
  Data file
    From P3G: file_name.gsa
  Instrument parameter file
    From P3G: file_name_cycle_inst_settings.instprm
  Crystallographic information file (.cif)
How to know what parameter file?
Oncat, experimental notes, ask your instrument scientist.
For PG3 you need the date, the frame and the mode

## Slide 6: Starting from an empty GSAS-II file
Console window
(won’t use today)
Data window
(where we’ll setup the data, phase information and run refinements)
Plotting window
(automatically plots based on what you do in the GUI)
We’ll start here

## Slide 7: Loading your data
?
Lets load the 30, 15, and 8 K data (runs 54503, 54502, and 54500)

## Slide 8: Loading your data
15 K
30 K
8 K
You may get this - Yes

## Slide 9: Loading your data
Next pop-up window will prompt for an instrument parameter file – need to change the filetype it is expecting to match Powgen’s

## Slide 10: Loading your data
Change to .instprm
Make sure the instprm file is correct for your experimental settings – right frame, mode, cycle…

## Slide 11: Data loaded
Now we have three patterns open, let’s look at them
Either click on ‘K’ and look for multiplot or select the plotting window and hit the ‘m’ key on your keyboard. Let’s also hit ‘t’ while we’re at it to get it into d-spacing

## Slide 12: Comparing patterns
Now zoom in
New peaks!
We’ll start with the 30 K nuclear fit then try to get a magnetic model for 8 K
No peaks above 14 Å

## Slide 13: 30 K Nuclear fit
Hit ‘m’ on the plotting window to toggle multiplot off
Now we could clean up and remove the lower temp files, or leave them in – either way works.
Select 54500, and 54502 then click okay

## Slide 14: 30 K Nuclear fit
Next we’ll cut the low count high TOF section since there are no peaks there
Either manually enter a number or drag the dotted line on the plotting window

## Slide 15: Loading a phase

## Slide 16: Checking the phase

## Slide 17: Checking the phase
Unit cell information
NB: always check to make sure it read the cif correctly

## Slide 18: Checking the phase
Information on the elements – isotope, stoichiometry, color, etc.

## Slide 19: Checking the phase
There are also tabs which contain more detailed information about the phase up here for instance, if we click on the atoms tab:

## Slide 20: Checking the phase
We get a table of the atoms in the phase. Here you can see the atomic positions the site symmetry, multiplicity, displacement parameter(s) and a column with the refinement flag.

## Slide 21: Checking the phase
If we click on the refinement box, we get a pull-down list with a selection of refinement flags.

## Slide 22: Checking the phase
If we click on the ‘Draw Atoms’ tab, we get a new tab in the plotting window with an (albeit strange) image of the crystal structure

## Slide 23: Checking the phase
This can be fixed by selecting all the atoms in the draw atoms tab… (double click in the corner to do it quickly)

## Slide 24: Checking the phase
Going to the newly appeared ‘Edit Figure’ option in the tool bar and selecting ‘Fill unit cell’
Remeber: in GSAS-II, the tool bar is adaptive to the active tab

## Slide 25: Checking the phase
This still looks a bit odd, we can fix this in the ‘Draw Options’ tab

## Slide 26: Checking the phase
Change the camera distance and anything else you might want to your liking – for instance if you prefer a white background
There are a lot of tools here for visualization
Now let’s get back to fitting

## Slide 27: Setting up the refinement
Increase the number of cycles to 10

## Slide 28: Setting up the refinement
Set the number of background terms to 6
Now let’s run a refinement

## Slide 29: Setting up the refinement
Go File -> Save project
First, let’s save the project
Give it some reasonable name – save it somewhere that makes sense

## Slide 30: Setting up the refinement
Go Calculate -> Refine
Now refine

## Slide 31: Running a cycle
A window will pop up showing refinement status and the plotting window will update with the fit

## Slide 32: Running a cycle
When it finishes a box will pop up with the parameter changes some goodness of fit measures and messages if you have a divergence or highly correlated parameters

## Slide 33: Inspecting the results
Fit is.. A decent start. Peak indexes seem right, intensity is a bit off. Let’s flag some structural parameters

## Slide 34: Inspecting the results
Let’s flag the unit cell to refine
Then Calculate -> Refine

## Slide 35: Inspecting the results
That didn’t improve much, let’s look closer

## Slide 36: Inspecting the results
Let’s look at what peaks aren’t fitting, go to Reflection List and hover over the high d-spacing peak to see it’s index
(2,0,0) is getting way over fit
(0,2,1) is getting under fit
Maybe we have some preferred orientation

## Slide 37: Adding a preferred orientation
Go to Data, let’s use the simplest model of MD preferred orientation with a unique axis of 1 0 0 (based on 2 0 0 being over fit) flag it to refine

## Slide 38: Status check
This is looking much better – we could perhaps improve it by adding atomic parameters and microstructure but for this tutorial we’ll stop here. Save your file here!

## Slide 39: Quick peek at a dark, unpaved, philosophical side path
At this point, if we look at peaks we see some systematic misfitting
– sample microstructure? Maybe.
– Instrument profile issues? Also Maybe.
We could venture over to the Instrument parameters data tree entry and consider refining the profile.
Powgen’s profile is complex and few standards have high d-spacing peaks. Also, Powgen’s design principle is single bank – all your data in one pattern as opposed to multiple (al la NOMAD, WISH). This makes developing a single profile function/parameter set very tricky.
We could get a better fit refining some of these profile parameters. We will not do so today and before you touch these you should have a good reason to do so and perhaps have a chat with your instrument scientist first.
Are you fitting your sample properties with the instrument?
What does that mean?
Do you care for what you are trying to extract from your data?

## Slide 40: Moving on to magnetism
We need a new .gpx with the 8 K data. There are multiple ways to do this, I’m just going to add the new histogram to this file. (N.B. we could’ve just left it in from the beginning)

## Slide 41: 8 K data
Now we have two histograms, let’s save this project with a new name now, something with 8 K in the name, using save project as.

## Slide 42: 8 K data
We need to dissociate the phase from the 30 K histogram. Go to phases -> Data and deselect ‘Use Histogram’ for the 54503 histogram.
Copy over the MD preferred orientation ratio (1.188) and unique axis (1 0 0)
To be safe, let’s turn off the unit cell refinement flag

## Slide 43: Refining the 8 K background
Remember to change your upper TOF limit (to 350000) and change the background to 10 terms.
We have two histograms, make sure you are on the right one.
Refine

## Slide 44: How’s it look?
Fit looks okay.. Considering we have huge unfit peaks! Let’s start the magnetic structure solution now!

## Slide 45: Solving the magnetic structure

## Slide 46: Getting the k-vector
As with FullProf, we need to tell GSAS-II what peaks we want to try and index with a k-vector.
To do so, go to Peak List (for the right histogram) in the data tree
Click ‘Switch to Extra Peak mode’

## Slide 47: Getting the k-vector
Now your pointer is ‘armed’
Zoom in on your plotting window and start selecting peaks!

## Slide 48: Getting the k-vector
As you select, the peak list will populate, I picked these three peaks.
N.B. if you are having issues picking peaks – make sure you turn off the zoom!
Now we will refine the intensity and position of these peaks, start with intensity, it’s already flagged to refine
Go to Peak Fitting -> Peakfit

## Slide 49: Getting the K-Vector
You should see your selected peaks’ intensity fit, in a different color.
Now lets flag the positions to refine and hit Peak Fitting -> Peakfit again
Fit looks pretty good now, we could add more complex peak shape but this is good enough for k-search

## Slide 50: Getting the k-vector
Go to Unit Cells list in the data tree
Cell Index/Refine -> Load Phase

## Slide 51: Getting the k-vector
Now your plotting window will have peak positions,
Next select ‘Search for k-vector’
Click ‘Start Search’

## Slide 52: Getting the k-vector
Now your plotting window will have peak positions,
Next select ‘Search for k-vector’
Click ‘Start Search’
Should get a list that looks something like this

## Slide 53: Running k-Subgroupsmag – From GSAS-II
Run k-SUBGROUPSMAG
A window will open for you to enter the k-vector, deselect preserve axes (this is to be consistent with the published structure) select Co for test atoms and all have moment

## Slide 54: Testing your MSG
Scroll down on the data window and you will see a table of allowed MSG
If will include the unit cell transformation, an offset vector for the axes (if there is one) and more.
You can click on the ‘try’ box to see how they index the pattern
If you click on a choice it will give you the allowed moment components

## Slide 55: Savepoint
Here I recommend saving the 8K nuclear fit as a checkpoint file. This serves two purposes:
You save your nuclear only fit to got back to if needed
By saving after doing k-search and k-SUBGROUPSMAG you have a starting point to test all your MSG. You can return to this .gpx, save it under another name (like name_mag2) and import the next MSG.

## Slide 56: Magnetic structure 1: C2’/c’

## Slide 57: Trialing a structure
Go to ‘Phases’ in the Data tree
Then go to Compute -> Select magnetic/subgroup phase
You will get a pop up window with a list of all the MSG – pick the one you want to try and click OK
Let’s start at the beginning and pick MSG(1)
Co0_0 and Co1_1 have moments with x,y,z components. Co2_2 only allows x and z

## Slide 58: Trialing a structure
You will now have a new phase entry, if you had Unit Cell parameters refining GSAS-II will automatically add constraints.
The imported MSG will just have the magnetic ions – as opposed to the full nuclear + magnetic structure

## Slide 59: Fitting the structure
If you go to the Atoms tab you will see the atomic parameters – which now include the magnetic components
Give them some nominal values (refining out of zero can be treacherous) and flag them to refine

## Slide 60: Fitting the structure
Make sure you click somewhere else after setting the refinement flags.
Otherwise, it wont actually set the flag.
Now let’s run a refinement
(Calculate -> refine)

## Slide 61: Fitting the structure
This doesn’t look great.
We’re missing a lot of intensity on the 10 Å peak and overfitting the 13.5 Å peak.
Time to try another structure.
We can either delete this phase and reimport a different model.
Or save this and go back to the nuclear project and start again.
I like saving each model separately so I can go back and take a closer look later if I need to.

## Slide 62: Magnetic structure 2: C2/c’

## Slide 63: Trying MSG 2 C2/c’
Going back to my 8 K .gpx, saving a copy as 8K_mag2, I will now import the second choice
Now Co2_2 only has a moment along Y

## Slide 64: Trying MSG 2 C2/c’
As before, give the moments some nominal non-zero value and flag them to refine.
Run a refinement

## Slide 65: Trying MSG 2 C2/c’
This fit also doesn’t look great.
We’re still missing the 10 Å peak
Let’s try the third choice

## Slide 66: Magnetic structure 3: C2/c’

## Slide 67: Trying MSG 2 C2’/c
Now we still have Co2_2 with x and z components but the symmetry element (2’(y)) is primed.

## Slide 68: Fitting the structure
Giving non-zero moments and flagging to refine

## Slide 69: Running a refinement

## Slide 70: Refinement results
Now this looks better! We are fitting all the magnetic peaks.
We can check on what moments we actually have in the Atoms tab.
Plot the structure in the plotting window.

## Slide 71: Exporting an MCIF
To export an mcif, go to your magnetic phase in the data tree,
Then go Export -> Phase as -> Quick CIF
Select the mag phase

## Slide 72: Viewing the MCIF
It will append the project name to your name and save as a .cif (this is fine).
If you open it in Vesta, you should get something like this.
Note: It does not have the non-magnetic sites. If you wanted to report this you would have to add the non-magnetic sites.
BCS could help with this.
Second note: This is a tad different than the reported structure. In the refinement used for the reported structure instrument parameters were refined. We did not do so in this example and it makes a difference in the refined moment components!