## Slide 1: Introduction to GSAS-II and New Features
July 24, 2026
Keith TAddei
11-ID-D Lead Instrument Scientist
Advanced Photon Source
Argonne National Lab

## Slide 3: GSAS I And EXPGUI

## Slide 4: GSAS-II

## Slide 5: GSAS-II Design Philosophy
Rebuild and expand GSAS with Python (mostly)
Open source with a scripting API
Handle ‘all’ types of data – area detectors and XRD calibration to protein crystallography to SAXS to magnetic structure solution
Expand visualization – structures, fits, displacements
Separate instrument parameters from sample parameters
Minimize user input for known quantities
Bob von Dreele
Brian Toby

## Slide 6: GSAS-II Highlighted Features
Integration and PDF reduction
‘Unlimited’ number of phases
Sequential and parametric fitting
Robust microstructure fitting and visualization
Simulate diffraction
Handle huge data sets, multiple data types simultaneously
Calibrate beamline – collate data to use in meta fitting
Links to ISODISTORT, Bilbao Crystallographic Server, RMCProfile,
Lots of very useful, thorough tutorials
Pink beam fitting
Von Dreele, et. al., J. Appl. Crystal. (2021)

## Slide 7: A new textbook on powder diffraction crystallography
Crystallographic Powder Diffraction Analysis with GSAS-II, An Introduction to Rietveld Analysis
by Brian Toby
Download as a PDF
  https://github.com/briantoby/PowderCrystallography/releases/latest
Printed copies will soon be available from Amazon.
Preview edition (July 2026)
29 chapters, ~340 pages
Open Source
Preview version available for comment and suggestions
Book sections:
  Prerequisites
  Basic Information
  Pattern Fitting
  Using GSAS-II
  Simplifying Models
  Advanced Concepts

## Slide 8: Using GSAS-II
Console window
Data window
Plotting window

## Slide 9: Console Window
Refinement cycles
Error information
Results of Parametric fits
Results of k-search/magnetic symmetry
Most of the time you can minimize, but is useful to follow when things go awry

## Slide 10: Data Window
Main menu
Submenu – this is context dependent!
Help – get to tutorials, update, and add submodules
Data tree
Top of tree: Project controls
Histogram (or IMG)
Phases
Can have more than one histogram, more than one phase, and assign each phase to histograms at will

## Slide 11: Data Window: Data Window

## Slide 12: Climbing the tree: Histogram

## Slide 13: Climbing the tree: Histogram

## Slide 14: Climbing the tree: Phase
Data Tabs
New options
Unit cell, scattering factors, advanced charge flipping, MC, Simulated Annealing controls

## Slide 15: Climbing the tree: Phase
New options
Associated histograms, plotting window controls, phase fraction, microstructure, preferred orientation

## Slide 16: Climbing the tree: Phase
New options
Most used for Refinement:
Atomic parameters, refinement flags iso/aniso ADPs, occupancies, magnetic components, warnings for unphysical values

## Slide 17: Climbing the tree: Phase
Won’t show this week but GSAS-II now links to ISODISTORT and can plot distortion modes

## Slide 18: Plotting window

## Slide 19: Plotting window

## Slide 20: Data Window: Flash Refinement
Load Data
Load Phase
Refine

## Slide 21: GSAS-II Takeaway
GSAS-II is powerful, fairly user friendly, and can do a lot more than I showed today!

## Slide 22: Installing GSAS-II

## Slide 23: Installing GSAS-II
https://advancedphotonsource.github.io/GSAS-II-tutorials/install.html
Windows:
https://advancedphotonsource.github.io/GSAS-II-tutorials/install-g2f-win.html
Mac:
https://advancedphotonsource.github.io/GSAS-II-tutorials/install-g2f-mac.html

## Slide 24: Important NExt step!
In order to link up to the Bilbao Crystallographic server you have to get an API key
Sounds hard, but there’s a GSAS-II tutorial for that
https://advancedphotonsource.github.io/GSAS-II-tutorials/RegisterBilbao/RegisterBilbao.html
Without this you won’t be able to access BCS
Keep your key – you can/will use it on all your devices
There’s a GSAS tutorial for that

## Slide 25: BCS API key
Request a BCS account: https://cryst.ehu.es/cgi-bin/cryst/programs/UserRegister.pl
Register for BCS account
Create BCS API key, login: https://cryst.ehu.es/cgi-bin/cryst/programs/User_Login.pl
1
2
3.1
3.2
3.3

## Slide 26: BCS API key
Add Key to GSAS-II preferences
5.1
5.2
5.3

## Slide 27: BCS API key
Trust but verify
6.1
X
√

## Slide 28: Gsas-II Magnetism tools preview

## Slide 29: GSAS-II and magnetism
In GSAS-I magnetism was only accessible through the command line. There was no k-vector, no search, no solution tools. You had to flag red/black operation for each element of the space group symmetry.
Now:
We will go through and play with k-vector identification

## Slide 30: Identifying k-vector
Ex 1: Co3(SeO3)2H2O
Two Methods:
Guess and check
k-search

## Slide 31: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
Hit ‘t’ key on plot window
Go to Unit cells list on data tree

## Slide 32: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
Older versions will require you to load the phase
Can we use the peak positions and the lattice vectors to work out k?

## Slide 33: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
Try multiples of the nuclear unit cell

## Slide 34: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
In the plotting window you’ll see the new peak positions

## Slide 35: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
Try more multiples of the nuclear unit cell

## Slide 36: Identifying k-vector
Ex 1: Co3(SeO3)2H2O – guess and check
That got them all!
?

## Slide 37: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Go to peak list
Switch to Extra Peak mode

## Slide 38: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Click in the plot window on the unindexed peaks, choose the strongest and start with just a few
They will show up in the peak list
Now we will refine their intensities (already flagged) – then positions

## Slide 39: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search

## Slide 40: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
It will run, zoom in on the plotting window – intensities fit okay…
Now refine the positions
Go to Peaking Fitting -> Peakfit again

## Slide 41: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Big improvement, now we can use these for a k-search
Go to the Unit Cells List

## Slide 42: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Check the ‘Search for k-vector’

## Slide 43: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Have some options for controlling how and where you search – defaults are good to start with
Click ‘Start Search’

## Slide 44: Identifying k-vector
Ex 2: Er2Ge2O7 – k-search
Violá, a list of k-vectors you can click through to trial
Not too bad?
Next step: link up with BCS! (later tutorial)

## Slide 45: 11-ID-D: a new high-energy, multimodal, x-ray beamline at the APS
Novel layout and optics for maximum high energy flux and focusing
Huge Q coverage for single crystal, powder, thin films, and PDF
Superconducting detector
1.5 μm beam – will get smaller