## Slide 1: The SNS Power Ramp-Up
June 10, 2026
Workshop on New Science and Applications at SNS
Sang-ho Kim
Research Accelerator Division
Notes: Accessing Title Slide Options The standard ORNL presentation template includes five branded title slide layouts:
  Title | Standard. The preferred layout for lab-wide and general presentations. Features a default aerial photograph of the lab.
  Title | Custom Image. Allows replacement of the default background with a custom full-slide image (16:9 or 4:3 landscape format).
  Title | Custom Portrait Image. Supports inclusion of a custom 4:3 portrait image positioned next to the introductory text.
  Title | Custom Landscape Image. Supports inclusion of a custom 16:9 landscape image positioned next to the introductory text.
  Title | Text Only. Offers additional space for longer titles and multiple presenters.
Additional Lab-approved title slides specific to directorates and user facilities are available in PowerPoint under the following folders: Custom Title Slides and User Facility Templates, located in Presentation Templates.
Custom Title Slide Guidelines
  Image Rights. Any custom images, graphics, or photography must be owned by ORNL or used with documented permission from the original creator or source.
  Appropriate Image Use. Select images that work well with the layout. Ensure the focal point of the image is not obscured by the title text and white overlay box.
  Relevance and Impact. Visuals are a key element of effective communication. Whenever possible, use imagery that enhances the message of your presentation and reflects ORNL’s mission and values.
  Quality and Clarity. Use high-resolution images for clarity on large screens. Avoid overly complex or dark images that may conflict with the title text.
  Text-Only Option. If no appropriate or approved imagery is available, or if imagery is not permitted for the subject matter, the Title | Text Only layout provides a clean, professional alternative.
Learn more about ORNL presentations
  https://ornl.sharepoint.com/sites/branding/SitePages/presentations.aspx

## Slide 2: Introduction

## Slide 3: SNS Layout
H- stripped to p
2.5
DTL
86.8
CCL
402.5 MHz
805 MHz
SRF, b=0.61
SRF, b=0.81
186
387
1000
LINAC; 1 GeV
Front-End: Produce
a 1-msec long, chopped, H-beam at 60 pps
upgrade
Accumulator Ring: Compress 1-ms long pulse to 700 ns
Liquid Hg Target
259 m
157 m
71 m
1300 MeV
SNS was originally designed for 1.4 MW with built-in upgrade provision

## Slide 4: SNS beam time-structure in linac and knobs for beam power
Macro pulse
(60 Hz spacing)
16.7 ms
Up to1 ms
No. of macro pulses in one second: up to 60 (1 ~ 60 pps)
Micro bunch
~2.5 ns
No. of micro bunches in one mini-pulse: up to 300 (100 ~ 300)
Bunch intensity: number of protons per micro bunch,
Controllable from Ion source
No. of mini-pulses in one macro pulse: up to 1100 (1 ~ 1100)
Mini-pulse
(Beam chopping
at LEBT)
One revolution in ring
T~910 ns at 1.3 GeV
Up to 0.8 T
Up to 1 ms

## Slide 5: Acceleration, accumulation, and extraction of beam pulse
Accumulator Ring
Liquid Hg Target
Linear Accelerator
H-
proton beam
thin carbon foil
From linear accelerator
accumulator ring
circulating proton beam
e-
e-
Turns
Beam current (A)
In Ring
In Linac
38 mA
1.4-MW
This happens in 1 ms, and repeats
60 times a second or 5.2 million times a day
Each line corresponds to one mini-pulse, ~700 ns
Carbon foil

## Slide 6: Proton Power Upgrade Project

## Slide 7: Proton Power Upgrade Project Goals
Accelerator: upgrade or replace components to enable 2.8 MW beam operation
First Target Station: upgrade for 2-MW beam at 1.3 GeV, 60 pps
First Target Station
Second Target Station
Second target station (STS) is a separate project (received CD-1, CD-3a and CD-3b)
Beam distribution after STS
  45 pps to First Target Station (2.0 MW)
  15 pps to Second Target Station (0.7 MW)
  Beam energy per pulse ~ 46.7 kJ
2 MW
0.7 MW

## Slide 8: Baseline Beam Pulse distribution (all 60 Hz spacing)
FTS: 2 MW at 60 pps
(33.3 kJ/pulse)
FTS: 2 MW at 45 pps
(44.5 kJ/pulse)
STS: 0.7 MW at 15 pps
(46.7 kJ/pulse)
First Target Station
Second Target Station
FTS
STS

## Slide 9: PPU project scope
Radio Frequency (RF) system upgrades
Additions for new cryomodules
Upgrades for existing systems
Extraction
Collimators
Superconducting Linac upgrades
Add 7 new cryomodules
Conventional facility upgrades
Klystron gallery extension
RTBT stub
First Target Station upgrades
2 MW, at 1.3 GeV, 60 pps
Ring system upgrades
Primarily injection and extraction
FE
DTL
CCL
SRF, b=0.61
SRF, b=0.81
upgrade
Liquid Hg Target

## Slide 10: SNS beam power history
Initial learning
Ion source, HVCM, SRF, Foil challenges
Target improvement
Reliable operations
Target, RFQ challenges
Power ramp-up
PPU
Toward > 2.8 MW
Currently running at 2.0 MW

## Slide 11: Neutron production at 2.0 MW beam
Reliable 2-MW neutron production during routine user operations

## Slide 12: Toward > 2.8 MW

## Slide 13: How we get > 2.8 MW
Launched 2.8 MW initiative in September 2024 with goal
  Demonstrate 2.8-MW equivalent beam intensity and 2.0-MW beam operation at 45 pps on the first target station
Objectives
  Identify weak links and ‘unknown unknowns’ earlier
  Stress test in advance wherever possible
  Ensure margin (capacity, beam energy, beam current, beam loss, etc.), reliability and long-term sustainability, including some topics for operational improvements
  Staff training for future
Eight teams primarily accelerator performance and operational limits including team effort for proof-of-principle test at the end of every run cycle

## Slide 14: 2.8-MW demonstration status and plan
2.6 MW equivalent intensity
at 10 pps (Nov. 2025)
2.8 MW-equivalent pulse-intensity
at 10 pps (June 2026)
2.0 MW on FTS
at 45 pps (June 2027)
2.8 MW-equivalent pulse-intensity
at 30 pps (Dec. 2026)
2.3 MW equivalent intensity
at 10 pps (May 2025)

## Slide 15: Beam distribution with Third Target Station (TTS)
Beam split system (magnets)
Controls and diagnostics for three flavor beams
Third beam line
Third target station

## Slide 16: Examples of Beam Pulse distributions with TTS (all 46.7 kJ/pulse): 46.7 x 60 = 2.8 MW
FTS: 1.87 MW
at 40 pps
STS: 0.7 MW
at 15 pps
TTS: 0.23 MW
at 5 pps
FTS: 1.96 MW
at 42 pps
STS: 0.7 MW
at 15 pps
TTS: 0.14 MW
at 3 pps

## Slide 17: 3 MW beam (50 kJ/pulse) with TTS
FTS: 2.0 MW
at 40 pps (50 kJ/pulse)
STS: 0.7 MW
at 15 pps (46.7 kJ/pulse)
TTS: 0.25 MW
at 5 pps (50 kJ/pulse)

## Slide 18: Expanded accelerator capability opens new opportunities for science, applications, and national needs
FTS
STS
TTS