## Slide 1
Developing muon-catalyzed fusion as an abundant new source of energy

## Slide 2: Fusion is a safe, abundant, clean source of energy Introduction
Fusion of the deuterium in a stream of tap water could power a city.

## Slide 3: Plasma fusion requires stable 100,000,000 ⁰C plasma Introduction
The deuterium-tritium fusion reaction has the highest cross section.
A cutaway view of the ITER tokamak, scheduled to burn DT in 2039.

## Slide 4: Muons can catalyze nuclear fusion reactions at lower temperature Introduction
d
t
t
µ
µ
Muon comes into orbit
Muon forms chemical bond between Deuterium atom and Tritium atom
Nuclear fusion
µ
Muon Reactivation
µ
Energetic alpha
Energetic neutron
Muon Recycling
Negatively-charged muon enters
99%
Sometimes muon sticks to the alpha particle product of the fusion
1%
Squeezes nuclei together and fusion occurs

## Slide 5: Sticking was seen as the key issue
Muons
Proton Beam
Many muons lost
Small amount of energy
NC or LTS accelerator
Klystron drivers
Acceleron Fusion Confidential
Electricity
200 MW
110 MW
Industrial
Process Heat
100 MW
Electricity to the Grid
10 GeV
Accelerator and muon production target
1 muon
Fusion cell and
breeding blanket
* 20 MeV
100 GeV
Balance of Plant
10 GeV/muon
40% efficient
40 GeV
30 GeV
Fusion Cell
Sticking-imposed limit of 300 fusions/muon
Rankine (steam) cycle balance of plant
25% recirculating power
fusions/muon
5000

## Slide 6: Energy balance
Muons
Ion Beam
Muons collected by fields inside target
Large amount of energy
New Approach
NbSn SC Accelerator
Magnetron Drivers
Brayton (helium) cycle balance of plant
Acceleron Fusion Confidential
4 GeV
Accelerator and muon production target
1 muon
Fusion cell and
breeding blanket
* MeV
10.2 GeV
Balance of Plant
GeV/muon
8.8 GeV
5 GeV
recirculating power
fusions/muon
300
64%
4
45%
34
efficient
3.1 GeV heat recycling 0.5 sec heat
3.6 GeV
Sticking-imposed limit of 300 fusions/muon
Fusion Cell

## Slide 7: Sticking may decrease with density Background
Ref: K. Nagamine, 2008
1000
200
500
250
100
H. Rafelski theory
170
330
Both experiment and theory predict that sticking decreases with density.
Data from four experimental groups is shown.
At high density, the measured sticking is uniformly lower (better) than predicted by theory
Density is stated as a fraction of liquid hydrogen atomic number density.
Sticking limit on the number of fusions per muon

## Slide 8: Diamond Anvil Cell
DAC paper submitted for publication and available on arXiv!
DAC compresses DT mixture to extreme pressures (densities up to 2.2 LHD)

## Slide 11: Loading Tritium into the U-beds

## Slide 12: Loading the Cell with Liquid DT
DT gas handling system paper in review and soon to be available on arXiv!

## Slide 13: Compression of the Liquid DT to a Solid

## Slide 14: 2024/2025 Beam Campaigns
MuFusE achieved first tritium-operation in our diamond anvil cell in October 2024
  World-record static DT pressure of 990 MPa: ~3 times higher than previous highest
  First μCF data collected at densities φ > 1.45 LHD
For 2025, significant engineering work to increase DAC volume, upgrade detectors and optics, and improve DAQ to handle fusion neutron pileup during DT operations
Data collected from 5 hydrogen compressions during 2025 beam period:
  3 DD + 2 DT cell compressions

## Slide 15: MuFusE Detector Systems
Neutron detectors record fusion activity
A muon entering the diamond anvil-cell is registered by the entry detector, triggering neutron detector waveform acquisition
Fusion catalysis ends with presumed sticking event
Muon decay electrons induce two-panel hits on the electron detector system

## Slide 16: Fusion Observation!
We observe both DD & DT μCF neutrons from our diamond anvil cell!
Events selected using pulse-shape discrimination.
DT events undercounted here due to pileup - accounted in full kinetics analysis workflow.

## Slide 17: MuFusE 2025 - DT Results (T<150K)
MuFusE Preliminary
MuFusE Preliminary
MuFusE Preliminary
Total cycling rates & non-decay loss probabilities determined from loss timescale of fusion events together with total detected energy yields.
50% tritium compression exhibits fastest absolute cycling rate observed in an equilibrated isotopologue mixture. In progress: analysis of sub-process kinetics, higher temperature runs, and loss sources.

## Slide 18: Pion and Muon Production
▶ A high-energy ion beam strikes the production target, initiating a hadronic cascade.
▶ Negative pions are produced primarily through ∆-resonance excitation in nucleon-nucleon collisions.

## Slide 19: Pion and Muon Production
▶ A high-energy ion beam strikes the production target, initiating a hadronic cascade.
▶ Negative pions are produced primarily through ∆-resonance excitation in nucleon-nucleon collisions.
▶ High-energy spallation neutrons propagate through the target and contribute a secondary pion-production channel.

## Slide 20: Pion and Muon Production
▶ A high-energy ion beam strikes the production target, initiating a hadronic cascade.
▶ Negative pions are produced primarily through ∆-resonance excitation in nucleon-nucleon collisions.
▶ High-energy spallation neutrons propagate through the target and contribute a secondary pion-production channel.
▶ Pion loss via ∆-resonance absorption sets an effective upper limit on target thickness.

## Slide 21: Pion Production: Model Uncertainties
▶ d 2 σ/d Ω dE quantifies π− yield as a function of production energy and angle.
▶ It directly constrains pion production rates, absorption, and the forward trajectories that seed secondary production.
▶ Across BIC, INCL++, and Bertini models with and without high-precision neutrons, predicted yields vary by up to a factor of 2.
▶ Direct measurement is essential to constrain model predictions and reliably optimize the muon source.

## Slide 22: Experimental Overview
Beam and Production Target
▶ 2 H and 4 He beams at ∼1 GeV/u
▶ Novel target materials
▶ Variable-width target
Momentum Resolution & Coverage
▶ Trajectory-tracking detectors
▶ Dipole bending magnet
Angular Resolution & Coverage
▶ Narrow collimator
▶ Rotating detector array
Negative Pion Identification
▶ Magnet charge filtering
▶ Cherenkov electron veto

## Slide 23: Beamline and Facility
NASA Space Radiation Laboratory at Brookhaven National Laboratory
▶ A) BNL’s Booster provides ions of all species to RHIC and NSRL
▶ B) Deuterons are supplied by the Tandem Van de Graaff accelerator
▶ C) The NSRL beam is supplied to target room with experimental support facilities

## Slide 24: Conceptual Fusion Power Plant Design

## Slide 25: Conceptual Fusion Power Plant: Fusion Core

## Slide 26: Technological Applications
Muon-catalyzed fusion is the most efficient process known for the accelerator-driven production of fast neutrons. Applications include:
  Production of electricity
  Neutron source for fusion materials testing
  Industrial production of tritium
  Industrial production of medical isotopes
  Recycling of used nuclear fuel