## Slide 1: Radioisotope Production at SNS (RIPS)
June 11th, 2026
Justin Griswold – Radioisotope Science and Technology Division
New Science and Applications at the SNS Workshop

## Slide 2: Proton Power Upgrade provides opportunity for excess beam power to produce radioisotopes
First Target Station
Second Target Station
FTS: 2.0 MW
at 40 pps (50 kJ/pulse)
STS: 0.7 MW
at 15 pps (46.7 kJ/pulse)
RIPS: 0.25 MW
at 5 pps (50 kJ/pulse)
Year | Power | Power Capability (predicted) | Approx. Power Margin | Maximum Beam Energy
2023 | 1.55 MW | 1.55 MW | 105 kW | 1.1 GeV
Today | 2.0 MW | 2.8 MW | 800 kW | 1.3 GeV
2035 (post STS) | 2.7 MW | 3.0 MW | 300 kW | 1.3 GeV
Potential Radioisotope Production Station

## Slide 3: Potential Beam Parameters – Radioisotope Production Target Station (RIPS)
Proton kinetic energy: 1.3 GeV
Beam energy per pulse: 50 kJ/pulse
Pulse length: 700 ns
Repetition rate: 5 Hz
Proton stopping range to 30 MeV in Th:
  RIPS (1.3 GeV): 78 cm
  BLIP (200 MeV): 4.8 cm
  IPF (100 MeV): 1.5 cm
  BLIP at BNL: 66-200 MeV protons (~150 µA)
  IPF at LANL: 100 MeV protons (~275 µA)
  RIPS: 1.3 GeV protons (192 µA)

## Slide 4: Radioisotope Production at SNS (RIPS) Workshop Hosted at ORNL in September 2023
Subject matter experts in high-energy accelerator radioisotope production and isotope separation techniques from five countries, four DOE national labs, and the DOE Office of Isotope R&D and Production attended the workshop
Accelerator physicists from BNL, LANL, LBNL, TRIUMF, CERN, PSI, and ILL presented
Key takeaways were importance of target design/survivability, safety considerations, and complexity of ISOL

## Slide 5: LDRD project initiated in FY24 to investigate the viability production of novel radioisotopes at the Spallation Neutron Source.
Identify isotopes of interest through the modeling and simulation of prospective irradiation parameters and target compositions
Provide a design concept for an experimental/demonstration facility
Develop a target design concept that can receive high energy beam pulses from the SNS accelerator
Identify enhanced isotope separation methods for SNS produced radionuclides

## Slide 6: Diverse team with experts in accelerator physics, isotope production, and separations.
STS
Yongjoong Lee
PSD
Charlie Rasco
ISED
Justin Griswold
Ethan Asano
Jonah Duran
Dave Rotsch
Adam Stevenson
Dan Stracener
NSCD
Sarah Cousineau
Sang-ho Kim
Fulvia Pilat

## Slide 7: Specific Aim #1: Identify isotopes of interest through the modeling and simulation of prospective irradiation parameters and target compositions

## Slide 8: Radioisotope Yield Calculations
Identified Critical Radionuclides
Identified Potential Targets
Beam Parameters and Codes
Finalized list of seven radionuclides based on need, physical properties (i.e. half-life), and production at other facilities
Targeted alpha therapy cancer treatment radioisotopes 225Ac (t1/2 = 9.92 days), 225Ra (decay parent of 225Ac, t1/2 = 14.8 days), and 230Pa (t1/2 = 17.4 days)
Beta emitters used for cancer therapy and SPECT imaging 111Ag (t1/2 = 7.42 days), 106Ru (t1/2 = 371.8 days), 155Tb (t1/2 = 5.35 days), and 161Tb (t1/2 = 6.96 days)
Thorium
Uranium
Tungsten
Tantalum
1.3 GeV Proton Beam
100 MeV energy deposition (target length varied)
200 μA beam current
Varied irradiation time from 3 to 14 days
Various physics models were used within each code:
FLUKA
PHITS
MCNP (coupled with PHITS-DCHAIN for activation/decay)
GEANT4 (coupled with PHITS-DCHAIN for activation/decay)
Simple thick thorium target model used for simulations (~620 g)

## Slide 9: Simulations revealed diverse inventory of radionuclides that could be produced in significant quantities through proton irradiation of a thorium target

## Slide 10: Sample Radioisotope Yield Calculations (225Ac, t1/2 = 9.92 days)
Significant variation observed between models
Thorium yields consistently outperformed all other targets for benchmark isotopes
Thick Thorium Target Irradiation
Thick Uranium Target Irradiation

## Slide 11: Significant Quantities of Various Medical Radionuclides Produced (Assumes 14-day irradiation of 620 g Th target)
Thick thorium (620 g, 7.5 cm thick) target degrades beam by ~100 MeV
The diversity of radionuclides produced at 1.3 GeV allows for flexibility as isotope demands shift
Significant science and engineering challenges remain for target design, target cooling, shielding, transportation, and post irradiation processing
Isotope | Half-life (d) | Activity (Ci) | Application
106Ru | 371.8 | 3.3–8.3 | β therapy
111Ag | 7.45 | 99–293 | SPECT
155Tb | 5.32 | 2.1–34 | SPECT
161Tb | 6.89 | 0.07–2.0 | β therapy
225Ac | 9.92 | 87–117 | α therapy
225Ra | 14.9 | 8.8–38 | α therapy
227Ac | 21.8 (y) | 0.2–0.4 | α therapy
230Pa | 17.4 | 3.6–28 | α therapy

## Slide 12: Specific Aim #2: Develop design concept for an experimental/demonstration facility.

## Slide 13: Experimental Test Station Concept
Concept test station at SNS linac dump area has been developed.
Protons are routinely routed to the linac beam dump, and energy can be varied from 800-1300 MeV.
Maximum power for beam studies is 7 kW.
Recent images of the Linac beam dump
Designed for easy access to irradiated targets.

## Slide 14: Experimental Test Station Concept
A simulated test irradiation was performed to model target survivability and radiation dose
Irradiation parameters:
  0.25 mm thorium target disc
  SS316 target capsule
  1kW
  1.3 GeV
  48 hours
Temperature and transient structural analysis were performed using ANSYS
Temperature analysis served as input to structural analysis and confirmed temperatures well below melting
Structural analysis showed that tensile and yield stresses were less than ASME thermal stress limits

## Slide 15: Experimental Test Stand Concept
MCNP6.2/CINDER2008 were used to calculate activation yields and dose rates.
After 24 hours of decay, the calculated dose from the activated target is less than the administrative limit of 100 mR/hr at 30 cm distance.
Top view of the decay dose (left) at EOB and (right) after 24 h of decay time
Top view (left) and side view (right) of the irradiation port surrounded by portable concrete shielding (yellow).

## Slide 16: Specific Aim #3: Develop a target design concept that can receive high energy beam pulses from the SNS accelerator.

## Slide 17: Production Target Concept
Five thin thorium discs (0.5 mm) encapsulated with graphite shock absorbers within 316L austenitic stainless-steel capsule.
Includes modular, two-cassette system with efficient cooling channels.
Each cassette can hold up to 20 capsules (200 thorium discs total).

## Slide 18: Production Target Concept
A super-gaussian (flat-top) beam profile is assumed with 700 ns pulse length, 250 kW beam power, and 1.3 GeV beam energy
Maximum energy deposition for a thorium disc was calculated with FLUKA to be 33.1 MeV/cm
Finite element simulations with ANSYS were performed to analyze steady-state/transient thermal and structural analysis.
Concluded that this thorium target design should withstand a 14-day irradiation
The strain response of the target capsule to a single beam pulse. Shown are the maximum, average, and minimum values of the principle elastic strain.
Initial concept of water manifold for coolant flow. Assumed mass flow rate of 1 kg/s.

## Slide 19: Specific Aim #4: Identify enhanced isotope separation methods for SNS produced radionuclides.

## Slide 20: Isotope Separation Methodology
Chemical separation methods developed for activated thorium targets have been developed in other studies, such as the Tri-Lab Production of 225Ac with BNL and LANL.
Current ORNL facilities such as the Radiochemical Engineering Development Center, or future facilities like the Radioisotope Processing Facility could be used for isotope processing.
Advancements in offline radioactive electromagnetic isotope separation are needed to ensure high specific activity medical radioisotopes.
Six-column separation process employed for Ac-225 recovery from thorium metal in Accelerator-produced Ac-225 project

## Slide 21: Closing Remarks and Next Steps to Making RIPS a Reality
Can utilize reliable surplus of SNS beam power for large-scale radioisotope production without new accelerator construction.
Models predict significant quantities of medical radionuclides can be produced using 1.3 GeV protons on a thorium target.
Diverse portfolio of nuclides enables rapid adaptation to changing market needs.
Further development of experimental test stand concept is essential to validating theoretical production yields and providing radiotracers for additional chemical separations development.
Enhanced radioactive mass separations could unlock ability to produce carrier-free radionuclides.
First Target Station
Second Target Station
Potential Radioisotope Production Station

## Slide 22: Acknowledgements
RIPS TEAM
Research sponsored by the Laboratory Directed Research and Development Program of Oak Ridge National Laboratory, managed by UT-Battelle, LLC, for the U. S. Department of Energy.
STS
Yongjoong Lee
PSD
Charlie Rasco
ISED
Justin Griswold
Ethan Asano
Jonah Duran
Dave Rotsch
Adam Stevenson
Dan Stracener
NSCD
Sarah Cousineau
Sang-ho Kim
Fulvia Pilat
Thanks to:
S. Thomas
A. Woody
R. Palmer
I. Popova
D. Willis
R. Hoerres
P. Kankanamalage

## Slide 23: Thank You!

## Slide 24: Extra Slides

## Slide 25: Beam Power to First Target Station Recently Increased to 2.0 MW

## Slide 26
Yields (mCi) for 230Pa (t1/2 = 17.4 days) after 3-, 7-, 10-, and 14-day irradiations of thick thorium target
Peak production is ~10-20 Ci at 14 days

## Slide 27
Yields (mCi) for 111Ag (t1/2 = 7.45 days) after 3-, 7-, 10-, and 14-day irradiations of thick thorium target
Peak production is ~100-300 Ci at 14 days

## Slide 28
Yields (mCi) for 106Ru (t1/2 = 373.59 days) (t1/2 = 17.4 days) after 3-, 7-, 10-, and 14-day irradiations of thick thorium target
Peak production is ~30-90 Ci at 14 days

## Slide 29
Yields (mCi) for 155Tb (t1/2 = 5.32 days) after 3-, 7-, 10-, and 14-day irradiations of thick thorium target
Peak production is ~0.5-30 Ci at 14 days

## Slide 30
Yields (mCi) for 161Tb (t1/2 = 6.906 days) after 3-, 7-, 10-, and 14-day irradiations of thick thorium target
Peak production is ~0.05-2 Ci at 14 days

## Slide 31: Study Case: Ac-225/Ra-225
Promising preclinical and clinical results for targeted alpha therapy with Ac-225
  Estimated annual global demand: 670 Ci (2.5 TBq) for 2 million patient doses per year
  Current global supply: 1.7 Ci (63 GBq)
    Main source: Ac-225 from fissile U-233 via Th-229: 1.1 Ci (41 GBq)

## Slide 32: Beam Parameters – Radioisotopes Prod. Target Station (RIPS)
Proton kinetic energy: 1.3 GeV
Beam energy per pulse: 50 kJ/pulse
Pulse length: 700 ns
Repetition rate: 5 Hz
  FTS: 40 Hz (2.00 MW)
  STS: 15 Hz (0.75 MW)
  RIPS: 5 Hz (0.25 MW)
Time averaged beam current: 192.3 uA
  BLIP/BNL: 165 uA@200 MeV
  IPF/LANL: 450 uA@100 MeV
Proton stopping range to 30 MeV in Th:
  RIPS (1.3 GeV): 78 cm
  BLIP (200 MeV): 4.8 cm
  IPF (100 MeV): 1.5 cm
RIPS offers huge potential for mass production of Ac-225/Ra-225:
Theoretical Yields at E.o.B: 10 Days Beamtime |  | 
 | Ac-225 @ E.o.B | Ra-225 @ E.o.B
RIPS/ORNL | 15.9 TBq | 1.66 TBq
BLIP/BNL | 0.85 TBq | 0.03 TBq
IPF/LANL | 0.16 TBq | 1.78 GBq

## Slide 33: Target Model – Isotopes Yield Estimates
Close up view of target capsule cross section
Target Material: Thorium
Th-disc dimension: Φ 60 mm x t 2.5 mm (82.8 g)
Target Layout:
  Th-disc is contained in SS316L capsule
  Flexible graphite sheets are placed between the Th-disc and capsule window
  Radioisotopes production unit consists of 20 capsules containing Th-discs
  Water coolant channel with 2.25 mm width between the target capsules
  Radioisotopes production unit and coolant are housed in a pressure vessel made of SS316L
Capsule Window:
T = 0.25 mm
Capsule Rim
Flexible Graphite Sheet:
T = 0.127 mm (5 mil)
Target:
T=2.5 mm

## Slide 34: Ac-225/Ra-225 Activities: 10 days Beamtime
Isotopes | E.o.B | 1 week decay
Ac-225 | 2.01 TBq | 1.32 TBq
Ra-225 | 0.26 TBq | 0.19 TBq
Chart: Target #
| Target1 | Target2 | Target3 | Target4 | Target5 | Target6 | Target7 | Target8 | Target9 | Target10 | Target11 | Target12 | Target13 | Target14 | Target15 | Target16 | Target17 | Target18 | Target19 | Target20
Ac-225 (JEFF-3.3): 10d beamtime; 0s decay | 84600000000 | 93300000000 | 99900000000 | 99600000000 | 104000000000 | 106000000000 | 109000000000 | 105000000000 | 103000000000 | 107000000000 | 100000000000 | 103000000000 | 105000000000 | 102000000000 | 103000000000 | 102000000000 | 101000000000 | 97800000000 | 94700000000 | 93200000000
Ac-225 (JEFF-3.3): 10d beamtime; 1w decay | 56200000000 | 61700000000 | 65800000000 | 66300000000 | 68200000000 | 70400000000 | 71100000000 | 69800000000 | 67900000000 | 70500000000 | 65800000000 | 67200000000 | 69000000000 | 66600000000 | 67300000000 | 66500000000 | 66700000000 | 64000000000 | 62000000000 | 61300000000
Ra-225 (JEFF-3.3): 10d beamtime; 0s decay | 12600000000 | 13000000000 | 13100000000 | 15300000000 | 12300000000 | 14800000000 | 12200000000 | 15500000000 | 13600000000 | 13600000000 | 12900000000 | 11800000000 | 14000000000 | 12100000000 | 12500000000 | 12200000000 | 13000000000 | 11700000000 | 11400000000 | 12100000000
Ra-225 (JEFF-3.3): 10d beamtime; 1w decay | 9130000000 | 9420000000 | 9480000000 | 11100000000 | 8870000000 | 10700000000 | 8840000000 | 11200000000 | 9800000000 | 9840000000 | 9290000000 | 8550000000 | 10100000000 | 8710000000 | 9060000000 | 8800000000 | 9380000000 | 8450000000 | 8220000000 | 8710000000

## Slide 35: Ac-225/Ra-225 Activities: Effective
Ac-225/Ra-225 Yield Efficiency:
  Chemical separation yields:
    Ac-225/Ac-227: 44%
    Ra-225: 98%
  Resonant laser ionization and mass separation
    Collection efficiency: 10%
Ac-225/Ra-225 Yields per 10 day run cycle: 0.11 TBq
  Ac-225: 53 GBq (4% of activity at 1 week decay)
  Ra-225: 184 GBq (98% of activity at 1 w. decay)
    60 GBq of Ac-225 of can be isolated after a 7-day operational cycle of the generator
About 23 times 10-day long annual run cycles would meet the global demand of 2.5 TBq to treat 2 million patients
  More energy budget with 1.3 GeV beam could be explored by installing more downstream target capsules to improve the Ac-225 yields
  Breakthrough in R&D in Ac-225 separation will improve the yields
A.K.H. Robertson et al.,
Inorganic Chemistry 2020 59 (17)
12156-12165
Johnson, J.D et al.,
Sci Rep 13, 1347 (2023)
Y.M. Palenzuela et al., Front. Med.
Vol. 8-2021

## Slide 36: Flexible Graphite: Heat Conductor and Shock Absorber
If capsules are EB welded in vacuum:
  Water coolant pressure could form thermal contacts between target discs and capsule with thermal contact conductance of 5000 W/m2/K
If capsules are laser beam welded in sub atmospheric helium pressure:
  Estimated thermal contact conductance > 10000 W/m2/K
Flexible graphite is a soft material commonly applied as gasket material
  Low density: Consumes less energy budget
  Low stiffness and expandability upon compression: Shock absorber
  Higher thermal conductivity than any gaseous medium: Efficient heat removal
IPF target capsule at TRIUMF

## Slide 37: Temperature
Wall Heat Transfer Coefficient:
  Channel gap x height: 2.25 mm x 60 mm
    Following LANSCE target design, the gap width could be reduced to 1.5 mm for efficient use of energy budget
  Channel water speed: 3 m/s
  Dittus-Boelter relation: 14243.3 W/m2/K
Beam energy deposition in dE/dz [MeV/cm]
  Capsule: 24.2 MeV/cm
  Flexible graphite: 4.71 MeV/cm
  Target disc: 33.1 MeV/cm
Maximum Steady Temperature:
  Capsule:
    Bulk: 63 C
    Water contacts: 55 C < boiling point
  Flexible graphite: 185 C
  Target disc: 191 C
Temperature increase per pulse:
  Capsule: 12.5 C
  Flexible graphite: 13.7 C
  Target disc: 53.5 C

## Slide 38: Some Thoughts …
With a 250 kW class RIPS target as presented, only about 0.1 GeV of 1.3 GeV energy budget is used meaning about 1.2 GeV of energy budget is still available
  Room for more target capsules in the downstream region of the presented target concept
    Increased production of medical isotopes with higher activities than presented
  Use 1.2 GeV remaining energy budget and fast neutrons for nuclear materials study
    Serving for high power targetry and fusion R&D where system lifetime is constrained by unknown post-irradiation material properties
  Muon target station in the upstream region of the RIPS target
    Muon beamline will supplement the existing neutron beamlines at ORNL for advancement of materials sciences (3.2 MeV/cm energy loss in graphite)
  Fast neutrons from the target could be guided to electronics irradiation station
    Existing electronics irradiation station does not the demand from the industry. The flux available from the RIPS target will largely exceed that of the ChipIr facility at ISIS, UK which uses a 32-kW solid tungsten spallation target as neutron source
Muon Target at J-PARC
ChipIr at TS2/ISIS

## Slide 39: Temperature
Heat transfer models used:
  Conductive heat transfer
  Convective heat transfer
    Buoyancy flow model in air
  Radiative heat transfer: P1 model
Maximum temperatures:
  Thorium disc/capsule: 129 C
  Vessel: 103 C

## Slide 40: Stress
Peak maximum principal stresses in structural components:
  Capsule: 11.5 Mpa << YS; UTS
  Vessel: 71 MPa < 1/2*YS; 1/3*UTS
    Strain hardened aluminum – Al5052-H38
      YS: 248 Mpa
      UTS: 276 Mpa
    Bottom wall thickness could be increased to reduce stress from the 1 bar air towards the accelerator vacuum

## Slide 41: Beam Parameters Used for Study
  Target shall be cooled only passively by conductive, convective, and radiative heat transfer
  The dose from the target after a week decay time after end of bombardment shall not exceed 10 mrem/hr at 30 cm from the port
Beam parameters:
  Beam energy: 0.8-1.3 GeV
  Pulse length: 1.0 ms with 1 – 60 Hz rep. rate
  Beam size: 8 mm; 3 mm
    Switching off last two quads for beam expansion
  Proton current: 4.8e12 p/s (0.77 uA)
  Beam power: 1.0 kW
  Beamtime: 20 hours
Potential target location

## Slide 42: Pilot Target Model
Target module consists of four components
  Target capsule made of SS316L
    Design follows the concept presented for SpA 2
  Target disc made of thorium
    Disc thickness: 0.25 mm (8 g)
  2 x flexible graphite sheets: 0.127 mm thick
  Retractable vessel made of Al5052
    Docked to the target port with bellow with a required stroke needed to free beam passage when not in use
      No need to break the accelerator vacuum for target handlings
    Houses the target capsule in atmospheric air environment separated from the accelerator vacuum
    Al5052 was chosen to reduce post radiation decay dose

## Slide 43: Target Model – Isotopes Yield Estimates for Test Irradiation
Dose from the target reduces to a manageable level (10 mrem/h@30 cm) after 5 days cooling
Isotopes yields:
  Ac-225 (t1/2 = 9.92d): 66.8 μ Ci (2.5 MBq) at E.o.B
  Ra-225 (t1/2 = 14.8d): 9.4 μCi (0.35 MBq) at E.o.B
Isotopes | Activity [uCi] | Error [%]
Th-227 | 22.41 | 3.4
Ac-227 | 0.10 | 2.0
Ac-225 | 66.76 | 2.1
Ra-225 | 9.38 | 4.2
Ra-223 | 20.59 | 3.7
Dose (mR/hr)

## Slide 44: Experimental Target Station
Demonstration of a miniature scale full cycle process from target manufacturing through 1.3 GeV irradiation, remote handling to isotopes separation
Manufacturing of target capsule with laser beam welding in sub atmospheric pressure helium
  Demonstration of manufacturability of the 250-kW target with in-beam thermal and mechanical characterizations
Simulation of target capsule handling and target disc extraction
Validation of isotopes yields:
  Post irradiation measurement of Ac-225/Ra-225 activities using gamma and alpha spectroscopy
  Chemical separation of Ac-225/Ac-227 and Ra-225 from irradiated Th-target
  Separation of Ac-225 from Ac-225/Ac-227 compound using resonant laser ionization and off-line mass separation
Chart: Isotopes Yields Normalized to 1.3 GeV
| 1300 | 1200 | 1099.9999999999998 | 999.99999999999989 | 899.99999999999989 | 799.99999999999989 | 700 | 600 | 500 | 400 | 300.00000000000006 | 200.00000000000003 | 100.00000000000003 | 0
Normalized Ac-225 Yields | 1 | 1.0021 | 1.0606 | 1.0392 | 1.0791 | 1.1035 | 1.2191 | 1.282 | 1.4023 | 1.3795 | 1.3618 | 1.1924 | 0.67439 | 0
Normalized Ra-225 Yields | 1 | 1.1068 | 0.99016 | 0.995 | 1.1261 | 1.2037 | 0.99997 | 1.2788 | 0.91762 | 0.83497 | 0.5632 | 0.37383 | 0.038849 | 0

## Slide 45: Initial Production Target Model Design Concept and Survivability
Th-disc dimension: Φ 60 mm x t 0.5 mm (16.6 g)
  Thin target to avoid beam pulse induced coherent longitudinal stress wave interference and to facilitate chemical separation of the isotopes by increasing surface to volume ratio
Target Layout:
  5 Th-discs are contained in SS316L capsule
  Other facilities use Inconel 718: Higher strength, but potential Nb-94 waste disposal issue (>0.2 Ci/m3) with 250 kW beam power
  Flexible graphite sheets are placed between the Th-discs and capsule window
    Efficient conductive heat transfer to water
    Short pulse beam induced shock absorber
    Reduced abrasive fretting of target capsule
  Steady-state temperature analysis:
  Capsule: 63 C (55 C at face)
    Bulk: 63 C
  Flexible graphite: 185 C
  Target disc: 191 C

## Slide 46: Steady Stress
Water pressure: 2 bar following BLIP
Peak maximum principal stress:
  Shell: 163 Mpa (less than 235 Mpa (YS) and 560 Mpa (UTS) of SS316L)
    Maximum stress caused by bending at the capsule window-rim interface due to water pressure => room for further optimization
Peak maximum principal stress:
  Target: 2.2 MPa (less than 144 Mpa (YS) and 219 Mpa (UTS) of Th)
  Flexible graphite: 210 kPa (compression)

## Slide 47: Dynamic Transient Structural Analysis – Capsule
Maximum principal strain variance:
  Number of beam pulses at 5 Hz for 10 days: 4.32e6
  Δε = 0.053% < fatigue limit

## Slide 48: Dynamic Transient Structural Analysis – Target Disc
Maximum principal stress amplitude:
  Coherent interference of longitudinal stress waves in the thickness direction is smoothened
  Longitudinal waves in the radial direction contributes most to the dynamic stress
  Δσ = 27 MPa = 0.188*YS; 0.123*UTS
Fatigue life estimate:
  No data on fatigue strength of thorium
  Rule of thumb estimate:
    Good chance that the maximum stress amplitude is below fatigue limit as Δσ << UTS/2
Maximum dynamic stress peak in flexible graphite sheets is below 1 Mpa and maximum strain variance is below 0.2%
  Little concern about fatigue failure of flexible graphite

## Slide 49: Dynamic Transient Structural Analysis – Thick Target Disc
Maximum principal stress amplitude in 2.5 mm thick thorium target disc:
  Coherent interference of longitudinal stress waves in the thickness direction is visible
  Δσ = 1.03*UTS; Δσ = 0.68*UTS => Most probably fail under 4.32e6 fatigue cycles

## Slide 50: Mass Distribution in p+238U Reaction at Various Energies
50 MeV
Data generated and provided by Dr. A. Gottberg for RIPS Workshop, September 2023

## Slide 51: Mass Distribution in p+238U Reaction at Various Energies
500 MeV
Data generated and provided by Dr. A. Gottberg for RIPS Workshop, September 2023

## Slide 52: Mass Distribution in p+238U Reaction at Various Energies
500 MeV
1000 MeV
Data generated and provided by Dr. A. Gottberg for RIPS Workshop, September 2023

## Slide 53: Mass Distribution in p+238U Reaction at Various Energies
500 MeV
1000 MeV
1400 MeV
Data generated and provided by Dr. A. Gottberg for RIPS Workshop, September 2023