## Slide 1: Beam Test Facility Performance Update
Presented to the SNS Accelerator Advisory Committee
Alexander Aleksandrov
SNS Beat Test Facility Manager, APBIIS
March 9, 2017

## Slide 2: SNS Beam Test Facility (BTF) layout, former ITSF
Particles | H-
Energy | 2.5 MeV
Current | < 50 mA
Pulse width | < 1 ms
Rep rate | < 60 Hz
Beam Power | < 7.5 kW
Ion Source and LEBT
RFQ
MEBT
High Power beam stop
Low Power beam stop

## Slide 3: SNS Beam Test Facility goals
Acceptance test of the new RFQ
  Output beam parameters to satisfy SNS requirements
  Operational characteristics to be better than for old RFQ
Test stand for SNS accelerator systems development
  External antenna Ion Source
  New Beam Loss Monitor data acquisition
  New Timing Master
  PPS detectors
  …
Test stand for accelerator physics R&D
  Halo formation in high intensity beam
  …
Proton source for other applications
  Moderator Demonstration Facility
  …
Done
In progress
In progress
In planning

## Slide 4: BTF PPS enclosure
2.5 MeV proton beam
Two modes of operation
  50mA, 1ms, 60Hz =7.5 kW (high power)
  50mA, 50us, 10Hz = 63W (low power)
Restricted area surrounded by fence
  Interlocked gates
  Radiation Area when beam is on
  RWP, EPD are required inside the fence
Unrestricted area outside fence
  general personnel allowed
Credited PPS system
  1 Chipmunk
  20 mrem/hour prompt (2s)
  2.5 mrem/hour rolling avg (15min)
PPS and MPS functions controlled by
Chief Operator in CCR
24/7 operation is allowed when CCR is staffed

## Slide 5: Beam Test Facility readiness review August 2, 2016
Reviewed safety, organization and operational aspects
  Lead by Alan Tatum (ORNL)
  Mostly non-RAD reviewers
Did not find major problems
  21 pre-start action items
  11 post-start action items
All closed by now

## Slide 6: Approval and first beam
Received authorization to run the facility on September 6th 2016
First beam out of the new RFQ!
September 8, 2016
8 mA
Courtesy of R. Welton

## Slide 7: Measurements and tests required for RFQ characterization
Beam current (transmission)
Beam energy
Transverse beam emittance
Longitudinal beam emittance
Stable operation with nominal beam power (high power beam test)
Recovery after ion source replacement
Sensitivity to ion source replacement

## Slide 8: Short beam pulse (50ms) operation
BCM04
BS06
BCM04
BS06
RFQ RF field amplitude
Ion source is always at full duty factor (1ms, 60Hz)
MPS limits RFQ duty factor to 50ms, 60Hz
Timing system controls overlap of IS and RFQ pulses: 1Hz, 2Hz, 5Hz or 10Hz
RFQ pulse can be positioned anywhere inside IS pulse
No chopper at BTF
LLRF feedback transient

## Slide 9: RFQ output beam current vs. RF field strength
design set point -
83kV inter-vane voltage

## Slide 10: RFQ field strength absolute calibration
Courtesy of A. Zhukov
X-ray spectrum
cut off energy
cut off energy vs. RF amplitude
X-ray window
X-ray spectrometer

## Slide 11: Measure LEBT beam current to evaluate absolute value of RFQ transmission
Courtesy of R. Welton
88% transmission @44mA
Ion Source #6

## Slide 12: Beam energy measurement using Time-Of-Flight technique
Movable phase detector (BPM)
2520±20 keV
BPM04
Independently confirmed by magnetic spectrometer measurements

## Slide 13: Transverse RMS emittance is close to design
horizontal
vertical
x [mm]
y [mm]
x’ [rad]
y’ [radian]
normalized,
different currents, ion sources, MEBT optics
Particle distribution generated from measured emittances and traced back to RFQ exit (PyORBIT)

## Slide 14: Longitudinal beam parameters
Bunch energy spectrum
Energy view screen and slit
video camera
Beam Shape Monitor
screen image
Longitudinal profiles at different slit positions
Longitudinal emittance
[⁰]
[⁰]

## Slide 15: High Power Beam Test (4kW)
30mA
900ms
60Hz
50mA
900ms
demo
RFQ resonant error
RFQ RF amplitude
Beam current
4kW at 2.5MeV = 1.6MW at 1GeV
Courtesy C. Peters

## Slide 16: Dependence on the ion source
Source | installed | removed | Days tested | RF set point | LEBT beam current | MEBT beam current typ/max | Issues
#6 | Aug 2014 | Aug 24, 2016 | ~14 days | ~60 kW | ~60 mA | na | Edump dips (end of run) thin walled insulator
#6 | Aug 29, 2016 | Oct 11, 2016 | ~2 days | ~60 kW ~30 kW ~35 kW ~40 kW | ~60 mA ~13 mA ~22 mA ~33 mA | Na 8 mA 18 mA 26 mA | Struggled with alignment, extractor heating
#6 | Oct 14, 2016 | Nov 25, 2016 | ~10 days | ~50 kW ~55 kW ~70 kW | ~45 mA ~50 mA C. Target failure | ~32 mA ~44 mA ~50 mA | Aligned with dummy source, o-ring unloaded, full power RFQ operation test, bend mode, lost chopper target
x3 | Nov 28, 2016 | Dec 9, 2016 | ~11 days | ~36 kW ~35 kW ~43 kW |  | ~40 mA ~44 mA ~50 mA | 5D measurements no explicit Cesiation!
#3 | Dec 14, 2016 | Jan 25, 2017 |  | ~53 kW ~44 kW ~43 kW |  | ~46 mA ~40 mA ~29 mA | Edump struggles, beam decay, 2 min Cs partially recovered beam
x4 | Jan 25, 2017 | running | 20+ days | ~32kW |  | ~40mA | Lens 2 conditioning, plasma ignition, water line leak
Courtesy of R. Welton

## Slide 17: RFQ swap plan
~2months to integrate new RFQ in SNS Front End
  New vacuum and water controls
Need extended shutdown period
  Combine with IRP replacement
Detailed resource loaded RFQ swap plan is being developed
  Start BTF disassembly 1-2 months before RFQ move
  Plan includes reintegration of old RFQ to BTF
November 2017 is projected BTF decommissioning date
  Might change if IRP schedule changes again
Develop flexible BTF beam study plans to accommodate any scenario most efficiently

## Slide 18: BTF current beam use program
Ion Source testing in real environment
  External antenna source
Beam diagnostics development
  High dynamic range measurements
New SNS accelerator subsystems testing
  Controls, Power Supplies, etc.
Beam Dynamics Study
  Beam Halo Experiment
    Funded by NSF grant through University of Tennessee (S. Cousineau is PI)
    Support for Postdocs, students + some hardware
Computer simulations tools benchmarking
  PyORBIT linac simulation code

## Slide 19: High Intensity Beam Dynamic Experiment
To understand mechanism of halo formation
Inspired by results of 2001 LEDA halo experiment at Los Alamos
We plan to avoid known LEDA experiment deficiencies
Inject into simplest accelerator structure: FODO line
Measure halo in output beam
Reproduce results in computer simulations
State-of-the-art and beyond
Negative LEDA simulation result was explained by lack of knowledge of initial distribution
Measure initial particles distribution in 6D phase space
Has been never done anywhere
missed ingredient in LEDA experiment

## Slide 20
Develop 6D particles distribution measurement system
Build a test FODO line
Develop reliable halo measurement system

## Slide 21: 6D Phase space measurement principle
SLIT_X_1
SLIT_Y_1
SLIT_X_2
SLIT_Y_2
dxdy
BEAMLET
dxdydx´dy´
BEAMLET
SLIT_X_4
SLIT_X_3
RF deflector
BENDING MAGNET
Magnetic spectrometer for energy determination
RF deflector or other time resolving device for temporal degree of freedom
FARADAY CUP or other detector

## Slide 22: 6D Phase space measurement difficulties: #1 Scan Time!
1 2 …….. m
Total number of bins
Number of steps per degree of freedom
dimensionality
For
Total scan time at
Total scan time at
Tens of hours of uninterrupted available beam time are required

## Slide 23: 6D Phase space measurement difficulties: #2 Signal Strength!
For
current after all 6 slits
Number of particles in
beam pulse is
Number of particles after 6 slits: at the distribution center
at
at
at

## Slide 24: 6D Phase space measurement Implementation at BTF
Beam
Quadrupoles
2 pairs of movable slits for
x, x’, y, y’ selection
90-DEG. BENDING MAGNET (spectrometer)
Bunch Shape
Monitor (z)
Movable slit for energy selection (z’)
Faraday Cup
Movable
View Screen

## Slide 25: X-Y Slits arrangement
200-by-200 μm aperture

## Slide 26: 6D Phase space measurement progress
4D scan
  Well developed automated script
  Full scan takes ~5hours @5Hz
5D scan
  Uses separate 4D scans with different energy slit positions
  Produced several 3-4 energy slices sets, ~20hours each
    Limited by beam availability
6D scan
  Working on improving BSM sensitivity, scan speed
    Demonstrated measurement of few hundreds point in 6D phase space
Longitudinal profile measured after 5 upstream slits

## Slide 27: 6D Phase space measurement progress
Learning to manipulate large data sets
Learning to validate data
Learning to generate initial particle distribution for PIC simulation
  2D+2D+2D
  4D + 2D
  6D
x-x’ projection obtained from measured 4D distribution
x-x’ emittance from 2D scan
x projection obtained from 4D measured distribution (blue)
x profile from 1D scan (red)
x’-y’ projection obtained from measured 4D distribution
Courtesy of B. Cathey
x [mm]
x’ [mrad]
x [mm]
x’ [mrad]
x [mm]
x’ [mrad]
y’ [mrad]
charge [a. u.]

## Slide 28: High Dynamic Range measurements (halo)
Measure transverse profiles with > 106 dynamic range
  (Switch amplifier gain to overcome ADC bit depth limit )
Need to develop 2D emittance measurement with similar dynamic range

## Slide 29: FODO lattice design and simulation
RFQ
Units: cm
Courtesy of Z. Zhang
Energy slit
BSM
Matching quads
FODO line
Achromatic
bend

## Slide 30: FODO lattice design and simulation (PyORBIT, TraceWin)
Phase advance=80o, G=26.6 T/m
Phase space density plot in y plane
Beam sizes (m = 1)
Beam sizes (m = 3)
Courtesy of Z. Zhang
Determine minimum number of FODO periods
Determine required mismatch factor
Matched beam size
Determine required beamline aperture

## Slide 31: Permanent Magnet FODO line quadrupoles
Courtesy of A. Menshov
Mounting structure will allow changing phase advance of FODO line using different combinations of magnets and drift lengths
39 half-length magnets have been ordered
Magnet gradient:
G = 5.7367487 kG / 2.25 cm = 2.549666 kG/cm
Magnet strength:
G x L = 2.549666 kG/cm x 3.50 cm = 8.9238 kG

## Slide 32: BTF FY17-18 beam line extension plan
Timeline is determined by IRP replacement schedule
Phase I
  Add achromatic 180⁰ bend
  Install HDR emittance station
  Ready for operation in April/May 2017
  Determine need for collimation section in front of FODO line
Phase II
  Add matching section and FODO line
  Hardware ready in August/September 2017
  Install before or after RFQ swap

## Slide 33: Beam line extension Phase I
6D phase space measurements
Achromatic bend
High Dynamic Range emittance measurements

## Slide 34: Beam line extension Phase II
RFQ
FODO line
Matching
quadrupoles
High Dynamic Range
Emittance station
BSM
~6 months lead time
Low power
beam dump
Installation timeline will be driven by IRP replacement schedule

## Slide 35: Moderator Demonstration Facility
MDF layout
space for AP line
Neutron target with test moderator
Neutron beam lines
LDRD grant in FY15-16 to
Design proton beam line
Feasibility study of 2.5MeV Li target
Feasibility study of neutronics and instrumentation
Accelerator driven source of neutrons, neutron beam lines and instrumentation for R&D on prospective moderator designs with hands on access
(~60W of 2.5Mev protons)
MDF is feasible and of great importance for future source development (STS)

## Slide 36: Long Term BTF development
Building wall
Beam dynamics beam line
PPS fence
BTF area expansion would allow the two experiments to co-exist and to add other capabilities

## Slide 37: Summary
BTF has been successfully commissioned with beam
New RFQ demonstrated excellent operational parameters exceeding the old RFQ performance in all areas
RFQ swap is planned simultaneously with IRP replacement
BTF is indispensable test bench for SNS accelerator systems improvement and testing
BTF provides unique opportunities for general accelerator physics R&D
There is ongoing R&D program and well developed plans for near and mid term future