## Slide 1: Target Design Reaching for 2 MW
Presented to the SNS Accelerator Advisory Committee
Saulius Kaminskas
Structural Analyst
March 9, 2017

## Slide 2: What challenges are on the horizon?
2.0 MW
Target Problems are the same just
More Challenging:
Linear Increase
of Power leads to Nonlinear Increase of fatigue damage
Fatigue damage
Cavitation damage
Fatigue – Cavitation coupled damage
1.4 MW
Reliable Operation at 1.4 MW
Reliable Operation at 2.0 MW
Design Space Exploration and Optimization
Robustness and Reliability Optimization
Advanced design development technologies
are available to succeed:

## Slide 3: Fatigue life nonlinearity vs beam power
Material S-N curve – “316 Stainless Steel” from Fe-Safe DB
0.85 MW
1
3
2
5
6
4
8
7
1.4 MW power
1.7 MW power
~3.5 months
~10 days
8 – Inner Window
7 – Front Upper Rib
6 – Side Baffle Base
5 – Center Baffle Base
4 – Front Lower Rib Channel
3 – Center Baffle Front Lower
2 – Front Lower Rib
1 – Center Baffle Front Upper
~5 months
~7 months
Jet-Flow target pulse fatigue life at different locations (Fe-Safe results)
2.30 MW
2.00 MW
1.70 MW
“fatigue life” indicates the beginning of fatigue damage – not the predicted cycles to failure

## Slide 4
Jet flow target pulse fatigue damage – results summary
But study did not include:
Thermal fatigue
Weld fatigue
Material degradation
Cavitation damage
Fatigue – Cavitation damage interaction
Those factors will deteriorate structure even more at 2 MW
6 – Side Baffle Base
5 – Center Baffle Base
4 – Front lower Rib Channel
3 – Center Baffle Front lower
2 – Front lower Rib
1 – Center Baffle Front upper
Fatigue damages:
1.7 MW – 4 locations in ~10 days
2.0 MW – 6 locations in ~20 days
Structure will lose integrity resulting in:
  unknown stresses
  reduced target reliability
1
6
5
4
3
2
Addition of gas injection will soften
the impacts of beam on the target
Ultimate Strategy:
  Optimize design towards 2 MW without gas injection
  Add gas injection for substantial increase of reliability and longevity margins

## Slide 5
Von Mises stresses at side baffle,
20 micro sec – Max = 29.06 Mpa
Pulse pressure, mercury – Max = 36.3 Mpa
Side baffle shape optimization area – Minimize local stresses
Optimization variables - nodes
to move
Original Target Design – simplified FE model is sufficient
Local shape optimization with TOSCA – Minimize max pulse stresses at side baffle

## Slide 6
Local shape improvement is limited by global deformation
Global Structural Response needs to be addressed first
Problem is complicated:
Pulse wave is changing max stress levels and locations
Optimization surface (steel) is in contact with mercury surface
Local shape, optimized with TOSCA
Design space boundaries are changing during the optimization process
Max stress reduced from 29.09 MPa to 26.44 MPa

## Slide 7
Local shape optimization for fatigue durability:
Minimize: simax
Subject to: pjmin ≤ pj ≤ pjmax
Where: simax – max stress at ith stress concentration
pj – local parametric geometry features (nodal coordinates)
Global geometry optimization for vessel structural response: *
Minimize: fg ( s1max, s2max, . . . ,snmax )
Subject to: Pjmin ≤ Pj ≤ Pjmax
Where: fg – aggregate function of max stresses simax
simax – max stress at ith stress concentration
Pj – parametrized design features (geometric locations, etc.)
Problem formulations for fatigue
* Interactive Design Space Exploration – solution for this problem
NOTE: minimize simax
is replaceable by
maximize life cycles

## Slide 8
Global interactive target optimization process
Back to CAD
> Highest priority (value)
> Lowest priority (value)
Initial Design Concept (CAD)
Design Space Exploration
Shape Optimizations (Local)
Topology Optimization
Multi-Objective Optimization
Robustness/Reliability (Stochastic) Optimization
Good enough?
Design of experiment,
Response surfaces,
Sensitivity exploration
Predominantly at fatigue susceptible locations
With respect to variabilities and uncertainties
Stresses vs frequency,
Stresses vs mercury flow
Stresses vs stresses at
different locations
Material distribution on a basis of exploration results
NO
YES

## Slide 9
Abaqus extended tools – Package for advanced design development technology
FEA Multiphysics Simulations:
CFD (Hg flow)
Static (Thermal)
Dynamic (Pulse)
Optimization:
Parametric
Multi-objective
Stochastic
Design exploration
Process Integration
Non-Parametric Optimization for:
Shape
Topology
Fluid
Fatigue and Durability
Evaluation for:
Pulse
Thermal
cycles
Integrate, Optimize, Understand Sensitivities & Trade-Offs
Achieve optimum overall design under quantified uncertainty
Explore Design Space,

## Slide 10: Parametric design space exploration with Isight: Multi-objective optimization – fatigue life vs Hg pump speed
Higher Hg pump speed  lower thermal stress  higher fatigue life
At the same time:
Higher Hg pump speed  higher Hg pressure  lower fatigue life
For simplified target FE model:
Response surface Indicates the point of optimal pump speed for longest thermal fatigue life
The search for trade-offs among other operation parameters is also possible to maximize the vessel fatigue life
Thermal stresses
Max = 162 MPa
Hg flow pressure stresses
Max = 52 MPa

## Slide 11
Geometric design exploration with Isight
Target virtual mock-up test
Design variables:
Baffle distance from symmetry line
Baffle thickness
Design response:
Max Mises stress
Mock-Up model:
Drew Winder
Design response surface:
Design of Experiment:
3D Scatter plot

## Slide 12
Geometric design exploration with Isight
Target virtual mock-up test - 2D plots for trade-off analysis
Max Stress vs Baffle Location Distance
Max Stress vs Baffle Thickness

## Slide 13
Why conventional practices are not sufficient
for efficient target design development
Lessons from Hardware Tests:
Real testing is possible only by placing target in service
Time from design to PIE results is long and overlaps a number of new target installations needed in between
The number of samples is too small for statistical observations
Improvement of Analysis Accuracy:

## Slide 14
What are the conventional and
optimized design development strategies?
Optimization Driven Design Development makes the New Quality available
Optimize
Design
Build
Validate
Design
Build
Test
Design
Build
Test
Analyze
Costs
Time
Reduction of development time
Decrease in costs
Conventional
Design Development
Optimized
Design Development

## Slide 15
Examples of successful industrial applications
Volkswagen compressor bracket optimization
Conventional design
Optimization driven design
NASA Lunar Lander
size and shape optimization
Topology optimization
Topology interpretation
Model
Optimal design

## Slide 16
Examples of successful industrial applications
Coronary Stent shape optimization for fatigue
Finite element model
Optimization workflow

## Slide 17
Employ Design Exploration for the best
Target Geometry to minimize fatigue
(optimize locations of baffles, ribs, etc.)
Use the Shape Optimization to
lower Fatigue Damages
(optimize fillets, thicknesses, etc.)
Perform Robustness/Reliability Optimization with respect to Uncertainties (material, manufacturing, cavitation, beam irregularity, etc.)
Path forward reaching for 2MW
Adopt and develop optimization driven design technologies for the real mercury target concept:
Develop the optimal design of target ultimately performing
with existing constraints
  Design Exploration Techniques
  Topology Optimization
  Localized Shape Optimization
  Stochastic Analysis Techniques
  Robustness/Reliability Optimization
  Multi-Objective Optimization
Conclusion: Advanced design technology based strategy is the path to success reaching 2 MW
Next 2 years – focus on
Pulse Fatigue Life Improvement:

## Slide 18
Questions,
Comments…
Thanks for your attention