## Slide 1: Production ion source performance and progress on the external antenna source
Presented to the SNS Accelerator Advisory Committee
Robert Welton
APBIIS
March 8, 2017

## Slide 2: Content
The SNS ion source and test facilities
Performance of the production ion source, operational issues, improvements and R&D highlights
BTF ion source systems and start-up
The external antenna ion source
Outlook: meeting SNS requirements with both RFQs and supporting BTF operations

## Slide 3: 2016 AAC comments
No specific ion source recommendations just general comments…..
The ion source continues to run with good reliability, although this year there were several failures of the edump which turn out to have been related to a change in vendor for the alumina insulator. The problem now seems to be resolved by reverting to the original supplier plus increasing the insulator thickness in the weakest area. Through ongoing improvements, the source intensity continues to get better, although it is not yet to the point where one has a comfortable margin over the operational requirements (partly due to the still reduced RFQ transmission). Good progress in several areas - operation at reduced gas pressure, improvements on understanding and elimination of plasma outages, and operation with higher extraction voltage to reduce the emittance and improve the RFQ transmission.
Test Stand external antenna studies were resumed, with good results on long term stability. This external antenna source seems close to using for operations. For test stand studies of source performance variations and operation at higher extraction voltages, it would be good to get water cooling on the front slits so that source emittances can be made at full duty factor.
One expects that the source performance will continue to improve, since there is much activity worldwide on H- sources, and the SNS team are active participants in this community effort.
No LEBT valve yet on either ITSF or operational source. Committee still supports the installation of this valve in both locations at the appropriate time.

## Slide 4: The SNS ion source and the electrostatic Low Energy Beam Transport (LEBT)
Both systems were designed at LBNL and improved over the years at ORNL
RF-driven, internal antenna, Cs-enhanced, multicusp H- ion source has been operating on the SNS from the start of the facility
The Low Energy Beam Transport (LEBT) is composed of 2 Einzel lenses which match the extracted beam into the RFQ
Outlet aperture assembly
LEBT beam current measurement
2 +13 MHz

## Slide 5: Source testing areas now include the BTF!
Ion Source Test Stand:
ion source, LEBT, diagnostics
Tomco 120kW RF generator
Small test stand
Ion Source
Big Blue Box
Diagnostic chamber
Plasma diagnostics: Spectroscopy and RGA
ORNL baseline source #2,3,4,5,6,7 and external antenna sources x3, x4 can be installed interchangeably on the SNS accelerator (8100), test stand (8100) and BTF (8320)
Nearly identical electrostatic Low Energy Beam Transports (LEBT) are also installed, interchangeably in each facility
Ion source, LEBT, RFQ, diagnostics

## Slide 6: SNS ion source history: pushing source performance while maintaining high reliability
140 H- sources have been started up for n-production. In recent years ion sources have been pushed harder due to decreased RFQ performance while maintaining high availability typically >99%
Less sources, less variations
E-dump failures
Only source #3 makes ~38 mA
Decaying beams before developing proper conditioning
Ramping up the beam with many improvements
Year of ~40 mA MEBT currents
source leaks & contamination
Reduced RFQ transmission
large leak
Antenna failures
RFQ input current
7A·h
run

## Slide 7: 2016 SNS run schedule: planned source rotation
#2
#4
#2
#4
LEBT
change
LEBT
change

## Slide 8
Delivered record performance in 2016, extended source service cycle, no unscheduled source changes high availability!
source #2
1.3 MW power
Target fails
Cs 852
~55 kW
34-36 mA
26 sccm
Cesiation
source #4
chopper%
source #2
source #4
Increased
extractor
voltage
33-34 mA
30-37 mA
1 MW
1 MW
1.2 MW
RFQ
Extractor water line bursts
2016 run summary: significantly increased source service cycle up to 96 days (record 7 amp-hours!), no unscheduled source replacements (71, 48, 96, 78 day service cycles) !!
Source / LEBT availability 99.5% !!!
For the last 41 days the H- source injects 59 mA into the RFQ, with 36 mA exiting. The source is expected to remain for a total of 122 days, accumulating ~10 A·h!
RFQ input: 52-60 mA

## Slide 9: System issues and improvements made in 2016
2016 ion source/LEBT downtime (31/5554h= 0.6%) was led by
  water hose failures and consequences
  13 MHz RF & AC system issues
  plasma outages/voltage/arc/dips
These motivated some of the system improvements undertaken in 2016:
  Lengthened Source/LEBT HV water lines, thereby slowing the deposition of material in the water, implemented the use of clear tubing, inspection and routine replacement
  Added protection components (MOVs) to the AC side of the13 MHz amplifier
  Installed a larger, more accessible, 45kV steering deck
  Designed and built a new ion source cage in preparation for the BTF RFQ installation on the SNS accelerator.

## Slide 10: Upgrading HV water lines, steering deck & ion source cage
New ion source cage on ion source test stand
New 45kV steering deck inside source HV enclosure
Previous configuration
D. Curry
-65kV
-65kV
-45kV
-45kV
New and old extractor water feed lines FE
Removable 45kV control chassis
Big Blue Box
Allows the use of rack mounted controls chassis
Former location of 2MHz supply

## Slide 11: 2016 R&D highlights: improved RFQ transmission, refined LEBT beam current measurements & quantification of antenna wear
Beam studies in May 2016 and theoretical work showed that increasing the extraction field reduced emittance and improved RFQ transmission yielding a few more mA out of the RFQ: implemented during run
Beam studies showed that our LEBT beam current measurements were refined by increased focusing of lens 2.
Chopper target beam current measurements were performed on the test stand allowing direct comparison of this technique with BCM & FC measurements to continually refine our technique
Internal antenna wear measurements of the most plasma exposed surface showed 0.5 µm/day (0.1%/day) and that long service cycles (even greater than target cycles) would not be limited by antenna wear
Extractor at 0 kV
RFQ input current
RFQ output current
lens 1 voltage
lens 2 voltage

## Slide 12: Engineering projects: LEBT-RFQ gate valve, replaceable chopper target and upgraded emittance scanner
Allison scanner with cooled TZM front plates
Measure emittance under operational conditions
Status: in design
Goal: measurements in 2017
Existing Chopper target
New Chopper target
Isolate LEBT & RFQ vacuum
Status: prototype made, testing on test stand
Install during RFQ move to front end
Replaceable chopper target
Old design: Service requires removal of the critical RFQ end wall
New design allows easy service from LEBT side
Status: in design
Goal: use on test stand, parts ready during RFQ move

## Slide 13: The BTF Ion Source Systems
Steering Deck
Ion Source Cage
HV enclosure
LEBT tank
Isolation transformers
19kVA
HV conduit
Includes all electrical & mechanical components supporting the ion source and LEBT, extensive use of 80-20 frameworks + custom sheet metal
Complete safety interlock chain, water shutoffs
All HV structures have a min of 6” gaps (2.5x FOS)
~3000l/s

## Slide 14: The BTF ion source systems timeline
July 2013 Ion Source / LEBT systems design and acquisition work begins in earnest (weekly meetings)
July 2014 RFQ acceptance test
March 2014 First Vacuum in LEBT tank
August 2014 construction largely complete
August 2014 installed 1st ion source #6
July 2015 - RFQ fully conditioned to 1ms, 60Hz, 550kW
Aug 2015 1st plasma and HV source operation
March 2016 1st beam extraction in LEBT
April 2016 1st LEBT beam measurements
August 2016 BTF operational readiness review
Sept 2016 beam through the RFQ!
Oct 2016 high current beam routinely produced, transition to operations

## Slide 15: Table of ion sources tested on the BTF
Source | installed | removed | Days tested | RF set point | LEBT beam current | MEBT beam current | Issues
#6 | Aug 2014 | Aug 24, 2016 | ~14 days | ~60 kW | ~60 mA | na | Edump dips (end of run) thin walled insulator
#6 | Aug 29, 2016 | Oct 11, 2016 | ~2 days | ~60 kW ~30 kW ~35 kW ~40 kW | ~60 mA ~13 mA ~22 mA ~33 mA | Na 8 mA 18 mA 26 mA | Struggled with alignment, extractor heating
#6 | Oct 14, 2016 | Nov 25, 2016 | ~10 days | ~50 kW ~55 kW ~70 kW | ~45 mA ~50 mA C. Target failure | ~32 mA ~44 mA ~50 mA | Aligned with dummy source, o-ring unloaded, full power RFQ operation test, bend mode, lost chopper target
x3 | Nov 28, 2016 | Dec 9, 2016 | ~11 days | ~36 kW ~35 kW ~43 kW |  | ~40 mA ~44 mA ~50 mA | 5D measurements no explicit Cesiation!
#3 | Dec 14, 2016 | Jan 25, 2017 |  | ~53 kW ~44 kW ~43 kW |  | ~46 mA ~40 mA ~29 mA | Edump struggles, beam decay, 2 min Cs partially recovered beam
x4 | Jan 25, 2017 | running | 20+ days | ~32kW |  | ~40mA | Lens 2 conditioning, plasma ignition, water line leak

## Slide 16: The SNS external antenna source
Outlet
aperture
Internal Antenna Source
External Antenna Source
8 Cs2CrO4 dispensers loaded into the collar
Mounting
flange
Antenna
Electron Dump
Filter field
Cs Collar
AlN Plasma Chamber
PEEK cooling jacket
RF Plasma gun
Multicusp magnets
Designed and developed at ORNL in previous years
An alternative to the internal antenna source which does not depend on the ‘art’ of porcelain enamel airbrushing conducted by a single manufacture. Presently the internal antenna quality is high but in the past quality lapses have resulted in considerable SNS downtime in 2010-2011. Source also requires much less RF power.
2015 AAC committee observation & findings, “It was also very nice to see that external antenna development has resumed on the test stand, since ultimately this will most likely be the preferred configuration, compared to the internal antenna.”

## Slide 17: SNS external antenna source background & plans
In 2014-15 the design evolved to allow persistent beams of 50-55 mA through the LEBT measured on the test stand (no RFQ) for periods 5-6 weeks
Now it is important to update documentation of source drawings and procedures (assembly, installation, operation, removal, refurbishment and troubleshooting) to bring the source to operational readiness.
This year testing resumes on the BTF to support long 6D experimental runs which is an ideal to develop this operational rigor with the source
~52mA for 34 days
~56mA for 40 days

## Slide 18: Recent external antenna source performance on the BTF – beam out of RFQ
Source x4: ~40mA, 14 days, 35kW
Source x3: ~40mA, 11 days, 35kW
~45 kW
~50 mA
In late 2017 all reliability data from extended BTF usage will be examined and compared with baseline source performance and the decision made to use on the SNS

## Slide 19: Summary and outlook
In 2016 we delivered record beam currents, up to 7 A·h and 99.5% availability with no unscheduled source changes, aiming for 10 A·h matching the target service cycle with a single source!
BTF ion source systems routinely delivered 40 mA out of the RFQ supporting the research program, tested with five different sources
Two external antenna ion sources were tested on the BTF produced up to 50 mA and 40 mA for multiple week runs. Reliability data will determine use on SNS accelerator.
Baseline source #2 or #4 can provide 1-1.2 MW operations with the Berkeley RFQ with sufficient margin
Sources with the new RFQ can provided 40 mA output beams, as demonstrated now routinely on the BTF, easily supporting 1.4 MW operations and closing the gap to PPU requirements!